Okechukwu Akpa

ELEC 7770-001, Spring 2008

Class Project

The project for Advance VLSI centered around the test and verification of a 32-bit multiplier circuit. The schematic of a 32-bit multiplier appears below.

Below is the Verilog behavioral model for an unsigned 32-bit multiplier used for this project.  ModelSim was used to create this circuit.

module unsingned_mult(start, clk, done, of, product, multiplier, multiplicand);

output done, of;

output [63:0] product;

input [31:0] multiplier, multiplicand;

input clk, start;

wire done, of;

wire [31:0] multiplier, multiplicand;

reg [31:0] unsingned_mult;

reg [63:0] product;

reg [5:0] control;

wire lsb = product[0];

wire [31:0] sum;

assign done = control[5];

wire shiftreg = ~control[5];

wire [31:0] lsbunsingned_mult = { 32{ lsb }} & unsingned_mult;

adder32 adder32i(.of( of ), .sum( sum ), .m1( product[63:32] ), .m2( lsbunsingned_mult ));

always @(posedge clk)

if (start)

unsingned_mult <= multiplier;

always @(posedge clk)

if (start)

control <= 6'b000000;

else

control <= control + shiftreg;

always @(posedge clk)

if (start)

product <= {32'b0, multiplicand};

else if (shiftreg)

product <= {of, sum, product[31:1]};

endmodule

module adder32(of, sum, m1, m2);

Verification

Some test cases were used to verify the operation of the multiplier which are summarized in the table below.

| Clk | Start | Multiplier (Hex) | Multiplicand (Hex) | Product | Done |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | 1B5679E | 2345A72 | 0 | 0 |
| 1 | 0 | 1B5679E | 2345A72 | 3C442D14DB05C | 1 |
| 1 | 1 | 1B5679E | 762A267 | 0 | 0 |
| 1 | 0 | 1B5679E | 762A267 | C9E5C780AAC92 | 1 |
| 1 | 1 | 4B5C79E | 232A2B7 | 0 | 0 |
| 1 | 1 | 4B5C79E | 232A2B7 | A5A0E9F1FADF2 | 1 |

This post synthesis verification proves the behavioral model works.  However, it would take considerable time to input all test cases to completely verify the design.  To prove how reliable the circuit design is Mentor Graphics will be used to optimize and provide additional testing.  This multiplier was synthesized in Leonardo using TSMC0.35 micron technology statistics from the netlist appear below.

Gate Composition

*******************************************************

Cell: unsingned_mult    View: INTERFACE    Library: work

*******************************************************

Cell       Library  References     Total Area

ao32        tsmc035_typ     1 x      2      2 gates

aoi21       tsmc035_typ     3 x      1      4 gates

aoi32       tsmc035_typ    30 x      2     52 gates

dff         tsmc035_typ   116 x      5    556 gates

inv01       tsmc035_typ    31 x      1     24 gates

inv02       tsmc035_typ    16 x      1     12 gates

mux21_ni    tsmc035_typ    98 x      2    177 gates

nand02      tsmc035_typ    36 x      1     36 gates

nand03      tsmc035_typ     1 x      1      1 gates

nand04      tsmc035_typ     3 x      1      4 gates

nor02ii     tsmc035_typ     1 x      1      1 gates

nor03_2x    tsmc035_typ     1 x      1      1 gates

oai21       tsmc035_typ     7 x      1      9 gates

oai32       tsmc035_typ    31 x      2     54 gates

or02        tsmc035_typ     1 x      1      1 gates

or03        tsmc035_typ     2 x      2      3 gates

or04        tsmc035_typ     1 x      2      2 gates

xnor2       tsmc035_typ     1 x      2      2 gates

xor2        tsmc035_typ    61 x      2    129 gates

Number of ports :                     132

Number of nets :                      541

Number of instances :                 441

Number of references to this view :     0

Total accumulated area :

Number of gates :                    1070

Number of accumulated instances :     441

Clock Frequency

Clock Frequency Report

Clock                : Frequency

------------------------------------

clk                  : 73.9 MHz

Critical Path and Delay

Critical Path Report

Critical path #1, (unconstrained path)

NAME                                  GATE              ARRIVAL              LOAD

---------------------------------------------------------------------------------

clock information not specified

delay thru clock network                                0.00 (ideal)

reg_product(0)_rep_10/Q               dff         0.00  0.55 dn             0.07

ix2959/Y                              nand02      0.22  0.78 up             0.02

ix1015/Y                              xor2        0.53  1.30 dn             0.04

ix2968/Y                              aoi32       0.32  1.62 up             0.03

ix131/Y                               inv01       0.10  1.72 dn             0.01

ix2981/Y                              aoi32       0.28  2.00 up             0.03

ix147/Y                               inv01       0.10  2.10 dn             0.01

ix2994/Y                              aoi32       0.28  2.37 up             0.03

ix163/Y                               inv01       0.10  2.47 dn             0.01

ix3007/Y                              aoi32       0.28  2.75 up             0.03

ix179/Y                               inv01       0.10  2.84 dn             0.01

ix3020/Y                              aoi32       0.28  3.12 up             0.03

ix195/Y                               inv01       0.10  3.22 dn             0.01

ix3033/Y                              aoi32       0.28  3.49 up             0.03

ix211/Y                               inv01       0.10  3.59 dn             0.01

ix3046/Y                              aoi32       0.28  3.87 up             0.03

ix227/Y                               inv01       0.10  3.97 dn             0.01

ix3059/Y                              aoi32       0.28  4.24 up             0.03

ix243/Y                               inv01       0.10  4.34 dn             0.01

ix3072/Y                              aoi32       0.28  4.62 up             0.03

ix259/Y                               inv01       0.10  4.71 dn             0.01

ix3085/Y                              aoi32       0.28  4.99 up             0.03

ix275/Y                               inv01       0.10  5.09 dn             0.01

ix3098/Y                              aoi32       0.28  5.36 up             0.03

ix291/Y                               inv01       0.10  5.46 dn             0.01

ix3111/Y                              aoi32       0.28  5.74 up             0.03

ix307/Y                               inv01       0.10  5.83 dn             0.01

ix3124/Y                              aoi32       0.28  6.11 up             0.03

ix323/Y                               inv01       0.10  6.21 dn             0.01

ix3137/Y                              aoi32       0.28  6.48 up             0.03

ix339/Y                               inv01       0.10  6.58 dn             0.01

ix3150/Y                              aoi32       0.28  6.86 up             0.03

ix355/Y                               inv01       0.10  6.96 dn             0.01

ix3163/Y                              aoi32       0.28  7.23 up             0.03

ix371/Y                               inv01       0.10  7.33 dn             0.01

ix3176/Y                              aoi32       0.28  7.61 up             0.03

ix387/Y                               inv01       0.10  7.70 dn             0.01

ix3189/Y                              aoi32       0.28  7.98 up             0.03

ix403/Y                               inv01       0.10  8.08 dn             0.01

ix3202/Y                              aoi32       0.28  8.35 up             0.03

ix419/Y                               inv01       0.10  8.45 dn             0.01

ix3215/Y                              aoi32       0.28  8.73 up             0.03

ix435/Y                               inv01       0.10  8.83 dn             0.01

ix3228/Y                              aoi32       0.28  9.10 up             0.03

ix451/Y                               inv01       0.10  9.20 dn             0.01

ix3241/Y                              aoi32       0.28  9.48 up             0.03

ix467/Y                               inv01       0.10  9.57 dn             0.01

ix3254/Y                              aoi32       0.28  9.85 up             0.03

ix483/Y                               inv01       0.10  9.95 dn             0.01

ix3267/Y                              aoi32       0.28  10.22 up             0.03

ix499/Y                               inv01       0.10  10.32 dn             0.01

ix3280/Y                              aoi32       0.28  10.60 up             0.03

ix515/Y                               inv01       0.10  10.69 dn             0.01

ix3293/Y                              aoi32       0.28  10.97 up             0.03

ix531/Y                               inv01       0.10  11.07 dn             0.01

ix3306/Y                              aoi32       0.28  11.34 up             0.03

ix547/Y                               inv01       0.10  11.44 dn             0.01

ix3319/Y                              aoi32       0.28  11.72 up             0.03

ix563/Y                               inv01       0.10  11.82 dn             0.01

ix3332/Y                              aoi32       0.28  12.09 up             0.03

ix579/Y                               inv01       0.10  12.19 dn             0.01

ix3345/Y                              aoi32       0.28  12.47 up             0.03

ix595/Y                               inv01       0.10  12.57 dn             0.01

ix1505/Y                              mux21_ni    0.28  12.85 dn             0.01

ix2839/Y                              ao32        0.47  13.32 dn             0.02

reg_product(63)/D                     dff         0.00  13.32 dn             0.00

data arrival time                                       13.32

Test vectors were generated in the sequential mode

CMD> report statistics

Total number of sequential instances           =   116

*****Circuit Statistics*****

# of primary inputs = 66

# of primary outputs = 66

# of library design cells = 441

# of library leaf cells = 441

# of combinational library primitives = 460

# of sequential library primitives = 116

# of simulation primitives = 1673

The vectors yielded various fault statistics

*****Fault List Statistics*****

Fault Class              Uncollapsed   Collapsed

Full (FU)                       3660        2646

Det_simulation (DS)             3086        2095

Hyp_testable (HT)                136         121

Posdet_untestable (PU)             4           4

Posdet_testable (PT)               3           3

Unused (UU)                      164         164

Atpg_untestable (AU)             232         232

Unobserved (UO)                   35          27

Fault coverage                86.27%      81.59%

Test coverage                 90.32%      86.99%

ATPG effectiveness            97.14%      96.64%

*****Test Patterns Statistics*****

Total Test Cycles Generated = 511

Total Test Cycles Simulated = 1567

Machine Name    : saratoga

User Name       : oza0001

User CPU Time   : 73.1 seconds

System CPU Time : 2.5 seconds

Memory Used     : 68.602 MB

The faults were classified as follows:

Full (FU) stands for the total number of faults in the circuit

Det_Simulation (DS) are faults detected by the simulation

Hyp_testable (HT) hypertrophic faults

Posdet_untestable (PU) proven ATPG_untestable and hard

Posdet_testable (PT)  potentially detectable posdet faults

Unused faults (UU) occur on nets that are not connected in the circuit

Atpg_untestable (AU) occur due to the violation of design rules

Unobserved faults (UO) are unobserved and undetected

A scan was inserted and combinational test vectors were generated.

A full scan design was implemented using the DFTadvisor tool.  The area statistics are shown below.

*******************************************************

Cell: unsingned_mult    View: INTERFACE    Library: work

*******************************************************

Cell       Library  References     Total Area

ao32        tsmc035_typ     1 x      2      2 gates

aoi21       tsmc035_typ     3 x      1      4 gates

aoi32       tsmc035_typ    30 x      2     52 gates

dff         tsmc035_typ   116 x      5    556 gates

inv01       tsmc035_typ    31 x      1     24 gates

inv02       tsmc035_typ    18 x      1     14 gates

mux21_ni    tsmc035_typ    98 x      2    177 gates

nand02      tsmc035_typ    36 x      1     36 gates

nand03      tsmc035_typ     2 x      1      2 gates

nand04      tsmc035_typ     3 x      1      4 gates

nor02_2x    tsmc035_typ     1 x      1      1 gates

nor03_2x    tsmc035_typ     1 x      1      1 gates

oai21       tsmc035_typ     7 x      1      9 gates

oai32       tsmc035_typ    31 x      2     54 gates

or02        tsmc035_typ     1 x      1      1 gates

or03        tsmc035_typ     1 x      2      2 gates

or04        tsmc035_typ     1 x      2      2 gates

xnor2       tsmc035_typ    31 x      2     59 gates

xor2        tsmc035_typ    31 x      2     66 gates

Number of ports :                     132

Number of nets :                      542

Number of instances :                 443

Number of references to this view :     0

Total accumulated area :

Number of gates :                    1065

Number of accumulated instances :     443

The fault classification for fastscan was different from that of the flextest.  There are fewer faults which means this implementation is better, however a new class of fault did occur which was:

Det_Implication (DI) which indicate faults that are detected by implication.

These statistics appear below.

CMD> report statistics

Statistics report

-------------------------------------------

#faults   #faults

fault class               (coll.)   (total)

-----------------------   -------   -------

FU (full)                   3016      4128

-----------------------   -------   -------

DS (det_simulation)         2231      3243

DI (det_implication)         719       819

UU (unused)                   66        66

-----------------------   -------   -------

test_coverage             100.00%   100.00%

fault_coverage             97.81%    98.40%

atpg_effectiveness        100.00%   100.00%

-------------------------------------------

#test_patterns                          42

#simulated_patterns                     64

CPU_time (secs)                        4.7

-------------------------------------------

Area in number of gates went from 1070 to 1065 which is an overhead of 0.47%.

As there is a five gate difference in the two designs, the estimated gate overhead is nominal.  What is gained is that the untested faults are eliminated inserting the scan.

# Text boxes

DONE

CK     START

OF

Add if LSB=1

Initialized product register

00000 . . . 00000  32-bit multiplier

shift

right

Test LSB

Control: Do

32 times

32-bit Adder

32

32

32

Multiplicand

64-bit product register