ELEC 7770-001, Spring 2012

Homework # 3 Problems

Assigned: Wednesday, March 7, 2012

# Due: Wednesday, March 21, 2012

# Problem 1: A ripple carry adder is made of full adder cells each having 1 unit of combinational delay. To convert a four-bit ripple carry adder into a four stage pipeline adder proceed as following:

# Consider the original adder as a one-stage pipeline with clock period of 4 time units. Construct the retiming graph. Note the critical path delay is 4 units.

# To model a four stage pipeline that will have a latency of four clock cycles, insert four clock delays on the edge that connects the output node to host.

# Retime the graph such that the longest combinational path has one unit of delay. This can be done either by solving the constraint set problem or by moving the clock delays according to retiming rules.

# Sketch the circuit schematic with flip-flops.

# Problem 2: The schematic of a processor is shown below. Grey bars are clocked pipeline registers and combinational delays are as indicated. Originally, a 100ps clock is routed for zero skew. Find the skews S1, S2, S3, S4 and S5 that will provide the fastest speed.

# Problem 3: An output buffer has an input capacitance of 250fF and a load capacitance of 100pF. How many inverters are required in a fixed-taper design to minimize the propagation delay? What are the capacitances of those stages? What is the total delay the buffer contributes if 100ps is the delay of the gate driving the buffer?

# Hint: Besides class notes, the following references may be helpful:

# H. C. Lin and L. Linholm, “An Optimized Output Stage for MOS Integrated Circuits,” IEEE Jour. Solid State Circuits, vol. SC-10, no. 2, pp. 106-109, April 1975.

# J. Segura and C. F. Hawkins, CMOS Electronics, How It Works, How It Fails, IEEE Press, Wiley-Interscience, 2004, pp. 116-118.

# Text boxes

S1

S5

S2

S3

S4

Adder

75ps

Instr

Cache

90ps

Adder

&

Reg

File

75ps

ALU

100ps

Data

Cache

90ps

CK