ELEC 7770 Spring 2014

Homework 1

Assigned 1/10/14, due 1/17/2014

Design a 4-bit ripple carry adder designed in 45 nm CMOS technology using the techniques covered in class. Apply 5 random test vectors at the best possible clock.

You will need to use the tools and techniques taught in class to complete this assignment.

- Write a VHDL or Verilog code for 4-bit ripple carry adder (The VHDL code for a 1 bit adder has been provided, feel free to use this code to create an 4-bit adder, else you can write your own).

- Using Spectrum, get the synthesized Verilog netlist. You should also use the report delay command to get the critical path.

- Import the netlist in DesignArchitect, and extract the spice netlist. You can also verify if the design is a ripple carry adder in the Schematic viewer.

- Modify the SPICE netlist for 45 nm technology (the ptm file has been provided), and run the HSPICE simulation for 5 random vectors of your choosing. You can either create a vector file, or force PULSE or PWL on each input node.

You must submit the following:

- Delay report obtained from Spectrum especially highlighting the critical path.

- A screen-shot of your design when imported in DesignArchitect to verify if the design is a ripple carry adder.

- A list of your 5 random vectors you used to run the spice simulation.

- Total power dissipated in the simulation (RMS and average).

  - Please explain the difference between average and RMS power if there is a difference in the two results and which one should be used.

- A screenshot of the sum and carry output transitions from EZWave.

- Explain briefly the reason for each transition at the application of each input vector.

E.g. If you are applying vectors at 1ns, comment why at 1ns the output of sum[3], sum[2], sum[1], sum[0], cout changed etc. Comment on all transitions.

This following is not part of HW 1:

- You need to be aware of the working of serial and parallel load and shift registers.

- Try to create and understand the design of a VHDL or Verilog model of a 4 bit load and shift register. You might need it in one of your HWs.