ELEC 7770-001, Spring 2014

Homework # 4 Problems

Assigned: Friday, April 4, 2014

# Due: Friday, April 11, 2014

Problem 1: A Bluetooth transmitter amplifier operates over a frequency band 2.4 – 2.5GHz. It is specified to have a minimum gain of 22dB and a gain flatness of 0.5dB. The scatter parameter S21 is measured as signal amplitude ratio under matched conditions as: S21 = 15.21 at 2.4GHz and S21 = 14.17 at 2.5GHz. Does the device meet specifications?

Problem 2: An RF power amplifier (PA) operates with a 3V dc supply. Following measurements are taken: RF input power 1dBm, RF output power 30dBm, device current 3A. What is the power added efficiency (PAE)?

# Problem 3: Show that for a nonlinear device with a single frequency input of amplitude A, the nth harmonic component in the output always contains a term proportional to An.

# Problem 4: Small signal gain of an amplifier is 20dB. What is the gain at 1dB compression point? The input-referred 1dB compression point power level is –15dBm. What is the output-referred 1dB compression power level?

# Problem 5: Input to a nonlinear device contains two signals in equal magnitude A of frequencies f1 and f2. Show that:

# Output amplitude of each fundamental frequency, f1 or f2, is

# 9

# a1 A  +  —  a3 A3  	≈ 	a1 A

# 4

# Output amplitude of each third-order intermodulation frequency, 2f1 – f2 or 2f2 – f1, is

# 3

# —  a3 A3

# 4

# Where a1 and a3 are constants.

# Problem 6: Write the distortion (harmonic and inter-modulation) frequencies generated from fundamental tones 100MHz and 100.5MHz up to seventh order. Identify distortion frequencies that are within 2MHz from the fundamental frequencies.

# What is the number of kth order distortion frequencies? Derive an expression.

# Problem 7: Determine the noise power expressed in dBm/Hz delivered to a matched load by a resistance of R ohms at the normal room temperature.

# Problem 8: For an RF device a spectrum analyzer provides the following data:

# Resolution bandwidth (RBW)			=	10Hz

# Carrier power,				Pc	=	– 3.31 dBm

# Power at 2kHz offset from carrier,  Po	=	– 81.17 dBm

# Determine phase noise in dBc/Hz at 2kHz from the carrier.