VLSI Testing

August 2013

Homework 1 Problems

Assigned Aug 17, 2013, due in class on Aug 19, 2013

Q1.	In a VLSI chip manufacturing process the probability of failing a good chip is α and that of passing a bad chip is β, where α << 1 and β << 1. If the yield is y, then show that the defect level (DL) is,

β(1 – y)

DL  ≈  ――――

(1 – α)y

When α = 0.05, β = 0.001 and y = 0.9, find DL in PPM.

Q2.	A state of the art mixed-signal automatic test equipment (ATE) costs $10M to purchase and install. Its maintenance and operating cost is $2M/year. Assuming that the ATE will be fully depreciated in 10 years, compute the cost of digital test time in cents per second.

Q3. What is the cost of a mixed-signal VLSI chip for the following data:

Cost of processing a wafer 		= 	$500

Number of chips on a wafer		= 	500

Analog test time 				= 	2.0s

Digital test clock rate 			= 	1GHz

Number of digital test vectors 	= 	109

Chip yield 					= 	78%

Assume the test cost data of Problem 2. What should the yield be to reduce the cost below $1.50?