VLSI Testing

August 2013

Homework 4 Problems

Assigned Aug 26, 2013, due Aug 29, 2013.

Answer the following questions, selecting just one answer per question.

--------------------------------------------------------------------------------------------

1. What is the total number of single stuck-at faults in a ten-input AND gate?

- 10

- 11

- 20

- 22

- None of the above

--------------------------------------------------------------------------------------------

2. What is the minimum number of single stuck-at faults guaranteed to be detected in a combinational circuit by a binary (0,1) vector?

- Number of primary inputs

- Number of primary outputs

- Twice the number of primary inputs

- Twice the number of primary outputs

- Half of all single stuck-at faults in the circuit

--------------------------------------------------------------------------------------------

3.  What is the exact number of single stuck-at faults activated in a combinational circuit by a binary (0,1) vector?

- Number of primary inputs

- Number of primary outputs

- Twice the number of primary inputs

- Twice the number of primary outputs

- Half of all single stuck-at faults in the circuit

--------------------------------------------------------------------------------------------

4.  How many faults can be simulated in a single pass by a parallel fault simulator running on a computer with 32 bit word?

- 1

- 2

- 16

- 31

- 32

--------------------------------------------------------------------------------------------

5.  What determines the size of a random fault sample used for coverage estimation?

- Sample size should be 1% of total faults

- Sample size should be 10% of total faults

- Sample should contain at least half of all faults

- Sample size is based on the required accuracy of coverage estimate

- Sample should contain all faults

--------------------------------------------------------------------------------------------

6. What does the symbol “D” mean in the five-value algebra used in test generation algorithms?

- Don’t care

- Same signal value in fault-free and faulty circuits

- Different signal values in fault-free and faulty circuits

- Logic 1 in fault-free circuit and logic 0 in faulty circuit

- Logic 0 in fault-free circuit and logic 1 in faulty circuit

--------------------------------------------------------------------------------------------

7. For testing a ten-input AND gate, find a single test vector that will detect the largest number of single stuck-at faults?

- 0000000000

- 0101010101

- 0011001100

- 0000011111

- 1111111111

--------------------------------------------------------------------------------------------

8. For a ten-input AND gate, what is the minimum number of test vectors that will detect all single stuck-at faults?

- 1

- 10

- 11

- 22

- 1024

--------------------------------------------------------------------------------------------

9. What is the sequential depth of a circuit?

- Number of logic gates in the circuit

- Total number of flip-flops

- Number of logic gates plus the number of flip-flops

- Maximum number of flip-flops on a primary input to primary output path

- None of the above

--------------------------------------------------------------------------------------------

10. What is the maximum number of vectors that may be needed to detect a single stuck-at fault in a cycle-free synchronous sequential circuit?

- 2n vectors where n is the number of primary inputs in the circuit

- Vectors may equal total number of flip-flops

- One vector more than the sequential depth

- Maximum number of flip-flops on a primary input to primary output path

- None of the above

--------------------------------------------------------------------------------------------

11. What is the critical path of a synchronous sequential circuit?

- Path with largest number of gates

- Combinational path with longest delay

- Path that is easiest to sensitize

- Path that is most difficult to sensitize

- Any path that can be robustly tested for delay fault

--------------------------------------------------------------------------------------------

12. What is the number of transition delay faults in a circuit?

- Number of paths in the circuit

- Same as the number of collapsed single stuck-at faults

- Same as the number of uncollapsed single stuck-at faults

- Number of gates in the circuit

- Number of flip-flops in the circuit

--------------------------------------------------------------------------------------------

13. What should be the complexity of a memory test sequence for an n-bit memory?

- O(n)

- O(n2)

- O(n1.5)

- O(n log n)

- Exponential in n

--------------------------------------------------------------------------------------------

14. What does a memory contains after completion of the MATS+ test sequence:

{  ↕  (w0);  ↑  (r0, w1);   ↓ (r1, w0) }?

- Alternating 0-1 pattern

- Random bits

- All 1’s

- All 0’s

- 0’s in half lower order addresses and the rest 1’s

--------------------------------------------------------------------------------------------

15. The testing of analog circuits requires:

- Test of stuck-at faults

- Test of path delay faults

- Measurement of resistors and capacitors

- Current and voltage measurements

- Verification of the circuit’s functional specification

--------------------------------------------------------------------------------------------

16. The essential minimum number of test pins added for scan design is:

- 1

- 3

- Number of flip-flops

- Log (Number of flip-flops)

- None

--------------------------------------------------------------------------------------------

17. How many clock cycles will the testing of a scan circuit with 10,000 scan flip-flops and 1,000 combinational vectors will take:

- 1 million

- 1 billion

- 1,000

- 10,000

- 10,021,004

--------------------------------------------------------------------------------------------

18. What are the principal benefits of scan design?

- High fault coverage

- Reduced test time during manufacturing

- Reduced test generation complexity and high fault coverage

- Faster circuit speed

- No hardware overhead for improved testing

--------------------------------------------------------------------------------------------

19. An n-stage linear feedback shift register (LFSR) with primitive feedback polynomial generates:

- All n-bit patterns in random order

- All n-bit patterns in random order except the all-0 pattern

- All integers from 0 to 2n – 1 in ascending order from 0

- All integers between 0 and 2n – 1 in ascending order ending at 0

- Only few selected patterns

--------------------------------------------------------------------------------------------

20. The aliasing probability for a signature analyzer constructed with an n-stage linear feedback shift register (LFSR) with primitive feedback polynomial is given by:

- 0.0

- 0.5

- Reduced test generation complexity and high fault coverage

- 2 – n

- 1/n

--------------------------------------------------------------------------------------------