Low-Power Design of Digital VLSI Circuits 
July-August 2011

Homework 1 Problems

Assigned 27/7/11, due 29/7/11

Answer the following questions, selecting just one answer per question.

--------------------------------------------------------------------------------------------

1. The inversion encoding for a reduced-power n-bit bus works as follows:

- Bits are always inverted

- Only half the bits are inverted

- Only true (logic 1) bits are inverted

- Only false (logic 0) bits are inverted

- All bits are inverted if the total number of transitions on all wires exceeds n/2

--------------------------------------------------------------------------------------------

2. A 1 microfarad capacitor is charged to a voltage 1 volt through a 500 kilo ohm series resistor. What is the energy dissipated in the resistor?

- 1 watt

- 1 calorie

- 1 micro joule

- 0.5 micro joule

- 1 microwatt

--------------------------------------------------------------------------------------------

3. A digital circuit dissipates 1 nanojoule of energy per cycle. If the clock rate is 2GHz, what is the power consumption of the circuit?

- 1 joule

- 1 nanowatt

- 1 watt

- 2 watt

(   0.5 watt

--------------------------------------------------------------------------------------------

4. Identify the largest component of power in a digital CMOS circuit:

- Static power

- Dynamic power

- Short-circuit power

- Leakage power

- Glitch power

--------------------------------------------------------------------------------------------

5.  How do glitches affect the power consumption of a digital circuit?

- Increase static power

- Increase dynamic and short-circuit power

- Only increase short-circuit power

- Have no influence on power consumption

- Radiate energy

---------------------------------------------------------------------------------------------

6. Short-circuit power can be reduced to zero if,

- Gates are fast

- Supply voltage is below the sum of magnitudes of P and N threshold voltages

- Clock frequency is sufficiently low

- Circuit is kept cool

- Signal rise and fall times are small

--------------------------------------------------------------------------------------------

7. Path balancing and glitch filtering are methods for,

- Speeding up the circuit

- Reducing noise

- Improving reliability

- Saving static or leakage power

- Saving dynamic power

--------------------------------------------------------------------------------------------

8. Higher threshold transistors are slower. So they are used in gates on non-critical paths to,

- Reduce dynamic power

- Balance delay

- Reduce leakage

- Reduce device area

- Improve chip yield

--------------------------------------------------------------------------------------------

9. What is the dynamic power consumption of a 1 million gate VLSI chip for which VDD = 1 volt, average gate capacitance = 1pF, average activity factor (counting both rising and falling transitions) = 10%, clock frequency = 2GHz?

- 100W

- 20W

- 10W

- 2W

- 1W

--------------------------------------------------------------------------------------------

10. Which is the most effective method for reducing the power consumption of a CMOS logic circuit?

- Reduce frequency

- Increase transistor threshold voltages

- Reduce transistor threshold voltages

- Reduce supply voltage

- Use body bias

--------------------------------------------------------------------------------------------