# VLSI Design & Test Seminar, Spring 2006

# (ELEC7950)

Built-In Self-Test for Radio Frequency

System-On-Chip

Speaker:	Bruce C. Kim, bruce.kim@ieee.org

University of Alabama

Date: 		Wednesday, March 1, 2006

Time: 		4:00 pm

Room: 	Broun 235

Abstract – The traditional way of testing RF SoC involves measurements of S-parameters, gain, noise figures and third-order input intercept points (IIP3) using variety of different RF test equipment. This is highly labor-intensive and requires expensive measurement equipment. Our proposed RF BIST (Built-In Self-Test) technique utilizes on-chip hardware circuit to measure important RF specifications without major external test equipment. Our new RF BIST circuit provides dc output voltages, thus making the overall test setup simple and inexpensive. These dc output voltages are converted to units of decibels and ohms by using the equations we developed for the RF device under test. The BIST technique requires an additional RF amplifier and two RF peak detectors. The BIST circuit is designed using 0.18μ SiGe technology. Simulation results are presented for an LNA working at 5GHz. Measurement data are compared with simulation results to validate the developed mathematical equations. The technique is simple and inexpensive.

Bruce C. Kim received his B.S.E.E. degree from the University of California, Irvine in 1981, his M.S. in electrical engineering from the University of Arizona in 1985, and his Ph.D. in electrical engineering from Georgia Institute of Technology in 1996. He is currently an Associate Professor with the Department of Electrical and Computer Engineering at the University of Alabama, Tuscaloosa. Prior to joining the University of Alabama, he was an Associate Professor with Arizona State University. His current research interests include RF IC testing, VLSI  integration with MEMS and nano technology circuits. Kim is a 1997 recipient of the National Science Foundation’s CAREER Award and received the Meritorious Service and Outstanding Contribution Awards from IEEE. He serves as the chair of the IEEE Components, Packaging, and Manufacturing Technology (CPMT) Society TC-11, the Technical Committee on Electrical Test, associate editor and guest editor of the IEEE Transactions on Advanced Packaging, and associate editor of IEEE Design & Test of Computers. He has been serving as the newsletter editor of IEEE Test Technology Technical Council and JETTA. He has served as the coauthor and advisor of educational awards from the IEEE CPMT Society and International Microelectronics and Packaging Society (IMAPS). He is a senior member of IEEE and IMAPS.

Seminar Website: http://www.eng.auburn.edu/~vagrawal/D&TSEMINAR_SPR06/D&TSeminar.html

Coordinator: Vishwani Agrawal, vagrawal@eng.auburn.edu