ELEC 5970-001/6970-001 Special Topics in Electrical Engineering
Low-Power Design of Electronic Circuits 
Fall 2005

Exam 2

Assigned 11/27/05, due 12/08/05

Attempt all problems.						Total points 30

Problem 1: A combinational one-bit adder cell with a carry input is fully tested by five vectors 000, 111, 001, 010 and 101.

- Give a procedure to re-sequence these vectors to minimize the peak power consumption during test.

- How will you further reduce the average power consumption of the re-sequenced test vectors?

10 points

Problem 2: A two-bit synchronous counter has two inputs, C and R, and one output Z. R is a synchronous reset such that when R=1, the clock forces the circuit to initial state S0. When R=0 and C=1, the clock cycles the counter through states, S0 → S1 → S2 → S3 → S0 . . . When R=0 and C=0, the counter holds its state. The output Z=1 only when the counter is in state S3. Otherwise, Z=0.

- Draw a state diagram and assign states for low-power consumption.

- Implement the combinational logic and sketch a complete schematic.

- Add clock gating logic to the counter designed in b.

10 points

Problem 3: A 200MHz multiplier core has a rated supply voltage of 5V and consumes 15W. The core is also designed to work at reduced supply voltages. Its delay at a supply voltage VDD with respect to the rated (5V) operation is specified as:

Relative delay  =  20.25(VDD – 0.5) – 2

The multiplier core is to be integrated into a 200MHz data path chip but the allocated power budget for the multiplier is only 5W. Devise a multi-core architecture for the multiplier assuming 10% hardware overhead per duplicated core.		10 points

Problem 4 (Bonus Question): (Material not covered in class) Which low-power design techniques do you consider suitable for analog circuits? Give your ideas about why they are suitable and how they can be implemented. Be brief.			3 points