## Slide 1: Pre-Computed Asynchronous Scan Invited Talk
Vishwani D. Agrawal
James J. Danaher Professor
Electrical and Computer Engineering
Auburn University, USA
With help from Praveen Venkataramani, PhD Candidate
Quito, Ecuador, April 13, 2012

## Slide 2: Scan Testing
SFF
SFF
SFF
Combinational
logic
PI
PO
SCANOUT
SCANIN
SE or TCK
Not shown: CK or
MCK/SCK feed all
SFFs.

## Slide 3: Test Time
Total scan test time (Number of scan test clock cycles × clock period):
TT = NT = [(ncomb + 2) nsff + ncomb + 4] × T
Where, ncomb = number of combinational vectors
nsff = number scan flip-flops in the longest scan chain
T = scan clock period
Example: 10,000 scan flip-flops in longest chain, 1,000 comb. vectors, total scan test length, TT ≈ 107 T.
Reference:
  M. L. Bushnell and V. D. Agrawal, Essentials of Electronic Testing for Digital, Memory and Mixed- Signal VLSI Circuits, Springer, 2000.

## Slide 4: Scan Power During a Clock Cycle
Clock period, T
time
Chip current, i(t)
0
T
Cycle energy, E = VDD ∫ i(t) dt
0
Cycle power, P = E/T

## Slide 5: Scan Power During Test With Synchronous Clock
1 2 3 4 5 6 7 8
Clock cycles
Cycle Energy, E
Emax
Cycle power, P
Pmax
E
E
E
E
E
E
E
E
P
P
P
P
P
P
P
P
Scan clock period, T = Emax/Pmax
T
T
T
T
T
T
T
T

## Slide 6: Test Time for Synchronous Clock
N Emax
TTsync = NT = ————
Pmax
Where,
N = Number of scan test clock cycles

## Slide 7: Power vs. Time
Reduce power:
  Use low activity vectors ⇒ slower rise in fault coverage ⇒ more vectors ⇒ longer test time
Reduce test time:
  Use high efficiency vectors ⇒ produce high activity ⇒ increase test power

## Slide 8: Can We Speed Up Scan Testing?
Maximum clock speed is limited by Emax of vectors and Pmax of circuit; T ≥ Emax/Pmax.
For most cycles E << Emax ⇒ reduce period.
Structural limits on clock period:
    Critical path delay (functional and scan)
    Set up and hold times < critical path delay
A variable clock period can be shorter than the global (synchronous) power constrained period, T = Emax/Pmax.

## Slide 9: Asynchronous Scan
Pre-compute energy {Ei} for all clock cycles {i}.
For given power constrain Pmax of the circuit, set the period Ti of ith clock cycle as:
Ti = max {Ei/Pmax, critical path delay}
= Ei/Pmax, for power constrained testing
Where critical path delay can be different for scan and normal mode cycles.

## Slide 10: Scan Power During Test With Asynchronous Clock
1 2 3 4 5 6 7 8
Clock cycle, i
Cycle Energy, E
Emax
Cycle power, P
Pmax
E
E
E
E
E
E
E
E
P
P
P
P
P
P
P
P
Scan clock period, Ti = Ei/Pmax
T1
T7
T5
T2
T8
T3
T4
T6

## Slide 11: Test Time for Asynchronous Clock
N N
TTasyn = Σ Ti = Σ Ei/Pmax
i=1 i=1
N 1 N
= ——— × — Σ Ei
Pmax N i=1
N Eav Etotal
= ——— = ———
Pmax Pmax

## Slide 12: Comparing Two Scans
Test time (arbitrary units)
200
150
100
50
0
TTsync
TTasyn
Pmax
Emax/Eav = 4

## Slide 13: Test Time Reduction
N Emax
TTsync = ————
Pmax
N Eav Etotal
TTasyn = ——— = ———
Pmax Pmax
TTsync/TTasyn = Emax/Eav ≥ 1

## Slide 14: Theorem
For any given Pmax, minimum test time has a lower bound, obtained upon dividing the smallest synchronous scan test time by the Emax/Eav ratio. This lower bound is achieved by asynchronous scan when every cycle consumes Pmax.

## Slide 15: Comparing Tests
time
Energy
Emax/Eav = 2
1.0
0.5
0.0
time
Energy
Emax/Eav = 5
1.0
0.5
0.0
Low power test

## Slide 16
Chart: Time (µs)
Asynchronous clock
Synchronous clock, T = 40ns
Pmax= 0.711 mW
Pav = 0.455 mW
TTsync, 40ns clock
TTasyn
Spice Simulation: s289 (14FF) Scan Test
Notes: Circuit s289 Total Test patterns = 33 ATPG patterns + 2 Additional set of patterns with alternate 1’s and 0’s
Pmax= 0.711 mW Pavg = 0.455 mW Test cycles = 14 Scan shift cycles + 1 Capture cycle
Synchronous clock period = 40ns Test Time Synchronous= 21.010 µs Test Time Asynchronous= 13.459 µs Gain=1.562

## Slide 17
Chart: Time (µs)
Asynchronous clock
Synchronous clock, T = 80ns
Spice Simulation: s289 (14FF) Scan Test
Pmax= 0.356 mW
Pav = 0.228 mW
TTasyn
TTsync, 80ns clock
Notes: Circuit s289 Total Test patterns = 33 ATPG patterns + 2 Additional set of patterns with alternate 1’s and 0’s
Pmax= 0.356 mW Pavg = 0.228 mW Test cycles = 14 Scan shift cycles + 1 Capture cycle
Synchronous clock period = 40ns Test Time Synchronous= 42.021 µs Test Time Asynchronous= 26.902 µs Gain=1.562

## Slide 18
Chart: Time (µs)
Asynchronous clock
Synchronous clock, T = 80ns
Pav = 0.228 mW
Spice Simulation: s289 (14FF) Scan Test
Notes: Circuit s289 Total Test patterns = 33 ATPG patterns + 2 Additional set of patterns with alternate 1’s and 0’s
Pmax= 0.228 mW Pavg = 0.228 mW Test cycles = 14 Scan shift cycles + 1 Capture cycle
Synchronous clock period = 40ns Test Time Synchronous= 42.021 µs Test Time Asynchronous= 42.021 µs Gain=1

## Slide 19
Chart: Pmax, Peak Power (mW)
| 0.71138000000000001 | 0.5319199999999995 | 0.38484000000000035 | 0.23791000000000018 | 0.17888999999999999 | 0.14313000000000001 | 0.11839000000000002
Synchronous Clock | 19.81 | 26.4132 | 39.6198 | 59.4297 | 79.2396 | 99.0495 | 118.8594
Asynchronous Clock | 12.83 | 16.1655 | 23.58 | 38.4513 | 51.1446 | 63.948 | 77.3244
Test Time Synchronous
Test Time Asynchronous
=
1.54
Test Time (Synchronous)
Test Time (Asynchronous)
Spice Simulation: s298 Test Time Ratio
Notes: Test time Gain = (Test Time Synchronous clock)/(Test time adaptive clock)
Synchronous Clock Asynchronous Clock Test Time Synchronous Test Time Asynchronous Ratio
0.711 0.711 19.81 12.83 1.544
0.532 0.532 26.41 16.17 1.634
0.385 0.385 39.62 23.58 1.680
0.238 0.238 59.43 38.45 1.546
0.179 0.179 79.24 51.14 1.549
0.143 0.143 99.05 63.95 1.549
0.118 0.118 118.86 77.32 1.537

## Slide 20
Chart: Time (µs)
Asynchronous clock
Synchronous clock, T 40ns
Spice Simulation: s713 Scan Test
Pmax = 1.06mW
Pav = 0.53mW
Notes: Circuit: s713
Total Vectors = 60 Atpg vectors
Constant clock period = 40ns
Gain: 2

## Slide 21: Conclusion
Total test energy (Etotal) is invariant for a test.
Cycle power (Pmax) is a circuit characteristic.
For power constrained scan testing,
  Synchronous clock test time = Etotal/Pav
  Asynchronous clock test time = Etotal/Pmax
Asynch. clock test will benefit from low energy tests.
Recent work on adaptive clock BIST (VTS’11, VLSI Design’12, etc.).
Future explorations may investigate energy reduction techniques like reduced voltage testing.
Test programming for asynchronous clock needs to be worked out.