## Slide 1: Simplicity Favors Regularity
James Tacey

## Slide 2: Overview
RISC architecture
Only 1 instruction type
Multicycle
Simplified datapath
2 user-controlled registers

## Slide 3: Instruction Architecture
Opcode Reg Dest Address
XXXX X XXXXXXXXXXX
Every instruction accesses memory
Regularity of the instructions allows simplicity in datapath and controller
Not every instruction uses every field

## Slide 4: Instructions
Opcode | Instruction | Effect
0000 | ADD REG, ADDRESS | REG + data in ADDRESS -> REG
0001 | SUB REG, ADDRESS | REG - data in ADDRESS -> REG
0010 | AND REG, ADDRESS | REG & data in ADDRESS -> REG
0011 | XOR REG, ADDRESS | REG XOR data in ADDRESS -> REG
0100 | NOT REG | NOT REG -> REG
0101 | SHL REG | SHL REG -> REG
0110 | SHR REG | SHR REG -> REG
0111 | OR REG, ADDRESS | REG¦¦ data in ADDRESS -> REG
1000 | LDR REG, ADDRESS | Load data in ADDRESS into REG
1001 | STR REG, ADDRESS | Store data in REG into ADDRESS
1010 | HLT | Halts processor
1011 | JRR ADDRESS | Jumps to address stored in internal register
1100 | JMP ADDRESS | Unconditional Jump
1101 | JR ADDRESS | Jump and store current address in internal register
1110 | JP REG, ADDRESS | Jump if REG is positive
1111 | JZ REG, ADDRESS | Jump if REG is zero

## Slide 5: Process Flow
Fetch
Decode
Memory Access
Execution
Write

## Slide 6: Datapath

## Slide 7: Pros and Cons
Pros:
  Simple and effective
  Only one type of instruction
  Many aspects of traditional datapath are integrated into controller
Cons:
  Requires memory access for every instruction
  Controller design is more complex

## Slide 8: Status
Working
  Fully simulated and verified as expected
  Downloads successfully to board
Problems
  Board does not run as expected
  In-System Memory Content Editor causes Quartus II to crash
  PC does not increment as expected

## Slide 9: Questions?