## Slide 1
Test Time Reduction in ATE Using Asynchronous Clocking
Praveen Venkataramani and Vishwani D. Agrawal
Department of Electrical and Computer Engineering, Auburn University, Auburn, AL 36849
Abstract
Advanced CMOS VLSI technologies for low power applications mandate power constrained testing that results in long test time and increased ATE (Automated Test Equipment) costs. We present a new methodology in which the test clock rate is dynamically varied based on the per cycle energy dissipation to optimally reduce the test time.
Synchronous vs. Asynchronous Testing
Scan Test of s298, 350nm CMOS, PMAX = 0.7mW
Summary
It is possible to reduce test time by dynamically customizing the test clock period based on cycle by cycle energy dissipation. The new test time is reduced by the ratio of peak energy to the average energy dissipated in a test cycle. The work on implementing the proposed method on an ATE is in progress at the Auburn University.
References
M. L. Bushnell and V. D. Agrawal, Essentials of Electronic Testing for Digital, Memory and Mixed-Signal VLSI Circuits. Boston: Springer, 2000.
P. Shanmugasundaram and V. D. Agrawal, “Dynamic Scan Clock Control for Test Time Reduction Maintaining Peak Power Limit,” Proc. 29th IEEE VLSI Test Symposium, May 2011, pp. 248 –253.
V. D. Agrawal, “Pre-Computed Asynchronous Scan (Invited Talk),” 13th IEEE Latin American Test Workshop, Quito, Ecuador, April 2012.
Theorem 1
The minimum test time for a synchronous test is the ratio of total energy consumed during the entire test to the average power for all test cycles.
The minimum possible test time is the ratio of total energy consumed during the entire test to the peak power of any test cycle. This test time is achievable by asynchronous clock testing:
Overview
Total scan test time (Number of scan test clock cycles × clock period):[1]
TT = N×T
Where,
N = total test clock cycles = (ncomb + 2) nsff + ncomb + 4
ncomb = number of combinational vectors
nsff = number scan flip-flops in the longest scan chain
T = scan clock period
, TT(async.) = ≤ TT(sync.)
Asynchronous Clock Testing (Proposed)
, TT(sync.) =
Synchronous Clock Testing (Conventional)
P = E/T
P = E/Ti
Theorem 2
Scan Test of s382, PMAX = 0.9mW, PAVG = 0.692mW
Scan Test of s713, PMAX = 1.03mW, PAVG = 0.53mW