## Slide 1: Invited Seminar Power and Time Tradeoff in VLSI Testing
Vishwani D. Agrawal
James J. Danaher Professor
Dept. of Electrical and Computer Engineering
Auburn University, Auburn, AL 36849
vagrawal@eng.auburn.edu
http://www.eng.auburn.edu/~vagrawal
Heritage Institute of Technology
Department of Computer Science
Kolkata, India, July 13, 2012

## Slide 2: Outline
Power consumption in VLSI circuits.
Test time.
Power constrained test.
Test scheduling for SoC devices.

## Slide 3: Power

## Slide 4: CMOS Logic (Inverter)
F. M. Wanlass and C. T. Sah, “Nanowatt Logic using Field-Effect Metal-Oxide-Semiconductor Triodes,” IEEE International Solid-State Circuits Conference Digest, vol. IV, February 1963, pp. 32-33.
No current flows from power supply!
Where is power consumed?
VDD
GND
PMOS
transistor
NMOS
transistor

## Slide 5: CMOS Gate Power
V
Ground
C
R = Ron
Large
resistance
vi (t)
v(t)
i(t)
time
v(t)
i(t)
isc(t)
Leakage
current
isc(t)
and
Leakage
Notes: 2

## Slide 6: Components of Power
Dynamic
  Signal transitions
    Logic activity
    Glitches
  Short-circuit (small)
Static
  Leakage
Ptotal = Pdyn + Pstat
= Ptran + Psc + Pstat

## Slide 7: Power Considerations in Design
A circuit performs certain function. Its design must allow the power consumption necessary to execute that function.
Circuit may be implemented low power dissipation in the functional mode.
Power buses are laid out to carry the maximum current necessary for the function.
Heat dissipation of package conforms to the average power consumption during the intended function.
Layout design and verification must account for “hot spots” and “voltage droop” – delay, coupling noise, weak signals.

## Slide 8: Testing Differs from Functional Operation
VLSI chip
system
System
inputs
System
outputs
Functional inputs
Functional outputs
Other chips

## Slide 9: Method of Testing
VLSI chip
Test vectors:
Pre-generated
and stored in
ATE
DUT output for
comparison with
expected response
stored in ATE
Automatic Test Equipment (ATE):
Control processor, vector memory,
timing generators, power module,
response comparator
Power
Clock
Packaged or unpackaged
device under test (DUT)

## Slide 10: Functional Inputs vs. Test Vectors
Functional inputs:
    Functionally meaningful signals
    Generated by circuitry
    Restricted set of inputs
    May have been optimized to reduce logic activity and power
Test vectors:
    Functionally irrelevant signals
    Generated by software to test modeled faults
    Can be random or pseudorandom
    May be optimized to reduce test time; can have high logic activity
    May use testability logic for test application

## Slide 11: An Example
VLSI chip
Binary to
decimal
converter
3-bit random
vectors
8-bit
1-hot
vectors
VLSI chip
system
VLSI chip in system operation
VLSI chip under test
High activity
8-bit
test vectors
from ATE

## Slide 12: Comb. Circuit Power Optimization
Given a set of test vectors
Reorder vectors to minimize the number of transitions at primary inputs
Combinational circuit
(tested by exhaustive
vectors)
01010101
00110011
00001111
01111000
Rearranged vector set 00110011 produces 7 transitions
00011110
11 transitions

## Slide 13: Reducing Comb. Test Power
1 1 0 0 0
1 0 1 0 0
1 0 1 0 1
1 0 1 1 1
V1
V2
V3
V4
V5
3
4
1
3
2
2
3
2
1
1
Original tests:
V1 V2 V3 V4 V5
10 input transitions
Traveling salesperson problem (TSP) finds the shortest distance closed path (or cycle) to visit all nodes exactly once.
But, we need an open loop solution.
Reordered tests:
V1 V3 V5 V4 V2
1 0 0 0 1
1 1 0 0 0
1 1 1 0 0
1 1 1 1 0
5 input transitions

## Slide 14: Open-Loop TSP
Add a node V0 at distance 0 from all other nodes.
Solve TSP for the new graph.
Delete V0 from the solution.
V1
V2
V3
V4
V5
3
4
1
3
2
2
3
2
1
1
V0
0
0
0
0
0

## Slide 15: Combinational Vector Ordering
TSP has exponential complexity; good heuristics are available.
For other extensions:
  V. Dabholkar, S. Chakravarty, I Pomeranz and S. Reddy, “Techniques for Minimizing Power Dissipation in Scan and Combinational Circuits During Test Application,” IEEE Trans. CAD, vol. 17, no. 12, pp. 1325-1333, Dec. 1998.
Typical average power saving:
  30-50%
  50-60% with vector repetition (to satisfy peak power)

## Slide 16: Traveling Salesperson Problem
A. V. Aho, J. E. Hopcroft anf J. D. Ullman, Data Structures and Algorithms, Reading, Massachusetts: Addison-Wesley, 1983.
E. Horowitz and S. Sahni, Fundamentals of Computer Algorithms, Computer Science Press, 1984.
B. R. Hunt, R. L. Lipsman, J. M. Rosenberg, K. R. Coombes, J. E. Osborn and G. J. Stuck, A Guide to MATLAB for Beginners and Experienced Users, Cambridge University Press, 2006.

## Slide 17: Example: A Branch and Bound Method
A combinational circuit is tested by a set of five vectors. The test system initializes to the first vector 0000, which should be retained as the starting vector. Remaining vectors can be arbitrarily sequenced. Find the minimum energy test sequence. How much does your sequence save over the original sequence? The given test vector sequence is:
Vector number  1 2 3 4 5
0 1 1 0 1
0 1 0 1 0
0 1 0 1 0
0 1 0 0 1

## Slide 18: Begin with a Greedy Solution
1
2
5
4
3
2
4
3
3
4
2
1
1 2
Designated start

## Slide 19: Branch and Bound Search
1
2
3
4
5
4
5
2
5
4
3
2
4
4
Slack = 2
3
2
2
1
3
1
3
2
4
2
2
2
Edge weight = 4
Slack = 6
Slack
= – 1
Greedy path
Length = 6
S = 0
S = 0
Terminate search when slack ≤ 0
All searches terminate
before reaching leaf
node. Minimum path
length = 6

## Slide 20: C6288: Test Vector Ordering
Paul Wray, “Minimize Test Power for Benchmark Circuit
c6288 by Optimal Ordering of Vectors,” Class Project,
ELEC 5270, Spring 2009.
PowerPoint Presentation and Report:
www.eng.auburn.edu/~vagrawal/COURSE/E6270_Spr09/course.html

## Slide 21: Scan Testing
Combinational
logic
Scan
flip-
flops
Primary
inputs
Primary
outputs
Scan-in
SI
Scan-out
SO
Scan enable
SE
DFF
mux
SE
SI
D
D
D’
D’
SO
1
0

## Slide 22: Some Properties of Scan Testing
Two modes of operation:
    Normal mode
    Scan mode
Three-step test application:
    Scan-in: sets inputs of logic in scan mode.
    Capture: captures logic outputs in normal mode.
    Scan-out: observes captured outputs in scan mode.
Tests are non-functional; some tests may consume excess power and could have been intentionally avoided in functional mode.

## Slide 23: Example: State Machine
S5
S1
S4
S2
S3
State encoding
S1 = 000
S2 = 001
S3 = 010
S4 = 011
S5 = 100
State transition | Comb. State input changes/clock
000 → 010 | 1
000 → 100 | 1
001 → 011 | 1
010 → 001 | 2
011 → 000 | 2
100 → 011 | 3 (Peak)
Av. transitions | 1.667
Functional transitions
Functional state
transitions

## Slide 24: Reduced Power Design
S5
S1
S4
S2
S3
Reduced power state encoding
S1 = 000
S2 = 011
S3 = 001
S4 = 010
S5 = 100
State transition | Comb. State input changes/clock
000 → 001 | 1
000 → 100 | 1
011 → 010 | 1
001 → 011 | 1
010 → 000 | 1
100 → 010 | 2 (Peak)
Av. transitions | 1.167 (– 30%)
Functional transitions
Functional state
transitions

## Slide 25: Scan Testing: Shift-in, Shift-out
Combinational
logic
FF=0
FF=0
FF=1
Primary
inputs
Primary
outputs
Scan-in
010
Scan-out
100
State transition | Per clock state changes
100 → 010 | 2
010 → 101 | 3
101 → 010 | 3
All transitions | 8
Scan transitions
Shift-in transition
Shift-out transition
Shift-in transitions = Σ (scan chain length – position of transition)
Shift-out transitions = Σ (position of transition)

## Slide 26: Scan Testing: Capture
Combinational
logic
FF=0
FF=1
FF=0
Primary
inputs
1
0
Primary
outputs
Capture transitions: 3
Note that 101 is not a
functional state in the
reduced power state
encoding.
1
0
1
1
1

## Slide 27: A Four Flip-Flop Example
Combinational
Logic
0
0
0
0
F4
F3
F2
F1
0 1 0 1 0
1 0 1 0 0
0 1 0 0 0
1 0 0 0 0
0 1 0 1
10 transitions
Scanout

## Slide 28: Change Scan Chain Order
Combinational
Logic
0
0
0
0
F4
F3
F2
F1
0 0 0 0 0
1 1 0 0 0
0 0 0 0 0
1 0 0 0 0
1 1 0 0
2 transitions
Scanout

## Slide 29: Capture Power
Combinational
Logic
1
0
0
1
F4
F3
F2
F1
0
1
0
1
Next vector states
3 transitions
Scanout
1
0
1
1
Input vector
Output vector

## Slide 30: Vector Order - Select Next Vector
Combinational
Logic
1
1
1
0
F4
F3
F2
F1
0
1
0
1
Next vector states
1111 or 1100 or 0011
Select 1100
3 transitions
Scanout
1
0
1
1
Input vector
Output vector
Captured response

## Slide 31: Dynamic Power of Scan Test
Capture power can be reduced:
  A vector generation problem
Shift-in and shift-out power is reduced by vector ordering.
Further reduction by scan chain ordering:
  Construct a flip-flop node graph; edges weighted with shift in/shift out activity
  Find shortest distance Hamiltonian paths between all node pairs
  Select the path that minimizes shift power

## Slide 32: Shift-in and Shift-out Matrices
F1 → F2 · → · Fj· → ·Fk ·→ · FN F1→F2 → · Fj · → ·Fk · → · FN
V1 0 1 ··· 1 ··· 0 ··· 1 1 1 ··· 1 ··· 0 ··· 0
V2 1 1 ··· 0 ··· 0 ··· 0 0 1 ··· 1 ··· 1 ··· 0
··· ··· ··· ··· ··· ··· ··· ··· ··· ··· ··· ··· ··· ··· ··· ··· ···
Ij Ik Oj Ok
··· ··· ··· ··· ··· ··· ··· ··· ··· ··· ··· ··· ··· ··· ··· ··· ···
VM 0 0 ··· 1 ··· 1 ··· 0 1 0 ··· 0 ··· 0 ··· 1
Flip-flop states for test input Test output states
N Scan flip-flops: F1 through FN; M vectors: V1 through VM

## Slide 33: A Complete Graph
F1
F2
F3
F6
F5
F4
w12
w23
w16
w13
w14
w15
w24
w25
w26
w34
w35
w36
w45
w46
w56
wjk = Hamming(Ij, Ik) + Hamming(Oj, Ok)

## Slide 34: Graph Solutions for Scan Power
High complexity of Hamiltonian path finding requires use of heuristics.
Average power saving: ~30-50% logic, ~10-20% flip-flops.
Y. Bonhomne, P. Girard, Landrault, and S. C. Pravossoudovtich, “Power Driven Chaining of Flip Flops in Scan Architectures,” Proc. International Test Conf., 2002, pp. 796–803.
Y. Bonhomne, P. Girard, L. Guiller, Landrault, and S. C. Pravossoudovtich, “Power-Driven Routing-Constrained Scan Chain Design,” J. Electronic Testing: Theory and Applications, vol. 20, no. 6, pp. 647–660, Dec. 2004.

## Slide 35: Low Power Scan Flip-Flop with Gated Data
DFF
mux
SE
SI
D
DFF
mux
SE
SI
D
SO
D’
D’
SO
SFF: Scan FF cell SFF-GD: Gated data scan FF cell
1
0
CK
CK

## Slide 36: Low Power Scan Flip-Flop with Gated Clock and Data
DFF
mux
SE
SI
D
D’
SO
SFF-GCKD: Gated clock and data scan FF cell
1
0
CK

## Slide 37: s5378: Normal Mode Operation
1,000 random vectors
Clock period = 50ns
Technology: TSMC025
FF cell used | No. of gates | Dynamic power (μW) |  |  |  | Leak. (μW) | Clock (μW) | FF (μW) | Total (μW)
 |  | Logic | Glitch | Dyn. | Sh.Ck. |  |  |  | 
FF | 2958 | 77.9 | 17.5 | 95.4 | 14.1 | 0.129 | 220 | 752 | 1082
SFF | 3137 | 81.8 | 19.5 | 101.3 | 13.9 | 0.130 | 220 | 752 | 1087
SFF-GD | 3317 | 85.1 | 19.8 | 104.9 | 15.0 | 0.132 | 220 | 752 | 1092
SFF-GCKD | 3675 | 89.9 | 56.8 | 146.7 | 23.9 | 0.136 | 119 | 33 | 323

## Slide 38: s5378: Scan Test
Mentor Graphics Fastscan, 98.9% coverage
Clock period = 50ns
Technology: TSMC025
FF cell used | No. of gates | Dynamic power (μW) |  |  |  | Leak. (μW) | Clock (μW) | FF (μW) | Total (μW)
 |  | Logic | Glitch | Dyn. | Sh.Ck. |  |  |  | 
SFF | 3137 | 356.8 | 60.4 | 417.2 | 26.2 | 0.146 | 220 | 849 | 1512
SFF-GD | 3317 | 93.5 | 33.6 | 127.2 | 7.7 | 0.150 | 220 | 851 | 1206
SFF-GCKD | 3675 | 146.8 | 241.9 | 388.7 | 61.9 | 0.154 | 119 | 164 | 734

## Slide 39: Reference for Power Analysis
J. D. Alexander, Simulation Based Power Estimation For Digital CMOS Technologies, Master’s Thesis, Auburn University, Dept. of ECE, December 2008.

## Slide 40: Shift Register Takes Most Power
D Q
D Q
D Q
D Q
D Q
D Q
D Q
D Q
D
CK
Output

## Slide 41: Reduced-Power Shift Register
D Q
D Q
D Q
D Q
D Q
D Q
D Q
D Q
D
CK(f/2)
multiplexer
Output
Flip-flops are operated at full voltage and half the clock frequency.

## Slide 42: Power Consumption of Shift Register
P = C’VDD2f/n
Degree of parallelism, n
1 2 4
Normalized power
1.0
0.5
0.25
0.0
Deg. of parallelism | Freq (MHz) | Power (μW)
1 | 33.0 | 1535
2 | 16.5 | 887
4 | 8.25 | 738
16-bit shift register, 2μ CMOS
C. Piguet, “Circuit and Logic Level
Design,” pages 103-133 in W. Nebel
and J. Mermet (ed.), Low Power
Design in Deep Submicron
Electronics, Springer, 1997.

## Slide 43: Low Power Scan Flip-Flop Reducing Shift Power
D Q
FF1
D Q
FF2
D Q
FFN
Scanin
Scanout
Multi-phase clock generator
CLK
Scan Enable

## Slide 44: Test Time

## Slide 45: Scan Testing
SFF
SFF
SFF
Combinational
logic
PI
PO
SCANOUT
SCANIN
SE or TCK
Not shown: CK or
MCK/SCK feed all
SFFs.

## Slide 46: Test Time
Total scan test time (Number of scan test clock cycles × clock period):
TT = NT = [(ncomb + 2) nsff + ncomb + 4] × T
Where, ncomb = number of combinational vectors
nsff = number scan flip-flops in the longest scan chain
T = scan clock period
Example: 10,000 scan flip-flops in longest chain, 1,000 comb. vectors, total scan test length, TT ≈ 107 T.
Reference:
  M. L. Bushnell and V. D. Agrawal, Essentials of Electronic Testing for Digital, Memory and Mixed- Signal VLSI Circuits, Springer, 2000.

## Slide 47: Scan Power During a Clock Cycle
Clock period, T
time
Chip current, i(t)
0
T
Cycle energy, E = VDD ∫ i(t) dt
0
Cycle power, P = E/T

## Slide 48: Scan Power During Test With Synchronous Clock
1 2 3 4 5 6 7 8
Clock cycles
Cycle Energy, E
Emax
Cycle power, P
Pmax
E
E
E
E
E
E
E
E
P
P
P
P
P
P
P
P
Scan clock period, T = Emax/Pmax
T
T
T
T
T
T
T
T

## Slide 49: Test Time for Synchronous Clock
N Emax
TTsync = NT = ————
Pmax
Where,
N = Number of scan test clock cycles

## Slide 50: Power vs. Time
A good test:
  Should not exceed given power budget, Pmax
  Have short test time, time → cost
Reduce power:
  Use low activity vectors ⇒ slower rise in fault coverage ⇒ more vectors ⇒ longer test time
Reduce test time:
  Use high efficiency vectors ⇒ produce high activity ⇒ increase test power

## Slide 51: Can We Speed Up Scan Testing?
Maximum clock speed is limited by Emax of vectors and Pmax of circuit; T ≥ Emax/Pmax.
For most cycles E << Emax ⇒ can reduce period.
Structural limits on clock period:
    Critical path delay (functional and scan)
    Set up and hold times < critical path delay
A variable clock period can be shorter than the global (synchronous) power constrained period, T = Emax/Pmax.

## Slide 52: Asynchronous Scan
Pre-compute energy {Ei} for all clock cycles {i}.
For given power constrain Pmax of the circuit, set the period Ti of ith clock cycle as:
Ti = max {Ei/Pmax, critical path delay}
= Ei/Pmax, for power constrained testing
Where critical path delay can be different for scan and normal mode cycles.

## Slide 53: Scan Power During Test With Asynchronous Clock
1 2 3 4 5 6 7 8
Clock cycle, i
Cycle Energy, E
Emax
Cycle power, P
Pmax
E
E
E
E
E
E
E
E
P
P
P
P
P
P
P
P
Scan clock period, Ti = Ei/Pmax
T1
T7
T5
T2
T8
T3
T4
T6

## Slide 54: Test Time for Asynchronous Clock
N N
TTasyn = Σ Ti = Σ Ei/Pmax
i=1 i=1
N 1 N
= ——— × — Σ Ei
Pmax N i=1
N Eav Etotal
= ——— = ———
Pmax Pmax

## Slide 55: Two Theorems
The minimum test time for a synchronous test is the ratio of total energy consumed during the entire test to the average power for all test cycles:
The minimum possible test time is the ratio of total energy consumed during the entire test to the peak power of any test cycle. This test time is achievable by asynchronous clock testing:

## Slide 56: Two Theorems
The minimum test time for a synchronous test is the ratio of total energy consumed during the entire test to the average power for all test cycles:
The minimum possible test time is the ratio of total energy consumed during the entire test to the peak power of any test cycle. This test time is achievable by asynchronous clock testing:

## Slide 57: Comparing Tests
time
Energy
Emax/Eav = 2
1.0
0.5
0.0
time
Energy
Emax/Eav = 5
1.0
0.5
0.0
Low power test

## Slide 58
Chart: Time (µs)
Asynchronous clock
Synchronous clock, T = 40ns
Pmax= 0.711 mW
Pav = 0.455 mW
TTsync, 40ns clock
TTasyn
Spice Simulation: s289 (14FF) Scan Test
Notes: Circuit s289 Total Test patterns = 33 ATPG patterns + 2 Additional set of patterns with alternate 1’s and 0’s
Pmax= 0.711 mW Pavg = 0.455 mW Test cycles = 14 Scan shift cycles + 1 Capture cycle
Synchronous clock period = 40ns Test Time Synchronous= 21.010 µs Test Time Asynchronous= 13.459 µs Gain=1.562

## Slide 59
Chart: Pmax, Peak Power (mW)
| 0.71138000000000001 | 0.5319199999999995 | 0.38484000000000035 | 0.23791000000000018 | 0.17888999999999999 | 0.14313000000000001 | 0.11839000000000002
Synchronous Clock | 19.81 | 26.4132 | 39.6198 | 59.4297 | 79.2396 | 99.0495 | 118.8594
Asynchronous Clock | 12.83 | 16.1655 | 23.58 | 38.4513 | 51.1446 | 63.948 | 77.3244
Test Time Synchronous
Test Time Asynchronous
=
1.54
Test Time (Synchronous)
Test Time (Asynchronous)
Spice Simulation: s298 Test Time Ratio
Notes: Test time Gain = (Test Time Synchronous clock)/(Test time adaptive clock)
Synchronous Clock Asynchronous Clock Test Time Synchronous Test Time Asynchronous Ratio
0.711 0.711 19.81 12.83 1.544
0.532 0.532 26.41 16.17 1.634
0.385 0.385 39.62 23.58 1.680
0.238 0.238 59.43 38.45 1.546
0.179 0.179 79.24 51.14 1.549
0.143 0.143 99.05 63.95 1.549
0.118 0.118 118.86 77.32 1.537

## Slide 60
Chart: Time (µs)
Asynchronous clock
Synchronous clock, T 40ns
Spice Simulation: s713 Scan Test
Pmax = 1.06mW
Pav = 0.53mW
Notes: Circuit: s713
Total Vectors = 60 Atpg vectors
Constant clock period = 40ns
Gain: 2

## Slide 61: Test Time Reduction
Circuit | Per cycle peak power (mW) | Test time |  | 
 |  | Synch. (ms) | Asynch. (ms) | Reduction (%)
s298 | 0.08 | 0.021 | 0.014 | 36
s713 | 0.27 | 0.030 | 0.015 | 50
s13207 | 2.11 | 2.220 | 1.354 | 39
s384584 | 7.22 | 7.423 | 5.925 | 20

## Slide 62: Summarizing Asynchronous Scan
Total test energy (Etotal) is invariant for a test.
Cycle power (Pmax) is a circuit characteristic.
For power constrained scan testing,
  Synchronous clock test time = Etotal/Pav
  Asynchronous clock test time = Etotal/Pmax
Asynch. clock test will benefit from low energy tests.
Future explorations may investigate energy reduction techniques like reduced voltage testing.
Test programming for asynchronous clock needs to be worked out.

## Slide 63: References
V. D. Agrawal, “Pre-Computed Asynchronous Scan (Invited Talk),” 13th IEEE Latin American Test Workshop, Quito, Ecuador, April 2012.
P. Venkataramani and V. D. Agrawal, “Test Time Reduction in ATE Using Asynchronous Clocking,” Sixth IEEE International Workshop on Design for Manufacturability and Yield (DFM&Y), San Francisco, CA, June 4, 2012.
P. Venkataramani and V. D. Agrawal, “Reducing ATE Time of Power Constrained Test by Asynchronous Clocking,” submitted to International Test Conf. Poster Session, Anaheim, CA, Nov. 6-8, 2012.
P. Venkataramani and V. D. Agrawal, “Reducing Test Time of Power Constrained Test by Optimal Selection of Supply Voltage,” submitted to 26th International Conf. VLSI Design, Pune, Jan. 5-10, 2013.

## Slide 64: Power and Test Time Tradeoff

## Slide 65: Built-In Self-Test (BIST)
Linear feedback shift register (LFSR)
Multiple input signature register (MISR)
Circuit under test (CUT)
Pseudo-random patterns
Circuit responses
BIST
Controller
Clock
C. E. Stroud, A Designer’s Guide to Built-In Self-Test, Boston: Springer,
2002.

## Slide 66: Test Scheduling Example
R1
R2
M1
M2
R3
R4
A datapath

## Slide 67: BIST Configuration 1: Test Time
LFSR1
LFSR2
M1
M2
MISR1
MISR2
Test time
Test power
T1: test for M1
T2: test for M2

## Slide 68: BIST Configuration 2: Test Power
R1
LFSR2
M1
M2
MISR1
MISR2
Test time
Test power
T1: test for M1
T2: test for M2

## Slide 69: Testing of MCM and SoC
Test resources: Typically registers and multiplexers that can be reconfigured as test pattern generators (e.g., LFSR) or as output response analyzers (e.g., MISR).
Test resources (R1, . . .) and tests (T1, . . .) are identified for the system to be tested.
Each test is characterized for test time, power dissipation and resources it requires.

## Slide 70: Resource Allocation Graph (A Bipartite Graph)
T1
T2
T3
T4
T5
T6
R2
R1
R3
R4
R5
R6
R7
R8
R9

## Slide 71: Definition: Bipartite Graph
A bipartite graph (or bigraph) is a graph whose vertices can be divided into two disjoint sets U and V such that every edge connects a vertex in U to one in V; that is, U and V are independent sets.
Equivalently, a bipartite graph is a graph that does not contain any odd-length cycles.
A bipartite graph has no clique of size 3 or larger.
A bipartite graph can be colored with two colors (chromatic number = 2).

## Slide 72: Test Compatibility Graph (TCG)
T1
(2, 100)
T2
(1,10)
T3
(1, 10)
T4
(1, 5)
T5
(2, 10)
T6
(1, 100)
Tests that form a
clique can be
performed concurrently.
Power
Test time
Pmax = 4

## Slide 73: Definition: Clique
A clique is an undirected graph in which every vertex is connected to every other vertex .
A clique is a complete graph.
the maximum clique problem, is to find the largest clique in a graph.
Finding whether there is a clique of a given size in a graph (the clique problem) is NP-complete.
C. Bron and J. Kerbosch (1973): “Algorithm 457: Finding All Cliques of an Undirected Graph.,” Communications of the ACM, vol. 16, no. 9. ACM Press: New York.

## Slide 74: A Similar Definition: SCC
A directed graph is called strongly connected if there is a path from each vertex in the graph to every other vertex.
Strongly connected components (SCC) of a directed graph are its maximal strongly connected subgraphs. If each strongly connected component is contracted to a single vertex, the resulting graph is a directed acyclic graph (DAG).
T. H. Cormen, C. E. Leiserson, R. L. Rivest, and C. Stein. Introduction to Algorithms, Second Edition, MIT Press and McGraw-Hill, 2001, ISBN 0-262-03293-7.
Finding SCCs, O(V+E)

## Slide 75: Find All Cliques in TCG
CLIQUE NO. i | TEST NODES | TEST LENGTH, Li | POWER, Pi
1 | T1, T3, T5 | 100 | 5
2 | T1, T3, T4 | 100 | 4
3 | T1, T6 | 100 | 3
4 | T1, T5 | 100 | 4
5 | T1, T4 | 100 | 3
6 | T1, T3 | 100 | 3
7 | T2, T6 | 100 | 2
8 | T2, T5 | 10 | 3
9 | T3, T5 | 10 | 3
10 | T3, T4 | 10 | 2
11 | T1 | 100 | 2
12 | T2 | 10 | 1
13 | T3 | 10 | 1
14 | T4 | 5 | 1
15 | T5 | 10 | 2
16 | T6 | 100 | 1

## Slide 76: Integer Linear Program (ILP)
For each clique (test session) i, define:
  Integer variable, xi = 1, test session selected, or xi = 0, test session not selected.
  Constants, Li = test length, Pi = power.
Constraints to cover all tests:
  T1 is covered if x1+x2+x3+x4+x5+x6+x11 ≥ 1
  Similar constraint for each test, Tk
Constraints for power: Pi × xi ≤ Pmax

## Slide 77: ILP Objective and Solution
Objective function:
  Minimize Σ Li × xi
  all cliques
Solution:
  x3 = x8 = x10 = 1, all other xi’s are 0
    Test session 3 includes T1 and T6
    Test session 8 includes T2 and T5
    Test session 10 includes T3 and T4
  Test length = L3 + L8 + L10 = 120
  Peak power = max {P3, P8, P10} = 3 (Pmax = 4)

## Slide 78: A System Example: ASIC Z*
RAM 2
Time=61
Power=241
RAM 3
Time=38
Power=213
ROM 1
Time=102
Power=279
ROM 2
Time=102
Power=279
RAM 1
Time=69
Power=282
RAM 4
Time=23
Power=96
Reg. file
Time = 10
Power=95
Random logic 1, time=134, power=295
Random logic 2, time=160, power=352
* Y. Zorian, “A Distributed Control Scheme for Complex VLSI Devices,”
Proc. VLSI Test Symp., April 1993, pp. 4-9.

## Slide 79: ASIC Z Test Schedule-Heuristic Solution
1200
900
600
300
Power
Power limit = 900
0 100 200 300 400
Test time 331
RAM 1
RAM 3
Random logic 2
Random logic 1
ROM 2
ROM 1
RAM 2
Reg. file
RAM 4
R. M. Chou, K. K. Saluja and V. D. Agrawal, “Scheduling Tests for VLSI Systems under Power Constraints,” IEEE Trans. VLSI Systems, vol. 5, no. 2, pp. 175-185, June 1997.

## Slide 80: ASIC Z: A Better Solution
Obtainable from ILP:
    {RL1, RL2, RAM2} Test length =160
    {RAM1, ROM1, ROM2} Test length = 102
    {RAM3, RAM4, RF} Test length = 38
    Total test length = 300
See, E. Larsson and C. P. Ravikumar, “Power-Aware System-Level Test Planning,” Chapter 6, Section 6.4.1 in Power-Aware Testing and Test Strategies for Low Power Devices, P. Girard, N. Nicolici and X. Wen (Eds.), Springer, 2010.

## Slide 81: References
N. Nicolici and B. M. Al-Hashimi, Power-Constrained Testing of VLSI Circuits, Boston: Springer, 2003.
E. Larsson, Introduction to Advanced System-on-Chip Test Design and Optimization, Springer 2005.
P. Girard, X. Wen and N. A. Touba, “Low-Power Testing,” in System on Chip Test Architectures, L.-T. Wang, C. E. Stroud and N. A. Touba, editors, Morgan-Kaufman, 2008.
N. Nicolici and P. Girard, Guest Editors, “Special Issue on Low Power Test,” J. Electronic Testing: Theory and Applications, vol. 24, no. 4, pp. 325–420, Aug. 2008.
P. Girard, N. Nicolici and X. Wen, Power-Aware Testing and Test Strategies for Low Power Devices, Springer, 2010.

## Slide 82: Recent Developments
Select clock frequency for each test session.
Select supply voltage for each test session.
Select clock frequency and voltage for each test session.

## Slide 83: Effects of Clock Frequency
Increase in clock frequency:
  Reduces test time
  Increases power dissipation
Theorem: Executing a single core test per session, at a clock frequency such that the power consumed per session is maximized to equal the power budget (Pmax), gives the smallest total test time and hence forms the lower bound for the optimal test time for any SoC.

## Slide 84: Revisit ASIC Z: Nominal Frequency

## Slide 85: ILP Selection for Test Session Frequency
V. Sheshadri, V. D. Agrawal, and P. Agrawal, “Optimal Power-Constrained SoC Test Schedules with Customizable Clock Rates,” to be presented at 25th IEEE International System-on-Chip Conf., Sept., 2012.
Fixed Nominal
Frequency
Freq. ≤ Nominal frequency

## Slide 86: Setting Clock Frequency and Voltage for Each Test Session
Frequency:
  Higher frequency – reduces time, increases power (less parallelism).
  Lower frequency – reduces power (more parallelism), increases test time.
Voltage:
  Higher voltage – increases speed (reduces time), increases power (less parallelism).
  Lower voltage – reduces power (more parallelism), slows the circuit (increases test time).

## Slide 87: ILP Selection of Frequency and Voltage
V. Sheshadri, V. D. Agrawal, and P. Agrawal, “Optimum Test Schedule for SoC with SpecifiedClock Frequencies and Supply Voltages,” submitted to 26th International Conf. on VLSI Design, Jan., 2013.

## Slide 88: Power Constrained Test Time of ASIC Z
Solution | Frequency | Voltage | Test time
Heuristic | Fixed | Fixed | 330
ILP | Fixed | Fixed | 300
ILP | Variable | Fixed | 268
ILP | Variable | Variable | 180

## Slide 89: Conclusion
Mathematics and computational methods are the keys to good engineering.