## Slide 1: Machine Intelligence for Efficient Test Pattern Generation
Soham Roy, Spencer K. Millican, and Vishwani D. Agrawal

## Slide 2: Outline of this presentation
Summary of backtracing in ATPG (automatic test pattern generation)
Summary of machine intelligence
Proposed method: applying machine intelligence to ATPG backtracing
  Creating training data
  Training an ANN (artificial neural network) to make backtracing decisions
Evaluation of the method, findings, and new questions

## Slide 3: ATPG (automatic test pattern generation) An example

## Slide 4: ATPG (automatic test pattern generation) An example
11
0X10X
1
1
1
0
1
D
D
Test found!

## Slide 5: ATPG (automatic test pattern generation) Backtrace and backtracks
Goal = 1
1
1
0
Failure! Backtrack…
Failed (undone) backtrace points
Goal = 1
1
1
Success!
1
1 0
0
Unsuccessful backtrace resulting in backtrack
Two successful backtraces resulting in goal met

## Slide 6: ATPG (automatic test pattern generation) Backtrace and backtracks
Goal = 1
1
1
0
Failure! Backtrack…
Failed (undone) backtrace points
Goal = 1
1
1
Success!
1
1 0
0
Unsuccessful backtrace resulting in backtrack
Two successful backtraces resulting in goal met

## Slide 7: Machine intelligence
Input problems
Solver
Desired outputs
Trainer
Supervised learning
Unsupervised learning
Trainer
Evaluator
Reinforced learning

## Slide 8: Training data from ATPG trials Recording (un)successful backtraces
 | Input Features |  |  |  |  |  |  |  |  |  |  |  | Output label
 | Gate type |  |  |  |  |  |  |  |  | COP(CC) | COP(CO) | Distance | Success/Failure
 | x1 | x2 | x3 | x4 | x5 | x6 | x7 | x8 | x9 | x10 | x11 | x12 | z
Line 5 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0.500 | 0.012 | 0.1 | 1
Line 14 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0.375 | 0.016 | 0.3 | 1
Line 6 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0.500 | 0.004 | 0.1 | 1
Line 10 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0.750 | 0.008 | 0.3 | 1
Line 14 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0.375 | 0.016 | 0.3 | 1
Line 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0.500 | 0.489 | 0.1 | 1
Line 8 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0.750 | 0.977 | 0.3 | 1
Line 12 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0.750 | 0.023 | 0.4 | 1
Line 13 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0.063 | 0.094 | 0.5 | 1
Line 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0.500 | 0.489 | 0.1 | 0
Line 8 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0.750 | 0.977 | 0.3 | 0
Line 12 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0.750 | 0.023 | 0.4 | 0
Line 13 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0.063 | 0.094 | 0.5 | 0
Line 3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0.500 | 0.012 | 0.1 | 1
Line 9 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0.750 | 0.023 | 0.3 | 1
Line 13 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0.063 | 0.094 | 0.5 | 1
Line 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0.500 | 0.489 | 0.1 | 1
Line 8 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0.750 | 0.977 | 0.3 | 1

## Slide 9: Training data from ATPG trials Recording (un)successful backtraces
 | Input Features |  |  |  |  |  |  |  |  |  |  |  | Output label
 | Gate type |  |  |  |  |  |  |  |  | COP(CC) | COP(CO) | Distance | Success/Failure
 | x1 | x2 | x3 | x4 | x5 | x6 | x7 | x8 | x9 | x10 | x11 | x12 | z
Line 5 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0.500 | 0.012 | 0.1 | 1
Line 14 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0.375 | 0.016 | 0.3 | 1
Line 6 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0.500 | 0.004 | 0.1 | 1
Line 10 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0.750 | 0.008 | 0.3 | 1
Line 14 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0.375 | 0.016 | 0.3 | 1
Line 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0.500 | 0.489 | 0.1 | 1
Line 8 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0.750 | 0.977 | 0.3 | 1
Line 12 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0.750 | 0.023 | 0.4 | 1
Line 13 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0.063 | 0.094 | 0.5 | 1
Line 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0.500 | 0.489 | 0.1 | 0
Line 8 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0.750 | 0.977 | 0.3 | 0
Line 12 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0.750 | 0.023 | 0.4 | 0
Line 13 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0.063 | 0.094 | 0.5 | 0
Line 3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0.500 | 0.012 | 0.1 | 1
Line 9 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0.750 | 0.023 | 0.3 | 1
Line 13 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0.063 | 0.094 | 0.5 | 1
Line 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0.500 | 0.489 | 0.1 | 1
Line 8 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0.750 | 0.977 | 0.3 | 1

## Slide 10: Training data from ATPG trials Recording (un)successful backtraces
 | Input Features |  |  |  |  |  |  |  |  |  |  |  | Output label
 | Gate type |  |  |  |  |  |  |  |  | COP(CC) | COP(CO) | Distance | Success/Failure
 | x1 | x2 | x3 | x4 | x5 | x6 | x7 | x8 | x9 | x10 | x11 | x12 | z
Line 5 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0.500 | 0.012 | 0.1 | 1
Line 14 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0.375 | 0.016 | 0.3 | 1
Line 6 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0.500 | 0.004 | 0.1 | 1
Line 10 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0.750 | 0.008 | 0.3 | 1
Line 14 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0.375 | 0.016 | 0.3 | 1
Line 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0.500 | 0.489 | 0.1 | 1
Line 8 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0.750 | 0.977 | 0.3 | 1
Line 12 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0.750 | 0.023 | 0.4 | 1
Line 13 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0.063 | 0.094 | 0.5 | 1
Line 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0.500 | 0.489 | 0.1 | 0
Line 8 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0.750 | 0.977 | 0.3 | 0
Line 12 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0.750 | 0.023 | 0.4 | 0
Line 13 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0.063 | 0.094 | 0.5 | 0
Line 3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0.500 | 0.012 | 0.1 | 1
Line 9 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0.750 | 0.023 | 0.3 | 1
Line 13 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0.063 | 0.094 | 0.5 | 1
Line 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0.500 | 0.489 | 0.1 | 1
Line 8 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0.750 | 0.977 | 0.3 | 1

## Slide 11: The Result of Training An ANN that guides backtracing
Input Nodes
(Features)
Hidden Layer
Neurons
Output Neuron
(Label)
Bias Node
X0 = +1
X1
X2
XM
Y1
Y2
YN
Z
w(X0,Y1)
w(Y1, Z)
w(YN, Z)
w(Y2, Z)
w(XM,YN)
w(XM,Y2)
Y1
0.23
0.72
Backtrace this way!

## Slide 12: Evaluation Comparing the ANN
Random backtracing ATPG
Training Database
c6288, b05, c3540, 100 hardest faults each
ANN Training
Remaining benchmarks
COP-guided backtracing
Distance-guided backtracing
ANN-guided backtracing
ATPG
CPU time, backtracks, & backtraces

## Slide 13: Evaluation Comparing the ANN
Random backtracing ATPG
Training Database
c6288, b05, c3540, 100 hardest faults each
ANN Training
Remaining benchmarks
COP-guided backtracing
Distance-guided backtracing
ANN-guided backtracing
ATPG
CPU time, backtracks, & backtraces

## Slide 14: Results Backtracks & CPU time
Chart: Benchmark Circuits
| c17 | b02 | b06 | b01 | b09 | b03 | c499 | b10 | b08 | c432 | b12 | b13 | c880 | c1355 | b04 | b07 | c2670 | b11 | c1908 | c7552 | c5315 | c3540 | b05 | c6288
Dist. | 0 | 50 | 0 | 0 | 800 | 540 | 20.3439 | 42.4051 | 53.7313 | -41.0063 | 211.6302 | 11.5677 | 160 | 177.1795 | 35.0831 | 234.7413 | -34.237 | 7350.1129 | 18.266 | -23.486 | 70.8031 | -29.6542 | 199.413 | 29.8831
COP | 0 | 0 | 0 | 0 | 13016.6667 | 320 | 2832.7553 | 43.038 | 1891.0448 | -30.1416 | 156.1919 | -8.5236 | -20 | 72.4064 | 201.5054 | 70.2281 | -40.6438 | 18.6606 | 135.9448 | -15.5414 | 168.0325 | -17.2439 | 37.3765 | 44.2007
Chart: Benchmark Circuits
| c17 | b02 | b06 | b01 | b09 | b03 | c499 | b10 | b08 | c432 | b12 | b13 | c880 | c1355 | b04 | b07 | c2670 | b11 | c1908 | c7552 | c5315 | c3540 | b05 | c6288
Dist. | -22.2222 | -10.4167 | -8.7248 | -12.2302 | -12.2633 | -25.0333 | -3.9876 | -9.7674 | -3.1983 | -46.3966 | 11.333 | -5.4068 | 0.80423 | 52.8258 | 16.3446 | 104.8271 | -42.7312 | 1926.1807 | -8.5073 | -23.2815 | -14.2664 | -26.4829 | 58.5106 | -15.9462
COP | 55.5556 | 308.3333 | -10.7383 | -18.705 | 0.81154 | 18.1092 | 1901.0962 | -9.8256 | 217.2175 | -49.1791 | 11.2304 | -26.5285 | -5.5873 | 47.9855 | 138.7378 | 41.9044 | -51.2004 | -21.0385 | 32.0036 | -21.9157 | 5.7358 | -18.8631 | -11.7865 | -19.3382

## Slide 15: Results Backtracks & CPU time
Chart: Benchmark Circuits
| c17 | b02 | b06 | b01 | b09 | b03 | c499 | b10 | b08 | c432 | b12 | b13 | c880 | c1355 | b04 | b07 | c2670 | b11 | c1908 | c7552 | c5315 | c3540 | b05 | c6288
Dist. | 0 | 50 | 0 | 0 | 800 | 540 | 20.3439 | 42.4051 | 53.7313 | -41.0063 | 211.6302 | 11.5677 | 160 | 177.1795 | 35.0831 | 234.7413 | -34.237 | 7350.1129 | 18.266 | -23.486 | 70.8031 | -29.6542 | 199.413 | 29.8831
COP | 0 | 0 | 0 | 0 | 13016.6667 | 320 | 2832.7553 | 43.038 | 1891.0448 | -30.1416 | 156.1919 | -8.5236 | -20 | 72.4064 | 201.5054 | 70.2281 | -40.6438 | 18.6606 | 135.9448 | -15.5414 | 168.0325 | -17.2439 | 37.3765 | 44.2007
Chart: Benchmark Circuits
| c17 | b02 | b06 | b01 | b09 | b03 | c499 | b10 | b08 | c432 | b12 | b13 | c880 | c1355 | b04 | b07 | c2670 | b11 | c1908 | c7552 | c5315 | c3540 | b05 | c6288
Dist. | -22.2222 | -10.4167 | -8.7248 | -12.2302 | -12.2633 | -25.0333 | -3.9876 | -9.7674 | -3.1983 | -46.3966 | 11.333 | -5.4068 | 0.80423 | 52.8258 | 16.3446 | 104.8271 | -42.7312 | 1926.1807 | -8.5073 | -23.2815 | -14.2664 | -26.4829 | 58.5106 | -15.9462
COP | 55.5556 | 308.3333 | -10.7383 | -18.705 | 0.81154 | 18.1092 | 1901.0962 | -9.8256 | 217.2175 | -49.1791 | 11.2304 | -26.5285 | -5.5873 | 47.9855 | 138.7378 | 41.9044 | -51.2004 | -21.0385 | 32.0036 | -21.9157 | 5.7358 | -18.8631 | -11.7865 | -19.3382

## Slide 16: Results Backtracks & CPU time
Chart: Benchmark Circuits
| c17 | b02 | b06 | b01 | b09 | b03 | c499 | b10 | b08 | c432 | b12 | b13 | c880 | c1355 | b04 | b07 | c2670 | b11 | c1908 | c7552 | c5315 | c3540 | b05 | c6288
Dist. | 0 | 50 | 0 | 0 | 800 | 540 | 20.3439 | 42.4051 | 53.7313 | -41.0063 | 211.6302 | 11.5677 | 160 | 177.1795 | 35.0831 | 234.7413 | -34.237 | 7350.1129 | 18.266 | -23.486 | 70.8031 | -29.6542 | 199.413 | 29.8831
COP | 0 | 0 | 0 | 0 | 13016.6667 | 320 | 2832.7553 | 43.038 | 1891.0448 | -30.1416 | 156.1919 | -8.5236 | -20 | 72.4064 | 201.5054 | 70.2281 | -40.6438 | 18.6606 | 135.9448 | -15.5414 | 168.0325 | -17.2439 | 37.3765 | 44.2007
Chart: Benchmark Circuits
| c17 | b02 | b06 | b01 | b09 | b03 | c499 | b10 | b08 | c432 | b12 | b13 | c880 | c1355 | b04 | b07 | c2670 | b11 | c1908 | c7552 | c5315 | c3540 | b05 | c6288
Dist. | -22.2222 | -10.4167 | -8.7248 | -12.2302 | -12.2633 | -25.0333 | -3.9876 | -9.7674 | -3.1983 | -46.3966 | 11.333 | -5.4068 | 0.80423 | 52.8258 | 16.3446 | 104.8271 | -42.7312 | 1926.1807 | -8.5073 | -23.2815 | -14.2664 | -26.4829 | 58.5106 | -15.9462
COP | 55.5556 | 308.3333 | -10.7383 | -18.705 | 0.81154 | 18.1092 | 1901.0962 | -9.8256 | 217.2175 | -49.1791 | 11.2304 | -26.5285 | -5.5873 | 47.9855 | 138.7378 | 41.9044 | -51.2004 | -21.0385 | 32.0036 | -21.9157 | 5.7358 | -18.8631 | -11.7865 | -19.3382

## Slide 17: Results Backtracks & CPU time
Chart: Benchmark Circuits
| c17 | b02 | b06 | b01 | b09 | b03 | c499 | b10 | b08 | c432 | b12 | b13 | c880 | c1355 | b04 | b07 | c2670 | b11 | c1908 | c7552 | c5315 | c3540 | b05 | c6288
Dist. | 0 | 50 | 0 | 0 | 800 | 540 | 20.3439 | 42.4051 | 53.7313 | -41.0063 | 211.6302 | 11.5677 | 160 | 177.1795 | 35.0831 | 234.7413 | -34.237 | 7350.1129 | 18.266 | -23.486 | 70.8031 | -29.6542 | 199.413 | 29.8831
COP | 0 | 0 | 0 | 0 | 13016.6667 | 320 | 2832.7553 | 43.038 | 1891.0448 | -30.1416 | 156.1919 | -8.5236 | -20 | 72.4064 | 201.5054 | 70.2281 | -40.6438 | 18.6606 | 135.9448 | -15.5414 | 168.0325 | -17.2439 | 37.3765 | 44.2007
Chart: Benchmark Circuits
| c17 | b02 | b06 | b01 | b09 | b03 | c499 | b10 | b08 | c432 | b12 | b13 | c880 | c1355 | b04 | b07 | c2670 | b11 | c1908 | c7552 | c5315 | c3540 | b05 | c6288
Dist. | -22.2222 | -10.4167 | -8.7248 | -12.2302 | -12.2633 | -25.0333 | -3.9876 | -9.7674 | -3.1983 | -46.3966 | 11.333 | -5.4068 | 0.80423 | 52.8258 | 16.3446 | 104.8271 | -42.7312 | 1926.1807 | -8.5073 | -23.2815 | -14.2664 | -26.4829 | 58.5106 | -15.9462
COP | 55.5556 | 308.3333 | -10.7383 | -18.705 | 0.81154 | 18.1092 | 1901.0962 | -9.8256 | 217.2175 | -49.1791 | 11.2304 | -26.5285 | -5.5873 | 47.9855 | 138.7378 | 41.9044 | -51.2004 | -21.0385 | 32.0036 | -21.9157 | 5.7358 | -18.8631 | -11.7865 | -19.3382

## Slide 18: Contributions
ANNs can be trained for backtracing
Simple ANNs can outperform comparative heuristics
ANN seamlessly combines multiple features
Many directions for future research
  Can more complex MI structures improve results further?
  Can careful training data generation avoid detrimental results?
  Can MI solve complex ATPG problems: delay fault testing; sequential test?

## Slide 19: Thank you

## Slide 20
 | Distance-based heuristic |  |  | COP-based heuristic |  |  | MAR (Gate type + Dist. + COP)) |  | 
Circuits | CPU Time (ms) | #backtraces | #backtracks | CPU Time (ms) | #backtraces | #backtracks | CPU Time (ms) | #backtraces | #backtracks
c17 | 7 | 64 | 0 | 14 | 60 | 0 | 9 | 63 | 0
b02 | 43 | 232 | 0 | 196 | 234 | 0 | 48 | 230 | 0
b06 | 136 | 507 | 0 | 133 | 497 | 0 | 149 | 504 | 0
b01 | 122 | 500 | 1 | 113 | 467 | 1 | 139 | 494 | 0
b09 | 973 | 3164 | 54 | 1118 | 3409 | 787 | 1109 | 3165 | 6
b03 | 563 | 1660 | 64 | 887 | 2294 | 42 | 751 | 2100 | 10
c499 | 43268 | 62596 | 40947 | 901794 | 1018944 | 997870 | 45065 | 55088 | 34025
b10 | 1552 | 3308 | 225 | 1551 | 3134 | 226 | 1720 | 3345 | 158
b08 | 1816 | 4357 | 824 | 5951 | 13978 | 10672 | 1876 | 4082 | 536
c432 | 53806 | 86667 | 80383 | 51013 | 106707 | 95187 | 100378 | 143811 | 136257
b12 | 28204 | 38893 | 12406 | 28178 | 32083 | 10199 | 25333 | 30181 | 3981
b13 | 1872 | 4575 | 733 | 1454 | 4372 | 601 | 1979 | 4518 | 657
c880 | 4763 | 11018 | 13 | 4461 | 10884 | 4 | 4725 | 11393 | 5
c1355 | 131094 | 166096 | 107432 | 126942 | 114414 | 66823 | 85780 | 97945 | 38759
b04 | 333397 | 299768 | 283018 | 684127 | 648375 | 631696 | 286560 | 227673 | 209514
b07 | 656053 | 1129726 | 1122016 | 454514 | 578032 | 570586 | 320296 | 343739 | 335189
c2670 | 111661 | 137112 | 93058 | 95148 | 124111 | 83992 | 194977 | 189151 | 141505
b11 | 280160 | 211461 | 198024 | 10918 | 17058 | 3154 | 13827 | 16779 | 2658
c1908 | 64861 | 60732 | 19534 | 93580 | 83310 | 38971 | 70892 | 58332 | 16517
c7552 | 456631 | 387827 | 202394 | 464760 | 393895 | 223409 | 595203 | 512991 | 264519
c5315 | 83255 | 95430 | 17632 | 102679 | 100739 | 27669 | 97109 | 86354 | 10323
c3540 | 385668 | 195191 | 153192 | 425641 | 221292 | 180218 | 524596 | 260946 | 217770
b05 | 99169 | 91433 | 72425 | 55189 | 48715 | 33230 | 62563 | 43497 | 24189
c6288 | 533987 | 230645 | 66304 | 512438 | 250662 | 73613 | 635292 | 212317 | 51049