## Slide 1: Specification Test Minimization for Given Defect Level
Suraj Sindia
Intel Corporation, Hillsboro, OR 97124, USA
szs0063@auburn.edu
Vishwani D. Agrawal
Auburn University, Auburn, AL 36849, USA
vagrawal@eng.auburn.edu
15th IEEE Latin-American Test Workshop
Fortaleza, Brazil
March 13, 2014

## Slide 2: Problem Statement
Given a set of complete specification-based tests for an analog or RF circuit, and
An acceptable defect level (DL),
Find the smallest set of tests that should be used.

## Slide 3: Motivation
International Technology Roadmap for Semiconductors (ITRS) 2009 http://www.itrs.net/Links/2009ITRS/Home2009.htm

## Slide 4: What is Defect Level?
Tested good
Tested bad
All fabricated chips
Good chip
Bad chip
Defect level:
DL = 2/21
Yield loss:
YL = 1/30
True yield:
Y = 20/30

## Slide 5: Definitions and Assumption
Specification Si is tested by test Ti.
Probability of testing Sj by Ti Is pij.
Assume that specification tests have zero defect level:
    p11 = p22 = ● ● ● = 1.0
This is perhaps the reason why the users and manufacturers of VLSI have more confidence in specification tests than in alternate tests.
This assumption can be relaxed in the future work.

## Slide 6: A Bipartite Graph
T2
T3
T1
T4
S1
S2
S3
S4
p11
p22
p33
p44
p34
p42
p12
p21
p13
Tests
Specifications

## Slide 7: An Integer Linear Program (ILP)
Consider k specifications and k tests.
Define k integer [0,1] variables {xi} for tests {Ti }:
    Discard Ti if xi = 0, else retain Ti
Define objective function:
k
minimize ∑ xi
i=1
Next, need linear constraints to stay within given defect level.

## Slide 8: Defect Level: A Faulty Device Passes
Defect level is probability of a faulty device passing all tests, i.e.,
Prob{All tests pass | device is faulty}
For given defect level (dl), this conditional probability should not exceed dl, i.e.,
k
1 – ∏ P(Sj) ≤ dl
j=1
Where, P(Sj) = Probability of testing specification Sj
k
= 1 – ∏ (1 – pij)xi
i=1

## Slide 9: Giving Equal Weight per Specification
Assume that each specification weighs equally in determining defect level,
P(S1) = P(S2) = ● ● ● = P(Sk)
or 1 – [P(Sj)]k ≤ dl
or (1 – dl)1/k ≤ P(Sj), j = 1, 2, ● ● ● , k
k
or (1 – dl)1/k ≤ P(Sj) = 1 – ∏ (1 – pij)xi
i=1
j = 1, 2, ● ● ● , k

## Slide 10: Linear Constraints
We derive k linear constraint relations for variables xi and constant dl:
k
(1 – dl)1/k ≤ 1 – ∏ (1 – pij)xi, j = 1, 2, ● ● ● , k
i=1
Therefore,
k
∑ xi ln(1 – pij) ≤ ln[1 – (1 – dl)1/k],
i=1 j = 1, 2, ● ● ● , k

## Slide 11: Operational Amplifier: TI LM741
Notes: In the figure the Y axis shows the minimum test time for the supply voltage on the X axis. The curve N x Tstructure shows test time at each voltage if the circuit is run at its functional speed. The curve 𝑁×𝐸𝑀𝐴𝑋𝑡𝑒𝑠𝑡/𝑃𝑀𝐴𝑋𝑓𝑢𝑛𝑐 shows test time using the test clock period .
As voltage reduces test power decreases, hence test frequency can be increased. On the right side, the test time is limited only by the test power, hence it is power constrained. However as voltage reduces beyon a certain value the test time is limited by the structural delay, hence structure constrained. Optimum voltage Vsynch is the point at which the cycle period start to become structurally constrained

## Slide 12: LM741 Specifications
Test | Specification | Values |  |  | Unit
 | Description | Min. | Nom. | Max. | 
T1 | DC gain | 50 | 200 |  | V/mV
T2 | Slew rate | 0.3 | 0.5 |  | V/μs
T3 | 3-dB bandwidth | 0.4 | 1.5 |  | MHz
T4 | Input referred offset voltage |  | ±10 | ±15 | mV
T5 | Power supply rejection ratio | 86 | 96 |  | dB
T6 | Common mode rejection ratio | 80 | 95 |  | dB
T7 | Input bias current |  | 30 | 80 | nA

## Slide 13: Monte Carlo Simulation
Simulate sample circuits for tests T1 through T7 using spice.
5,000 circuit samples generated:
    5% random deviation around nominal value of each components (12 resistors and 1 capacitor)
    10% random deviation in DC gain of each BJT

## Slide 14: Compute probabilities pij
X = circuits failing Ti
Y = circuits failing Tj
Z = circuits failing both Ti and Tj
pij = Prob{Test Tj fails | spec Si is faulty} = Z/Y
Example:
    45 circuits had spec. S1 failure, detected by T1
    81 circuits had spec. S2 failure, detected by T2
    17 circuits had both failures
    p12 = 17/81 = 0.21, p21 = 17/45 = 0.38, p11 = p22 = 1.0

## Slide 15: Spice Simulation of 5,000 Samples
p12 = 17/81
= 0.21
p21 = 17/45
= 0.38
Samples failing T1

## Slide 16: Probabilities pij for LM741
pij | T1 | T2 | T3 | T4 | T5 | T6 | T7
S1 | 1.00 | 0.38 | 0.78 | 0.51 | 0.76 | 0.93 | 0.98
S2 | 0.21 | 1.00 | 0.75 | 0.20 | 0.27 | 0.35 | 0.27
S3 | 0.56 | 0.97 | 1.00 | 0.19 | 0.21 | 0.51 | 0.38
S4 | 0.92 | 0.64 | 0.48 | 1.00 | 0.84 | 0.76 | 1.00
S5 | 0.92 | 0.59 | 0.35 | 0.57 | 1.00 | 0.59 | 0.84
S6 | 0.80 | 0.54 | 0.62 | 0.37 | 0.42 | 1.00 | 0.87
S7 | 0.61 | 0.31 | 0.33 | 0.35 | 0.43 | 0.63 | 1.00

## Slide 17: ILP
Define xi  [0,1], such that xi = 0  discard Ti.
Objective function:
7
minimize ∑ xi
i=1
Subject to:
7
∑ xi ln(1 – pij) ≤ ln[1 – (1 – dl)1/7],
i=1 j = 1, 2, ● ● ● , 7
where dl = defect level

## Slide 18: Test Minimization
DL PPM | ILP solution |  |  |  |  |  |  | Tests selected | Test size reduction
 | x1 | x2 | x3 | x4 | x5 | x6 | x7 |  | 
0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 7 | 0%
1 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 6 | 14%
100 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 6 | 14%
1,000 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 5 | 29%
10,000 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 4 | 43%

## Slide 19: Conclusion
ILP provides an effective tradeoff between test cost (test time) and quality (defect level).
Test time may further reduce if shorter tests are favored in the cost function.
The assumption of equal weight for each specification can be removed by adding weight to critical specifications.
Defect introduction in Monte Carlo samples need careful examination.
Diagnostic tests may need to preserve diagnostic resolution rather than defect level.
Applications to alternate test could be a useful extension.