## Slide 1: Multi-Heuristic Machine Intelligence Guidance in Automatic Test Pattern Generation
31st Microelectronics Design and Test Symposium’ 22
Virtual Event
Soham Roy (Speaker), Spencer K. Millican, Vishwani D. Agrawal
Dept. of ECE, Auburn University, Auburn, AL 36849
May 26, 20222
Notes: Hello everyone and welcome to my talk titled, “Multi-Heuristic Machine Intelligence Guidance in Automatic Test Pattern Generation”.

## Slide 2: Outline
Motivation
Modus Operandi
Experimental results
Conclusions
Future Works
Notes: I begin by giving the motivation for this study. Then, I will introduce machine intelligence and how it is applied to our study. I will also analyze our experimental results. Finally, I will conclude this talk by briefly pointing out the major contributions of this study and future avenues that may be taken to achieve more interesting results.

## Slide 3
Motivation | ATPG - An example
ATPG
Search for an input vector to detect a given fault.
Complexity increases exponentially with circuit size.
11
0X10X
1
1
1
0
1
D
D
Test found!
Notes: In 1967, D-algorithm established ATPG as a standard method of generating high-quality tests in the logic circuit industry. However, as circuits became larger, it was noticed that ATPG can have frustratingly long runtimes. Subsequent studies lowered ATPG runtime in numerous ways, but since the introduction of PODEM in 1981, the theoretical upper limit of ATPG runtime has remained constant. Let us see an example: for a circuit with n primary inputs (these I may include scan latches in case of DFT circuits), ATPG may need to simulate up to 2^ (n) vectors to find a test. Although ATPG algorithms typically find tests without simulating close to this many vectors, this upper bound still exists and is occasionally seen in modern circuits.

## Slide 4
Motivation | ATPG - Backtraces and backtracks
Goal = 1
1
1
0
Failure! Backtrack…
Failed (undone) backtrace points
Goal = 1
1
1
Success!
1
1 0
0
Unsuccessful backtrace resulting in backtrack
Two successful backtraces resulting in goal met
Notes: To avoid this upper limit, most ATPG algorithms employ backtracing subroutines. These subroutines trace backwards (hence the name) through the circuit starting from an objective — such as activating or propagating a fault — and attempt to find input assignments to accomplish the objective. Multiple backtraces from an objective, leading to multiple input assignments, may be required to meet the objective, but if these input assignments accomplish the final goal — that is, find a test for the fault — then only a subset of input vectors must be simulated, which is nothing compared to the theoretical maximum of two to the power .
However, this ideal situation presumes no backtracks occur during ATPG. Sometimes, the backtracing subroutine may make an input assignment that makes the current or future objectives impossible. When this occurs, ATPG must undo, or backtrack, to some previous assignment, which means ATPG wastes time simulating unnecessary input vectors.
Beyond PODEM, numerous ATPG algorithms attempt to reduce runtime by creating fewer objectives, but to our knowledge, no studies compare ways of backtracing *from* an objective. When backtracing, we must decide which direction to take, because choosing a wrong direction could result in a backtrack.
To avoid this upper limit, most ATPG algorithms employ backtracing subroutines. These subroutines trace backwards (hence the name) through the circuit starting from an objective — such as activating or propagating a fault — and attempt to find input assignments to accomplish the objective. Multiple backtraces from an objective, leading to multiple input assignments, may be required to meet the objective, but if these input assignments accomplish the final goal — that is, find a test for the fault — then only a subset of input vectors must be simulated, which is nothing compared to the theoretical maximum of two to the power 𝑛.
However, this ideal situation presumes no backtracks occur during ATPG. Sometimes, the backtracing subroutine may make an input assignment that makes the current or future objectives impossible. When this occurs, ATPG must undo, or backtrack, to some previous assignment, which means ATPG wastes time simulating unnecessary input vectors.
Beyond PODEM, numerous ATPG algorithms attempt to reduce runtime by creating fewer objectives, but to our knowledge, no studies compare ways of backtracing *from* an objective. When backtracing, we must decide which direction to take, because choosing a wrong direction could result in a backtrack.

## Slide 5
Modus Operandi - Random Pattern Test Generation (RTPG)
Set Input Probabilities
Generate Random Vector
Simulate Faults
Check Coverage
Continue
Change Probabilities
Stop (Adequate Coverage or Random Vectors Ineffective)
Notes: In 1972, random pattern test generation (RPTG) was used for testing the ILLIAC IV parallel computer. The coverage of random patterns always saturated between 60-80% and switching to D-algorithm program at that point proved beneficial. An essential part of the RPTG scheme is a fault simulator that selects useful patterns. In the present work, we first run an RPTG scheme on a set of benchmarks and try to cover easy-to-detect faults, before switching to PODEM ATPG to detect the remaining hard-to-detect faults.

## Slide 6
Modus Operandi - Machine intelligence (MI)
Input problems
Solver
Desired outputs
Trainer
Supervised learning
Unsupervised learning
Trainer
Evaluator
Reinforced learning
“S. Roy, S. K. Millican, and V. D. Agrawal, “Unsupervised Learning in test Generation for Digital Integrated Circuits,” in Proceedings of the European Test Symposium, Belgium (Virtual Event), Feb. 2021.”
Principal Component Analysis (PCA)
Notes: To develop a new backtracing and D-Frontier drive strategy, I look towards the technology of machine intelligence. Machine intelligence describes a broad category of algorithms that automatically program themselves through experience. This experience can come from unclassified data which the program finds patterns in, which is unsupervised learning; or the experience can come from a database of training problems with desired outcomes, which is supervised learning; or the experience can come from iterative re-evaluation and adjustment, which is reinforced learning. In this study, I applied PCA in form of heuristic to guide ATPG without using any neural network. This is known as unsupervised learning in terms of machine intelligence.

## Slide 7
Modus Operandi - Principal Component Analysis (PCA)
Notes: Principal component analysis is a method that rotates the dataset in a way such that the rotated features are statistically uncorrelated. This rotation is often followed by selecting only a subset of the new features, according to how important they are for explaining the data. PCA is a way of reducing the number of independent variables in a dataset and is particularly applicable when the ratio of data points to independent variables is low. PCA transforms a linear combination of variables such that the resulting variable expresses the maximum variance within the combination of variables.
PCA is a statistical procedure that uses an orthogonal transformation to convert a set of observations of possibly correlated variables into a set of values of linearly uncorrelated variables called principal components. This transformation is defined in such a way that the first principal component has the largest possible variance (that is, accounts for as much of the variability in the data as possible)

## Slide 8
Modus Operandi - PCA applied to RTPG filtered faults
Features: Distance,
COP,
SCOAP
PCA
COP-guided backtracing
Distance-guided backtracing
PCA-guided backtracing
ATPG
CPU time, backtracks, & backtraces
Database containing circuit line’s information based on features
SCOAP-guided backtracing
Notes: The motivation behind this study is the exponential complexity of automatic test pattern generation (ATPG) that uses heuristics in making choices during test generation, but in practice no single heuristic fits all situations. In such cases, unsupervised learning can combine practically any number of known heuristics, such as input-output distance (logic depths), gate type, fanout information, and testability measures like COP and SCOAP through principal component analysis, and the most prominent principal components can guide ATPG choices.
Most importantly, we filtered out the easy-to-detect faults using random test pattern generator and left over hard-to-detect faults are for our novel scheme PCA.
I apply this novel scheme to benchmark circuits by first performing principal component analysis to combine three heuristics, distance, COP, and SCOAP, and store the principal components (PC) in a database. Then, the most prominent PCs out of this database guide backtrace direction in the PODEM ATPG program. Here, we are comparing four versions of PODEM, each using a different heuristic, i.e., Distance, COP, SCOAP or principal component.

## Slide 9
Modus Operandi – Principal Component Analysis (PCA) for backtracing
Gate Type | Objective value at output of a gate based on Distance [1] |  | Objective value at output of a gate based on COP [2] |  | Objective value at output of a gate based on SCOAP SC0 [3] |  | Objective value at output of a gate based on SCOAP SC1 [3] |  | Objective value at output of a gate based on PCA | 
Value | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
AND | Min | Max | Min | Min | Min | Min | Max | Max | ? | ?
NAND | Max | Min | Min | Min | Min | Min | Max | Max | ? | ?
OR | Max | Min | Max | Max | Max | Max | Min | Min | ? | ?
NOR | Min | Max | Max | Max | Max | Max | Min | Min | ? | ?
Gate Type | Objective value at output of a gate based on Distance [1] |  | Objective value at output of a gate based on COP [2] |  | Objective value at output of a gate based on SCOAP SC0 [3] |  | Objective value at output of a gate based on SCOAP SC1 [3] |  | Objective value at output of a gate based on PCA | 
Value | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
AND | Min | Max | Min | Max | Min | Max | Min | Max | Min | Max
NAND | Max | Min | Max | Min | Max | Min | Max | Min | Max | Min
OR | Max | Min | Max | Min | Max | Min | Max | Min | Max | Min
NOR | Min | Max | Min | Max | Min | Max | Min | Max | Min | Max
P. Goel, “An Implicit Enumeration Algorithm to Generate Tests for Combinational Logic Circuits,” IEEE Transactions on Computers, vol. C-30, pp. 215–222, 1981.
F. Brglez, “On Testability Analysis of Combinational Circuits,” Proc. International Symp. Circuits and Systems, pp. 221–225, 1984.
L. Goldstein, “Controllability/Observability Analysis of Digital Circuits,” IEEE Transactions on Circuits and Systems, vol. 26, pp. 685– 693, 1979.
Notes: In combining heuristics in PC, it is necessary that they work cooperatively, and not contradict each other. The upper table shows how individual heuristic works. For example, consider a backtrace through an AND gate with two or more inputs being guided by distance D to primary inputs (PI). To justify the output value 0, the backtrace must take the input at minimum distance from PI [8]. In Table I, this is indicated by minimum D for AND gate for output value 0. To justify a 1 at the output, the backtrace follows the input with maximum D, shown as “max”. We observe that the four heuristics do not agree for any gate. Hence, if combined by PCA, the major component (P) cannot be given guidance criteria, as shown by “question marks” in the table.
The lower table takes a two-step approach to overcome the above difficulty. First, some heuristic data, shown in bold, are complemented. For example, when AND gate output is 1, the COP controllability CC1 is replaced with 1 - CC1, and SC0 with 1 - SC0. Also, when the AND gate output is 0, SC1 is replaced by 1 - SC1. This reverses the corresponding backtrace criteria now shown in bold italics. Similar changes are made for NAND, OR and NOR gates, giving complete synchronization of the choice criteria for all heuristics. However, it necessitates separate PCAs for gate outputs 0 and 1, respectively, requiring two major PCs, P0
and P1, with corresponding backtrace criteria (see the lower table).

## Slide 10
D-drive selection criterion w.r.t heuristics |  |  | 
Distance | COP | SCOAP | PCA
Min | Max | Min | Min
Modus Operandi – Principal Component Analysis (PCA) for D-drive
P. Goel, “An Implicit Enumeration Algorithm to Generate Tests for Combinational Logic Circuits,” IEEE Transactions on Computers, vol. C-30, pp. 215–222, 1981.
F. Brglez, “On Testability Analysis of Combinational Circuits,” Proc. International Symp. Circuits and Systems, pp. 221–225, 1984.
L. Goldstein, “Controllability/Observability Analysis of Digital Circuits,” IEEE Transactions on Circuits and Systems, vol. 26, pp. 685– 693, 1979.
Notes: Similar approach is taken to calculate the composite heuristic for D-drive that selects a D from the D-frontier to be propagated toward PO. Once again, various heuristic data, distance, COP observability, and SCOAP observability, all normalized to the range [0,1], are examined in this table for conflicts. Thus, heuristic data for COP observability, shown in boldface, are complemented as 1- COP observability, while distance, SCOAP remain unchanged.

## Slide 11
Testability class of fault | Backtracks for various guidance data |  |  | 
 | Distance | COP | SCOAP | PCA
Hard-to-detect #1 | 122 | 720 | 105 | 56
Hard-to-detect #2 | 86 | 92 | 94 | 80
Hard-to-detect #3 | 36 | 170 | 68 | 0
Hard-to-detect #4 | 2 | 978 | 2 | 0
Hard-to-detect #5 | 22 | 19 | 154 | 5
Hard-to-detect #6 | 2 | 2 | 2 | 0
Hard-to-detect #7 | 13 | 2 | 2 | 0
Easy-to-detect #1 | 1 | 26 | 7 | 0
Easy-to-detect #2 | 1 | 22 | 9 | 0
Easy-to-detect #3 | 2 | 250 | 2 | 0
Redundant #1 | 94 | 92 | 94 | 80
Redundant #2 | 98 | 92 | 96 | 86
Experimental Results – Backtracks in PODEM ATPG of B07
Notes: We used sample of faults (easy-to-detect, hard-to-detect, and redundant) for circuits to prove the power and efficiency of PCA-guidance via a fault-by-fault approach. Table in this slide shows a reduced number of backtracks (almost zero in several cases) for 12 faults (7 hard-to-detect, 3 easy-to-detect, and 2 redundant faults) of the benchmark circuit b07. Although, the number of backtracks for redundant faults were reduced, they did not drop to zero, confirming that it must take at least one backtrack to complete the search for a test for a redundant fault.

## Slide 12
Experimental Results - ATPG for RTPG filtered faults (backtracks)
Chart: Benchmark Circuits
| c17 | b02 | b01 | b06 | b03 | b09 | c432 | b08 | b10 | c499 | b13 | c880 | b07 | c1355 | b11 | b04 | c1908 | b05 | b12 | c2670 | c3540 | c6288 | c5315 | c7552
Distance | 0 | 0 | 0 | 0 | 12 | 25 | 8972 | 484 | 70 | 22516 | 503 | 8 | 51983 | 32161 | 3165 | 106169 | 1374 | 24485 | 5424 | 81445 | 51995 | 43675 | 17615 | 7594
COP | 0 | 0 | 0 | 0 | 1 | 774 | 30786 | 5450 | 35 | 19162 | 507 | 0 | 145033 | 54794 | 2048 | 124252 | 47579 | 25205 | 3883 | 427761 | 272745 | 65996 | 23345 | 60922
SCOAP | 0 | 0 | 0 | 0 | 20 | 774 | 8972 | 3066 | 40 | 172426 | 514 | 0 | 120147 | 28619 | 4078 | 127103 | 41612 | 24022 | 5112 | 392880 | 232004 | 24268 | 14583 | 70011
PCA | 0 | 0 | 0 | 0 | 0 | 0 | 3691 | 490 | 5 | 3268 | 464 | 0 | 5469 | 4353 | 1815 | 34840 | 2593 | 21609 | 2187 | 24955 | 22378 | 5303 | 4883 | 1393
Notes: Circuits are arranged left to right in order of increasing number of nodes. This figure shows combined backtracks for all stuck-at faults left over from RTPG. Corresponding to the four versions of PODEM, there are four bars for total backtracks in the bar chart, for each circuit. Notably, the black bars indicate consistent improvement by the PCA guidance.
There are no reconvergent fanouts in c17, b02, b01, and b06, and hence there is no backtrack possibility. An example of zero backtracks by PCA-based PODEM ATPG is b09

## Slide 13
Experimental Results - ATPG for RTPG filtered faults (CPU Time)
Chart: Number of nodes in the benchmark circuits
| 13 | 32 | 54 | 65 | 190 | 198 | 203 | 204 | 223 | 275 | 415 | 469 | 490 | 619 | 801 | 803 | 938 | 1032 | 1197 | 1566 | 1741 | 2480 | 2608 | 3827
Distance | 1 | 1 | 2 | 4 | 49 | 353 | 4547 | 697 | 179 | 10033 | 241 | 462 | 26910 | 25459 | 4361 | 109468 | 9496 | 31355 | 7671 | 63321 | 84352 | 125895 | 25997 | 25532
COP | 5 | 5 | 2 | 4 | 45 | 464 | 10294 | 2453 | 171 | 12526 | 252 | 514 | 94002 | 64724 | 2777 | 134805 | 61989 | 29022 | 7406 | 281841 | 404917 | 101858 | 31920 | 76556
SCOAP | 1 | 1 | 2 | 4 | 55 | 467 | 4539 | 1565 | 171 | 94009 | 277 | 373 | 67572 | 22412 | 5834 | 119120 | 45894 | 31738 | 8630 | 250795 | 342650 | 191660 | 19695 | 102221
PCA | 1 | 1 | 2 | 3 | 45 | 259 | 1580 | 717 | 155 | 2290 | 231 | 502 | 4526 | 8089 | 2733 | 37531 | 12213 | 27389 | 5672 | 24917 | 32500 | 47028 | 10960 | 17264
Notes: Circuits are arranged left to right in order of increasing number of nodes. Trend curves in the graph are the power-law fit for the four PODEM versions. Notably, the black curve indicates consistent improvement by the PCA guidance.
Results show that multiple heuristics combined as a linear combination effectively reduce backtracks and CPU time of ATPG over any single heuristic. Circuits b03, c432, b10, b13, c880, b07, b05, b12, c5315, c7552, c1355, c2670, c3540, b04, b11, b08, c499 and c6288 had significant reduction in backtracks and CPU times. PCA is frequently the best guidance for ATPG, but even when it is not, it is never the worst.

## Slide 14: Conclusions
Practical ATPG systems combine a simple program (e.g., random vector ATPG) for easy faults and a complex program (e.g., MI-based or quantum-computing ATPG) for hard-to-detect faults.
PCA was used to combine multiple features, and a linear transformation formulated the ATPG backtracing using a new major PC (the first PC) that replaces the tradition single-heuristic guidance found in practical ATPG (tested on hard-to-detect faults).
Notes: Practical ATPG systems combine a simple program (e.g., random vector ATPG) for easy faults and a complex program (e.g., MI-based or quantum-computing ATPG) for hard-to-detect faults. PCA was used to combine multiple features, and a linear transformation formulated the ATPG backtracing using a new major PC (the first PC) that replaces the tradition single-heuristic guidance found in practical ATPG (tested on hard-to-detect faults).

## Slide 15
Future Work
All ATPG algorithms use various heuristics to achieve a lower test generation runtime but achieving the lowest ATPG run-time is still an open problem.
Backtraces can be reduced to generate more efficient tests requiring fewer PI assignments.
A total backtrack elimination has a cost in CPU time.
A quick detection of redundant faults in a circuit
Comparing k-means clustering against PCA.
Using large industry-standard circuits to observe the performance trends of MI-guided ATPG system.
Notes: All ATPG algorithms use various heuristics to achieve a lower test generation runtime, but achieving the lowest ATPG run-time is still an open problem. This study uses MI to combine various ATPG inputs as heuristics, narrow down the search space, and achieve speed-up in ATPG runtime. However, with the dramatic rise in research on quantum computing, it is only natural to use those ideas to break the VLSI testing area out of its plateau. Reconvergent fanout-free circuits do not have any backtracks, but backtraces can be reduced to generate more efficient tests requiring fewer PI assignments. A total backtrack elimination has a cost in CPU time, finding a ``sweet-spot" may be feasible to obtain optimized non-zero backtracks for minimal CPU time.
a quick detection of redundant faults in a circuit may expedite ATPG by MI-guided ATPG Comparing $k$-means clustering against PCA as the second unsupervised learning technique could reveal some interesting results. This study used academic benchmark circuits instead of large industry-standard circuits; the authors believe the observed performance trends are likely to be valid for larger circuits and prove to be valuable in the future.

## Slide 16: Thank You

## Slide 17: Q & A