## Slide 1: Characterizing Processors for Energy and Performance Management
Harshit Goyal Vishwani D. Agrawal
Master’s Student James J. Danaher Professor
Department of Electrical and Computer Engineering
Auburn University
December 4, 2015

## Slide 2: Outline
Problem Statement
Background
Methodology
Simulation setup
Results
Applications
Conclusion

## Slide 3: Problem Statement
Obtain data on voltage, frequency and cycle efficiency of the processor for power and performance management.
Determine operating conditions (voltage and frequency) for optimal time energy operations.

## Slide 4: Background

## Slide 5: Where Does Power Go in CMOS?
Dynamic Power
  Due to charging and discharging of capacitances.
Short Circuit Power
  Occurs during signal transitions when both pullup and pulldown paths are partially conducting causing a direct path between Vdd and GND.
Static Power
  This power dissipation occurs all the time through leakage even when the device is in standby mode.

## Slide 6: Characterization
What is Characterization?
Characterization over Process, Voltage, Frequency, Power, Temperature
Performance Metric
Energy Efficiency Metric

## Slide 7: Performances Measures
Time Performance of Processor
  Speed of a processor is measured in cycles per second or clock frequency (f).
  Execution time of a program using C clock cycles = C/f
  Time performance = f/C
Energy Performance of a Processor
  Efficiency of a processor may be measured in cycles per joule or cycle efficiency (η).
  Energy dissipated by a program using C clock cycles = C/η
  Energy performance = η/C

## Slide 8: Methodology
Technology Characterization
  Simulate a reasonable size adder circuit using selected vectors.
Scale adder data to obtain processor power (cycle efficiency) and frequency at different operating points using scale factors.
Develop power management scenarios using cycle efficiency and frequency.

## Slide 9: Simulation Tools Used
Questa Sim
    Design, compile and simulate designs
  Leonardo Spectrum
    ASIC and standard cell synthesis
  Design Architect-IC
    Schematic Capture
  HSPICE
    Circuit simulation and verification

## Slide 10: Micro-Benchmark Circuit Used
Adder circuit
  Fundamental block of functional units
  Often in processor’s critical path
  Used 16-bit Ripple Carry Adder.
PTM Models
  Characterized in two PTM models: bulk CMOS and High-K
  Technology node: 45nm, 32nm and 22nm

## Slide 11: Results

## Slide 12: Vector Selection
  1000 random vectors were generated using a MATLAB code
  Simulation in H-spice at voltage 1.4v and frequency 1.3GHz gives cycle avg. power
  100 vectors were selected such that:
    34 consume avg. power
    33 are above avg. power including the peak power vector
    33 consume below avg. power including the min. power vector.

## Slide 13: Adder Simulation Data
Simulation Data from H-spice for 32nm Bulk CMOS PTM Model
Voltage (v) | Critical path Delay (ps) | Average Power (µW) | Dynamic Power (µW) | Static Power (µW) | Peak Power (µW) | Maximum Frequency (GHz) | Average EPC (fJ) | Peak EPC (fJ)
1.2 | 321 | 138 | 106 | 33 | 413 | 3.12 | 44 | 133
1.15 | 339 | 113 | 91 | 22 | 358 | 2.95 | 38 | 121
1.1 | 360 | 92 | 77 | 15 | 304 | 2.77 | 33 | 110
1.05 | 386 | 74 | 64 | 10 | 249 | 2.59 | 29 | 96
1 | 419 | 60 | 53 | 7.25 | 198 | 2.39 | 25 | 83
0.9 | 510 | 38 | 35 | 3.57 | 130 | 1.96 | 19 | 66
0.8 | 666 | 22 | 20 | 1.78 | 74 | 1.5 | 15 | 49
0.7 | 1002 | 11 | 10 | 0.92 | 38 | 1 | 11 | 38
0.6 | 1780 | 4.85 | 4.43 | 0.42 | 15 | 0.56 | 8.63 | 28
0.5 | 4522 | 1.39 | 1.18 | 0.21 | 4.45 | 0.22 | 6.27 | 20
0.4 | 18910 | 0.252 | 0.1734 | 0.0786 | 0.7251 | 0.0529 | 4.76 | 13.71
0.35 | 44163 | 0.1069 | 0.0555 | 0.0513 | 0.2433 | 0.0226 | 4.72 | 10.74
0.3 | 112700 | 0.0508 | 0.0174 | 0.0334 | 0.0862 | 0.0089 | 5.72 | 9.71
0.25 | 279360 | 0.0253 | 0.0044 | 0.0209 | 0.037 | 0.0036 | 7.08 | 10.33
0.2 | 715480 | 0.0138 | 0.0011 | 0.0127 | 0.0174 | 0.0014 | 9.85 | 12.47
0.15 | 1852000 | 0.0074 | 0.0002 | 0.0072 | 0.0086 | 0.0005 | 13.68 | 15.86
Voltage (v) | Critical path Delay (ps) | Average Power (µW) | Dynamic Power (µW) | Static Power (µW) | Peak Power (µW) |  | Average EPC (fJ) | Peak EPC (fJ)
1.2 | 321 | 138 | 106 | 33 | 413 | 3.12 | 44 | 133
1.15 | 339 | 113 | 91 | 22 | 358 | 2.95 | 38 | 121
1.1 | 360 | 92 | 77 | 15 | 304 | 2.77 | 33 | 110
1.05 | 386 | 74 | 64 | 10 | 249 | 2.59 | 29 | 96
1 | 419 | 60 | 53 | 7.25 | 198 | 2.39 | 25 | 83
0.9 | 510 | 38 | 35 | 3.57 | 130 | 1.96 | 19 | 66
0.8 | 666 | 22 | 20 | 1.78 | 74 | 1.5 | 15 | 49
0.7 | 1002 | 11 | 10 | 0.92 | 38 | 1 | 11 | 38
0.6 | 1780 | 4.85 | 4.43 | 0.42 | 15 | 0.56 | 8.63 | 28
0.5 | 4522 | 1.39 | 1.18 | 0.21 | 4.45 | 0.22 | 6.27 | 20
0.4 | 18910 | 0.252 | 0.1734 | 0.0786 | 0.7251 | 0.0529 | 4.76 | 13.71
0.35 | 44163 | 0.1069 | 0.0555 | 0.0513 | 0.2433 | 0.0226 | 4.72 | 10.74
0.3 | 112700 | 0.0508 | 0.0174 | 0.0334 | 0.0862 | 0.0089 | 5.72 | 9.71
0.25 | 279360 | 0.0253 | 0.0044 | 0.0209 | 0.037 | 0.0036 | 7.08 | 10.33
0.2 | 715480 | 0.0138 | 0.0011 | 0.0127 | 0.0174 | 0.0014 | 9.85 | 12.47
0.15 | 1852000 | 0.0074 | 0.0002 | 0.0072 | 0.0086 | 0.0005 | 13.68 | 15.86
Notes: Dynamic static power

## Slide 14: Processor Specifications
Processor Specifications:
  Intel Sandy bridge 2500K
    Technology node - 32nm
    Voltage range – 1.2v to 1.5v
    Overclock Speed ()- 5.01GHz
    Clock Speed ()- 3.3GHz
    Peak Power ()-125.6W
    TDP ()- 95W
Assuming that voltage was not raised for overclock frequency, using the equations below we found the static (36W) and dynamic power (59W) for the processor at the rated voltage 1.2 volts.

## Slide 15: Scaling Factors
All the scaling factors were found using processor’s specifications given at rated voltage 1.2v.
Scale factors for processor’s EPC:
    EPC SCALE FACTORTDP =
    EPC SCALE FACTORPEAK =
Scale factors for processor’s frequency:
  Structural Constrained Frequency:
  Power Constrained Frequency (a and b):
Scale Factors | Calculated Values
EPC SCALE FACTORTDP | 0.583
EPC SCALE FACTORPEAK | 0.347
ω | 0.786
a | 1.107
b | 0.526
Scale Factors | Calculated Values
EPC SCALE FACTORTDP | 0.583
EPC SCALE FACTORPEAK | 0.347
ω | 0.786
a | 
b | 
Notes:   28.78nJ
  = = 25.06nJ
    SCALING FACTORTDP =
    SCALING FACTORPEAK =
  〖𝑷𝒓𝒐𝒄𝒆𝒔𝒔𝒐𝒓 𝑬𝑷𝑪〗_(𝑻𝑫𝑷 )= (𝑻𝒉𝒆𝒓𝒎𝒂𝒍 𝑫𝒆𝒔𝒊𝒈𝒏 𝑷𝒐𝒘𝒆𝒓)/(𝑵𝒐𝒎𝒊𝒏𝒂𝒍 𝑭𝒓𝒆𝒒𝒖𝒆𝒏𝒄𝒚)= (𝟗𝟓 𝑾𝒂𝒕𝒕)/(𝟑.𝟑×〖𝟏𝟎〗^𝟗 𝑯𝒆𝒓𝒕𝒛)=28.78nJ
  𝑷𝒓𝒐𝒄𝒆𝒔𝒔𝒐𝒓 〖𝑬𝑷𝑪〗_(𝑷𝒆𝒂𝒌 )= (𝑷𝒆𝒂𝒌 𝑷𝒐𝒘𝒆𝒓)/(𝑺𝒕𝒓𝒖𝒄𝒕𝒖𝒓𝒂𝒍 𝑭𝒓𝒆𝒒𝒖𝒆𝒏𝒄𝒚)= (𝟏𝟐𝟓.𝟔 𝑾𝒂𝒕𝒕)/(𝟓.𝟎𝟏×〖𝟏𝟎〗^𝟗 𝑯𝒆𝒓𝒕𝒛)= 25.06nJ
    SCALING FACTORTDP = (〖𝑬𝑷𝑪〗_𝑻𝑫𝑷 𝑷𝒓𝒐𝒄𝒆𝒔𝒔𝒐𝒓)/〖𝑬𝑷𝑪〗_(𝑻𝑫𝑷 𝑨𝒅𝒅𝒆𝒓) =(𝟐𝟖.𝟕𝟖×〖𝟏𝟎〗^(−𝟗))/(𝟒𝟒.𝟑𝟗×〖𝟏𝟎〗^𝟏𝟓 )=𝟎.𝟓𝟖𝟑
    SCALING FACTORPEAK = (〖𝑬𝑷𝑪〗_𝑷𝒆𝒂𝒌 𝑷𝒓𝒐𝒄𝒆𝒔𝒔𝒐𝒓)/〖𝑬𝑷𝑪〗_(𝑷𝒆𝒂𝒌 𝑨𝒅𝒅𝒆𝒓) =(𝟐𝟓.𝟎𝟔×〖𝟏𝟎〗^(−𝟗))/(𝟏𝟑𝟐.𝟓𝟒×〖𝟏𝟎〗^𝟏𝟓 )=𝟎.𝟑𝟒𝟕

## Slide 16: Processor Cycle Efficiency and Frequency vs. Voltage
Because our own greatest access and insight involves Intel designs and data, our graphs and estimates draw heavily on them.
Notes: Epc vs voltage

## Slide 17: Application

## Slide 18: Power and Structure Constrained Frequency
Power constrained frequency : It is the frequency that is limited by the maximum rated power (TDP) for the circuit under test.
  Power Constrained Frequency
Structure constrained: It is the frequency that is limited by the structural (critical path) delay of the circuit under test.
    Structural Constrained Frequency

## Slide 19: Power and Performance Management
Voltage (v) | Structural Constrained Frequency (GHz) | Power Constrained Frequency (GHz)
1.3 | 5.685 | 1.144
1.25 | 5.366 | 2.23
1.2 | 5.01 | 3.3
1.15 | 4.74 | 4.38
1.136 | 4.67 | 4.67
1.1 | 4.46 | 5.38
1.05 | 4.16 | 6.41
1 | 3.84 | 7.45
0.9 | 3.15 | 9.8
Voltage (v) |  | Power Constrained Frequency (GHz)
1.3 | 5.685 | 1.144
1.25 | 5.366 | 2.23
1.2 | 5.01 | 3.3
1.15 | 4.74 | 4.38
1.136 | 4.67 | 4.67
1.1 | 4.46 | 5.38
1.05 | 4.16 | 6.41
1 | 3.84 | 7.45
0.9 | 3.15 | 9.8

## Slide 20: Power and Performance Management cont.…
TIME AND ENERGY FOR A PROGRAM THAT EXECUTES IN 2 BILLION CLOCK CYCLES |  |  |  |  |  |  |  | 
Voltage (V) | Frequency f (GHz) | Cycle Efficiency η (MHz/Joules) | Power Consumption (Watts) |  | Execution Time (Seconds) |  | Total TDP Energy Consumed by Program (Joules) | 
Nominal Operating Voltage (1.2V) | 3.3 | 34.74 | 95W |  | 0.61s |  | 57.57 J | 
Operating Voltage (1.2V) Overclocked at 5.01GHz | At 3.3 (80% task) | 34.74 | 76W | 101W | 0.48 | 0.56s | 36.8 | 56.8 J
 |  |  |  |  | 0.0798 |  |  | 
 |  |  |  |  |  |  | 20 | 
 | At 5.01 (20% task) | 39.88 | 26W |  |  |  |  | 
Optimum Operating Voltage (1.136 V) | 4.67 | 49.15 | 95W |  | 0.43s (30%) |  | 40.69 J (30%) | 
TIME AND ENERGY FOR A PROGRAM THAT EXECUTES IN 2 BILLION CLOCK CYCLES |  |  |  |  |  |  |  | 
 | Frequency f (GHz) | Cycle Efficiency η (MHz/Joules) | Power Consumption (Watts) |  | Execution Time (Seconds) |  | Total TDP Energy Consumed by Program (Joules) | 
Nominal Operating Voltage (1.2V) | 3.3 | 34.74 | 95W |  | 0.61s |  | 57.57 J | 
Operating Voltage (1.2V) Overclocked at 5.01GHz | At 3.3 (80% task) | 34.74 | 76W | 101W | 0.48 | 0.56s | 36.8 | 56.8 J
 |  |  |  |  | 0.0798 |  |  | 
 |  |  |  |  |  |  | 20 | 
 | At 5.01 (20% task) | 39.88 | 26W |  |  |  |  | 
Optimum Operating Voltage (1.136 V) | 4.67 | 49.15 | 95W |  | 0.43s (30%) |  | 40.69 J (30%) | 

## Slide 21: Conclusion
The results shows efficiency improvement method for processor.
Applicable to any technology node for which the modelling data is available.
Power management can achieve higher performance (30% reduction in execution time and 30% lower energy consumption)
Overclocking with increase in voltage can still improve the performance further.

## Slide 22: References
[1] D. A. Patterson and J. L. Hennessy, Computer Organization& Design, the Hardware/Software Interface. San Francisco, California: Morgan Kaufman, fourth edition, 2008.
[2] Aditi shinde and V. D. Agrawal, “Managing Performance and Efficiency of a Processor”, in proc. 45th Southeastern Symp. System Theory, 2013.
[3] "CPUBoss." CPUBoss. Web. 25 Sept. 2014.
[4] K. Kim and V. D. Agrawal, “Dual Voltage Design for Minimum Energy using Gate Slack,” in Proc. International Conf. on Industrial Technology, 2011, pp. 419–424.
[5] K. Kim and V. D. Agrawal, “Minimum Energy CMOS Design with Dual Subthreshold Supply and Multiple Logic-Level Gates,” in Proc. International Symp. Quality Electronic Design, 2011, pp. 689–694.
[6]. Bienia, C. et. al. The PARSEC benchmark suite: Characterization and architectural implications. The 17th International Symposium on Parallel Architectures and Compilation Techniques (2008).
[7]. Borkar, Shekhar, and Andrew A. Chien. "The future of microprocessors."Communications of the ACM 54.5 (2011): 67-77.
[8] Wang, A; Chandrakasan, AP.; Kosonocky, S.V., "Optimal supply and threshold scaling for subthreshold CMOS circuits," VLSI, 2002. Proceedings. IEEE Computer Society Annual Symposium on , vol., no., pp.5,9, 2002

## Slide 23: Questions?
Thank You