## Slide 1: Weighted Random and Transition Density Patterns for Scan-BIST
Farhana Rashid*
Vishwani D. Agrawal
Auburn University
ECE Department, Auburn, Alabama 36849
* Presently with Intel Corp., Austin, Texas 78746

## Slide 2: A BIST Architecture
Combinational Logic
TPG
SAR
PI
PO
p1 = Prob{bit = 1}, or
TD = Prob{bit makes transition}

## Slide 3: WRP and TDP
Random pattern:
    0100101110, p1 = 0.5
Weighted random patterns (WRP):
    1011101101, p1 = 0.7
    0010011000, p1 = 0.3
Transition density patterns (TDP):
    0111001011, TD = 0.5
    1101001001, TD = 0.7
    0011101111, TD = 0.3
LFSR
LOGIC
FF
Random
patterns
WRP
TDP

## Slide 4: Outline
Motivation
Problem Statement and Contribution
Introduction and Background
Fault coverage analysis of WRP and TDP for scan-BIST
Test Time reduction by using dynamically adapted scan clock
Results
Conclusion and future work

## Slide 5: Motivation
Design BIST for
  High coverage
  Satisfying power constrain
  Reduced test time

## Slide 6: Problem Statement and Contribution
Examine effect of weighted random patterns and transition density patterns on fault coverage.
Reduce test application time for test-per-scan BIST.
Proposed solution:
  Pre-select weighted random patterns or transition density patterns to produce high coverage test with shortest test length.
  Further reduce test time with adaptive activity-driven scan clock.

## Slide 7: Performance of Weighted Random Patterns (WRP)
Number of test per scan vectors for 95% coverage
s1269

## Slide 8: Performance of Transition Density Patterns (TDP)
Number of test per scan vectors for 95% coverage
s1269

## Slide 9: Best WRP and TDP for 95% Fault Coverage
Circuit name | Target Fault Coverage (%) | Weighted Random Vectors |  |  | Transition Density Vectors | 
 |  | Bestp1 | No. Of Vectors | TD = 2 × p1 × (1 – p1) | Best TD | No. of Vectors
s382 | 95 | 0.3 | 56 | 0.42 | 0.45 | 124
s510 | 95 | 0.4 | 136 | 0.48 | 0.5 | 152
s635 | 95 | 0.9 | 97 | 0.18 | 0.1 | 1883
s820 | 95 | 0.45 | 2872 | 0.495 | 0.45 | 5972
s1196 | 95 | 0.55 | 1706 | 0.495 | 0.45 | 2821
s1296 | 95 | 0.6 | 22 | 0.48 | 0.5 | 24
s1494 | 98.8 | 0.5 | 4974 | 0.5 | 0.45 | 3158
s1512 | 95 | 0.75 | 538 | 0.375 | 0.2 | 338

## Slide 10: BIST-TPG for WRP and TDP

## Slide 11: TDP and WRP of s1512 for 95% Coverage
TD = 0.25
406 vectors
WRP
p1 = 0.75
768 vectors

## Slide 12: Adaptive Test Clock for BIST

## Slide 13
Circuit | Random Patterns (R), p1 = 0.5 test time (ns) | Weighted Random Patterns (WRP) |  | Transition Density Patterns (TDP) | 
 |  | Best p1 | Test time (ns) | Best TD | Test time (ns)
s298 | 10050 | 0.5 | 10050 | 0.5 | 1974026
s382 | 10320 | 0.3 | 6661 | 0.4 | 8287
S820 | 348392 | 0.4 | 268971 | 0.4 | 504453
S953 | 418073 | 0.4 | 162371 | 0.3 | 231833
S1196 | 264652 | 0.6 | 221416 | 0.3 | 262350
S1488 | 124572 | 0.6 | 117901 | 0.5 | 72831
s13207 | 31565011 | 0.35 | 16180025 | 0.3 | 10149712
s15850 | 16341260 | 0.5 | 16341260 | 0.3 | 20109065
90% Fault Coverage BIST, 25-100MHz Adaptive Clock

## Slide 14: Conclusion
Low toggle rate vectors, often suggested for reducing test power, generally cause slow rise in fault coverage and result in increased test time.
We show that a proper weight or transition density, which is circuit dependent, can be best for fault coverage.
Any, low or high, toggle rate can be used for quicker fault coverage with adaptive scan clock for an overall reduction in test time.
Combining multiple transition densities or weights can further reduce test time and/or enhance fault coverage; see my thesis referenced in the paper.

## Slide 15: References
F. Rashid, “Controlled Transition Density Based Power Constrained Scan-BIST with Reduced Test Time,” Master’s thesis, Auburn University, Alabama, USA, May 2012.
P. Shanmugasundaram and V. D. Agrawal, “Dynamic Scan Clock Control for Test Time Reduction Maintaining Peak Power Limit,” in Proc. 29th IEEE VLSI Test Symp., May 2011, pp. 248–253.