## Slide 1: Multivalued Logic for Reduced Pin Count and Multi-Site SoC Testing
Baohu Li and Vishwani D. Agrawal
Auburn University, ECE Dept., Auburn, AL 36849, USA
24th IEEE North Atlantic Test Workshop
Johnson City, NY, May 11-13, 2015

## Slide 2: Outline
Problem statement and motivation
Background
MVL test channel for reduced pin-count SoCs
Hardware and test flow design for MVL test data application
Experimental setup and results
Conclusion and future work

## Slide 3: Problem Statement and Motivation
Problem statement
    Multi-site test has a high demand on pin reduction for DUTs;
    Serialization/deserialization of test data is a popular pin reduction technique but it sacrifices test speed.
    The reduction in test speed for such schemes gets worse for multi-core SoCs.
    Motivation
    To find a way to send test data with fewer test pins for SoCs without compromising test speed.

## Slide 4
Multi-site testing and pin reduction
    Multi-site testing aims at best utilizing the ATE resources to test many DUTs at the same time.
    Reduction of test pins uses fewer ATE resources to test a DUT, helping solve bandwidth mismatch problem and increase parallelism in multi-site testing.
Serialization/deserialization of test data
    A commonly implemented scheme to reduce test pins
      Scan test with three pins, J. Moreau et al., [ITC 09]
      Scan architecture using SerDes in GPU chips, A. Sang. et al., [VTS11]
      SmartScan, K. Chakravadhanula et al., [ITC13]
    Test Data are serially sent by ATE with fewer test channels and deserialized in DUTs.
Background

## Slide 5
Serialization/deserialization of test data
    In this example, to send 5 bits of test data, the SerDes using a single wire needs 5 cycles, compared to 1 cycle in the traditional 5-wire case (sacrifice test speed).
Background

## Slide 6
Problem gets worse with multi-core SoCs
Background
Scan speed: 1/5 of clock f → 1/20 of clock f
Limited by the data rate of single channel

## Slide 7
Testing with MVL channel is proposed in our recent work:
- MVL test application [LATS 15]
Previous Work: Adopting MVL Signal to Increase Test Channel Capacity
25 = 32 levels
Data Rate = clock f x log2N
Enhancement

## Slide 8
Two potential error sources for MVL test application
  ADC nonlinearities;
  Noise effect.
Solutions
  Calibration of ADC nonlinearities (use higher resolution DAC to generate calibrated MVL signal)
  Error detection and test data reapply. (Error detection circuitry and test flow with repeated test)
    Proposed in MVL test application [LATS 15]
Previous Work: Assuring Error-Free MVL Test Data Application

## Slide 9
MVL Test Channel for Reduced Pin-Count SoCs
    How MVL test application resolves test speed sacrifice in RPCT scheme
Scan speed: 1/20 of clock f → 1/5 of clock f
Speed increases by data rate enhancement of MVL channel (log216)

## Slide 10
A Test Flow
    Requirements on MVL-compatible test flow
      Calibration procedure
      Applied test data verification
      Retest mechanism
      MVL-bypass mode test

## Slide 11
RTL diagram
Hardware Design of 4-bit MVL Channel with 8-bit DAC
Be able to:
Generate MVL signal;
Run ADC calibration.

## Slide 12
Simulation result of calibration procedure
    Dout is the ramp-up DAC inputs for calibration;
    Vre is the captured ADC output, corresponding to Dout;
    R1-R14 store the calibrated result.
Hardware Design of 4-bit MVL Channel with 8-bit DAC

## Slide 13
RTL diagram
Hardware Design of MVL-Compatible DUT
Mode | Test | BL | Cal | Bypass
ADC Nonlinearity Calibration | 0 | 0 | 1 | 0
MVL Test | 1 | 1 | X | 0
ATS Capture | 0 | 0 | 0 | X
Binary Test | 1 | 0 | X | 1
Be able to:
Decode MVL signal;
Generate ATS for applied
test data verification;
Switch between MVL test
and MVL-bypass mode.

## Slide 14
Setup of ATE based experiment
    Advanrest T2000GS tester builds MVL test channel
    An ADC and a DE2 FPGA board build MVL-compatible DUT with RPCT interface and test decompresser.
Experiments conducted
    Apply scan test with compressed test data through RPCT interface using MVL signal
    Justify the test speed improvement with MVL channel
Experimental Setup and Results

## Slide 15
Experimental Setup
Build MVL channel with Advantest T2000GS

## Slide 16
Experimental Setup
Build MVL-compatible device with RPCT and decompresser

## Slide 17
Experimental Setup
Hardware setup

## Slide 18
20 inputs, including EDT channel inputs and other primary inputs, are sent in 4-bit MVL format; clocks and reset remain binary.
Test channels are reduced from 23 to 4.
MVL test feasibility is established by obtaining test result identical to another test case using binary channel and a 1-to-20 RPCT interface.
Test time with MVL channel is 30.88ms, compared to 123.51ms with binary channel (clock f = 2MHz).
Test Result and Speed Improvement

## Slide 19
Application of MVL test channel on RPCT with test compression is proposed.
Reliability issues and proposed solutions are discussed in previous work [LATS 15]; Hardware and a test flow are proposed in this work.
ATE-based experiments show notable test speed improvement with RPCT.
Overhead remains an issue but will be helped as data converter techniques evolve.
Conclusion

## Slide 20
Device with integrated ADC should be tested for feasibility.
An experiment to validate ADC calibration scheme should be conducted.
Test flow should be examined with experiments.
Future Work

## Slide 21
[VTS 11] A. Sanghani et al., “Design and Implementation of A Time-Division Multiplexing Scan Architecture Using Serializer and Deserializer in GPU Chips,” Proc. 29th IEEE VLSI Test Symp., 2011, pp. 219-224.
[ITC 13] K. Chakravadhanula, et al., “SmartScan - Hierarchical Test Compression for Pin-limited Low Power Designs,” Proc. International Test Conf., 2013. Paper 4.2.
[ITC 09] J. Moreau et al., “Running scan test on three pins: yes we can!,” Proc. International Test Conf., 2009, pp. 1-10.
[LATS 15] B. Li et al., Adopting Multi-Valued Logic for Reduced Pin-Count Testing," Proc. 16th Latin-American Test Symposium, 2015.
Reference