## Slide 1
Improved Random Pattern Delay Fault Coverage Using Inversion Test Points
Soham Roy, Brandon Stiene, Spencer Millican and Vishwani Agrawal
Notes: Hello and thank you for giving me the opportunity.

## Slide 2
Pseudo-random Test
Practical Built-In-Self-Test scheme
  Cheap
  Simple
  In-field
Widely used in previous and current technologies.
Quality degraded due to undetected hard-to-detect faults, sometimes called as “Random Pattern Resistant” faults.
  Low fault coverage.
Notes: Circuit testing is critical part.
Picture Explanation !! Main PRINCIPLE behind is explained!
  CUT is fed by PIs and memory in normal mode or by PRPG in test-mode.
  The circuit outputs are either observed directly in normal mode or compacted by MISR in form of signature which is then compared with the simulated values. If there is a mismatch, fault is detected otherwise not.
REASON: RPR [Next Slide]

## Slide 3
Random pattern resistant faults
Random Pattern Resistant Fault
P (Exciting Stuck-at-1 on OR gate) =
P (Propagating Stuck-at-1 on AND gate) =
P (Detection of Stuck-at-1) = {Highly improbable}
Notes: Unlikely to be detected using random stimulus.
Explain the logic representation. Mathematics behind!

## Slide 4
Motivation: To detect random pattern resistant faults
Methods to improve pseudo-random pattern test:
  Deterministic seeding
  Pattern weighting
  Test-point insertion
Test-point: A hardware modification to enhance testability which may change in logic functionality when active.
Methods to improve test-point insertion
  Location selection algorithms
  Enable selection algorithms
  Test-point implementation/architecture
Notes: Many methods to improve PS random test.
Fair comparison is done between the two architectures based of SAF and TDF.

## Slide 5
“Conventional” test-point architecture
J. Rajski and J. Tyszer, Arithmetic Built-in Self-test for Embedded Systems. Upper Saddle River, NJ, USA: Prentice-Hall, Inc., 1998.
TPE: Test-point enable
Control-0 test-point
Control-1 test-point
Observe test-point
Notes: To improve fault coverage of pseudo-random– TPI
Currently in industry, TPI uses conventional TP architecture.
Explain the functioning of control-0 , control-1 and observe TPs.
Advantage:
  Defects can be excited under random
  Circuit paths can be activated to allow defects to be propagated to circuit outputs under random stimulus.

## Slide 6
An active control TP forces a line to a set value, only one stuck-at value can be excited when a control test-point is active preventing logic on the controlled signal from passing through the test-point.
Control TPs prevent signal transitions and will block all delay faults from passing through the TP.
Control test points prevent delay faults on the output of the TP from being excited.
Detriments of “Conventional ”test-point architecture
Stuck-at fault model
TPE: Test-point enable
Notes: Faults can’t be observed on the controlled signal as its masked shown in figure with the use of control -1 to excite SA0

## Slide 7
An active control TP forces a line to a set value, only one stuck-at value can be excited when a control test-point is active preventing logic on the controlled signal from passing through the test-point.
Control TPs prevent signal transitions and will block all delay faults from passing through the TP.
Control test points prevent delay faults on the output of the TP from being excited.
Transition delay fault model
Detriments of “Conventional ”test-point architecture
TPE: Test-point enable
Notes: It prevents signal transitions and blocks delay faults – passing through the circuit outputs.
Prevents delay faults being excited at the output of TP and less likely to excite delay faults driven by the controlled line.

## Slide 8
Inversion-based test-point architecture
Stuck-at fault model
Y. Fang and A. Albicki, “Efficient testability enhancement for combinational circuit,” in Proceedings of International Conference on Computer Design (ICCD), Oct 1995, pp. 168–172.
TPE: Test-point enable
Notes: 1. It changes signal value probabilities .
2. Here advantages:
  Excites both SA0/1 to pass through TP
  It excites delay faults at the output of TP and delay faults driven by the controlled line.

## Slide 9
Inversion-based test-point architecture
Transition delay fault model
TPE: Test-point enable
Notes: It inverts signal value probabilities .

## Slide 10
Possible detriments of inversion- based test point architecture
Detriments of inversion-based test-point architecture
TPE: Test-point enable
Notes: Possible disadvantages can be explained here:
Under less random stimulus environment:
Conventional TP: constant is set and circuit path is activated. Fault is propagating.
Inversion-based TP: signal probability is inverted still circuit path can’t be activated.

## Slide 11
Test-point insertion algorithm
H. C. Tsai, K.-T. Cheng, C. J. Lin, and S. Bhawmik, “A hybrid algorithm for test point selection for scan-based BIST,” in Proceedings of the 34th Design Automation Conference, June 1997, pp. 478–483.
Start
Generate candidate test-points
For every test-point, calculate controllability (CC) and observability (CO) for every line.
Fault coverage calculation.
Pick best test-point. [List-based search]
Insert test-point into circuit.
Satisfy target fault coverage or the number of test-points
End
Yes
No
Notes: The experiment was done on high performance work station.
The code was written in C++ and the algorithm is as follows:
  # TPs in accordance to number of nodes in the circuit.
  Calculate COP values for every line in the circuit.
  Do fault simulation for 3 copies of the circuit {Original[no TPs]} and FC analysis
  Pick best TP and insert them (CircuitWithConvTPs, CircuitWithInvTPs) and do FS and FC analysis.
  If the target FC is not met || max. # TPs not achieved yet. Repeat the process.
  Terminate.

## Slide 12
ITC’99 and ISCAS’85 benchmarks
Stuck-at fault coverage for 65,536 vectors
Benchmark circuits
Fault coverage (%)
Notes: SAF: proposed architecture does not negatively impact saf, but appears more likely to increase it.
Inversion TP appears to gain more fault coverage than conventional keeping same number of TPs.

## Slide 13
ITC’99 and ISCAS’85 benchmarks
Transition delay fault coverage for 65,536 vectors
Benchmark circuits
Fault coverage (%)
Notes: TDF:
Conventional TP decrease fault significantly.
Positive impact of inversion TP. Except b05 and c432

## Slide 14
ITC’99 and ISCAS’85 benchmarks
Test-point insertion CPU seconds
Chart: 
| b04 | b05 | b07 | b11 | b12 | b13 | c432 | c1355 | c2670 | c3540
Conv. | 222.29 | 1323.91 | 34.82 | 88.62 | 247.18 | 3.88 | 3.41 | 109.04 | 5542.43 | 1006.89
Inv. | 106.15 | 39.21 | 16.79 | 38.39 | 75.79 | 1.02 | 1.61 | 28.54 | 402.99 | 352.33
Time (s)
Benchmark circuits
CPU: Intel core i7-8700
RAM: 8 GB
Clock: 3.2 GHz
Notes: SAF: proposed architecture does not negatively impact saf, but appears more likely to increase it.
Inversion TP appears to gain more fault coverage than conventional keeping same number of TPs.
TDF:
Conventional TP decrease fault significantly.
Positive impact of inversion TP. Except b05 and c432

## Slide 15
Conclusions and Future Directions
Conclusion
Inversion test-points compared to conventional control test-points.
No negative impact on stuck-at fault coverage.
Increase delay fault coverage.
Notes: No neg. SAF coverage
DELAY fault coverage increases.

## Slide 16
Conclusions and Future Directions
Future Directions
Impact of observe test points on delay fault detection.
Impact of test-points on the detection of redundant faults and producing false failures.
Notes: Observe TPs on DELAY fault detection
TPs on detection of redundant faults and provide false failures which might lower the yield unnecessarily.

## Slide 17
Thank You
Notes: Thank you for your time!