## Slide 1: Dynamic SCAN Clock control In BIST Circuits
Priyadharshini Shanmugasundaram
Vishwani D. Agrawal
vagrawal@eng.auburn.edu

## Slide 2: Problem Statement
Reduce test time without exceeding power budget
    Test power and test time are known problems
    Increasing test frequency increases test power - undesirable

## Slide 3: A Built-In Self-Test (BIST) Architecture

## Slide 4: Test Power Considerations
Circuit activity increases during testing and leads to high test power dissipation
  Drop in power supply voltage due to IR drop
    Drop in voltage lowers current flowing through transistor
    Time taken to charge load capacitor increases
      Causes stuck and delay faults
  Ground bounce
    Increase in ground voltage
    Incorrect operation of transistors
      Causes stuck and delay faults
  Excessive heating
    Permanent damage in circuit
  Good chip labeled bad → yield loss
Test clock frequency lowered to reduce power dissipation

## Slide 5: Main Idea
Different test vector bits consume different amounts of power
Test frequency chosen based on peak test power consumption
    All test vector bits applied at same frequency
Test vector bits consuming lower power can be applied at higher frequencies without exceeding power budget of the chip

## Slide 6: Speeding Up Scan Clock
Clock periods
Cycle power
Power
budget
Clock periods
Cycle power
Power
budget

## Slide 7: A Dynamic Scan Architecture

## Slide 8: Dynamic Control of Scan Clock
Monitor number of transitions in scan chain
Speed-up scan clock when activity in scan chain is low or slow-down scan clock when activity in scan chain is high
Example: Dynamic control of scan clock
Non-transition: Present bit in scan chain identical to previous bit (00 or 11)
Scan-in time
  Without dynamic control
  With dynamic control
  Reduction

## Slide 9: Mathematical Analysis -
Verified with simulations
  C program to generate random vectors, N=1000,
 | Reduction in Scan-In Time (%) | 
 | Simulation | Equation
1 | 0 | 0
2 | 0.34 | 0
4 | 12.64 | 12.5
8 | 18.78 | 18.75
16 | 22.03 | 21.88
32 | 23.56 | 23.44
64 | 25.17 | 24.22
128 | 27.41 | 24.61
 | Reduction in Scan-In Time (%) | 
 | Simulation | Equation
1 | 0 | 0
2 | 0.34 | 0
4 | 12.64 | 12.5
8 | 18.78 | 18.75
16 | 22.03 | 21.88
32 | 23.56 | 23.44
64 | 25.17 | 24.22
128 | 27.41 | 24.61
Reduction in scan-in time higher for lower
Reduction in scan-in time vs.
Variation of scan-in time reduction with for different values of

## Slide 10: Experimental Results -
Test-per-scan BIST model
Flip-flops added at primary inputs and outputs of Test-per-scan BIST model and chained together
  Total number of scan flip-flops = Number of primary inputs + Number of D-type flip-flops + Number of primary outputs
Circuits built with and without Dynamic Scan Clock Control
  MentorGraphics ModelSim used to find testing time in both cases
  Synopsys DesignCompiler used to estimate area
  Synopsys PrimeTime PX used for power (activity per unit time) analysis

## Slide 11: Experimental Results -
Circuit | Number of scan flip-flops | Number of frequencies | Reduction in time (%) | Increase in area (%)
s27 | 8 | 2 | 7.49 | 14.72
s386 | 20 | 4 | 15.25 | 15.29
s838 | 67 | 4 | 13.51 | 11.73
s5378 | 263 | 4 | 13.03 | 6.65
s13207 | 852 | 8 | 19.00 | 3.98
s35932 | 2083 | 8 | 18.74 | 2.55
s38584 | 1768 | 8 | 18.91 | 2.13
Reduction in test time in ISCAS89 benchmark circuits – single scan chain, self tested
Activity per unit time analysis (Synopsys PrimeTime PX) – s386 circuit
Test time reduction
  22.5%
Activity per unit time closer to peak limit using dynamic scan clock technique
  Peak limit never exceeded
Chart: Clock Cycle
Uniform clock | 0.0167 | 0.0168 | 0.0152 | 0.0159 | 0.0143 | 0.0145 | 0.0131 | 0.0131 | 0.0124 | 0.0113 | 0.0105 | 0.00964 | 0.00816 | 0.00627 | 0.00641 | 0.00784 | 0.00784 | 0.006 | 0.00544 | 0.004566
Dynamic clock | 0.0167 | 0.0168 | 0.0152 | 0.0159 | 0.0143 | 0.0145 | 0.0131 | 0.0174 | 0.0165 | 0.015 | 0.014 | 0.0129 | 0.0109 | 0.00836 | 0.00726 | 0.0157 | 0.0157 | 0.012 | 0.0109 | 0.009133
Peak limit | 0.0174 | 0.0174 | 0.0174 | 0.0174 | 0.0174 | 0.0174 | 0.0174 | 0.0174 | 0.0174 | 0.0174 | 0.0174 | 0.0174 | 0.0174 | 0.0174 | 0.0174 | 0.0174 | 0.0174 | 0.0174 | 0.0174 | 0.0174
Single scan vector

## Slide 12: Experimental Results -
Circuit | Number of scan flip-flops | Number of frequencies | Test time reduction (%) |  | 
u226 | 1416 | 8 | 46.68 | 18.75 | 0
d281 | 3813 | 16 | 46.74 | 21.81 | 0
d695 | 8229 | 32 | 48.28 | 23.36 | 0
f2126 | 15593 | 64 | 49.15 | 24.18 | 0
q12710 | 26158 | 128 | 49.45 | 24.53 | 0
p93791 | 96916 | 512 | 49.72 | 24.81 | 0
a586710 | 41411 | 256 | 49.73 | 24.77 | 0
Circuit | Number of scan flip-flops | Number of frequencies | Test time reduction (%) |  | 
u226 | 1416 | 8 | 46.68 | 18.75 | 0
d281 | 3813 | 16 | 46.74 | 21.81 | 0
d695 | 8229 | 32 | 48.28 | 23.36 | 0
f2126 | 15593 | 64 | 49.15 | 24.18 | 0
q12710 | 26158 | 128 | 49.45 | 24.53 | 0
p93791 | 96916 | 512 | 49.72 | 24.81 | 0
a586710 | 41411 | 256 | 49.73 | 24.77 | 0
Chart: Activity Factor
| 0.46-0.47 | 0.47-0.48 | 0.48-0.49 | 0.49-0.5 | 0.5-0.51 | 0.51-0.52 | 0.52-0.53 | 0.53-0.54
 | 9 | 63 | 175 | 259 | 239 | 154 | 52 | 10
Chart: Activity Factor
| 0-0.01 | 0.01-0.02 | 0.02-0.03 | 0.03-0.04 | 0.04-0.05 | 0.05-0.06 | 0.06-0.07 | 0.07-0.08 | 0.08-0.09 | 0.09-0.1
Number of vectors | 9202 | 4774 | 170 | 43 | 0 | 2 | 2 | 3 | 0 | 0
Reduction in test time in ITC02 benchmark circuits
Distribution of activity factor for test vectors of s38584 circuit
a) without don’t care bits (961 vectors)
b) with don’t care bits (14196 vectors)

## Slide 13: Improved Dynamic Clock

## Slide 14: Conclusion
Dynamic control of scan clock frequency is proposed
    Reduces testing time without exceeding power budget
    On-chip activity monitor for self testing circuits to keep track of activity in scan chain
Vectors with low average scan-in activity and much higher peak activity give high reduction in test time.
Up to 50% reduction in test time may be possible.
Other references:
    P. Shanmugasundaram, Test Time Optimization in Scan Circuits, Master’s Thesis, Department of ECE, Auburn University, Auburn, Alabama, December 2010.
    P. Shanmugasundaram and V. D. Agrawal, “Dynamic Scan Clock Control for Test Time Reduction Maintaining Peak Power Limit,” Proc. VLSI Test Symposium, May 2011.
    P. Shanmugasundaram and V. D. Agrawal, “Dynamic Scan Clock Control in BIST Circuits,” Proc. International Conference on Industrial Electronics, Mar 2011.