## Slide 1: Dual Voltage Design for Minimum Energy Using Gate Slack
Kyungseok Kim and Vishwani D. Agrawal
ECE Dept. Auburn University
Auburn, AL 36849, USA
IEEE ICIT-SSST Conference
Auburn, March 14, 2011

## Slide 2: Low Power Design Using Dual-Vdd
Apply VDDH to gates on critical paths to maintain performance, while VDDL to gates on non-critical paths to reduce power:
  Clustered Voltage Scaling (CVS) [1]
  Extended Clustered Voltage Scaling (ECVS) [2]
Time complexity of two heuristic algorithms [3]:
  Worst case O(n2), n is total number of gates in a circuit
CVS
ECVS
LC
FF
LCFF
FF
LCFF
VDDH
VDDL

## Slide 3
Motivation
MILP (Mixed Integer Linear Program) algorithms for dual-Vdd design give a global optimal solution, but they cannot be applied to very large circuits due to huge run-time cost [5,6].
Time complexity O(n2) of the published heuristic algorithms for dual-Vdd design also may not have affordable run-time for very large modern SoC.
Gate slack analysis has linear time complexity in number of gates in a circuit; this is different from the all-path slack analysis that can be exponential .

## Slide 4
Gate Slack
Delay of the longest path through gate i [4]:
Dp,i = TPI(i) + TPO(i)
gate i
TPI (i): longest time for an event to arrive at gate i from PI
TPI (i)
TPO (i)
TPO (i): longest time for an event from gate i to reach PO
Slack time for gate i: Si = Tc – Dp,i
where Tc = Maxi { Dp,i } for all i

## Slide 5
Gate Slack Distribution (C2670)
Total number of gates = 901
Nominal Vdd = 1.2V for PTM 90nm CMOS
Critical path delay Tc = 564.2 ps

## Slide 6
Upper Slack Time (Su)
Su is minimum slack of a gate such that it can tolerate VDDL assignment:
Su = Tc where β = ≈
Su=239ps
VDDL Gates
S’u=0
VDDH=1.2V
VDDL=0.69V
≥ 1

## Slide 7
Lower Slack Time (Sl)
Sl=7ps
VDDH
Gates
VDDH=1.2V
VDDL=0.69V
≥ 1

## Slide 8
Classification for Positive Slack (C2670)
Sl = 7ps
Su = 239ps
VDDH Gates
VDDH = 1.2V
VDDL Gates
VDDL= 0.69V
Possible
VDDL Gates

## Slide 9
ISCAS’85 Benchmark (Subtheshold)
Circuit | Total gate | Activity α | VDDH (V) | VDDL (V) | VDDL gates (%) | Esing. (fJ) | Edual (fJ) | Reduc. (%) | MILP[5] (s)** | Slack (s)**
C432 | 154 | 0.19 | 0.25 | 0.23 | 5.2 | 7.9 | 7.8 | 1.1 | 0.3 | 2.5
C499 | 493 | 0.21 | 0.22 | 0.18 | 9.7 | 20.2 | 19.8 | 2.0 | 0.3 | 19.2
C880 | 360 | 0.18 | 0.24 | 0.18 | 46.4 | 14.4 | 11.2 | 22.2 | 5.8 | 17.9
C1355 | 469 | 0.21 | 0.21 | 0.18 | 10.2 | 19.5 | 19.0 | 2.5 | 0.2 | 13.3
C1908 | 584 | 0.20 | 0.24 | 0.21 | 24.3 | 26.5 | 25.0 | 5.8 | 3.2 | 47.6
C2670 | 901 | 0.16 | 0.25 | 0.21 | 46.4 | 32.8 | 28.0 | 14.8 | 35.9 | 134.4
C3540 | 1270 | 0.33 | 0.23 | 0.14 | 7.0 | 88.0 | 84.6 | 3.8 | 3.2 | 256.5
C5315 | 2077 | 0.26 | 0.24 | 0.19 | 47.1 | 116.8 | 98.0 | 16.1 | 852.3 | 692.0
C6288 | 2407 | 0.28 | 0.29 | 0.18 | 2.7 | 165.4 | 162.0 | 2.1 | 2.6 | 1293.7
C7552 | 2823 | 0.20 | 0.25 | 0.21 | 42.3 | 131.7 | 117.1 | 11.1 | 1452.2 | 1408.3
** CPU Time : Intel Core 2 Duo 3.06GHz, 4GB RAM

## Slide 10
Circuit | Single |  | MILP [5] |  |  |  | Slack-time Algorithm |  |  | 
 | VDDH (V) | Esing. (fJ) | VDDL (V) | VDDL gates (%) | Edual reduc. (%) | CPU time (s)** | VDDL (V) | VDDL gates (%) | Edual reduc. (%) | CPU time (s)**
C432 | 1.2 | 160.1 | 0.75 | 5.2 | 3.9 | 0.6 | 0.75 | 5.2 | 3.9 | 15.8
C499 | 1.2 | 460.6 | 0.79 | 19.5 | 5.9 | 403.8 | 0.79 | 19.5 | 5.9 | 194.4
C880 | 1.2 | 277.6 | 0.59 | 56.9 | 51.0 | 455.0 | 0.60 | 57.5 | 50.8 | 62.1
C1355 | 1.2 | 453.0 | 0.69 | 13.6 | 4.3 | 340.2 | 0.69 | 13.6 | 4.3 | 132.0
C1908 | 1.2 | 496.5 | 0.67 | 26.9 | 19.0 | 2146.9 | 0.67 | 26.9 | 19.0 | 247.8
C2670 | 1.2 | 647.6 | 0.69 | 57.9 | 47.8 | 20848.9 | 0.69 | 57.9 | 47.8 | 480.7
C3540 | 1.2 | 1844.0 | 0.70 | 11.6 | 9.6 | 601.0 | 0.70 | 11.6 | 9.6 | 1243.5
C6288 | 1.2 | 3066.0 | 1.18 | 53.1 | 2.9 | 10523.7 | 0.47 | 2.9 | 2.6 | 6128.0
Selected ISCAS’85 (Nominal)
** Intel Core 2 Duo 3.06GHz, 4GB RAM

## Slide 11
Gate Slack Distribution (Nominal)
C880
C1908
C6288
C2670
Optimized
Optimized
Optimized
Optimized

## Slide 12: Conclusion and Future Work
Proposed slack analysis classifies all gates into VDDL, possible VDDL, and VDDH gates.
New slack-based algorithm for dual-Vdd has a linear time complexity, O(n), for n gates in the circuit.
The methodology of slack classification can be applied to other power optimization disciplines, such as dual-Vth.
A hybrid (MILP + slack analysis) algorithm for dual-Vdd design (ECVS) is being investigated to achieve both fast run-time and best optimal solution.

## Slide 13
[1] K. Usami and M. Horowitz, “Clustered Voltage Scaling Technique for Low- Power Design,” Proc. International Symposium on Low Power Design, 1995, pp. 3–8.
[2] K. Usami, M. Igarashi, F. Minami, T. Ishikawa, M. Kanzawa,M. Ichida and K. Nogami, “Automated Low-Power Technique Exploiting Multiple Supply Voltages Applied to a Media Processor,” IEEE Journal of Solid-State Circuits, vol. 33, no. 3, pp. 463–472, 1998.
[3] D. Chinnery and K. Keutzer, Closing the Power Gap Between ASIC & Custom: Tools and Techniques for Low Power Design. Springer, 2007.
[4] A. K. Majhi , V. D. Agrawal, J. Jacob and L. M. Patnaik, “Line Coverage of Path Delay Faults,” IEEE Trans. VLSI Systems, vol. 8, no. 5, pp. 610–614.
[5] K. Kim and V. D. Agrawal, “True Minimum Energy Design Using Dual Below-Threshold Supply Voltages,” Proc. 24th International Conference on VLSI Design, Jan. 2011.
[6] K. Kim and V. D. Agrawal, “Minimum Energy CMOS Design with Dual Subthreshold Supply and Multiple Logic-Level Gates,” Proc.12th International Symposium on Quality Electronic Design, Mar. 2011.
References

## Slide 14
Thank you!!
&
Questions?