## Slide 1: Dynamic Scan Clock Control In BIST Circuits
Priyadharshini Shanmugasundaram
priyas@nvidia.com
Vishwani D. Agrawal
vagrawal@eng.auburn.edu

## Slide 2: Testing of VLSI Circuits and Power
High circuit activity during test leads to functional slowdown and high test power dissipation:
  Peak power - Large IR drop in power distribution lines
    Voltage droop and ground bounce (power supply noise)
    Reduced voltage slows the gates down (delay fault)
  Average power - Excessive heating
    Timing failures
    Permanent damage to circuit
  Good chip may be labeled as bad → yield loss
Existing solution: Use worst-case test clock rate to keep average and peak power within specification.
  Results in long test time.

## Slide 3: Problem Statement
Reduce test time without exceeding the power specification:
Proposed solution: Adaptive test clock
    Use worst-case clock rate when circuit activity is not known
    Monitor circuit activity and speed up the clock when activity reduces

## Slide 4: Built-In Self-Test (BIST)
1
0
1
0
1
0
Combinational Logic
Primary
outputs
Primary
inputs
RA: Response analyzer
RBG: Random bit generator
SSR: Scan shift
register (flip-flops
with dual inputs)
SSR, RBG
and RA have
common clock
and reset
Test multiplexers

## Slide 5: RBG Generates 010101
1
0
1
0
1
0
Primary
outputs
Primary
inputs
RA: Response analyzer
RBG: Random bit generator
SSR: Scan shift
register (flip-flops
with dual inputs)
SSR, RBG
and RA have
common clock
and reset
Test multiplexers

## Slide 6: RBG Generates 111000
0
0
0
1
1
1
Primary
outputs
Primary
inputs
RA: Response analyzer
RBG: Random bit generator
SSR: Scan shift
register (flip-flops
with dual inputs)
SSR, RBG
and RA have
common clock
and reset
Test multiplexers

## Slide 7: Main Idea
Observation: Different sequences of test vector bits consume different amounts of power.
Conventional test clock frequency is chosen based on maximum test power consumption.
    All test vector bits are applied at the same frequency.
Test vector bit sequences consuming lower power can be applied at higher clock frequencies without exceeding power budget of the chip.

## Slide 8: Speeding Up Scan Clock
Clock periods
Cycle power
Power
budget
Clock periods
Cycle power
Power
budget

## Slide 9: Monitoring Test Activity
1
0
1
0
1
0
Combinational Logic
Primary
outputs
Primary
inputs
RA: Response analyzer
RBG: Random bit generator
Non-transition
monitor
SSR, RBG
and RA have
common clock
and reset
Test multiplexers

## Slide 10: A Dynamic Scan Architecture

## Slide 11: Clock Rate vs. SSR Activity
fmax
fmax/2
fmax/3
fmax/4
0 N/4 2N/4 3N/4 N
Number of non-transitions counted
Clock rate
N
N/2
N/4
0
SSR transitions per clock
N = number of flip-flops in scan shift register (SSR)
M = number of adjustable clock rates = 4, in this illustration

## Slide 12: Dynamic Control of Scan Clock
Monitor number of transitions in scan chain
Speed-up scan clock when activity in scan chain is low or slow-down scan clock when activity in scan chain is high
Scan-in time
  Without dynamic control
  With dynamic control
  Reduction
Number of flip-flops in scan shift register (SSR), N = 8
Number of adjustable clock rates , M = 4
Maximum clock rate, fmax = f

## Slide 13: ISCAS89 Benchmark Circuits
Circuit | Number of Scan flip-flops | Number of clock rate steps | Test time reduction (%) |  | Area overhead (%)
 |  |  | Experiment | Theory | 
s27 | 8 | 2 | 7.49 | 0.0 | 14.72
s386 | 20 | 4 | 15.25 | 12.64 | 15.29
s838 | 67 | 4 | 13.51 | 12.64 | 11.73
s5378 | 263 | 4 | 13.03 | 12.64 | 6.65
s13207 | 852 | 8 | 19.00 | 18.78 | 3.98
s35932 | 2083 | 8 | 18.74 | 18.78 | 2.55
s38584 | 1768 | 8 | 18.91 | 18.78 | 2.13

## Slide 14: S386: Activity for One Scan-In
Chart: Clock Cycles
Uniform clock | 0.0167 | 0.0168 | 0.0152 | 0.0159 | 0.0143 | 0.0145 | 0.0131 | 0.0131 | 0.0124 | 0.0113 | 0.0105 | 0.00964 | 0.00816 | 0.00627 | 0.00641 | 0.00784 | 0.00784 | 0.006 | 0.00544 | 0.004566
Dynamic clock | 0.0167 | 0.0168 | 0.0152 | 0.0159 | 0.0143 | 0.0145 | 0.0131 | 0.0174 | 0.0165 | 0.015 | 0.014 | 0.0129 | 0.0109 | 0.00836 | 0.00726 | 0.0157 | 0.0157 | 0.012 | 0.0109 | 0.009133
Peak limit | 0.0174 | 0.0174 | 0.0174 | 0.0174 | 0.0174 | 0.0174 | 0.0174 | 0.0174 | 0.0174 | 0.0174 | 0.0174 | 0.0174 | 0.0174 | 0.0174 | 0.0174 | 0.0174 | 0.0174 | 0.0174 | 0.0174 | 0.0174
Input activity = 25%
Time reduction = 22.5%

## Slide 15: ITC02 Benchmark Circuits
Circuit | Number of scan flip-flops | Number of clock rate steps | Test time reduction (%) |  | 
u226 | 1416 | 8 | 46.68 | 18.75 | 0
d281 | 3813 | 16 | 46.74 | 21.81 | 0
d695 | 8229 | 32 | 48.28 | 23.36 | 0
f2126 | 15593 | 64 | 49.15 | 24.18 | 0
q12710 | 26158 | 128 | 49.45 | 24.53 | 0
p93791 | 96916 | 512 | 49.72 | 24.81 | 0
a586710 | 41411 | 256 | 49.73 | 24.77 | 0

## Slide 16: Improvement: Monitor Input & Output

## Slide 17: Conclusion
Dynamic control of scan clock rate reduces test time without exceeding power specification.
Vectors with low average scan-in activity and high peak activity give more reduction in test time.
Up to 50% reduction in test time is possible.
References:
    P. Shanmugasundaram, Test Time Optimization in Scan Circuits, Master’s Thesis, Department of ECE, Auburn University, Auburn, Alabama, December 2010.
    P. Shanmugasundaram and V. D. Agrawal, “Dynamic Scan Clock Control for Test Time Reduction Maintaining Peak Power Limit,” Proc. 29th IEEE VLSI Test Symposium, May 2-4, 2011.