## Slide 1
An Efficient Algorithm for Dual-Voltage Design Without Need for Level-Conversion
SSST 2012
Mridula Allani
Intel Corporation, Austin, TX 78746
(Formerly with Auburn University)
Dr. Vishwani D. Agrawal
Department of Electrical and Computer Engineering
Auburn University, Auburn, AL 36849
March 12, 2012

## Slide 2: Outline
Motivation
Problem statement
Background
Contributions
  Algorithm to find VDDL
  Algorithm to assign VDDL
Results
Future work
References

## Slide 3: Motivation
Current dual voltage designs use 0.7VDD as the lower supply voltage.
Algorithms to assign low voltage have exponential or polynomial complexity.
Require efficient algorithms that can increase energy savings in large circuits.

## Slide 4: Problem Statement
Develop a linear time algorithm to find an optimal lower voltage VDDL, given a single voltage VDDH without affecting the critical path delay.
Develop new algorithms for voltage assignment to gates in dual-VDD design.

## Slide 5: Background
Basic idea: decrease energy consumption without any delay penalty.
Done by assigning lower supply voltage to gates on non-critical paths.
Different algorithms propose different ways of finding non-critical path gates for lower voltage.

## Slide 6: Background
Authors Kuroda and Hamada say that power reduction ratio
is minimum when 0.6VDD ≤ VDDL ≤ 0.7VDD .
Authors Chen, et al., Kulkarni, et al., Srivatstava, et al., claim that the optimal value of VDDL for minimizing total power is 50% of VDD.
Rule of thumb proposed by Hamada, et. al. says

## Slide 7: Background
CVS Structure
[Usami and Horowitz]
ECVS Structure [Usami, et. al.]
VDDL
VDD
Level Converter
K. Usami and M. Horowitz, “Clustered Voltage Scaling Technique for Low-Power Design," Proceedings of the International Symposium on Low Power Design, pp. 23-26, 1995.
K. Usami, et. al.,“Automated Low-Power Technique Exploiting Multiple Supply Voltages Applied to a Media Processor," IEEE Journal of Solid-State Circuits, vol. 33, no. 3, pp. 463-472, Mar. 1998.

## Slide 8: Background
Kulkarni, et al.
  Greedy heuristic based on gate slacks.
  Uses 0.7VDD or 0.5VDD as VDDL.
  Includes power and delay overhead of level converters.
Sundararajan and Parhi
  Linear programming based model.
  Minimizes the power consumption.
  Includes level converter delay overheads.

## Slide 9: Background
Recent work [Kim and Agrawal]:
  Assign VDDL to gates with Si ≥Su.
  Assign VDDL to gates with Sl ≤ Si ≤ Su one by one without violating timing or topological constraints.
  Repeat last two steps across all voltages to find the best VDDL and the corresponding dual-voltage design with the least energy.
Ref. K. Kim and V. D. Agrawal, “Dual Voltage Design for Minimum Energy Using Gate Slack,” Proceedings of the IEEE International Conference on Industrial Technology, pp. 419-424 , March, 2011.

## Slide 10: Grouping of gates
Chart: c880
 | 0 | 100 | 300 | 500
 | 0 | 100 | 300 | 500
45o line
Su = 336.9 ps
P
G
≥0
∑(dli–dhi)≤min{Si}
Notes: Full paths
CVS gates begin from PI

## Slide 11: Groups when VDDL = 1.2V
Chart: c880
 | 0 | 100 | 300 | 500
 | 0 | 100 | 300 | 500
45o line
P
G
VDD = 1.2V
VDDL = 1.2V
Tc = 510 ps
Su = 0 ps
Notes: Full paths
CVS gates begin from PI

## Slide 12: Groups when VDDL = 1.19V
Chart: c880
 | 0 | 100 | 300 | 500
 | 0 | 100 | 300 | 500
45o line
P
G
VDD = 1.2V
VDDL = 1.19V
Tc = 510 ps
Su = 14.6 ps
Notes: Full paths
CVS gates begin from PI

## Slide 13: Groups when VDDL = 0.49V
Chart: c880
 | 0 | 100 | 300 | 500
 | 0 | 100 | 300 | 500
45o line
Su = 336.9 ps
P
G
Tc = 510 ps
Notes: Full paths
CVS gates begin from PI

## Slide 14: Groups when VDDL = 0.39V
Chart: c880
 | 0 | 100 | 300 | 500
 | 0 | 100 | 300 | 500
45o line
P
G
VDD = 1.2V
VDDL = 0.39V
Su = 469ps
Tc = 510 ps
Notes: Full paths
CVS gates begin from PI

## Slide 15: Groups when VDDL = 0.1V
Chart: c880
 | 0 | 1000 | 5000 | 140000
 | 0 | 1000 | 5000 | 140000
G
VDD = 1.2V
VDDL = 0.1V
Su = 510 ps = Tc
Tc = 510 ps
P
45o line
Notes: Full paths
CVS gates begin from PI

## Slide 16: Theorems
1. Gates above the 45o line in the ‘Delay increment versus
slack’ plot cannot be assigned lower supply voltage without violating the timing constraint.
2.
where βi = dli/dhi and dli is the low voltage delay and dhi is the high voltage delay of gate i. The maximum value of βi; βmax, will give us the lower bound on the gate slacks.

## Slide 17: Theorems
3. Groups within P which satisfy
can be assigned lower supply voltage without violating
the timing constraint. (where, P’ is a sub-set of P yi = dli – dhi , dli = low voltage delay of gate i, dhi = high voltage delay of gate i and Si = slack of the gate i at VDD.)
4. Group with slacks greater than Su, G, can always be
assigned the lower supply voltage without causing any
topological violations.
Notes: Theorem 4

## Slide 18: Algorithm to find VDDL
Assume all gates are assigned VDDH initially.
Calculate gate slacks.
Group gates according to their slacks and delays.

## Slide 19: Algorithm to find VDDL
VDDL = VDDL1, when using no level converter.
VDDL = (VDDL1VDDL2)1/2, when using level converter.

## Slide 20: Results: VDDL selection algorithm
ISCAS’85 | Total gates | Without level converters |  |  |  |  |  |  |  |  |  |  | 
 |  | VDDL = VDDL1 |  |  | VDDL = VDDL2 |  |  | VDDL= (VDDL1+VDDL2 )/2 |  |  | VDDL = (VDDL1VDDL2)1/2 |  | 
 |  | VDDL (V) | Gates in VDDL | Esav(%) | VDDL (V) | Gates in VDDL | Esav(%) | VDDL (V) | Gates in VDDL | Esav (%) | VDDL (V) | Gates in VDDL | Esav (%)
C432 | 154 | 0.80 | 8 | 2.9 | 0.89 | 8 | 2.3 | 0.84 | 8 | 2.7 | 0.84 | 8 | 2.7
C499 | 493 | 0.76 | 113 | 13.7 | 1.11 | 141 | 4.1 | 0.93 | 123 | 10.0 | 0.91 | 129 | 11.1
C880 | 360 | 0.49 | 213 | 49.3 | 0.71 | 229 | 41.3 | 0.6 | 229 | 47.7 | 0.58 | 229 | 48.8
C1355 | 469 | 0.77 | 76 | 9.5 | 1.11 | 108 | 3.4 | 0.94 | 76 | 6.3 | 0.92 | 76 | 6.7
C1908 | 584 | 0.60 | 221 | 28.4 | 1.00 | 221 | 11.6 | 0.80 | 221 | 21.9 | 0.77 | 221 | 22.3
C2670 | 901 | 0.48 | 570 | 53.1 | 0.82 | 570 | 33.7 | 0.65 | 570 | 44.7 | 0.62 | 570 | 46.4
C3540 | 1270 | 0.52 | 149 | 9.5 | 0.73 | 149 | 7.4 | 0.62 | 149 | 8.6 | 0.61 | 149 | 8.7
C5315 | 2077 | 0.49 | 1220 | 49.0 | 0.75 | 1226 | 36.0 | 0.62 | 1220 | 43.1 | 0.60 | 1220 | 44.1
C6288 | 2407 | 0.55 | 75 | 2.5 | 1.00 | 77 | 0.98 | 0.77 | 77 | 1.9 | 0.73 | 77 | 2.0
C7288 | 2823 | 0.54 | 1582 | 44.7 | 0.71 | 2123 | 8.9 | 0.62 | 1672 | 43.4 | 0.61 | 1672 | 43.4

## Slide 21: Results: Comparison with reported data
ISCAS’85 | Total gates | Without level converters |  |  |  |  |  | 
 |  | VDDL=VDDL1 |  |  | VDDL= 0.7VDD = 0.84V |  | VDDL= 0.5VDD = 0.6V | 
 |  | VDDL (V) | Gates in VDDL | Esav (%) | Gates in VDDL | Esav ( %) | Gates in VDDL | Esav (%)
C432 | 154 | 0.80 | 8 | 2.9 | 8 | 2.7 | 8 | 3.9
C499 | 493 | 0.76 | 113 | 13.7 | 121 | 12.5 | 56 | 8.5
C880 | 360 | 0.49 | 213 | 49.3 | 229 | 32.4 | 229 | 47.7
C1355 | 469 | 0.77 | 76 | 9.5 | 76 | 8.3 | 64 | 10.2
C1908 | 584 | 0.60 | 221 | 28.4 | 221 | 19.3 | 221 | 28.4
C2670 | 901 | 0.48 | 570 | 53.1 | 570 | 32.3 | 570 | 47.5
C3540 | 1270 | 0.52 | 149 | 9.5 | 149 | 6.0 | 149 | 8.8
C5315 | 2077 | 0.49 | 1220 | 49.0 | 1240 | 30.5 | 1220 | 44.1
C6288 | 2407 | 0.55 | 75 | 2.5 | 77 | 1.6 | 75 | 2.3
C7288 | 2823 | 0.54 | 1582 | 44.7 | 2359 | 42.6 | 1672 | 43.9

## Slide 22: Algorithm to assign VDDL
Assume all gates are at VDD initially.
Calculate slacks of all gates.
Assign VDDL to all gates i whose slacks,
Si ≥Su
Recalculate slacks.

## Slide 23: Algorithm to assign VDDL
Assign VDDL to a group of gates in P satisfying the condition
Recalculate slacks.
Are there are any VDDL gates feeding into any VDDH gates or is there any gate with negative slack?

## Slide 24: Algorithm to assign VDDL
If answer to any of the questions is yes, then put the corresponding gate back to VDDH .
Recalculate slacks.
Repeat previous five steps until we do not have any unprocessed VDDH gate in group P.

## Slide 25: c880 slack distribution
Chart: Initial Slack of c880
 | 0 | 100 | 300 | 500
 | 0 | 100 | 300 | 500
45o line
Su =336.9 ps
P
G
VDD = 1.2V
VDDL = 0.49V

## Slide 26: Slack data after VDDL assignment
Chart: Final Slack of c880
 | 0 | 100 | 300 | 500
 | 0 | 100 | 300 | 500
45o line
Su = 336.9ps
P
G
VDD = 1.2V
VDDL = 0.49V

## Slide 27: Dual voltage design without level converter
ISCAS’85 | Total gates | VDDL=VDDL1 Determination and assignment |  |  |  | SPICE Results ** |  |  | [Kim and Agrawal] | 
 |  | VDDL (V) | Gates in VDDL | Esav (%) | CPU* (s) | Esingle VDD (fJ) | Edual VDD( fJ) | Esav (%) | Esav (%) | CPU (s)
C432 | 154 | 0.80 | 8 | 2.9 | 1.78 | 161.3 | 155.4 | 3.7 | 3.9 | 15.8
C499 | 493 | 0.76 | 113 | 13.7 | 9.41 | 463 | 427 | 7.8 | 5.9 | 194.4
C880 | 360 | 0.49 | 213 | 49.3 | 5.39 | 277.6 | 115.8 | 58.3 | 50.8 | 62.1
C1355 | 469 | 0.77 | 76 | 9.5 | 8.75 | 455.2 | 433.1 | 4.9 | 4.3 | 132
C1908 | 584 | 0.60 | 221 | 28.4 | 11.43 | 496.5 | 378.3 | 23.8 | 19.0 | 247.8
C2670 | 901 | 0.48 | 570 | 53.1 | 23.49 | 660.3 | 251.5 | 61.9 | 47.8 | 480.7
C3540 | 1270 | 0.52 | 149 | 9.5 | 45.44 | 1843 | 1620 | 12.2 | 9.6 | 1244
C5315 | 2077 | 0.49 | 1220 | 49.0 | 109.47 | 2320 | 1272 | 45.2 | N/R | N/R
C6288 | 2407 | 0.55 | 75 | 2.5 | 154.94 | 1932 | 1869 | 3.3 | 2.6 | 6128
C7288 | 2823 | 0.54 | 1582 | 44.7 | 191.04 | 2465 | 1562 | 36.6 | N/R | N/R
Intel Core i5 2.30GHz, 4GB RAM
**90nm PTM model

## Slide 28: CPU Time Vs. Number of Gates
Chart: Number of gates
| 160 | 202 | 383 | 546 | 880 | 1211 | 1705 | 2341 | 2416 | 3624
Sundararajan and Parhi | 7.83 | 10.1 | 54.4 | 47.2 | 739 | 1229 | 1743 | 4243 | 7736 | 9475
Our algorithm | 1.78 | 9.41 | 5.39 | 8.75 | 11.43 | 23.49 | 45.44 | 109.47 | 154.94 | 191.04
Kim and Agrawal | 15.8 | 194.4 | 62.1 | 132 | 247.8 | 480.7 | 1244 | 6128

## Slide 29: Future work
Accommodate level converter energy overheads.
Consider leakage energy reduction.
Dual threshold designs.
Simultaneous dual supply voltage and dual threshold voltage designs.
Include the effects of process variations.

## Slide 30: References
T. Kuroda and M. Hamada, “Low-Power CMOS Digital Design with Dual Embedded Adaptive Power Supplies," IEEE Journal of Solid-State Circuits, vol. 35, no. 4, pp. 652-655, Apr. 2000.
M. Hamada, Y. Ootaguro, and T. Kuroda, “Utilizing Surplus Timing for Power Reduction,” in Proceedings of the IEEE Custom Integrated Circuits Conference, pp. 89-92, 2001.
C. Chen, A. Srivastava, and M. Sarrafzadeh, “On Gate Level Power Optimization Using Dual-Supply Voltages," IEEE Transactions on Very Large Scale Integration (VLSI) Systems, vol. 9, no. 5, pp. 616-629, Oct. 2001.
S. H. Kulkarni, A. N. Srivastava, and D. Sylvester, “A New Algorithm for Improved VDD Assignment in Low Power Dual VDD Systems," in Proceedings of the International Symposium on Low Power Design, pp. 200-205 , 2004.
A. Srivastava, D. Sylvester, and D. Blaauw, “Concurrent Sizing, Vdd and Vth Assignment for Low-Power Design," Proceedings of the Design, Automation and Test in Europe Conference, pp. 107-118, 2004.
K. Kim, Ultra Low Power CMOS Design. PhD thesis, Auburn University, ECE Dept., Auburn, AL, May 2011.

## Slide 31: References
K. Kim and V. D. Agrawal, “Dual Voltage Design for Minimum Energy Using Gate Slack,” in Proceedings of the IEEE International Conference on Industrial Technology, pp. 419-424 , Mar. 2011.
K. Usami and M. Horowitz, “Clustered Voltage Scaling Technique for Low-Power Design," in Proceedings of the International Symposium on Low Power Design, pp. 23-26, 1995.
K. Usami, M. Igarashi, F. Minami, T. Ishikawa, M. Kanzawa, M. Ichida, and K. Nogami, “Automated Low-Power Technique Exploiting Multiple Supply Voltages Applied to a Media Processor," IEEE Journal of Solid-State Circuits, vol. 33, no. 3, pp. 463-472, Mar. 1998.
V. Sundararajan and K. K. Parhi, “Synthesis of Low Power CMOS VLSI Circuits Using Dual Supply Voltages," in Proceedings of the 36th Annual Design Automation Conference, pp. 72-75, 1999.
M. Allani and V. D. Agrawal, “Level-Converter Free Dual-Voltage Design of Energy Efficient Circuits Using Gate Slack,” Submitted to Design Automation and Test in Europe Conference, March 12-16, 2012.

## Slide 32
Thank you.