## Slide 1: Managing Performance and Efficiency of a Processor
Aditi Shinde
Vishwani D. Agrawal
Department of Electrical and Computer Engineering
Auburn University, Auburn, AL 36849

## Slide 2
4004
8008
8080
8085
8086
286
386
486
Pentium®
P6
1
10
100
1000
10000
1970
1980
1990
2000
2010
Year
Power Density (W/cm2)
Hot Plate
Nuclear
Reactor
Rocket
Nozzle
Sun’s
Surface
Source: Patrick P. Gelsinger , Keynote, ISSCC, Feb. 2001
Motivation: The power problem!

## Slide 3: contribution
Propose a new cycle efficiency rating for energy similar to the maximum clock frequency rating for time.
Analogy:
  Cycle efficiency is similar to miles per gallon (mpg).
  Maximum clock frequency is similar to miles per hour (mph)

## Slide 4: Performance IN TIME
Performance is measured with respect to a program.
Performance =
D. A. Patterson and J. L. Hennessy, Computer Organization & Design, the Hardware/Software Interface, Fourth Edition, San Francisco, California: Morgan Kaufman Publishers, Inc., 2008.

## Slide 5: Performance IN ENERGY (EFFICIENCY)
Efficiency is also measured with respect to a program.
Efficiency
D. A. Patterson and J. L. Hennessy, Computer Organization & Design, the Hardware/Software Interface, Fourth Edition, San Francisco, California: Morgan Kaufman Publishers, Inc., 2008.

## Slide 6: Two Performances
Time performance
Energy efficiency
D. A. Patterson and J. L. Hennessy, Computer Organization & Design, the Hardware/Software Interface, Fourth Edition, San Francisco, California: Morgan Kaufman Publishers, Inc., 2008.

## Slide 7: Time performance of a processor
Speed of a processor is measured in cycles per second or clock frequency (f).
Execution time of a program using C clock cycles = C/f
Time performance = f/C

## Slide 8: ENERGY performance of a processor
Efficiency of a processor may be measured in cycles per joule or cycle efficiency (η).
Energy dissipated by a program using C clock cycles = C/η
Energy performance = η/C

## Slide 9: Characterizing device technology
Consider 90nm CMOS technology.
Use predictive technology model (PTM).
Example circuit: Eight-bit ripple carry adder.
Nominal voltage = 1.2 volts.
Simulated for varying operating conditions (VDD = 100mV through 1.2V) using Spice:
  With random vectors for energy per cycle (EPC = 1/η).
  With critical path vectors for clock period (1/f).
Reference: W. Zhao and Y. Cao, “New Generation of Predictive Technology Model for Sub-45nm Early Design Exploration,“ IEEE Trans. Electron Devices, vol. 53, no. 11, pp. 2816–2823, 2006.

## Slide 10: Energy per Cycle of 8-bit adder
K. Kim, “Ultra Low Power CMOS Design,” PhD Dissertation, Auburn University, Dept. of ECE, Auburn, Alabama, May 2011.

## Slide 11: CLOCK Cycle time of 8-bit adder
K. Kim, “Ultra Low Power CMOS Design,” PhD Dissertation, Auburn University, Dept. of ECE, Auburn, Alabama, May 2011.

## Slide 12: Pentium M processor
Published data: H. Hanson, K. Rajamani, S. Keckler, F. Rawson, S. Ghiasi, J. Rubio, “Thermal Response to DVFS: Analysis with an Intel Pentium M,” Proc. International Symp. Low Power Electronics and Design, 2007, pp. 219-224.
VDD = 1.2V
Maximum clock rate = 1.8GHz
Critical path delay, td = 1/1.8GHz = 555.56ps
Power consumption = 120W
Energy per cycle, EPC = 120/(1.8GHz) = 66.67nJ

## Slide 13: Cycle efficiency and frequency for pentium m

## Slide 14: Example
For a program that executes in 1.8 billion clock cycles.
Voltage VDD | Frequency f MHz | Cycle Efficiency, η | Execution Time second | Total Energy Consumed | Power f/η
1.2 V | 1800 megacycles/s | 15 megacycles/joule | 1.0 | 120 Joules | 120W
0.6 V | 277 megacycles/s | 70 megacycles/joule | 6.5 | 25 Joules | 39.6W
200 mV | 54.5 megacycles/s | 660 megacycles/joule | 33 | 2.72 Joules | 0.083W

## Slide 15: Conclusion
New performance rating: cycle efficiency η has the unit cycles per joule.
Clock frequency f in cycles per second is a similar rating with respect to time.
Similarity to other popular ratings:
  η → mpg
  f → mph
  Power = f/η
Two ratings allow effective time and energy management of an electronic system.