## Slide 1: Synchronous Versus Asynchronous Testing
Vishwani D. Agrawal
James J. Danaher Professor
Electrical and Computer Engineering
Auburn University, Auburn, AL 36849, USA
Collaborator: Praveen Venkataramani
Texas Instruments – Bangalore, July 11, 2012

## Slide 2: Power Considerations in Design
A circuit is designed for certain function. Its design must allow the power consumption necessary to execute that function.
Low power design methods can reduce the power need.
Power buses are laid out to carry the maximum current necessary for the function.
Heat dissipation of package conforms to the average power consumption during the intended function.
Layout design and verification must account for “hot spots” and “voltage droop” – delay, coupling noise, weak signals.

## Slide 3: Why Is Test Power Different?
VLSI chip
Decoder
3-bit random
vectors
8-bit
1-hot
vectors
VLSI chip
system
VLSI chip in system operation
VLSI chip under test
High activity
8-bit
test vectors
from ATE

## Slide 4: Test Time Problem: Consider Scan Testing
SFF
SFF
SFF
Combinational
logic
PI
PO
SCANOUT
SCANIN
SE or TCK
Not shown: CK or
MCK/SCK feed all
SFFs.

## Slide 5: Test Time is Also a Problem
Total scan test time (Number of scan test clock cycles × clock period):
TT = NT = [(ncomb + 2) nsff + ncomb + 4] × T
Where, ncomb = number of combinational vectors
nsff = number scan flip-flops in the longest scan chain
T = scan clock period
Example: 10,000 scan flip-flops in longest chain, 1,000 comb. vectors, total scan test length, TT ≈ 107 T.
Reference:
  M. L. Bushnell and V. D. Agrawal, Essentials of Electronic Testing for Digital, Memory and Mixed- Signal VLSI Circuits, Springer, 2000.

## Slide 6: Scan Power During a Clock Cycle
Clock period, T
time
Chip current, i(t)
0
T
Cycle energy, E = VDD ∫ i(t) dt
0
Cycle power, P = E/T

## Slide 7: Scan Power During Test With Synchronous Clock
1 2 3 4 5 6 7 8
Clock cycles
Cycle Energy, E
Emax
Cycle power, P
Pmax
E
E
E
E
E
E
E
E
P
P
P
P
P
P
P
P
Scan clock period, T = Emax/Pmax
T
T
T
T
T
T
T
T

## Slide 8: Test Time for Synchronous Clock
N Emax Etotal
TTsync = NT = ———— = ———
Pmax Pavg
Where,
N = Number of scan test clock cycles
T = Scan clock period = Emax/Pmax
Etotal = Total energy of all clock cycles
Pavg = Average power/clock cycle

## Slide 9: Power vs. Time
A good test:
  Should not exceed given power budget, Pmax
  Have short test time, time → cost
Reduce power:
  Use low activity vectors ⇒ slower rise in fault coverage ⇒ more vectors ⇒ longer test time
Reduce test time:
  Use high efficiency vectors ⇒ produce high activity ⇒ increase test power

## Slide 10: Can We Speed Up Scan Testing?
Maximum clock speed is limited by Emax of vectors and Pmax of circuit; T ≥ Emax/Pmax.
For most cycles E << Emax ⇒ can reduce period.
Structural limits on clock period:
    Critical path delay (functional and scan)
    Set up and hold times < critical path delay
A variable clock period can be shorter than the global (synchronous) power constrained period, T = Emax/Pmax.

## Slide 11: Asynchronous Scan
Pre-compute energy {Ei} for all clock cycles {i}.
For given power constrain Pmax of the circuit, set the period Ti of ith clock cycle as:
Ti = max {Ei/Pmax, critical path delay}
= Ei/Pmax, for power constrained testing
Where critical path delay can be different for scan and normal mode cycles.

## Slide 12: Scan Power During Test With Asynchronous Clock
1 2 3 4 5 6 7 8
Clock cycle, i
Cycle Energy, E
Emax
Cycle power, P
Pmax
E
E
E
E
E
E
E
E
P
P
P
P
P
P
P
P
Scan clock period, Ti = Ei/Pmax
T1
T7
T5
T2
T8
T3
T4
T6

## Slide 13: Test Time for Asynchronous Clock
N N
TTasyn = Σ Ti = Σ Ei/Pmax
i=1 i=1
N 1 N
= ——— × — Σ Ei
Pmax N i=1
N Eav Etotal
= ——— = ———
Pmax Pmax

## Slide 14: Two Theorems
The minimum test time for a synchronous test is the ratio of total energy consumed during the entire test to the average power for all test cycles:
The minimum possible test time is the ratio of total energy consumed during the entire test to the peak power of any test cycle. This test time is achievable by asynchronous clock testing:

## Slide 15: Comparing Tests
time
Energy
Emax/Eav = 2
1.0
0.5
0.0
time
Energy
Emax/Eav = 5
1.0
0.5
0.0
Low power test

## Slide 16
Chart: Time (µs)
Asynchronous clock
Synchronous clock, T = 40ns
Pmax= 0.711 mW
Pav = 0.455 mW
TTsync, 40ns clock
TTasyn
Spice Simulation: s289 (14FF) Scan Test
Notes: Circuit s289 Total Test patterns = 33 ATPG patterns + 2 Additional set of patterns with alternate 1’s and 0’s
Pmax= 0.711 mW Pavg = 0.455 mW Test cycles = 14 Scan shift cycles + 1 Capture cycle
Synchronous clock period = 40ns Test Time Synchronous= 21.010 µs Test Time Asynchronous= 13.459 µs Gain=1.562

## Slide 17
Chart: Pmax, Peak Power (mW)
| 0.71138000000000001 | 0.5319199999999995 | 0.38484000000000035 | 0.23791000000000018 | 0.17888999999999999 | 0.14313000000000001 | 0.11839000000000002
Synchronous Clock | 19.81 | 26.4132 | 39.6198 | 59.4297 | 79.2396 | 99.0495 | 118.8594
Asynchronous Clock | 12.83 | 16.1655 | 23.58 | 38.4513 | 51.1446 | 63.948 | 77.3244
Test Time Synchronous
Test Time Asynchronous
=
1.54
Test Time (Synchronous)
Test Time (Asynchronous)
Spice Simulation: s298 Test Time Ratio
Notes: Test time Gain = (Test Time Synchronous clock)/(Test time adaptive clock)
Synchronous Clock Asynchronous Clock Test Time Synchronous Test Time Asynchronous Ratio
0.711 0.711 19.81 12.83 1.544
0.532 0.532 26.41 16.17 1.634
0.385 0.385 39.62 23.58 1.680
0.238 0.238 59.43 38.45 1.546
0.179 0.179 79.24 51.14 1.549
0.143 0.143 99.05 63.95 1.549
0.118 0.118 118.86 77.32 1.537

## Slide 18
Chart: Time (µs)
Asynchronous clock
Synchronous clock, T 40ns
Spice Simulation: s713 Scan Test
Pmax = 1.06mW
Pav = 0.53mW
Notes: Circuit: s713
Total Vectors = 60 Atpg vectors
Constant clock period = 40ns
Gain: 2

## Slide 19: Test Time Reduction
Circuit | Per cycle peak power (mW) | Test time |  | 
 |  | Synch. (ms) | Asynch. (ms) | Reduction (%)
s298 | 0.08 | 0.021 | 0.014 | 36
s713 | 0.27 | 0.030 | 0.015 | 50
s13207 | 2.11 | 2.220 | 1.354 | 39
s384584 | 7.22 | 7.423 | 5.925 | 20

## Slide 20: Summarizing Asynchronous Scan
Total test energy (Etotal) is invariant for a test.
Peak cycle power (Pmax) is a circuit characteristic.
For power constrained scan testing,
  Synchronous clock test time = Etotal/Pav
  Asynchronous clock test time = Etotal/Pmax
Asynch. clock test will benefit from low energy tests.
Future explorations may investigate energy reduction techniques like reduced voltage testing.
Test programming for asynchronous clock needs to be worked out.

## Slide 21: References
V. D. Agrawal, “Pre-Computed Asynchronous Scan (Invited Talk),” 13th IEEE Latin American Test Workshop, Quito, Ecuador, April 2012.
P. Venkataramani and V. D. Agrawal, “Test Time Reduction in ATE Using Asynchronous Clocking,” Sixth IEEE International Workshop on Design for Manufacturability and Yield (DFM&Y), San Francisco, CA, June 4, 2012.
P. Venkataramani and V. D. Agrawal, “Reducing ATE Time of Power Constrained Test by Asynchronous Clocking,” submitted to International Test Conf. Poster Session, Anaheim, CA, Nov. 6-8, 2012.
P. Venkataramani and V. D. Agrawal, “Reducing Test Time of Power Constrained Test by Optimal Selection of Supply Voltage,” submitted to 26th International Conf. VLSI Design, Pune, Jan. 5-10, 2013.