## Slide 1: True Minimum Energy Design Using Dual Below-Threshold Supply Voltages
Kyungseok Kim and Vishwani D. Agrawal
ECE Dept. Auburn University
Auburn, AL 36849, USA
24th International Conference on VLSI Design
Chennai, January 4, 2011

## Slide 2: Energy Constrained Systems
System Properties [1]
Low activity rates
Relaxed performance requirements
Long battery lifetime (more than 1 year)
Energy harvesting from the environment
  Solar, Vibration, Thermoelectric
Examples :
Micro-sensor networks, Pacemakers, RFID tags, and Portable devices

## Slide 3
3
Minimum Operating Voltage (Vmin)
Swanson and Meindl (1972) [2]
Vmin = 8kT/q ≈ 200 mV at 300K
Ideal limit of the lowest possible supply voltage (2001) [3]
Vmin = 2kT/q ≈ 57 mV at 300K
Minimum Energy Operation
Minimum Energy per Cycle (Emin )
Emin normally occurs in subthreshold region ( Vdd < Vth) if speed is not constrained.
Practical Emin may be higher for system performance
  Vdd cannot be scaled down to achieve Emin

## Slide 4
Previous Work
Published subthreshold or near-threshold VLSI design and operating voltage for minimum energy per cycle [4]
All work assumes scaling of a single Vdd

## Slide 5
Motivation
Energy budget for energy constrained systems may need to be more stringent for long battery life or energy harvesting.
Minimum energy operation has a huge penalty in system performance.
Near-threshold design gives moderate speed, but increases energy consumption about 2X from Emin.
Utilizing time slack for low power design is common at above-threshold, but has not been explored in subthreshold operation.
Sizing affects functional failure and fixed mult-Vth by foundries may not be adequate to utilize time slack in subthreshold region. But, two supply voltages are manageable and acceptable in today’s VLSI design

## Slide 6: Dual-Vdd Design
Apply VDDH to gates on critical paths to maintain performance, while VDDL to gates on non-critical paths to reduce power.
Two heuristic algorithms
  Clustered Voltage Scaling (CVS) [5]
  Extended Clustered Voltage Scaling (ECVS) [6]
- Use level converters in a combinational circuit block to achieve
more power saving than CVS.
Level converter has unacceptable delay overhead in subhreshold region.
PTM 90nm CMOS Gate delay | Nominal VDDH=1.2V, VDDL=0.8V | Subthreshold VDDH=0.3V, VDDL=0.25V
INV (fanout = 4) Level converter (LC) | 23.64 psec 112.33 psec | 1.52 nsec 121.86 nsec
LC / INV (FO=4) | 4.8 | 80.2
Eliminate use of LCs by topological constraints in MILP !!

## Slide 7
MILP for VDDL Assignment
Objective Function
Performance requirement TC (VDDH) is given.
Integer variable Xi : 0 for a VDDH cell or 1 for a VDDL cell.
The optimal VDDL is searched with MILP constraints by multiple-run between Vmin and VDDH.

## Slide 8
Timing Constraints
Ti is the latest arrival time at the output of gate i from PI events [7]
1
3
2
4
T2 ≥ T1 + td,VDDL×X2 + td,VDDH×(1-X2)

## Slide 9: Topological Constraints
Xj
Xi
j
k
i
HH: Xi – Xj = 0
LL: Xi – Xj = 0
LH: Xi – Xj = -1
HL: Xi – Xj = 1
VDDL
VDDH
VDDH
=0
=0
=1
VDDL
=1

## Slide 10
16-bit Ripple Carry Adder (RCA)
PTM 90nm CMOS (α=0.21, total gates=179) |  |  | 
Operation | VDD (V) | Energy/cycle (fJ) | Clock rate
Nominal | 1.2 | 263.4 | 1.16 GHz
Minimum Energy Single VDD | 0.21 | 9.65 | 2.15 MHz
Dual VDD ( energy opt.) | 0.21, 0.14 | 7.37 | 2.15 MHz
Dual VDD ( perf. opt.) | 0.27, 0.19 | 9.42 | 8.41 MHz
Energy Saving
23.6%
Speed-up
4X

## Slide 11
Gate Slack Distribution
Non-optimized 16-bit RCA
Single Vdd = 0.21V at Emin
Optimized 16-bit RCA
VDDH= 0.21V, VDDL= 0.14V
large slack gates
Topological
constraints

## Slide 12
4x4 Multiplier
PTM 90nm CMOS (α=0.32, total gates=140) |  |  | 
Operation | VDD (V) | Energy/cycle (fJ) | Clock rate
Minimum Energy Single VDD | 0.17 | 9.48 | 1 MHz
Dual VDD ( energy opt.) | 0.17, 0.12 | 8.99 | 1 MHz
Dual VDD ( perf. opt.) | 0.19, 0.13 | 9.19 | 1.67 MHz
Path balanced circuits reduce energy saving or speed-up from dual Vdd design.
Non-optimized
Optimized
Energy Saving 5.2%

## Slide 13
Selected ISCAS’85 Benchmark
Benchmark circuit | Total gates | Activity α | VDDH (V) | VDDL (V) | VDDL gates (%) | Esingle (fJ) | Edual (fJ) | Reduc. (%) | Freq. (MHz)
C880 | 360 | 0.18 | 0.24 | 0.18 | 46.4 | 14.4 | 11.2 | 22.2 | 13.6
c2670 | 901 | 0.16 | 0.25 | 0.21 | 46.4 | 32.8 | 28.0 | 14.8 | 17.4
C5315 | 2077 | 0.26 | 0.24 | 0.19 | 47.1 | 116.8 | 98.0 | 16.1 | 9.8
C6288 | 2407 | 0.28 | 0.29 | 0.18 | 2.7 | 165.4 | 162.0 | 2.1 | 9.4
C7552 | 2823 | 0.20 | 0.25 | 0.21 | 42.3 | 131.7 | 117.1 | 11.1 | 13.6
MILP solution at minimum energy single Vdd = VDDH
** PTM 90nm CMOS

## Slide 14
Gate Slack Distribution
c880
c5315
c6288
c7552

## Slide 15
MILP for High Performance
MILP is applicable for all performance criteria between minimum energy mode and nominal high performance mode
Benchmark circuit | Total gate | Activity α | VDDH (V) | VDDL (V) | VDDL gates (%) | Esingle (fJ) | Edual (fJ) | Reduc. (%)
C880 | 360 | 0.18 | 1.2 | 0.59 | 56.9 | 277.6 | 136.1 | 51.0
c1908 | 584 | 0.20 | 1.2 | 0.67 | 26.9 | 496.5 | 402.4 | 19.0
C2670 | 901 | 0.16 | 1.2 | 0.69 | 57.9 | 647.6 | 337.9 | 47.8
C3540 | 1270 | 0.33 | 1.2 | 0.70 | 11.6 | 1844.0 | 1667.0 | 9.6
C6288 | 2407 | 0.28 | 1.2 | 1.18 | 53.1 | 3066.0 | 2976.0 | 2.9
** PTM 90nm CMOS
Delay exponentially depends on Vdd in subthreshold region, but is polynomial dependence following the alpha-power law model [8] in above-threshold operation.
This delay characteristic causes less energy saving for subthreshold circuits

## Slide 16: Conclusion and Future Work
Dual Vdd design is valid for energy reduction below the minimum energy achievable by a single Vdd as well as for substantial speed-up within the minimum energy budget of a bulk CMOS subthreshold circuit.
Use of a conventional level converter is impractical due to huge delay in subthreshold dual-Vdd design and is eliminated by topological constraints in MILP.
Presented MILP for mininum energy CMOS design is applicable from minimum energy operation to high performance operation.
Delay of a subthreshold circuit is susceptible to process variation and investigation is needed in the minimum energy design.
Removing topological constraints in MILP by a proper level-shifting device is needed to achieve more energy saving.
Investigate technology scaling effect for dual-Vdd design in subtheshold region.

## Slide 17
[1] A. Wang, B. H. Calhoun, and A. P. Chandrakasan, Sub-Threshold Design for Ultra Low-Power Systems. Springer, 2006.
[2] R. M. Swanson and J. D. Meindl, “Ion-Implanted Complementary MOS Transistors in Low-Voltage Circuits,” IEEE JSSC, vol. 7, no. 2, April 1972.
[3] A. Bryant, J. Brown, P. Cottrell, M. Ketchen, J. Ellis-Monaghan, E. Nowak, I. Div, and E. Junction, “Low-power CMOS at Vdd= 4kT/q,” in Device Research Conference, 2001, pp. 22–23.
[4] M. Seok, D. Sylvester, and D. Blaauw, “Optimal Technology Selection for Minimizing Energy and Variability in Low Voltage Applications,” in Proc. of International Symp. Low Power Electronics and Design, 2008, pp. 9–14.
[5] K. Usami and M. Horowitz, “Clustered Voltage Scaling Technique for Low-Power Design,” in Proceedings of International Symposium on Low Power Design, 1995, pp. 3–8.
[6] K. Usami, M. Igarashi, F. Minami, T. Ishikawa, M. Kanzawa,M. Ichida, and K. Nogami, “Automated Low-Power Technique Exploiting Multiple Supply Voltages Applied to a Media Processor,” IEEE Journal of Solid-State Circuits, vol. 33, no. 3, pp. 463–472, 1998.
[7] T. Raja, V. D. Agrawal, and M. L. Bushnell, “Minimum Dynamic Power CMOS Circuit Design by a Reduced Constraint Set Linear Program,” in Proceedings of 16th International Conference on VLSI Design, Jan.2003, pp. 527–532.
[8] T. Sakurai and A. Newton, “Alpha-Power Law MOSFET Model and Its Applications to CMOS Inverter Delay and Other Formulas,” IEEE Journal of Solid-State Circuits, vol. 25, no. 2, pp. 584–594, Apr. 1990.
References

## Slide 18
Thank you!!
&
Questions?