## Slide 1: Externally Tested Scan Circuit with Built-In Activity Monitor and Adaptive Test Clock
Priyadharshini Shanmugasundaram
priyas@nvidia.com
Vishwani D. Agrawal
vagrawal@eng.auburn.edu
Hyderabad, India, January 11, 2012

## Slide 2: Testing of VLSI Circuits and Power
High circuit activity during test leads to functional slowdown and high test power dissipation:
  Peak power - Large IR drop in power distribution lines
    Voltage droop and ground bounce (power supply noise)
    Reduced voltage slows the gates down (delay fault)
  Average power - Excessive heating
    Timing failures
    Permanent damage to circuit
  Good chip may be labeled as bad → yield loss
Existing solution: Use worst-case test clock rate to keep average and peak power within specification.
  Results in long test time.

## Slide 3: Problem Statement
Reduce test time without exceeding the power specification:
Proposed solution: Adaptive test clock
    Use worst-case clock rate when circuit activity is not known
    Monitor circuit activity and speed up the clock when activity reduces

## Slide 4: Previous Publications
P. Shanmugasundaram and V. D. Agrawal, “Dynamic Scan Clock Control in BIST Circuits,” RASDAT, January 2011.
P. Shanmugasundaram and V. D. Agrawal, “Dynamic Scan Clock Control in BIST Circuits,” Proc. 43rd IEEE Southeastern Symposium on System Theory, March 14-16, 2011, pp. 239-244.
P. Shanmugasundaram and V. D. Agrawal, “Dynamic Scan Clock Control for Test Time Reduction Maintaining Peak Power Limit,” Proc. 29th IEEE VLSI Test Symposium, May 2-4, 2011, pp. 248-253.
P. Shanmugasundaram, Test Time Optimization in Scan Circuits, Master’s Thesis, Department of ECE, Auburn University, Auburn, Alabama, December 2010.

## Slide 5: Built-In Self-Test (BIST)
1
0
1
0
1
0
Combinational Logic
Primary
outputs
Primary
inputs
RA: Response analyzer
RBG: Random bit generator
SR: Scan register (flip-flops
with dual inputs)
SR, RBG
and RA have
common clock
and reset
Test multiplexers

## Slide 6: RBG Generates 010101
1
0
1
0
1
0
Primary
outputs
Primary
inputs
RA: Response analyzer
RBG: Random bit generator
SR: Scan register (flip-flops
with dual inputs)
SR, RBG
and RA have
common clock
and reset
Test multiplexers

## Slide 7: RBG Generates 111000
0
0
0
1
1
1
Primary
outputs
Primary
inputs
RA: Response analyzer
RBG: Random bit generator
SR: Scan register (flip-flops
with dual inputs)
SR, RBG
and RA have
common clock
and reset
Test multiplexers

## Slide 8: Main Idea
Observation: Different sequences of test vector bits consume different amounts of power.
Conventional test clock frequency is chosen based on maximum test power consumption.
    All test vector bits are applied with the same clock frequency.
Test vector bit sequences consuming lower power can be applied at higher scan clock frequencies without exceeding power budget of the chip.

## Slide 9: Scan Clock Frequency
Upper bounds:
  Maximum shift frequency allowed by shift register structure, F1
  Shift frequency determined by the highest scan activity and peak power budget, F2
  F1 >> F2
Fixed scan clock: use F2
Adaptive clock: monitor activity and vary clock frequency between F1 and F2

## Slide 10: Speeding Up Scan Clock
Clock periods
Cycle power
Power
budget
Clock periods
Cycle power
Power
budget

## Slide 11: Monitoring Test Activity
1
0
1
0
1
0
Combinational Logic
Primary
outputs
Primary
inputs
RA: Response analyzer
RBG: Random bit generator
Non-transition
monitor
SR, RBG
and RA have
common clock
and reset
Test multiplexers

## Slide 12: Monitoring Scan-in,

## Slide 13: Clock Rate vs. SR Activity
F1 = fmax
fmax/2
fmax/3
F2 = fmax/4
0 N/4 2N/4 3N/4 N
Number of non-transitions counted
Clock rate
N
N/2
N/4
0
SSR transitions per clock
N = number of flip-flops in scan shift register (SR)
M = number of adjustable clock rates = 4, in this illustration

## Slide 14: Monitor Scan-out,

## Slide 15: Experimental Result -
ATPG pattern sets, generated by Tetramax, for four large benchmark circuits analyzed for trends in peak activity factor
  Mean ()
  Standard deviation ()
Peak activity factor was lower than 0.65 in vector sets of all large benchmark circuits

## Slide 16: Externally Tested Circuit
Advantest T2000GS Automatic Test Equipment (ATE)
Start scan-in assuming for captured state
Results for ITC02 benchmark t512505
  N = 76,714 flip-flops (full-scan)
  Scan clock frequency steps, v = 512
Reference case scan clock frequency determined for activity , assumed 100kHz

## Slide 17: Adaptive Clock Testing
ATE supplies 51.2 MHz test clock
Test for stuck-at faults
DUT with monitoring and clock control implemented in FPGA
Synchronizer implemented in FPGA as a vector buffer, working with 51.2MHz clock
Adaptive clock:
  Begin scan-in with 100kHz scan clock. Set counter.
  Step up frequency when count of non-transitions entering scan chain is . Set counter.
  Step down frequency when count of non-transitions leaving scan chain is . Set counter.

## Slide 18: Test Time Reduction (%) in t512505
 | 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.65
0 | 0 | 7.59 | 15.29 | 22.98 | 30.67 | 38.36 | 46.06 | 49.90
0.1 | 0 | 0 | 7.59 | 15.29 | 22.98 | 30.67 | 38.36 | 42.21
0.2 | 0 | 0 | 0 | 7.59 | 15.29 | 22.98 | 30.67 | 34.52
0.3 | 0 | 0 | 0 | 0 | 7.59 | 15.29 | 22.98 | 26.83
0.4 | 0 | 0 | 0 | 0 | 0 | 7.59 | 15.29 | 19.13
0.5 | 0 | 0 | 0 | 0 | 0 | 0 | 7.59 | 11.44
0.6 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3.75
0.65 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.65
0 | 0 | 7.59 | 15.29 | 22.98 | 30.67 | 38.36 | 46.06 | 49.90
0.1 | 0 | 0 | 7.59 | 15.29 | 22.98 | 30.67 | 38.36 | 42.21
0.2 | 0 | 0 | 0 | 7.59 | 15.29 | 22.98 | 30.67 | 34.52
0.3 | 0 | 0 | 0 | 0 | 7.59 | 15.29 | 22.98 | 26.83
0.4 | 0 | 0 | 0 | 0 | 0 | 7.59 | 15.29 | 19.13
0.5 | 0 | 0 | 0 | 0 | 0 | 0 | 7.59 | 11.44
0.6 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3.75
0.65 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 19: Conclusion
Dynamic control of scan clock frequency proposed:
  Reduces testing time without exceeding power budget.
  On-chip activity monitor for self testing circuits keeps track of activity in scan chain and adjusts scan clock rate.
  On-chip or off-chip activity monitor can be used for externally tested circuits.
  Hand-shake protocol used for communication between ATE and DUT.
Vectors with low average scan-in activity and high peak activity achieve large reduction in test time.
Method can be implemented in circuits using compression hardware
  Activity monitored at every internal scan chain.
Up to 50% reduction in test time achieved in circuits when start frequency not pre-determined
  Results more significant when start frequency is pre-determined.