## Slide 1: Analog and RF Circuit Testing
Suraj Sindia
Vishwani D. Agrawal
Auburn University
ECE Dept., Auburn, AL 36849, USA
www.eng.auburn.edu/~vagrawal
Education Day, VDAT, July 2, 2012

## Slide 2: Outline
Introduction to analog/RF circuit test
Techniques for analog/RF circuit test
  Specification based test with examples
  Alternate test with examples
Conclusion
Notes: We will first motivate our talk with a discussion of the need for testing analog and RF circuits. Then we proceed to discuss the prevalent techniques for testing analog and RF circuits. We begin with the most widely used technique today in the industry, namely, Specification based test, then proceed to describe the less-used fault-model based and alternate test techniques. In each case, we use the same circuit examples that would help us in comparing the relative merits of each technique over the other. We finally conclude with a summary of the state of the art and directions of future research for more enthusiastic participants who would like to pursue this line of research.

## Slide 3: Outline
Introduction to analog/RF circuit test
Techniques for analog/RF circuit test
  Specification based test with examples
  Alternate test with examples
Conclusion
Notes: Let’s begin with an introduction to analog and RF circuit testing.

## Slide 4: Introduction
What are analog circuits?
  Circuits that process input signals in continuous time and give out an output signal also in continuous time are referred to as analog circuits.
  Examples: Operational amplifier, voltage regulator, charge pump, level shifter, filters, etc.
What are RF circuits?
  These are also analog circuits with the condition that their input signals are at a frequency, typically higher than 100s of kHz. They are form different blocks of signal chain in RF signal transmission or reception.
  Examples: Low noise amplifier, mixer, couplers, intermediate frequency filter, etc.
Notes:   Circuits that process input signals in continuous time and give out an output signal also in continuous time are referred to as analog circuits. Analog circuits are virtually everywhere. As a simple example, your car stereo system you would find a multitude of analog circuits used for:
  1) voltage amplification (i.e. increasing the signal strength);
  2) voltage regulation (i.e. providing a steady DC bias);
  3) level shifting (to generate high values of DC voltage from a relatively smaller value);
  4) filtering out undesirable tones from the signal that is to be played out;
  In fact all circuits, including so called “digital circuits” can be viewed as analog circuits. It is just that when we are dealing with digital circuits, we interpret the signals that we see at different nets as digital signals. That is, we label voltages close to the supply voltage as logic HIGH, and voltage close to zero as logic LOW. If you were to probe a node using an oscilloscope, you’d still see continuous time signals out of the probe.
  <click ENTER here>
  What are RF circuits?
  These are also analog circuits with the condition that their input signals are at a frequency, typically higher than 100s of kHz. Typical examples include low noise amplifier, mixer, couplers, intermediate frequency filter, which form different blocks of signal chain in RF signal transmission or reception.
  Having answered the question “What are analog and RF circuits?”, leads us to the next question, which is, “How do we design these circuits?”, but I must caution, this is not a subject for today’s talk. We shall therefore jump the gun and address the next question – Given that we have a manufactured analog circuit, “How does one test it?” But before that, we will digress and see “Why is testing analog circuits important and an increasingly hard problem?”

## Slide 5: Analog Circuits
Operational amplifier (analog)
Programmable gain amplifier (mixed-signal)
Filters, active and passive (analog)
Comparator (mixed-signal)
Voltage regulator (analog or mixed-signal)
Analog mixer (analog)
Analog switches (analog)
Analog to digital converter (mixed-signal)
Digital to analog converter (mixed-signal)
Phase locked loop (PLL) (mixed-signal)

## Slide 6: An RF Communications System
Duplexer
LNA
PA
LO
LO
LO
VGA
VGA
Phase
Splitter
Phase
Splitter
Digital Signal Processor (DSP)
ADC
ADC
DAC
DAC
90°
90°
0°
0°
RF
IF
BASEBAND
Superheterodyne Transceiver

## Slide 7: Components of an RF System
Radio frequency
    Duplexer
    LNA: Low noise amplifier
    PA: Power amplifier
    RF mixer
    Local oscillator
    Filter
Intermediate frequency
    VGA: Variable gain amplifier
    Modulator
    Demodulator
    Filter
Mixed-signal
    ADC: Analog to digital converter
    DAC: Digital to analog converter
Digital
    Digital signal processor (DSP)

## Slide 8: Why Do We Test Analog/RF Circuits?
Follows from the philosophy of testing:
  Manufacturing defects and process variation cause a circuit to deviate from its intended behavior.
  Testing circuits, ensures that they meet their desired behavior within the limits specified by the system.

## Slide 9: Is Testing Analog/RF Circuits a Hard Problem?
The answer is a resounding YES. But why?
  No standard procedure.
    Different circuits need different test equipment.
  No standard fault model.
    Precise modeling of fault behavior is not possible.
    Different components need different fault models.
    In contrast, “stuck-at” fault model has served us well in digital circuit testing.
In spite of the small proportion (<5%) of area they occupy on a System-on-Chip (SoC), analog circuits contribute to as much test cost as digital circuits.
Notes: SoC – System on Chip

## Slide 10: Methods of Analog/RF Testing
Specification-based testing
Model-based testing
  Catastrophic fault model
  Range model
Alternate test

## Slide 11: Outline
Introduction to analog/RF circuit test
Techniques for analog/RF circuit test
  Specification based test with examples
  Alternate test with examples
Conclusion

## Slide 12: Analog Circuit Testing: Specification Based Test
Specification based test
  Widely followed methodology in the industry.
  Compares the circuit output to its datasheet specifications.
  Uses a combination of DSP and measurement tools for validating circuit under test.

## Slide 13: Specification Based Test
Circuit Under Test
vin
vout
Datasheet
Spec. 1
●●●
Spec. N
Test programs on Automatic Test Equipment (ATE) arrive at pass/fail decision
based on whether circuit under test (CUT) meets all data-sheet specifications.
ATE

## Slide 14: VLSI Test Lab at Auburn University

## Slide 15: Specification Based Test: An Example
Non-inverting amplifier that employs an operational amplifier – μA741.
Rf= 4k
R1= 1k
Rin= 1k
Vo
Vin
VDD= 5V
μA741

## Slide 16: Specification Based Test: Amplifier Example
Specification | Nominal value | Minimum value | Maximum value
DC gain | 5 | 4.9 | 5.1
3dB Bandwidth | 100kHz | 90kHz | 110kHz
Signal to noise ratio | 45dB | 43dB | 47dB
Input offset current | 500nA | 300nA | 520nA
Input offset voltage | 0.5mV | 0.3mV | 0.52mV
Output offset voltage | 2.5mV | 1.5mV | 2.6mV

## Slide 17: Specification Based Test: Procedure
Each specification is measured for circuit under test (CUT).
Measured value is verified to be within minimum/maximum limits.
CUT is labeled GOOD, if and only if all measured specifications are within limits, else it is rejected.

## Slide 18: Measuring DC Gain: Test Setup
Rf= 4k
R1= 1k
Rin= 1k
Vo
Vin
VDD= 5V
0V-1V
Compute Vo/Vi, by varying Vin in the range 0-1V
at intervals of 0.1V
μA741

## Slide 19: DC Gain: Results
Measured DC gain at various sample points for two CUT.
DC Gain = Vo/Vin
Vin (in V)
Vo/Vin= 1+Rf/R1= 5
(Ideal)
Failing Device
Passing Device

## Slide 20: Measuring Bandwidth: Test Setup
Rf= 4k
R1= 1k
Rin= 1k
Vo
Vin = 1V
VDD= 5V
μA741
Variable
frequency
source

## Slide 21: Bandwidth Measurement Procedure
Procedure:
  Set input voltage amplitude to 1V.
  Sweep input frequency from 10Hz to 10MHz.
  Find gain at each frequency.
  Frequency at which gain falls 3dB below its value at 10Hz is the bandwidth.

## Slide 22: Bandwidth Measurement: Results
BW of PASSING part = 93kHz
BW of FAILED part = 87.5kHz
(Acceptable BW: 90-110kHz)
Measured spectrum of two CUT on NI ELVIS*
-3dB gain threshold
*NI ELVIS: National Instruments Electronic Virtual Instrumentation Suite
Frequency (Hz)
Gain (dB)

## Slide 23: Outline
Introduction to analog/RF circuit test
Techniques for analog/RF circuit test
  Specification based test with examples
  Alternate test with examples
Conclusion

## Slide 24: Analog Circuit Testing: Alternate Test
Alternate test
  Has limited acceptance in the industry. Has been used for RF/analog circuits in academic literature.
  CUT is classified as PASS/FAIL based on an economically measurable parameter instead of direct measurement of specification.
  A regression model relating the easier-to-measure parameter with all the circuit specifications is developed a priori. This regression model is then used to classify the CUT as PASS/FAIL.

## Slide 25: Alternate Test: An Example
Rf= 4k
R1= 1k
Rin= 1k
Vo
Vin
VDD= 5V
μA741
Problem:
To measure the DC gain and Input offset current
using only one measurement – supply current.

## Slide 26: Alternate Test: An Example
Specifications and limits on alternate measurement: IDD, zero-input supply current.
 |  | MINIMUM | MAXIMUM
Actual specification | DC gain (Nominal = 5) | 4.9 | 5.1
Alternate measurement | IDD | 3.8mA | 4.1mA
DC gain
 |  | MINIMUM | MAXIMUM
Actual specification | Input offset Current (Nominal=500nA) | 300nA | 520nA
Alternate measurement | IDD | 3.85mA | 4.2mA
Input
offset
current

## Slide 27: Alternate Test: DC Gain
Measured scatter plot of DC gain vs. IDD of 300 devices
Acceptable
DC gain
Accepted
IDD range
Yield loss = 3.33%
Defect level = 26.29%
IDD (mA)
DC Gain

## Slide 28: Alternate Test for DC Gain: Summary
Out of 300 devices tested for DC gain:
  No. of truly good parts = 195
  No. of good parts passing the alternate test = 185
  No. of bad parts passing the alternate test = 66
  No. of good parts rejected by the test = 10
    True yield = 195/300 = 65%
    Yield loss = (195-185)/300 = 3.33%
    Defect level = 66/(185+66) = 26.29%

## Slide 29: Alternate Test: Input Offset Current
Accepted Ioffset current
Accepted IDD
IDD (mA)
Ioffset(nA)
Yield loss = 9.67%
Defect level = 0%
Measured scatter plot of Ioffset vs. IDD of 300 devices

## Slide 30: Alternate Test for Ioffset: Summary
Out of 300 devices tested for Ioffset:
  No. of true good parts = 299
  No. of good parts passing the alternate test = 270
  No. of bad parts passing the alternate test = 0
  No. of good parts rejected by the test = 29
    True yield = 299/300 = 99.67%
    Yield loss = (299-270)/300 = 9.67%
    Defect level = 0/(270+0) = 0%

## Slide 31: Conclusion
Specification based test is a prevalent technique used for circuit testing.
  Set of measured performance parameters are compared with the datasheet limits through direct measurements, using custom-built instrumentation.
Alternate test is a novel method for testing analog/RF circuits.
  Uses an indirect easier-to-measure quantity to classify the chip as pass or fail.
  Pass/fail limits for measured quantity are determined by experiment or Monte Carlo simulation to minimize yield loss (YL) and defect level (DL).

## Slide 32: A Problem to Solve
An alternate test for an operational amplifier consists of the measurement of the zero input supply current, IDD(0). To set the pass/fail thresholds for IDD(0), Monte Carlo simulations are performed for 1,000 sample circuits in which component values are randomly varied. The computed gain and IDD(0) for these samples are shown in the following graph, where each sample appears as a point (assume that the total number of points is 1,000). Compute the defect level and yield loss as percentages.

## Slide 34: Answer
IDD(0)
GAIN
Acceptable
Gain
Pass
Fail
Fail
14 bad chips fail test
15 bad chips fail test
3 good chips fail test
4 bad chips pass test
3 bad chips pass test
2 good chips fail test

## Slide 35
True Yield:
Y = [(1,000 – 14 – 2 – 15 – 3)/1,000]·× 100 = 96.7%
Yield loss:
YL = (Good chips failing test/All fabricated chips) × 100
= [(2+3)/(1,000 – 14 – 2 -15 – 3)] × 100 = 0.51%
Defect level:
DL = (Bad chips passing test/All chips passing test) × 100
= [(3+4)/(1,000 – 14 – 2 – 15 – 3)]·× 100 = 0.72%

## Slide 36: References – Analog Test
A. Afshar, Principles of Semiconductor Network Testing, Boston: Butterworth-Heinemann, 1995.
M. Burns and G. Roberts, Introduction to Mixed-Signal IC Test and Measurement, New York: Oxford University Press, 2000.
M. L. Bushnell and V. D. Agrawal, Essentials of Electronic Testing for Digital, Memory and Mixed-Signal VLSI Circuits, Boston: Springer, 2000.
R. W. Liu, editor, Testing and Diagnosis of Analog Circuits and Systems, New York: Van Nostrand Reinhold, 1991.
M. Mahoney, DSP-Based Testing of Analog and Mixed-Signal Circuits, Los Alamitos, California: IEEE Computer Society Press, 1987.
A. Osseiran, Analog and Mixed-Signal Boundary Scan, Boston: Springer, 1999.
T. Ozawa, editor, Analog Methods for Computer-Aided Circuit Analysis and Diagnosis, New York: Marcel Dekker, 1988.
B. Vinnakota, editor, Analog and Mixed-Signal Test, Upper Saddle River, New Jersey: Prentice-Hall PTR, 1998.

## Slide 37: References – RF Test
S. Bhattacharya and A. Chatterjee, "RF Testing," Chapter 16, pages 745-789, in System on Chip Test Architectures, edited by L.-T. Wang, C. E. Stroud and N. A. Touba, Amsterdam: Morgan-Kaufman, 2008.
M. L. Bushnell and V. D. Agrawal, Essentials of Electronic Testing for Digital, Memory & Mixed-Signal VLSI Circuits, Boston: Springer, 2000.
J. Kelly and M. Engelhardt, Advanced Production Testing of RF, SoC, and SiP Devices, Boston: Artech House, 2007.
B. Razavi, RF Microelectronics, Upper Saddle River, New Jersey: Prentice Hall PTR, 1998.
J. Rogers, C. Plett and F. Dai, Integrated Circuit Design for High-Speed Frequency Synthesis, Boston: Artech House, 2006.
K. B. Schaub and J. Kelly, Production Testing of RF and System-on-a-chip Devices for Wireless Communications, Boston: Artech House, 2004.

## Slide 38: References – Alternate Test
P. N. Variyam, S. Cherubal and A. Chatterjee, “Prediction of Analog Performance Parameters Using Fast Transient Testing,” IEEE Trans. Computer-Aided Design, vol. 21, no. 3, pp. 349-361, March 2002.
H.-G. Stratigopoulos and Y. Makris, “Error Moderation in Low-Cost Machine-Learning-Based Analog/RF Testing,” IEEE Trans. Computer-Aided Design, vol. 27, no. 2, pp. 339-351, February 2008.