## Slide 1: Power Problems in VLSI Circuit Testing Keynote Talk
Vishwani D. Agrawal
James J. Danaher Professor
Electrical and Computer Engineering
Auburn University, Auburn, AL 36849, USA
VDAT, Kolkata, July 4, 2012

## Slide 2: Outline
Functional vs. test power.
Test power and test time for scan testing.
Asynchronous scan.
BIST with adaptive clock.
References

## Slide 3: Power Considerations in Design
A circuit is designed for certain function. Its design must allow the power consumption necessary to execute that function.
Power buses are laid out to carry the maximum current necessary for the function.
Heat dissipation of package conforms to the average power consumption during the intended function.
Layout design and verification must account for “hot spots” and “voltage droop” – delay, coupling noise, weak signals.

## Slide 4: Testing Differs from Functional Operation
VLSI chip
system
System
inputs
System
outputs
Functional inputs
Functional outputs
Other chips

## Slide 5: Basic Mode of Testing
VLSI chip
Test vectors:
Pre-generated
and stored in
ATE
DUT output for
comparison with
expected response
stored in ATE
Automatic Test Equipment (ATE):
Control processor, vector memory,
timing generators, power module,
response comparator
Power
Clock
Packaged or unpackaged
device under test (DUT)

## Slide 6: Functional Inputs vs. Test Vectors
Functional inputs:
    Functionally meaningful signals
    Generated by circuitry
    Restricted set of inputs
    May have been optimized to reduce logic activity and power
Test vectors:
    Functionally irrelevant signals
    Generated by software to test modeled faults
    Can be random or pseudorandom
    May be optimized to reduce test time; can have high logic activity
    May use testability logic for test application

## Slide 7: An Example
VLSI chip
Binary to
decimal
converter
3-bit random
vectors
8-bit
1-hot
vectors
VLSI chip
system
VLSI chip in system operation
VLSI chip under test
High activity
8-bit
test vectors
from ATE

## Slide 8: Scan Testing
SFF
SFF
SFF
Combinational
logic
PI
PO
SCANOUT
SCANIN
SE or TCK
Not shown: CK or
MCK/SCK feed all
SFFs.

## Slide 9: Test Time
Total scan test time (Number of scan test clock cycles × clock period):
TT = NT = [(ncomb + 2) nsff + ncomb + 4] × T
Where, ncomb = number of combinational vectors
nsff = number scan flip-flops in the longest scan chain
T = scan clock period
Example: 10,000 scan flip-flops in longest chain, 1,000 comb. vectors, total scan test length, TT ≈ 107 T.
Reference:
  M. L. Bushnell and V. D. Agrawal, Essentials of Electronic Testing for Digital, Memory and Mixed- Signal VLSI Circuits, Springer, 2000.

## Slide 10: Scan Power During a Clock Cycle
Clock period, T
time
Chip current, i(t)
0
T
Cycle energy, E = VDD ∫ i(t) dt
0
Cycle power, P = E/T

## Slide 11: Scan Power During Test With Synchronous Clock
1 2 3 4 5 6 7 8
Clock cycles
Cycle Energy, E
Emax
Cycle power, P
Pmax
E
E
E
E
E
E
E
E
P
P
P
P
P
P
P
P
Scan clock period, T = Emax/Pmax
T
T
T
T
T
T
T
T

## Slide 12: Test Time for Synchronous Clock
N Emax
TTsync = NT = ————
Pmax
Where,
N = Number of scan test clock cycles

## Slide 13: Power vs. Time
Reduce power:
  Use low activity vectors ⇒ slower rise in fault coverage ⇒ more vectors ⇒ longer test time
Reduce test time:
  Use high efficiency vectors ⇒ produce high activity ⇒ increase test power

## Slide 14: Can We Speed Up Scan Testing?
Maximum clock speed is limited by Emax of vectors and Pmax of circuit; T ≥ Emax/Pmax.
For most cycles E << Emax ⇒ can reduce period.
Structural limits on clock period:
    Critical path delay (functional and scan)
    Set up and hold times < critical path delay
A variable clock period can be shorter than the global (synchronous) power constrained period, T = Emax/Pmax.

## Slide 15: Asynchronous Scan
Pre-compute energy {Ei} for all clock cycles {i}.
For given power constrain Pmax of the circuit, set the period Ti of ith clock cycle as:
Ti = max {Ei/Pmax, critical path delay}
= Ei/Pmax, for power constrained testing
Where critical path delay can be different for scan and normal mode cycles.

## Slide 16: Scan Power During Test With Asynchronous Clock
1 2 3 4 5 6 7 8
Clock cycle, i
Cycle Energy, E
Emax
Cycle power, P
Pmax
E
E
E
E
E
E
E
E
P
P
P
P
P
P
P
P
Scan clock period, Ti = Ei/Pmax
T1
T7
T5
T2
T8
T3
T4
T6

## Slide 17: Test Time for Asynchronous Clock
N N
TTasyn = Σ Ti = Σ Ei/Pmax
i=1 i=1
N 1 N
= ——— × — Σ Ei
Pmax N i=1
N Eav Etotal
= ——— = ———
Pmax Pmax

## Slide 18: Comparing Two Scans
Test time (arbitrary units)
200
150
100
50
0
TTsync = Etotal/Pav
TTasyn = Etotal/Pmax
Pmax
Emax/Eav = 4

## Slide 19: Two Theorems
The minimum test time for a synchronous test is the ratio of total energy consumed during the entire test to the average power for all test cycles:
The minimum possible test time is the ratio of total energy consumed during the entire test to the peak power of any test cycle. This test time is achievable by asynchronous clock testing:

## Slide 20: Comparing Tests
time
Energy
Emax/Eav = 2
1.0
0.5
0.0
time
Energy
Emax/Eav = 5
1.0
0.5
0.0
Low power test

## Slide 21
Chart: Time (µs)
Asynchronous clock
Synchronous clock, T = 40ns
Pmax= 0.711 mW
Pav = 0.455 mW
TTsync, 40ns clock
TTasyn
Spice Simulation: s289 (14FF) Scan Test
Notes: Circuit s289 Total Test patterns = 33 ATPG patterns + 2 Additional set of patterns with alternate 1’s and 0’s
Pmax= 0.711 mW Pavg = 0.455 mW Test cycles = 14 Scan shift cycles + 1 Capture cycle
Synchronous clock period = 40ns Test Time Synchronous= 21.010 µs Test Time Asynchronous= 13.459 µs Gain=1.562

## Slide 22
Chart: Pmax, Peak Power (mW)
| 0.71138000000000001 | 0.5319199999999995 | 0.38484000000000035 | 0.23791000000000018 | 0.17888999999999999 | 0.14313000000000001 | 0.11839000000000002
Synchronous Clock | 19.81 | 26.4132 | 39.6198 | 59.4297 | 79.2396 | 99.0495 | 118.8594
Asynchronous Clock | 12.83 | 16.1655 | 23.58 | 38.4513 | 51.1446 | 63.948 | 77.3244
Test Time Synchronous
Test Time Asynchronous
=
1.54
Test Time (Synchronous)
Test Time (Asynchronous)
Spice Simulation: s298 Test Time Ratio
Notes: Test time Gain = (Test Time Synchronous clock)/(Test time adaptive clock)
Synchronous Clock Asynchronous Clock Test Time Synchronous Test Time Asynchronous Ratio
0.711 0.711 19.81 12.83 1.544
0.532 0.532 26.41 16.17 1.634
0.385 0.385 39.62 23.58 1.680
0.238 0.238 59.43 38.45 1.546
0.179 0.179 79.24 51.14 1.549
0.143 0.143 99.05 63.95 1.549
0.118 0.118 118.86 77.32 1.537

## Slide 23
Chart: Time (µs)
Asynchronous clock
Synchronous clock, T 40ns
Spice Simulation: s713 Scan Test
Pmax = 1.06mW
Pav = 0.53mW
Notes: Circuit: s713
Total Vectors = 60 Atpg vectors
Constant clock period = 40ns
Gain: 2

## Slide 24: Summarizing Asynchronous Scan
Total test energy (Etotal) is invariant for a test.
Cycle power (Pmax) is a circuit characteristic.
For power constrained scan testing,
  Synchronous clock test time = Etotal/Pav
  Asynchronous clock test time = Etotal/Pmax
Asynch. clock test will benefit from low energy tests.
Future explorations may investigate energy reduction techniques like reduced voltage testing.
Test programming for asynchronous clock needs to be worked out.

## Slide 25: A BIST Architecture
Combinational Logic
TPG
SAR
PI
PO
p1 = Prob{bit = 1}, or
TD = Prob{bit makes transition}

## Slide 26: WRP and TDP
Random pattern:
    0100101110, p1 = 0.5
Weighted random patterns (WRP):
    1011101101, p1 = 0.7
    0010011000, p1 = 0.3
Transition density patterns (TDP):
    0111001011, TD = 0.5
    1101001001, TD = 0.7
    0011101111, TD = 0.3
LFSR
LOGIC
FF
Random
patterns
WRP
TDP

## Slide 27: Speeding Up Random Test
Examine effect of weighted random patterns and transition density patterns on fault coverage.
Reduce test application time for test-per-scan BIST.
Proposed solution:
  Pre-select weighted random patterns or transition density patterns to produce high coverage test with shortest test length.
  Further reduce test time with adaptive activity-driven scan clock.

## Slide 28: Performance of Weighted Random Patterns (WRP)
Number of test per scan vectors for 95% coverage
s1269

## Slide 29: Performance of Transition Density Patterns (TDP)
Number of test per scan vectors for 95% coverage
s1269

## Slide 30: Best WRP and TDP for 95% Fault Coverage
Circuit name | Target Fault Coverage (%) | Weighted Random Vectors |  |  | Transition Density Vectors | 
 |  | Bestp1 | No. Of Vectors | TD = 2 × p1 × (1 – p1) | Best TD | No. of Vectors
s382 | 95 | 0.3 | 56 | 0.42 | 0.45 | 124
s510 | 95 | 0.4 | 136 | 0.48 | 0.5 | 152
s635 | 95 | 0.9 | 97 | 0.18 | 0.1 | 1883
s820 | 95 | 0.45 | 2872 | 0.495 | 0.45 | 5972
s1196 | 95 | 0.55 | 1706 | 0.495 | 0.45 | 2821
s1296 | 95 | 0.6 | 22 | 0.48 | 0.5 | 24
s1494 | 98.8 | 0.5 | 4974 | 0.5 | 0.45 | 3158
s1512 | 95 | 0.75 | 538 | 0.375 | 0.2 | 338

## Slide 31: BIST-TPG for WRP and TDP

## Slide 32: Adaptive Test Clock for BIST

## Slide 33
Circuit | Random Patterns (R), p1 = 0.5 test time (ns) | Weighted Random Patterns (WRP) |  | Transition Density Patterns (TDP) | 
 |  | Best p1 | Test time (ns) | Best TD | Test time (ns)
s298 | 10050 | 0.5 | 10050 | 0.5 | 1974026
s382 | 10320 | 0.3 | 6661 | 0.4 | 8287
S820 | 348392 | 0.4 | 268971 | 0.4 | 504453
S953 | 418073 | 0.4 | 162371 | 0.3 | 231833
S1196 | 264652 | 0.6 | 221416 | 0.3 | 262350
S1488 | 124572 | 0.6 | 117901 | 0.5 | 72831
s13207 | 31565011 | 0.35 | 16180025 | 0.3 | 10149712
s15850 | 16341260 | 0.5 | 16341260 | 0.3 | 20109065
90% Fault Coverage BIST, 25-100MHz Adaptive Clock

## Slide 34: Summarizing Adaptive BIST
Low toggle rate vectors, often suggested for reducing test power, generally cause slow rise in fault coverage and result in increased test time.
We find that a proper weight or transition density, which is circuit dependent, can be best for fault coverage.
Any toggle rate, low or high, can be used for quicker fault coverage with adaptive scan clock for an overall reduction in test time.
Combining multiple transition densities or weights can further reduce test time and/or enhance fault coverage.

## Slide 35: References
P. Shanmugasundaram and V. D. Agrawal, “Dynamic Scan Clock Control for Test Time Reduction Maintaining Peak Power Limit,” in Proc. 29th IEEE VLSI Test Symp., May 2011, pp. 248–253.
V. D. Agrawal, “Pre-Computed Asynchronous Scan (Invited Talk),” 13th IEEE Latin American Test Workshop, Quito, Ecuador, April 2012.
F. Rashid, “Controlled Transition Density Based Power Constrained Scan-BIST with Reduced Test Time,” Master’s thesis, Auburn University, Alabama, USA, May 2012.
P. Venkataramani and V. D. Agrawal, “Reducing Test Time of Power Constrained Test by Optimal Selection of Supply Voltage,” submitted to 26th International Conf. VLSI Design, Pune, Jan. 5-10, 2013.