## Slide 1: Technology Characterization Model and Scaling For Energy Management Harshil Goyal Dr. Vishwani D. Agrawal VDAT - 2019
Department of Electrical and Computer Engineering
Auburn University, AL 36849 USA

## Slide 2: Outline
Introduction
Problem Statement
Background
Methodology
Simulation setup
Results
Applications
Conclusion
Notes: Energy and performance are important aspects of microprocessors and their verification and management require, measurement, estimation and analysis and these aspects are discussed through this research.

## Slide 3: Introduction
Most VLSI chips, including microprocessors, come with prescribed operating conditions, found in specifications supplied by the manufacturer. While such specifications serve a majority of users, they are not optimized for specific applications.
Application-specific optimization of operation requires power-delay characterization of the chip at various supply voltages.
Notes: This paper presents an inexpensive alternative that a user can adopt with reasonable effort and with readily available information. One needs the specifications of the processor and knowledge of its semiconductor technology. Relevant data from specifications include nominal voltage, clock frequency, thermal design power (TDP), maximum frequency (fmax) and peak power (Pmax).
The main idea of this paper is to simulate a model digital circuit at the circuit-level using the technology of the target device. The model can be any circuit of convenient size. The simulator can be any efficient version of Spice with accurate technology models. In our illustration of the methodology, we use HSPICE [1] and, in the absence of actual models, employ the predictive technology model (PTM) [2]. The simulation is repeated at several voltages over the entire range in which the device can function. The results are then matched with the device specification data to determine suitable scale factors for size (area), voltage and frequency.

## Slide 4: Problem Statement
Obtain data on voltage, frequency and cycle efficiency of the processor for time and energy optimization.
Determine operating conditions (voltage and frequency) for optimal time and energy operation.
Notes: With this available information we illustrate a power management method that manages the highest performance including turbo (over-clocking), lowest energy, and all in-between operating modes.

## Slide 5: Motivation
Experimental set up is expensive.
Simulation requires a complete model of the chip, often not available from the manufacturer.
Even if a simulation model is available, accurate timing and power analysis can be expensive.
Notes: Application-specific optimization of operation could be done through either actual hardware experiment or entire chip simulation, both operations present difficulties.

## Slide 6: Performances Measures
Time Performance of Processor
  Speed of a processor is measured in cycles per second or clock frequency (f).
  Execution time of a program using C clock cycles = C/f
  Time performance = f/C
Energy Performance of a Processor
  Efficiency of a processor may be measured in cycles per joule or cycle efficiency (η).
  Energy dissipated by a program using C clock cycles = C/η
  Energy performance = η/C
Notes: So having cycle efficiency one can determine no. of cycles that can be completed per given energy resource. As an analogy to automobile performance, frequency is analogous to miles per hour MPH and efficiency eta is analogous to miles per gallon MPG

## Slide 7: Simulation Tools Used
Questa Sim
    Design, compile and simulate designs
  Leonardo Spectrum
    ASIC and standard cell synthesis
  Design Architect-IC
    Schematic capture
  HSPICE
    Circuit simulation and verification
Notes: In the initial phase of a CMOS product chip architecture and design, an assessment of power and performance at the technology node of interest is made from the compact models provided by the silicon foundry. In the design implementation phase, circuits and physical layouts are optimized by incorporating these models in the EDA tools. There are different tools for circuit modeling, netlist generation, simulation, process variation, and result analysis.

## Slide 8: Processor Specifications
Intel i5 Sandy Bridge 2500K | Specifications
Technology Node | 32nm
Voltage Range | 1.2 - 1.5 volts
Nominal Base Frequency, | 3.3 GHz
Overclock Frequency, | 5.01 GHz
Thermal Design Power, TDP | 95 Watts
Peak Power | 132 Watts
Intel i5 Sandy Bridge 2500K | Specifications
Technology Node | 32nm
Voltage Range | 1.2 - 1.5 volts
 | 3.3 GHz
 | 5.01 GHz
Thermal Design Power, TDP | 95 Watts
Peak Power | 132 Watts
Notes: Processor specifications we used for our experiment.

## Slide 9: Intel Definitions
TDP- is the average maximum power in watts the processor dissipates when operating at base frequency with all cores active under a manufacturer defined, high complexity workload.
Peak power is the maximum power dissipated by the processor.
Notes: TDP is not the maximum power the CPU may consume - there may be periods of time when the CPU dissipates more power than that allowed by its thermal design. TDP is usually 20%-30% lower than the CPU maximum power dissipation.
Peak power is the maximum power dissipated by the processor under the worst case conditions - at the maximum core voltage, maximum temperature and maximum signal
loading conditions.

## Slide 10: Model Circuit Used
Adder circuit
  Fundamental block of functional units
  Often in processor’s critical path
  Used 16-bit Ripple Carry Adder (RCA)
PTM Models
  Characterized in two PTM models: bulk CMOS and High-K
  Technology node: 45nm, 32nm and 22nm
Notes: PTM models are predictive model files for the future transistor and interconnect technologies. Bulk CMOS uses Silicon on insulator (SOI) technology where we use a layered silicon–insulator–silicon substrate in place of conventional silicon substrates in semiconductor manufacturing.
High-κ dielectrics are used in semiconductor manufacturing processes where they are usually used to replace a silicon dioxide gate dielectric or another dielectric layer of a device. Replacing the silicon dioxide gate dielectric with a high-κ material allows increased gate capacitance without the associated leakage effects.

## Slide 11: Vector Selection (contd.)
  Out of 1000 random vectors 50 vector pairs were selected:
    16 consume avg. power
    17 consume above avg. power including the peak power vector pair
    17 consume below avg. power including the min. power vector pair
Notes: Input vector selection is an important step in determining the average power and critical path delay. Initially, 1,000 random vectors were generated using a MATLAB program which resulted in power consumption of each vector ie. average power per vector.
The graph shows the power consumption by 50 selected vector pairs when they were embedded in the set of 1,000 vectors and then re-simulated as 100 standalone vectors. The reason to select vectors through such a rigorous procedure is that use of the adder circuit and random vectors assumes an overall imitation of processor. Also with such a selection we can say that activity generated in both the circuits is same.

## Slide 12: Model Circuit (Adder) Simulation by H-Spice (32nm Bulk PTM Techbology)
Voltage | Power from simulation |  |  |  | Timing from simulation |  | Energy per cycle |  | 
Vdd (v) | pavg. (µW) | pdyn (µW) | pstatic (µW) | Ppeak (µW) | Critical path Delay (ps) | fmax (GHz) | edyn (fJ) | estatic (fJ) | eavg. (fJ)
1.2 | 124.03 | 91.37 | 32.66 | 397.71 | 320.85 | 3.12 | 29.32 | 10.48 | 39.8
1.15 | 100.5 | 78.31 | 22.19 | 335.74 | 338.91 | 2.95 | 26.54 | 7.52 | 34.06
1.1 | 81.93 | 66.72 | 15.21 | 261.9 | 360.46 | 2.77 | 24.05 | 5.48 | 29.53
1.05 | 66.21 | 55.74 | 10.47 | 217.46 | 386.5 | 2.59 | 21.54 | 4.05 | 25.59
1 | 53.77 | 46.51 | 7.26 | 178.2 | 418.72 | 2.39 | 19.47 | 3.04 | 22.51
0.95 | 42.65 | 37.58 | 5.07 | 144.77 | 459.03 | 2.18 | 17.25 | 2.33 | 19.58
0.9 | 33.4 | 29.83 | 3.57 | 115.34 | 509.72 | 1.96 | 15.21 | 1.8202 | 17.03
0.8 | 19.08 | 17.32 | 1.751 | 73.71 | 666.65 | 1.5 | 11.55 | 1.167 | 12.72
0.7 | 9.59 | 8.73 | 0.856 | 35.76 | 986.51 | 1.014 | 8.62 | 0.844 | 9.46
0.6 | 3.97 | 3.57 | 0.406 | 14.71 | 1792.1 | 0.558 | 6.39 | 0.727 | 7.12
0.5 | 1.138 | 0.956 | 0.182 | 4.01 | 4511.7 | 0.222 | 4.31 | 0.819 | 5.13
0.4 | 0.229 | 0.15 | 0.079 | 0.695 | 18928 | 0.053 | 2.84 | 1.488 | 4.33
0.35 | 0.1 | 0.048 | 0.051 | 0.233 | 44168 | 0.023 | 2.13 | 2.27 | 4.4
0.3 | 0.047 | 0.014 | 0.033 | 0.09 | 112760 | 0.009 | 1.601 | 3.75 | 5.35
0.25 | 0.025 | 0.004 | 0.021 | 0.036 | 279310 | 0.004 | 1.056 | 5.85 | 6.91
0.2 | 0.014 | 0.0009 | 0.013 | 0.017 | 716150 | 0.0014 | 0.645 | 9.08 | 9.73
0.15 | 0.0074 | 0.0002 | 0.0072 | 0.0086 | 1851700 | 0.0005 | 0.3494 | 13.27 | 13.62
Notes: Describe 1st row of table

## Slide 13: Power and EPC for Adder
Average, peak, dynamic and static power
PDP/Energy per cycle (EPC)
Notes: It can be observed that the power exponentially reduces as the supply voltage reduces. Therefore, the total average energy, that is calculated by the Power Delay Product (PDP), also reduces when the supply voltage reduces as shown in 2nd figure. sub-threshold region. With down scaling of Vdd beyond the threshold voltage, there is an exponential increase in circuit delay that increases the time per operation (clock cycle) over which the circuit leaks. As a result, the minimum energy point occurs at around 0.378 volts that is about 4.31 fJ per addition. This result is attractive for energy-efficient design of portable devices that require to dissipate low energy while operating with limited battery sources.

## Slide 14: Scale Factors

## Slide 15: Area Scale Factors
All the scaling factors were found using processor’s specifications given at rated voltage 1.2v assuming that voltage was not raised for overclock frequency.
Total power both circuits are given as:
  (1) (Total Power for Adder)
  (2) (Total Power for Processor)
Since we selected our vectors in specific way therefore the activity produced in both the circuits is assumed to be same and hence the activity factor in this case is 1. Now, if β is the scale factor representing the relative size of processor to adder circuit and σ is the voltage factor i.e. both the adder as well as processor are simulated at same supply voltage, then eq. 1 modifies eq. 2 as:
  Solving for β gives:
  at rate voltage and frequency
Notes: Area Scale Factor ( Beta): It represents the relative size of processor to that of the adder (RCA). Since edyn is a function of signal activity in the model, the difference in activities of the model circuit and the processor is implicit in the area scale factor. We have, therefore, not used a separate scale factor for activity.
Voltage Scale Factor ( Sigma): It accounts for the difference between the voltage at which adder (RCA) is simulated and the processor supply voltage.
Area Scale Factor (𝜷 Beta): It represents the relative size of processor to that of the adder (RCA). Since edyn is a function of signal activity in the model, the difference in activities of the model circuit and the processor is implicit in the area scale factor. We have, therefore, not used a separate scale factor for activity.
Voltage Scale Factor (𝝈 Sigma): It accounts for the difference between the voltage at which adder (RCA) is simulated and the processor supply voltage.

## Slide 16: Frequency Scale Factors
Processor base frequency () describes the rate at which the processor's transistors open and close. The processor base frequency is the operating point where TDP is defined and is given as:
  Where, δ is a scale factor for and is given by,
  δ (Frequencies at rated voltage =1.2 volts)
In a structure constrained system, the frequency ) is limited by the critical path delay of the circuit as follows:
  (3)
  Where, is a scale factor for and is given by,
  (Frequencies at rated voltage =1.2 volts)
Notes: Nominal Frequency Scale Factor (δ delta): It is the ratio of processor's nominal frequency to adder's maximum frequency at rated voltage, e.g., Vdd = 1.2 volts, and is used to find suitable frequency for processor at any supply voltage.
Maximum Frequency Scale Factor (Gamma): It is the ratio of processor's maximum frequency to adder's maximum frequency at rated voltage, e.g., Vdd = 1.2 volts, and is used to find the maximum (structural or critical path) frequency for processor at any supply voltage.
Nominal Frequency Scale Factor (δ delta): It is the ratio of processor's nominal frequency to adder's maximum frequency at rated voltage, e.g., Vdd = 1.2 volts, and is used to find suitable frequency for processor at any supply voltage.
Maximum Frequency Scale Factor (𝜸 Gamma): It is the ratio of processor's maximum frequency to adder's maximum frequency at rated voltage, e.g., Vdd = 1.2 volts, and is used to find the maximum (structural or critical path) frequency for processor at any supply voltage.

## Slide 17: Frequency Scale Factors (contd.)
In a power constrained system [10-12], the frequency ) is limited by the maximum allowable power of the circuit. In general it can be represented as,
  (4)

## Slide 18: Scale Factor Summary
Scale Factors | Calculated Values
Voltage factor, σ | 1
fnom factor, δ | 1.0588
Fmax factor, γ | 1.6075
Area factor, β | 7.3414
Scale Factors | Calculated Values
Voltage factor, σ | 1
fnom factor, δ | 1.0588
Fmax factor, γ | 1.6075
Area factor, β | 

## Slide 19: Energy per Cycle and Cycle Efficiency for Processor
The energy per cycle for the processor for the nominal frequency and overclock/maximum frequency for a any given Vdd is defined by:
  (5)
  (6) (fnom F0 fmax)
Here in this case, F0 = fmax = 5.01 GHz, therefore we call EPCFo as EPCfmax
As we know, cycle efficiency is given by η=1/EPC , eq. 5 and 6 gives:
  and, (fnom F0 fmax)
Here, EPCFo = EPCfmax therefore we call0 as peak cycle efficiency.

## Slide 20: Scaled Values for Intel i5 2500K Processor
Voltage | Scaled Power |  |  | Scaled Frequency |  | Energy per cycle |  | Cycle efficiency | 
Vdd (v) | Pavg. (W) | Pdyn (W) | Pstatic (W) | fnom (GHz) | fmax (GHz) | Efnom (nJ) | Efmax (nJ) | η (106cycles/J) | ηo (106cycles/J)
1.2 | 95 | 71.02 | 23.98 | 3.3 | 5.01 | 28.79 | 26.31 | 34.74 | 38.01
1.15 | 77.16 | 60.87 | 16.29 | 3.12 | 4.74 | 24.7 | 22.92 | 40.49 | 43.63
1.1 | 63.03 | 51.86 | 11.17 | 2.94 | 4.46 | 21.46 | 20.16 | 46.6 | 49.6
1.05 | 51.01 | 43.33 | 7.69 | 2.74 | 4.16 | 18.62 | 17.66 | 53.7 | 56.61
1 | 41.48 | 36.15 | 5.33 | 2.53 | 3.84 | 16.4 | 15.68 | 60.96 | 63.76
0.95 | 32.93 | 29.21 | 3.72 | 2.31 | 3.5 | 14.28 | 13.73 | 70.04 | 72.85
0.9 | 25.81 | 23.19 | 2.62 | 2.08 | 3.15 | 12.43 | 11.99 | 80.48 | 83.37
0.8 | 14.75 | 13.47 | 1.286 | 1.588 | 2.41 | 9.29 | 9.01 | 107.66 | 110.96
0.7 | 7.42 | 6.79 | 0.628 | 1.073 | 1.629 | 6.91 | 6.71 | 144.71 | 149.02
0.6 | 3.07 | 2.77 | 0.298 | 0.591 | 0.897 | 5.2 | 5.02 | 192.43 | 199.02
0.5 | 0.877 | 0.743 | 0.133 | 0.235 | 0.356 | 3.74 | 3.54 | 267.7 | 282.35
0.4 | 0.174 | 0.117 | 0.058 | 0.056 | 0.085 | 3.12 | 2.76 | 321.02 | 361.92
0.35 | 0.075 | 0.038 | 0.038 | 0.024 | 0.036 | 3.14 | 2.6 | 318.66 | 384.45
0.3 | 0.035 | 0.011 | 0.024 | 0.0094 | 0.014 | 3.77 | 2.89 | 265.04 | 346.44
0.25 | 0.018 | 0.0029 | 0.015 | 0.0038 | 0.0058 | 4.83 | 3.45 | 206.93 | 290.03
0.2 | 0.01 | 0.0007 | 0.0093 | 0.0015 | 0.0022 | 6.77 | 4.62 | 147.71 | 216.41
0.15 | 0.0054 | 0.0001 | 0.0053 | 0.0006 | 0.0009 | 9.46 | 6.32 | 105.74 | 158.31
Notes: Explain the 1st row of table and how it matches the specification given by processor manufacturer after scaling values from model circuit.
Also explain that the data obtained for processor after scaling gives cycle efficiency 321.02 mega cycles/J for nominal frequency at vdd 0.4v whereas the cycle efficiency 384.45 mega cycles/J for maximum frequency is at vdd 0.35v.

## Slide 21: Processor Power and Cycle Efficiency Plots
Because our own greatest access and insight involves Intel designs and data, our graphs and estimates draw heavily on them.
Notes: Epc vs voltage

## Slide 22: Applications

## Slide 23: Power and Performance Management
Proposed “Power Management" showing three voltage regions.
Notes: Power management provides a system solution to boost the processor frequency to values higher than the nominal whenever required as per performance criteria. For workloads that are not operating at the cooling/power supply limits this can often result in real performance increase. The focus of this experiment is to evaluate the benefits of proposed method and establish the relationship between the workload and related system characteristics which determine the benefits. Performance optimization is shown in super threshold region where as Energy optimization is shown in sub-threshold region.

## Slide 24: Energy Efficient Point (Sub-Threshold Region)

## Slide 25: Power and Performance Management (Super-Threshold Region)
Notes: Through this graph we aim to find the best voltage and frequency at which a power constrained system can run with maximum frequency without exceeding the peak power or violating the critical path delay constraint of the circuit. As mentioned above the frequency can be increased while limiting the power by reducing the supply voltage. However, there exists a point where the voltage will not be enough to charge the output load capacitance within the right amount of time. Thus the value at the output will be wrong. At this point the circuit is considered structure constrained and the frequency is now dependent on the critical path delay of the circuit. Using curve fitting tool in Microsoft excel we get two polynomials equations of degree 3 to these two functions.

## Slide 26: Optimum Voltage and Frequency (contd.)
Voltage Vdd (Volts) | Clock Frequencies (MHz) |  | Cycle Efficiency (106 cycles/J) | 
 | Structure Constrained (fmax) | Power Constrained (fTDP) | Peak η0 at fmax | ηTDP at fTDP
1.3 | 5486 | 2243 | 31.09 | 23.57
1.25 | 5257 | 2761 | 34.22 | 29.04
1.2 | 5010 | 3300 | 38.01 | 34.74
1.15 | 4740 | 4040 | 43.63 | 42.52
1.112 | 4531 | 4531 | 47.91 | 47.91
1.1 | 4460 | 4750 | 49.6 | 49.98
1.05 | 4160 | 5520 | 56.61 | 58.11
1 | 3840 | 6270 | 63.76 | 66.02
0.95 | 3500 | 7210 | 72.85 | 75.87
0.9 | 3150 | 8280 | 83.37 | 87.11
Notes: Using the curve fitting the previous graph in excel we got 4 polynomial equations and, we measure ftp and fmax for different supply voltages. We observe that as we decrease supply voltage, fTDP increases but at the same time fmax reduces. Similarly we measure cycle efficiencies from equations using the two frequencies ftdp and fmax. Note that cycle efficiency increases in both the cases with decrease in supply voltage because energy per cycle consumed is less when the frequency is more.
Solving these equations by a numerical solver in MATLAB, we obtain two complex and one real roots. Discarding complex roots, the real root gives Vdd = 1:112 volts. This is the optimum voltage Vddopt at which the processor will run fastest without exceeding the TDP. We can calculate fopt by substituting Vdd = Vddopt, which gives fopt = 4531 MHz. Similarly, we can calculate nopt these equations by substituting Vdd = Vddopt, which gives nopt = 47.91 cycles/J.

## Slide 27: Managing Processor Operation for Time and Energy
TIME AND ENERGY FOR A PROGRAM USING C = 2 BILLION CLOCK CYCLES |  |  |  |  |  | 
Operating Modes | Voltage (volts) | Clock Frequency f (MHz) | Cycle Efficiency η (106cycles/J) | Power Consumption (Watts) | Execution Time (seconds) | Total Energy (Joules)
Nominal Operating Point | 1.2 | 3300 | 34.74 | 95W | 0.61 | 57.57
Overclocked Operating Point 20% Overclock | 1.2 | 3300 (80%) 5010 (20%) | 27.792+ 7.602 = 35.394 | 95W 132W | 0.485+ 0.0798 = 0.57 | 46.06+10.52 = 56.58
Highest Performance Operation | 1.112 | 4531 | 47.91 | 95W | 0.44 (-28%) | 41.75 (-28%)
Dynamic Voltage Scaling (DVS) | 0.92 | 3300 | 79.01 | 41.77W (-56%) | 0.61 (0%) | 25.31 (-56%)
Highest Energy Efficiency | 0.35 | 36.39 | 384.45 | 0.0946 | 54.96 | 5.20
TIME AND ENERGY FOR A PROGRAM USING C = 2 BILLION CLOCK CYCLES |  |  |  |  |  | 
Operating Modes | Voltage (volts) | Clock Frequency f (MHz) | Cycle Efficiency η (106cycles/J) |  |  | 
Nominal Operating Point | 1.2 | 3300 | 34.74 | 95W | 0.61 | 57.57
Overclocked Operating Point 20% Overclock | 1.2 | 3300 (80%) 5010 (20%) | 27.792+ 7.602 = 35.394 | 95W 132W | 0.485+ 0.0798 = 0.57 | 46.06+10.52 = 56.58
Highest Performance Operation | 1.112 | 4531 | 47.91 | 95W | 0.44 (-28%) | 41.75 (-28%)
Dynamic Voltage Scaling (DVS) | 0.92 | 3300 | 79.01 | 41.77W (-56%) | 0.61 (0%) | 25.31 (-56%)
Highest Energy Efficiency | 0.35 | 36.39 | 384.45 | 0.0946 | 54.96 | 5.20
Notes: I will be explaining two application that we developed using this experiment

## Slide 28: Summary
PTM Models | Intel Processor used | Manufacturer’s Specifications |  |  |  |  | Optimized Operation |  |  |  |  |  | 
 |  | Nominal Operation |  |  | Optimized |  | Maximum Speed |  |  | Minimum Energy |  |  | 
 |  | fTDP (MHz) | Vdd (v) | ηTDP (106 c/J) | Vdd (v) | ηTDP (106 c/J) | Vddopt (v) | fopt (MHz) | ηopt (106 c/J) |  | Vdd (v) | fη0 (MHz) | η0 (106 c/J)
45nm bulk | Core 2 Duo T9500 | 2600 | 1.25 | 74.29 | 1.07 | 108.58 | 1.2 | 2920 | 82.28 |  | 0.35 | 33.51 | 829.29
45nm High-K | Core 2 Duo T9500 | 2600 | 1.25 | 74.29 | 0.79 | 350.91 | 1.226 | 3120 | 89.08 |  | 0.3 | 304.48 | 1795
32nm bulk | Core i5-2500K | 3300 | 1.2 | 34.74 | 0.92 | 79.01 | 1.112 | 4531 | 47.91 |  | 0.35 | 36.39 | 384.45
32nm High-K | Core i5-2500K | 3300 | 1.2 | 34.74 | 0.67 | 267.57 | 1.155 | 4940 | 51.77 |  | 0.3 | 414.23 | 953.81
22nm bulk | Core i7- 3820QM | 2700 | 0.8 | 60 | 0.7 | 96.22 | 0.742 | 3171 | 86.89 |  | 0.38 | 177.25 | 213.99
22nm High-K | Core i7- 3820QM | 2700 | 0.8 | 60 | 0.61 | 137.65 | 0.76 | 3626 | 80.38 |  | 0.3 | 332.58 | 375.76
Notes: This table represents the data for various Intel processors when simulated using different PTM Models using the same methodology that we used for our selected processor, validating that our method can be applied to any processor given with its manufacturer specifications.

## Slide 29: Conclusion
Present Work
  Simulation based evaluation.
  Power management is described through:
    Improving rated cycle efficiency
    Performance optimization
    Energy optimization
Future Work
  Process variation can be taken in account
  Effect of noise margin in sub-threshold region
  Better evaluation of activity factor
Notes: Here our area factor includes the activity factor but a better evaluation can be achieved for any difference between adder circuit and chosen processor.

## Slide 30: References
[1] H. Goyal, “Characterizing Processors for Time and Energy Optimization,” Master's
thesis, Auburn University, Auburn, Alabama, USA, Aug 2016.
[2] H. Goyal and V. D. Agrawal, “Characterizing Processors for Energy and Performance Management,” in Proc. 16th International Workshop on Microprocessor/SoC Test and Verification (MTV), Austin, Texas, Dec. 3-4, 2015.
[3] H. Goyal and V. D. Agrawal, “Characterizing Processors for Energy and Performance Management,” IEEE VLSI Test Symposium, Las vegas, CA, April 2016 (Poster).
[4] D. A. Patterson and J. L. Hennessy, Computer Organization & Design, the Hardware/Software Interface. San Francisco, California: Morgan Kaufman, fourth edition, 2008.
[5] A. Shinde and V. D. Agrawal, “Managing Performance and Efficiency of a Processor,” in Proc. 45th Southeastern Symp. System Theory, 2013, pp. 59-62.
[6] K. Kim and V. D. Agrawal, “Dual Voltage Design for Minimum Energy using Gate Slack,” in Proc. International Conf. on Industrial Technology, 2011, pp. 419–424.
[7] K. Kim and V. D. Agrawal, “Minimum Energy CMOS Design with Dual Subthreshold Supply and Multiple Logic-Level Gates,” in Proc. International Symp. Quality Electronic Design, 2011, pp. 689–694.
[8] C. Bienia, et al., “The PARSEC Benchmark Suite: Characterization and Architectural Implications,” in Proc. 17th International Symposium on Parallel Architectures and Compilation Techniques, 2008.

## Slide 31: References
[9] A. Wang, A. P. Chandrakasan, and S. V. Kosonocky, "Optimal Supply and Threshold Scaling for Subthreshold CMOS Circuits,” in Proc. IEEE Computer Society Annual Symposium on VLSI, 2002, pp. 5-9.
[10] P. Venkataramani, “Reducing ATE Test Time by Voltage and Frequency Scaling,” PhD dissertation, Auburn University, Auburn, AL, USA, May 2014.
[11] P. Venkataramani, S. Sindia, and V. D. Agrawal, “A Test Time Theorem and its Applications,” Journal of Electronic Testing: Theory and Applications, vol. 30, no. 2, pp. 229-236, 2014.
[12] P. Venkataramani and V. D. Agrawal, “Reducing Test Time of Power Constrained Test by Optimal Selection of Supply Voltage,” in Proc. 26th International Conf. VLSI Design, Jan. 2013, pp. 273-278.
[13] Design Architect User Guide. Mentor Graphics Corp., Wilsonville, OR, 1991-1995.
[14] HSPICE Signal Integrity User Guide. Synopsys, Inc., 700, East Middlefield Road, Mountain View, CA 94043, 2010.
[15] Leonardo Spectrum User Guide. Mentor Graphics Corp., Wilsonville, OR, 2011.
[16] Questa Sim User Guide. Mentor Graphics Corp., Wilsonville, OR, 2011.
[17] Intel Core i5-2500K Processor (6M Cache, up to 3.70 GHz) Specifications, 2016. http://ark.intel.com/products/52210/Intel-Core-i5-2500K-Processor-6M-Cache-up-to-3 70-GHz.

## Slide 32: Questions?
Thank You