## Slide 1: Two-Pattern ∆IDDQ Test for Recycled IC Detection
Prattay Chowdhury, Ujjwal Guin, Adit D. Singh, Vishwani D. Agrawal
Dept. of Electrical and Computer Engineering,
Auburn University, Auburn, AL-36849, USA

## Slide 2: Outline
Motivation and contributions
IDDQ modeling in gates
Aging and its effect
Process variation
Non-uniform aging in circuit
Proposed method to detect recycled IC
Simulation results and discussion
Conclusion

## Slide 3: Motivation and Contribution
Recycled ICs – used ICs represented as new – are a well recognized problem in today’s global component supply chain.
A method for detecting recycled ICs.
  No hardware modification required to the existing design.
  No golden samples required.
  Can identify devices used as little as six months.

## Slide 4: Aging and its effect on IDDQ
Negative Bias Temperature Instability (NBTI) is a major aging phenomenon, which occurs in PMOS devices.
Aging in NMOS devices is significantly lower.
Due to NBTI aging PMOS threshold voltage (vth) increases.
Increased vth increases leakage resistance (RP) of a PMOS device.

## Slide 5: IDDQ Modeling in CMOS Gates
Pattern AB=11 controls age dependent IDDQ of NAND gate.

## Slide 6: IDDQ Modeling in CMOS Gates - Cont.
Inputs |  | NAND |  | NOR |  | Inverter | 
A | B | IDDQ(A) | IDDQ(U) | IDDQ(A) | IDDQ(U) | IDDQ(A) | IDDQ(U)
0 | 0 | V/2RN | IN/2 | 2V/RN | 2IN | V/RN | IN
0 | 1 | V/RN | IN | V/RP | IP | NA | NA
1 | 0 | V/RN | IN | V/RP | IP | NA | NA
1 | 1 | 2V/RP | 2IP | V/2RP | IP/2 | V/RP | IP
IDDQ(A) = Absolute IDDQ current
IDDQ(U) = IDDQ current in terms of IN and IP where IN= V/RN and IP= V/RP

## Slide 7: Non-uniform Aging of gates on a Chip
PMOS devices of gates 4 and 5 (red) age faster and those of gates 6 and 7 (blue) age slower.
Pattern T1 controls IDDQ through fast aged gates and pattern T2 controls IDDQ though slow aged gates.

## Slide 8: Process variations
Process variation causes variations in threshold voltages of MOS devices.
Random variation affects vth of MOSFETs within a chip.
Systematic variation affects vth of MOSFETs on different chips.
These variations create inaccuracy in IDDQ-based aging decision.

## Slide 9: Process Variation Resilience
IDDQ for T1 and T2 :
k1 and k2 = Number of PMOS OFF when T1 and T2 applied
r1 and r2 = Number of NMOS OFF when T1 and T2 applied
The difference, I2 – I1:

## Slide 10: Process Variation Resilience – Cont.
ΔIP is contributed by PMOS and ΔIN is contributed by NMOS
Select T1 and T2 such that r1 ≈ r2 to eliminate process variation in NMOS devices.
Effect of random process variation is nullified when #gates is large.

## Slide 11: Process Variation Resilience – Cont.
Normalization of ΔIDDQ removes systematic process variation.
A normalized value used for recycled IC detection:

## Slide 12: Simulation Results
ISCAS benchmarks c432, c499, c880, c1908 and c3540 simulated.
Synthesis is done in Synopsys design compiler and HSPICE netlist created using IC validator.
Synopsys VCS provided controllability analysis
CMOS 32nm Predictive Technology Model (PTM)
Aging simulations at 25 degree Celsius and 1V

## Slide 13: IDDQ for new Circuits
Benchmark | Netlist-1 ΔI % | Netlist-2 ΔI % | Netlist-3 ΔI % | Netlist-4 ΔI % | ΔIT % max(ΔI %)
c432 | 3.65 | 3.65 | 3.5 | 3.80 | 3.80
c499 | 1.36 | 1.54 | 1.62 | 1.39 | 1.62
c880 | 4.26 | 4.46 | 4.65 | 4.58 | 4.65
c1908 | 2.14 | 2.38 | 2.76 | 2.94 | 2.94
c3540 | 3.74 | 3.85 | 4.19 | 3.88 | 4.19

## Slide 14: IDDQ for used circuits
Usage | Benchmark | Netlist-1 ΔI % | Netlist-2 ΔI % | Netlist-3 ΔI % | Netlist-4 ΔI % | min (ΔI) %
6 months | c432 | 5.16 | 5.09 | 4.97 | 5.23 | 4.97
 | c499 | 3.26 | 3.51 | 3.56 | 3.31 | 3.26
 | c880 | 5.26 | 5.45 | 5.65 | 5.54 | 5.26
 | c1908 | 4.35 | 4.58 | 4.71 | 4.88 | 4.35
 | c3540 | 4.86 | 4.91 | 5.17 | 5.00 | 4.86
12 months | c432 | 5.37 | 5.33 | 5.19 | 5.48 | 5.19
 | c499 | 3.59 | 3.80 | 3.88 | 3.59 | 3.59
 | c880 | 5.44 | 5.62 | 5.81 | 5.76 | 5.44
 | c1908 | 4.58 | 4.83 | 5.02 | 5.09 | 4.58
 | c3540 | 5.03 | 5.07 | 5.32 | 5.14 | 5.03

## Slide 15: Conclusion
Two pattern test can effectively identify recycled ICs used for as little as six months
The test requires no additional design change in the device
Test can be applied by any available automatic test equipment (ATE)
Finding optimal two pattern can be investigated further.

## Slide 16
Thank you!
Questions?