## Slide 1: DPPM for Analog and RF Circuits
Vishwani D. Agrawal
Auburn University, Auburn, AL 36849, USA
vagrawal@eng.auburn.edu
Suraj Sindia
Intel Corporation, Hillsboro, OR 97124, USA
szs0063@auburn.edu
32nd IEEE VLSI Test Symposium
Napa, California
April 14, 2014

## Slide 2: Problem Statement
Given:
  A set of complete specification-based tests for an analog or RF circuit, and
  An acceptable defect level (DL),
Find the smallest set of tests that should be used.

## Slide 3: A Bipartite Graph
T2
T3
T1
T4
S1
S2
S3
S4
p11
p22
p33
p44
p34
p42
p12
p21
p13
Tests
Specifications

## Slide 4: Operational Amplifier: TI LM741
Notes: In the figure the Y axis shows the minimum test time for the supply voltage on the X axis. The curve N x Tstructure shows test time at each voltage if the circuit is run at its functional speed. The curve 𝑁×𝐸𝑀𝐴𝑋𝑡𝑒𝑠𝑡/𝑃𝑀𝐴𝑋𝑓𝑢𝑛𝑐 shows test time using the test clock period .
As voltage reduces test power decreases, hence test frequency can be increased. On the right side, the test time is limited only by the test power, hence it is power constrained. However as voltage reduces beyon a certain value the test time is limited by the structural delay, hence structure constrained. Optimum voltage Vsynch is the point at which the cycle period start to become structurally constrained

## Slide 5: Test Minimization
DL PPM | ILP solution |  |  |  |  |  |  | Tests selected | Test size reduction
 | x1 | x2 | x3 | x4 | x5 | x6 | x7 |  | 
0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 7 | 0%
1 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 6 | 14%
100 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 6 | 14%
1,000 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 5 | 29%
10,000 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 4 | 43%

## Slide 6: Conclusion
Specification tests are given.
Monte Carlo spice simulation determines probability, pij, of ith test checking for jth specification.
An integer linear program (ILP) determines the defect level for any number of tests.
References:
  S. Sindia and V. D. Agrawal, “Specification Test Minimization for Given Defect Level,” Proc. 15th IEEE Latin-American Test Workshop, Fortaleza, Brazil, March 13, 2014.
  A detailed paper submitted to ITC 2014.