## Slide 1: Failure Evasion: Statistically Solving the NP Complete Problem of Testing Difficult-to-Detect Faults
Murali Venkatasubramanian Vishwani D. Agrawal
Ph.D. Candidate James J. Danaher Professor
Department of Electrical and Computer Engineering
Auburn University

## Slide 2: Outline
Definition of problem statement
Research summary of ATPG
Overview of proposed algorithm
Analysis of results
Elaboration of Future work
Conclusion

## Slide 3: Purpose
Given a stuck-at fault, find a test.
  Specifically, finding tests for hard to detect stuck-at faults.
Rephrase the VLSI Testing problem as a database search problem.
  Need for research to harness potential of database search.
Application of “Mahalanobis distance” metric towards test generation.
  Improve the bottleneck of finding the unique tests.

## Slide 4: Background

## Slide 5: Overview of ATPG Research
Fault detection problem is NP complete [Ibarra and Sahni, 1975; Fujiwara and Toida, 1982; Seroussi and Bshouty, 1988].
Worst-case computational complexity is an exponential function in circuit size.
  Nature of NP problem.
Generation of test vectors a classic VLSI problem.
  Tackled by numerous algorithms.

## Slide 6: ATPG Research (contd..)
Deterministic algorithms derived from structural description of circuits.
  D Algorithm [Roth, 1966].
  PODEM [Goel, 1981].
  FAN [Fujiwara and Shimono, 1983].
  And various others...
Test sets derived from functional description of circuits [Akers, 1972; Reddy, 1973].
Use of weighted random test generators.
  Heuristics like input switching activity and weight assignment [Schnurmann et al., 1972].
  Skewing input probabiltiy to attain maximum output entropy [Agrawal, 1981].
Adaptive test generation
  Genetic algorithms [Saab et al. 1992; O’Dare and Arslan, 1994; Corno et al., 1996].
  Anti-random test generators [Malaiya, 1995].
  Using spectral properties of successful tests to generate new test vectors [Yogi and Agrawal, 2006].

## Slide 7: Conceptual Outline
Current algorithms hit a bottleneck when testing hard-to-detect faults.
  Because we are testing hard-to-detect faults, we generally have many trial vectors that do not work.
All known algorithms use previous successes to generate new test vectors.
But, test generation has lots more failed attempts than successful ones.
  Current algorithms ignoring a lot of potentially valuable information.
How to design a new test algorithm which utilizes the information from failed attempts effectively?

## Slide 8
Our Methodology

## Slide 9: Algorithm Genesis
How does one prosper in life??
  Repeating steps from previous successes.
    As people say, do not change a successful formula.
  Learning from past failures and avoiding them.
Main conjecture is to avoid all vectors with properties similar to known failed test vectors.
  The direction of search gets skewed towards the correct test vector.
Use an innovative statistical method which computes “Mahalanobis distance” [Mahalanobis, 1936].
  Calculates how many standard deviations away is a point P from a distribution D.
Proposed algorithm utilizes both successful and failed test vectors.
  Moving away from failed vectors will lead to solution in quicker iterations.

## Slide 10: Mahalanobis Distance
  x = vector of data
  μ = Vector of mean values of independent variables
  S-1 = Inverse covariance matrix
Measures how similar or dissimilar are a set of conditions to a sample set.
  Used to find outliers in a dataset.
Properties:
  Elliptical pattern of distribution of variables.
  Variations in each direction are different.
  Accounts for covariance between variables.

## Slide 11: Graphical Illustration
If X and Y are uncorrelated, there would be a circular or spherical distribution.
  Euclidian distribution.
Correlations between X and Y causes an elliptical pattern to emerge.
  Variables with alike properties are at same Mahalanobis distance.

## Slide 12: Applications of Mahalanobis Distance
Used for classifying faults in analog testing [Long et al., 2012; Han et al., 2013].
Also used for multi-dimensional Iddq testing [Nakamura and Tanaka, 2010].
However, Mahalanobis distance has never been used to derive tests for stuck-at faults.
Proposed algorithm classifies test vectors in the vector space into three categories:
  Activation vectors
  Propagation vectors
  Failed vectors

## Slide 13: Proposed Implementation

## Slide 14: Algorithm: A Working Example
Initial probability values for random search
Initial Probability values for proposed algorithm

## Slide 15: After 5 Iterations..
Probability values for random search
Probability values for proposed algorithm

## Slide 16: After 10 Iterations..
Probability values for random search
Probability values for proposed algorithm

## Slide 17: After 15 Iterations..
Probability values for random search
Probability values for proposed algorithm

## Slide 18: Results

## Slide 19: Presentation of Results
A n primary input (PI) circuit can have N = 2n possible test vector combinations.
  A test can be found from among these N vectors.
Hence, VLSI testing problem can rephrased as an unsorted database search problem of N elements.
  In our best interest to implement one of the fastest unsorted database search algorithms to find test vectors.
Grover's quantum search algorithm [Grover, 1996] can search through an unsorted database in sub-linear time.
  Deemed the fastest way to search an unsorted database theoretically [Bennett el al., 1997].
Growing interest in quantum computing leading to revisiting of NP hard problems.
  Find optimal solutions in linear time.

## Slide 20: Presentation (contd..)
Simulated various benchmark circuits using our proposed algorithm.
  Focused on stuck-at faults with only 1-2 tests.
  Derived average iteration time for each case.
Compared results with random search and Grover’s quantum database search.
Use of Grover’s algorithm a yardstick to show efficiency of our algorithm.

## Slide 21: Test Circuit Analysis
The given circuit has a stuck-at-1 fault on a line.
Fault site has:
  One successful test.
  Eight activation vectors.
  Four propagation vectors.
Performed 100 trial runs on the faulty circuit.

## Slide 22: Test Circuit Results (#PIs = 6)
Iterative search duration distribution to search for the correct test vector.

## Slide 23: Comparing Average Iterations
Circuit | Search space size, N = 2#PI | Grover’s quantum search (√N) | Proposed algorithm | Random search (~ N/2)
Decoder (#PI = 8) | 256 | 16 | 24 | 133
Ones Counter (#PI = 9) | 512 | 23 | 76 | 288
int2float (#PI = 11) | 2048 | 46 | 180 | 1010
Parity logic (#PI = 16) | 65536 | 256 | 847 | 32751
mux logic (#PI = 21) | 2097152 | 1448 | 6842 | 1048573

## Slide 24: Search Algorithm Complexity

## Slide 25: Conclusion
Showed evolution of ATPG algorithms over the past 50 years.
Redefined the testing problem as a database search problem.
Used “Mahalanobis distance” to formalize algorithm.
Results demonstrate proof of concept of our algorithm.
Comparison with quantum search shows algorithm is on same order of search time or iteration time.

## Slide 26
Success consists of going from failure to failure without loss of enthusiasm.
- Sir Winston Churchill

## Slide 27: References
[1] O. H. Ibarra and S. Sahni, “Polynomially complete fault detection problems,” IEEE Trans. Computers, vol. 24, no. 3, pp. 242–249, 1975.
[2] H. Fujiwara and S. Toida, “The complexity of fault detection problems for combinational logic circuits,” IEEE Transactions on Computers, vol. 100, no. 6, pp. 555–560, 1982.
[3] G. Seroussi and N. H. Bshouty, “Vector sets for exhaustive testing of logic circuits,” IEEE Transactions on Information Theory, vol. 34, no. 3, pp. 513–522, 1988.
[4] J. P. Roth, “Diagnosis of automata failures: A calculus and a method,” IBM Journal of Research and Development, vol. 10, no. 4, pp. 278–291, 1966.
[5] P. Goel, “An implicit enumeration algorithm to generate tests for combinational logic circuits,” IEEE Transactions on Computers, vol. 100, no. 3, pp. 215–222, 1981.
[6] H. Fujiwara and T. Shimono, “On the acceleration of test generation algorithms,” IEEE Transactions on Computers, vol. 100, no. 12, pp. 1137–1144, 1983.
[7] S. B. Akers, “Universal test sets for logic networks,” IEEE Conference Record of 13th Annual Symposium on Switching and Automata Theory, 1972, pp. 177–184.
[8] S. M. Reddy, “Complete test sets for logic functions,” IEEE Transactions on Computers, vol. 100, no. 11, pp. 1016–1020, 1973.

## Slide 28: References (contd..)
[9] H. D. Schnurmann, E. Lindbloom, and R. G. Carpenter, “The weighted random test-pattern generator,” IEEE Transactions on Computers, vol. 100, no. 7, pp. 695–700, 1975.
[10] V. D. Agrawal, “An information theoretic approach to digital fault testing,” IEEE Transactions on Computers, vol. 30, no. 8, pp. 582–587, 1981.
[11] D. G. Saab, Y. G. Saab, and J. A. Abraham, “CRIS: A Test Cultivation Program for Sequential VLSI Circuits,” in Proc. IEEE/ACM International Conference on Computer-Aided Design, 1992, pp. 216–219. [12] M. O’Dare and T. Arslan, “Generating Test Patterns for VLSI Circuits Using a Genetic Algorithm,” Electronics Letters, vol. 30, no. 10, pp. 778–779, 1994. [13] F. Corno, P. Prinetto, M. Rebaudengo, and M. S. Reorda, “GATTO: A Genetic Algorithm for Automatic Test Pattern Generation for Large Synchronous Sequential Circuits,” IEEE Transactions on Computer-Aided Design of Integrated Circuits and Systems, vol. 15, no. 8, pp. 991–1000, 1996. [14] Y. K. Malaiya, “Antirandom Testing: Getting The Most Out of Black-box Testing,” in Proc. 6th IEEE International Symp. Software Reliability Engineering, 1995, pp. 86–95. [15] N. Yogi and V. D. Agrawal, “Spectral RTL test generation for gate-level stuck-at faults,” Proc. 15th IEEE Asian Test Symposium, 2006, pp. 83–88.

## Slide 29: References (contd..)
[16] S. T. Chakradhar, V. D. Agrawal, and S. G. Rothweiler, “A Transitive Closure Algorithm for Test Generation,” IEEE Transactions on Computer-Aided Design of Integrated Circuits and Systems, vol. 12, no. 7, pp. 1015–1028, 1993.
[17] P. Girard, L. Guiller, C. Landrault, and S. Pravossoudovitch, “A Test Vector Ordering Technique for Switching Activity Reduction During Test Operation,” in Proc. 9th IEEE Great Lakes Symp. VLSI, 1999, pp. 24–27.
[18] P. Venkataramani, S. Sindia, and V. D. Agrawal, “A Test Time Theorem and its Applications,” Journal of Electronic Testing: Theory and Applications, vol. 30, no. 2, pp. 229–236, 2014. [19] V. Sheshadri, V. D. Agrawal, and P. Agrawal, “Power-aware SoC Test Optimization Through Dynamic Voltage and Frequency Scaling,” in Proc. IFIP/IEEE 21st International Conference on Very Large Scale Integration (VLSI-SoC), 2013, pp. 102–107. [20] R. Drechsler, S. Eggersgluβ, G. Fey, A. Glowatz, F. Hapke, J. Schloeffel, and D. Tille, “On Acceleration of SAT-Based ATPG for Industrial Designs,” IEEE Transactions on ComputerAided Design of Integrated Circuits and Systems, vol. 27, no. 7, pp. 1329–1333, July 2008. [21] S. Kirkpatrick, C. D. Gelatt, M. P. Vecchi, et al., “Optimization by Simulated Annealing,” Science, vol. 220, no. 4598, pp. 671– 680, 1983.

## Slide 30: References (contd..)
[22] P. W. Shor, “Polynomial-time Algorithms For Prime Factorization and Discrete Logarithms on a Quantum Computer,” SIAM Journal on Computing, vol. 26, no. 5, pp. 1484–1509, 1997. [23] L. K. Grover, “A Fast Quantum Mechanical Algorithm for Database Search,” in Proc. 28th Annual ACM Symposium on Theory of Computing, 1996, pp. 212–219.
[24] M. A. Nielsen and I. L. Chuang, Quantum Computation and Quantum Information. New York: Cambridge University Press, 10th edition, 2011. [25]P. C. Mahalanobis, “On the Generalized Distance in Statistics,” Proceedings of the National Institute of Sciences (Calcutta), vol. 2, pp. 49–55, 1936.
[25] M. Venkatasubramanian and V. D. Agrawal, “Quest for a Quantum Search Algorithm for Testing Stuck-at Faults in Digital Circuits,” in Proc. 29th IEEE International Symp. Defect and Fault Tolerance in VLSI and Nanotechnology Systems, pp. 127–132, Oct. 2015.
[26] M. Venkatasubramanian and V. Agrawal, “Database Search and ATPG – Interdisciplinary Domains and Algorithms,” in 29th IEEE International Conference on VLSI Design, Jan. 2016.
[27] M. Venkatasubramanian and V. Agrawal, “A New Test Vector Search Algorithm for a Single Stuck-at Fault using Probabilistic Correlation,” in IEEE 23rd North Atlantic Test Workshop (NATW), pp. 57 – 60, May 2014.