## Slide 1: What has been done -- studies of machine intelligence in test
IEEE VLSI Test Symposium’ 21
Virtual Event
Soham Roy
Department of Electrical and Computer Engineering
Auburn University, Auburn, Alabama, USA
Notes: Hello everyone and welcome to my talk titled, “What has been done --- studies of machine intelligence in test”. My name is Soham Roy, and I am a PhD candidate of Electrical and Computer Engineering department at Auburn University in Auburn, Alabama, USA under the supervision of Prof. Spencer Millican and Prof. Vishwani Agrawal.

## Slide 2: Outline
Analog and RF Testing
Digital Testing
Memory Testing and Repair
Hardware Security and Emerging Technologies
Conclusions
Notes: Today, I am going to cover various areas in IC testing where Machine intelligence has been a proven technique. Areas like analog and RF, Digital, Memory and Repair, Hardware security and emerging technologies. Finally, I will conclude the talk.

## Slide 3: Analog and RF Testing
Hardware implementation of analog ANN BIST
Estimation of parametric test metrics using machine learning algorithms
An adaptive RF front-end design
Notes: In analog and RF testing, I am going to outline first two topics mentioned here. I will talk about them covering two major aspects: what has been done and what has been achieved.

## Slide 4: Analog and RF Testing
Fig 1: Built-in self-test (BIST) of a radio frequency (RF) device under test (DUT)
Hardware implementation of analog ANN BIST
Notes: A machine learning approach used on-chip artificial neural networks (ANNs) on RF devices under test (DUT) to analyze sensor measurements and indicate PASS/FAIL
The ANN compacts off-chip extraction and post-processing measurements to a single-bit output, making a standalone built-in self-test (BIST) shown in Fig. 1.
The ANN training is performed off-line by measuring patterns of fabricated chips and mapping them to one-bit outputs (indicating PASS/FAIL).

## Slide 5: Analog and RF Testing
Hardware implementation of analog ANN BIST (Experimental setup and observation)
Experiments on low noise amplifiers (LNAs) circuits with two RF amplitude detectors produced DC signals
DC signals were fed to an analog ANN classifier.
Additional experiments replaced the hardware classifier with a software classifier.
The software classifier training error outperforms the hardware classifier, but the validation error is comparable in both cases.
However, for more neurons in the hidden layer, the hardware classifier’s validation error is substantial compared to the software classifier
Notes: Experiments on low noise amplifiers (LNAs) circuits with two RF amplitude detectors placed at the inputs and outputs of LNA produced DC signals comparable to RF power seen at the detector inputs. These DC signals were fed to an analog ANN classifier. This classifier was trained in different configurations with 2, 4, and 8 neurons in a single hidden layer and repeated five times to average out randomness of the training algorithm’s stochastic nature. Additional experiments replaced the hardware classifier with a software classifier using the Matlab Neural Network toolbox trained by a resilient backpropagation algorithm. It was observed that the software classifier training error outperforms the hardware classifier, but the validation error is comparable in both cases. However, for more neurons in the hidden layer, the hardware classifier’s validation error is substantial compared to the software classifier

## Slide 6: Analog and RF Testing
Fig. 2: Simulation flow for parametric test metrics estimation
Estimation of parametric test metrics using machine learning algorithms
Notes: There is need to replace standard specification-based testing to improve fault coverage of analog ICs. Test engineers also developed an alternate procedure to estimate analog parameters to reduce test costs, yield loss, and test escapes. These test metrics should be accurately estimated at the simulation level ahead of silicon manufacturing to minimize the test development time and cost. A proposed test strategy that includes machine learning algorithms, as shown in Fig. 2:
A trained ANN is used to classify circuits whose parametric metrics are estimated closer to the specification, known as “extreme” instances.
Circuit netlists are synthesized using the available process design kit (PDK) from the IP vendors and simultaneously train the ANN with the process metrics to classify the “extreme” circuits.
These “extreme” circuits define a statistical blockade.
The ANN is re-trained with the simulated circuit netlists so that the class of the “extreme” circuits is closer to the specification and the process is repeated.
The re-training of ANN progressively increases the probability of generating correct “extreme” instances.

## Slide 7: Analog and RF Testing
Estimation of parametric test metrics using machine learning algorithms (Contributions)
The algorithm in this technique outputs a more refined parametric fault model compared to the generalized technique
This method is applied to a low noise amplifier and data converters.
Notes: The contributions of this techniques are listed. The algorithm outputs a more refined parametric fault model compared to the generalized technique specific fault model and helps estimate fault coverage and yield loss more precisely. This method is applied to a low noise amplifier (LNA) and shown to reduce simulation run-time by eliminating the redundant specification tests and replacing them with the proposed ML-based parametric measurements. This technique is applied to data-converters, but not yet explored for other analog ICs whose simulation run-time is high, such as phase-locked-loop (PLL).

## Slide 8: Digital Testing
Scan Chain Diagnosis
Classifying Fault Models
Board testing
Built-in Self-Test
Wafer Testing
Volume Diagnosis
Test Compression
Testability Measures
Timing Analysis
ATPG
Notes: In digital testing, I am going to outline first two topics mentioned here: Wafer testing and ATPG

## Slide 9: Digital Testing
Wafer Testing
Fig. 3: ML-based die inking process
Notes: Generally, logic defects occur in clusters on the wafers, thus clustering algorithms can identify defect concentrations across the wafers. Such algorithms works in two steps: 1) cluster containment and 2) learning. The algorithm first identifies the wafers with cluster patterns and screens out passing dies having no defects inside these clusters, thereby marking them for high risk of failure. This process repeats based on cluster size, wafer location, and failure composition across multiple wafers to avoid additional yield loss and failure analysis. The mentioned technique proposed a similar cluster-detecting ML using support vectors machines (SVMs). The SVM’s kernel is a radial basis function, generally a Gaussian function, for distance computation to identify the die from the defective clusters during classification, as shown in Fig. 3.

## Slide 10: Digital Testing
Fig. 4: Schneider circuit
Notes: The application of machine learning is related to the heuristic part of ATPG algorithms. All algorithms have been using different heuristics to speed-up the ATPG process. These heuristics can be: the distance between the primary inputs and and outputs to signal sites, testability measures, voting of digital logic values on fanout stem depending on its branches, and other learning techniques using implication graphs, etc. ANN based machine learning [119] can achieve the following goal: learning from ATPG with any or no fixed set of rules to guide tracing backward, develop an intelligent system to use circuit information (in this case it is distance and COP) during ATPG. The measure of success will be fewer backtracks compared to conventional heuristics.
In 1967 paper, Roth et al. used Schneider circuit of Figure 8 as an example to demonstrate the exhaustiveness of D-algorithm; it would always find a test if one existed. The fault line 6 stuckat-0 has a test 0000, which can be found if paths through lines 9 and 10 are simultaneously sensitized to output 12. Some of the older single path sensitization algorithms would fail to find this test.
We use Schneider circuit to show a different benefit of ML, which is to reduce backtracks. Three PODEM based ATPG programs were used to find the test for line 6 stuckat-0 fault. These programs are described in a recent paper on the use of ML in ATPG. The first program, PODEM(D), is a straightforward implementation of PODEM with backtrace heuristic of logic distance. The second program, PODEM(C), is similar but backtrace is guided by COP testability measure. The third program, PODEM(M), has an ANN guiding the backtrace. The ANN was trained from histories of successful and failed backtraces when conventional PODEM was applied to typical logic circuits, as well as logic distance and COP data of circuit nodes. For the target fault in Figure 4, all three programs found the test, which is not surprising because PODEM is an exhaustive algorithm. However, PODEM(D) and PODEM(C) each had to backtrack once, while PODEM(M) required no backtrack. Also, when the ANN was trained with just one feature (either distance or COP), it did require one backtrack. For complex circuits, we may not be so lucky to have zero backtrack but the experience shows that machine intelligence, by combining multiple heuristics, produces tests with fewer backtracks [119]

## Slide 11: Supervised Learning-Based ATPG: Machine intelligence applied
Random backtracing ATPG
Training Database
c6288, b05, c3540; 100 hardest faults each
ANN Training
Remaining benchmarks
COP-guided backtracing
Distance-guided backtracing
ANN-guided backtracing
ATPG
CPU time, backtracks, & backtraces
S. Roy, S. K. Millican, and V. D. Agrawal, “Machine Intelligence for Efficient Test Pattern Generation,” in Proceedings of the IEEE International Test Conference, Washington D.C, Nov. 2020.
Digital Testing Recent Study on Machine Intelligence-Based ATPG
Notes: For an accurate evaluation of machine intelligence guided backtracing, we used ISCAS’85 and ITC’99 benchmarks for training and evaluation. For training, we selected benchmarks c6288, b05, and c3540, and for these benchmarks we run ATPG on what the COP algorithm predicts to be the 100 hardest to detect faults. This generates our training database, which we then feed into an open-source ANN training program with various hyperparameters to minimize the ANN’s error.
After this training, we use the ANN in the PODEM algorithm to generate tests for all faults in the remaining benchmark circuits. While doing so, we measured the CPU time, number of backtraces, and number of backtracks performed during ATPG. We repeat this process using conventional backtracing heuristics to guide backtracing, that is, using COP and circuit depths to inputs. We should note that since we use original software, we can ensure the backtrace subroutines are the only differences between these methods, hence they are the only source of differences in performance.

## Slide 12: Supervised Learning-Based ATPG Experimental Results - ATPG for all faults (backtracks)
Chart: Benchmark Circuits
| c17 | b02 | b06 | b01 | b09 | b03 | c499 | b10 | b08 | c432 | b12 | b13 | c880 | c1355 | b04 | b07 | c2670 | b11 | c1908 | c7552 | c5315 | c3540 | b05 | c6288
Dist. | 0 | 50 | 0 | 0 | 800 | 540 | 20.3439 | 42.4051 | 53.7313 | -41.0063 | 211.6302 | 11.5677 | 160 | 177.1795 | 35.0831 | 234.7413 | -34.237 | 7350.1129 | 18.266 | -23.486 | 70.8031 | -29.6542 | 199.413 | 29.8831
COP | 0 | 0 | 0 | 0 | 13016.6667 | 320 | 2832.7553 | 43.038 | 1891.0448 | -30.1416 | 156.1919 | -8.5236 | -20 | 72.4064 | 201.5054 | 70.2281 | -40.6438 | 18.6606 | 135.9448 | -15.5414 | 168.0325 | -17.2439 | 37.3765 | 44.2007
S. Roy, S. K. Millican, and V. D. Agrawal, “Machine Intelligence for Efficient Test Pattern Generation,” in Proceedings of the IEEE International Test Conference, Washington D.C, Nov. 2020.
Notes: Since results depend heavily on benchmark sizes, we chose to normalize plots with respect to ANN-guided backtracing results, which we believe more accurately reflect the goal of ATPG research, that is, to reduce ATPG runtime by a factor as opposed to by a constant. Therefore, positive plots in these figures reflect results favorable to the machine intelligence.
The results on decreasing backtracks show promising results. We see that for most benchmarks, using the ANN in lieu of conventional heuristics decreases the number of backtracks, often considerably so. This is impressive given the ANN’s rudimentary inputs, that is, only a single line’s worth of information and the ANN’s inputs are the same as the heuristics compared against. This encourages us to explore more complex machine intelligence structures that can process more information. But we acknowledge the outliers, and these outliers raise several questions: are they caused by poor training or selection of training data sources; or much more information be analyzed to perform better in these or similar benchmarks? This gives us several future research directions.

## Slide 13: Supervised Learning-Based ATPG Experimental Results - ATPG for all faults (CPU Time)
Chart: Benchmark Circuits
| c17 | b02 | b06 | b01 | b09 | b03 | c499 | b10 | b08 | c432 | b12 | b13 | c880 | c1355 | b04 | b07 | c2670 | b11 | c1908 | c7552 | c5315 | c3540 | b05 | c6288
Dist. | -22.2222 | -10.4167 | -8.7248 | -12.2302 | -12.2633 | -25.0333 | -3.9876 | -9.7674 | -3.1983 | -46.3966 | 11.333 | -5.4068 | 0.80423 | 52.8258 | 16.3446 | 104.8271 | -42.7312 | 1926.1807 | -8.5073 | -23.2815 | -14.2664 | -26.4829 | 58.5106 | -15.9462
COP | 55.5556 | 308.3333 | -10.7383 | -18.705 | 0.81154 | 18.1092 | 1901.0962 | -9.8256 | 217.2175 | -49.1791 | 11.2304 | -26.5285 | -5.5873 | 47.9855 | 138.7378 | 41.9044 | -51.2004 | -21.0385 | 32.0036 | -21.9157 | 5.7358 | -18.8631 | -11.7865 | -19.3382
S. Roy, S. K. Millican, and V. D. Agrawal, “Machine Intelligence for Efficient Test Pattern Generation,” in Proceedings of the IEEE International Test Conference, Washington D.C, Nov. 2020.
Notes: When we look at the CPU time, I see some familiar trends mirrored from the backtrack results: these makes sense, since we are motivated to avoid backtracks to reduce CPU time. However, we see the magnitude of favorable results diminishes, and some benchmarks that had fewer backtracks with ANN-based backtracing have increased CPU time.
We find that this is due to the matrix multiplication needed to evaluate the ANN, which adds overhead compared to simpler backtracing subroutines. However, this raises a question: at what point is the backtrack-reducing potential of machine intelligence outweighed by its computational overhead? As an extreme example, an ANN may be “perfect” and avoid all backtracks for every circuit, but if this comes at the expense of days of calculation per backtrace, its utility is mute. Again, this creates an interesting avenue for future research.

## Slide 14: Unsupervised Learning-Based ATPG: PCA applied
Features: Distance,
COP,
SCOAP
PCA
COP-guided backtracing
Distance-guided backtracing
PCA-guided backtracing
ATPG
CPU time, backtracks, & backtraces
Database containing circuit line’s information based on features
SCOAP-guided backtracing
Digital Testing Recent Study on Machine Intelligence-Based ATPG
Notes: The motivation behind this study is the exponential complexity of automatic test pattern generation (ATPG) that uses heuristics in making choices during test generation, but in practice no single heuristic fits all situations.
In such cases, unsupervised learning can combine practically any number of known heuristics, such as input-output distance (logic depths), gate type, fanout information, and testability measures like COP and SCOAP through principal component analysis, and the most prominent principal components can guide ATPG choices.
I apply this novel scheme to benchmark circuits by first performing principal component analysis to combine three heuristics such as distance, COP, and SCOAP and store it in a database. Then, the most prominent PCs out of the database guide backtrace directions in the PODEM ATPG program. Here, we are trying to compare four different heuristic guided PODEM i.e., Distance, COP, SCOAP and principal component.

## Slide 15: Unsupervised Learning-Based ATPG Experimental Results - ATPG for all faults (backtracks and CPU Time)
Notes: Experiments used testable and redundant faults to prove the efficacy of guidance provided by PCA to PODEM ATPG. Figure on the left (circuits are arranged by logic depths) and the figure
on the right show relevant findings on ATPG CPU time (ms) and the number of backtracks with respect to distance, COP, SCOAP, and PCA (P0 and P1 guidance).
This experiment demonstrates how combining multiple heuristics into a linear combination through PCA can achieve better ATPG CPU time and fewer backtracks compared to conventional
single heuristics.

## Slide 16: Memory Testing and Repair
Machine learning based BISR DRAM test and repair
Machine learning based software-assisted in-chip self-test flash memory test and repair
Improving SRAM yield using statistical blockade
Notes: In analog and RF testing, I am going to outline first two topics mentioned here.

## Slide 17: Memory Testing and Repair
Machine learning based BISR DRAM test and repair
Fig. 5: Neural Network for Memory Repair
Notes: Memory repair was first introduced in 64 Kbit DRAM to improve the chip yield using redundant rows and columns, but increasing memory sizes makes the search space becomes too large and the types of faults become complicated.
Therefore, conventional repair algorithms, both greedy and exhaustive, became ineffective. The memory repair problem was then formulated as NP-complete, and heuristic algorithms were introduced, that included branch and bound, approximation, best-first search, and others. These algorithms have worst-case complexities that are nearly exponential and they are not easily implementable in BISR.
This technique focuses on a self-repair scheme using BISR to repair memory subarrays by reconfiguring the redundant rows/columns. As “Repair Most (RM)” is simple and easily implementable hardware, the performance of ANN-based memory repair algorithm was compared against RM.
Conventional repair algorithms run slow on digital computers, whereas neural network (as shown in the slide)’s collective computational property provides a faster solution. A gradient descent algorithm can be 2- to-4 times better than conventional “RM” algorithms in repair schemes as gradient descent minimizes the network’s cost function in the locality of the starting energy value.
Both hill-climbing and gradient descent algorithms using NN take minimal area overhead of approximately 3%. It is also reported that the chips yield increased from 10% to 100% by improved repair. Besides, the NN hardware is more fault-tolerant and robust than conventional logic circuits, and therefore is a best candidate for the self-repair circuit.

## Slide 18: Memory Testing and Repair
Machine learning based software-assisted in-chip self-test flash memory test and repair
Fig. 6: Repair algorithm analysis flow
Notes: Redundant component analysis can be done on-line in software-assisted in-chip self-test (SIST), but a major bottleneck is reconfiguring the redundant components efficiently (i.e., quickly and accurately).
This ML-based technique works in following steps: 1) In the development phase, bitmaps are collected for selected devices that compose training/test datasets, and 2) During production, training features are extracted using the coloring algorithm and the discarded devices are labeled as false failures.
3) A detailed analysis is done on the extracted training features and the results are fed back to the color algorithm designers. 4) Supervised and unsupervised training techniques are deployed to assess the false fails; whether or not they are correctly discriminated against in training features.
Experimental results show that the ML-based predictor of a model “decision tree,” compared to other models such as “random forest” and “feed-forward”, has a better score and minimal variance with the fastest and easy-to-implement subroutine. The overall approach is empirically proven on real time data and demonstrates that it is feasible to predict a false fail device with better accuracy.

## Slide 19: Hardware Security and Emerging Technologies
Hardware defense and attack mechanism
Testing of carbon-nanotube field-effect-transistor (CNTFET) devices, monolithic 3D (M3D) devices (specifically resistive RAMs (ReRAMs)) and many more
Notes: Recently, ML has been used for hardware defense and attack. Hardware defense techniques use ML-based algorithms against hardware Trojans and IC counterfeiting. Countermeasures with and without a golden chip are two broad categories to defend against hardware Trojans. Methods extract training data from golden chips to classify on-chip sensor data, gate-level design nodes, and traffic congestion prevails on-chip.
Nevertheless, there is ample research scope in expediting device-level testing followed by circuit and SoC-level testing using ML for some of the emerging technologies such as carbon nanotube field-effect-transistor (CNTFET) devices, monolithic 3D (M3D) devices (specifically resistive RAMs (ReRAMs)) and many more.

## Slide 20: Conclusions
Certain properties of ML may become a menace for ICs used in the defense, healthcare, space, and automotive industries:
  The accuracy in classifying test data after training the ANN is not fully convincing. 100% training and test accuracy will not fetch the correct classification of data in a real-time, which may lead to a catastrophe in critical systems.
  ML in hardware security can prove dangerous if the attackers use ML-based model to attack either good (false positive) or bad (false negative) ICs.
  Emerging technology design and their conventional testing is in a nascent stage and full of imperfections and variations, and therefore supplying products based on these technologies using ML may not provide confidence to IC suppliers and customers.
Notes: This survey highlighted key aspects of ML-based testing of analog, digital, memory, RF, and counterfeit devices, and motivates integrating ML into testing ICs of the future
ML-based testing requires either a repair or reconfiguration mechanism, which may provide redundancy in terms of area overhead, but may provide a fast prediction of anomalies in a system with robustness and resiliency.

## Slide 21
Thank You
Notes: I would like to end by thanking individually for their time and attention. Hope in the future, I can give you encouraging results based on surveys based on this study. The floor is now open for Q & A.

## Slide 22
Q&A
Notes: SR