## Slide 1: Alternative Timing in Digital Logic
George Conover

## Slide 2: Agenda
Current Design
Asynchronous Circuits
  Pros and Cons
  Design
  Microprocessors
Elastic Circuits
  GALS
  Elastic Clocks
Simulations

## Slide 3: Intel Processor Speeds
Chart: 
| 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008
Pentium CPUs (MHz) | 66 | 100 | 133 | 200 | 300 | 450 | 1130 | 2000 | 2800 | 3200 | 3460 | 3800 | 3800 | 3800
Multi Core CPUs (MHz) | 450 | 866 | 933 | 2000 | 2800 | 3200 | 3600 | 3660 | 3730 | 3330 | 3200

## Slide 4: Current Methods
Increase Throughput:
  Multi-core
  Superscalar
  Better-Than-Worst-Case
Decrease Power
  Clock Gating
  Mix Low/High Threshold Transistors
  Reduced Pipeline
  Automatic Voltage Scaling
  Clock Throttling
  Glitch Reduction

## Slide 5: Modern Microprocessor Core
AMD Opteron

## Slide 6: Asynchronous Circuits
Advantages:
  No Clock
  Low Power
  Average Case Timing
  Modular
  Resistant to Environmental Effects
  Natural Voltage Scaling
  Low Electromagnetic Interference
Disadvantages:
  Difficult to Design
  Difficult to Test
  Restricted Optimization
  Minimal CAD Support

## Slide 7: Asynchronous Circuit Design
Delay Insensitive Design
  Often not possible
Quasi-Delay Insensitive Design
  Isocronic forks – fanout assumed to arrive at all destinations simultaneously
  Wire delays neglected
Asynchronous Latches
C-Element
X | Y | Out
0 | 0 | 0
0 | 1 | Out
1 | 0 | Out
1 | 1 | 1

## Slide 8: Asynchronous Communication
Request/Acknowledge protocol
  Can send request to multiple components
  C elements used to synchronize acknowledgements
  Relies on self-timing to generate signals
4 phase
2 phase

## Slide 9: Glitch Free Design
X | Y | Z | Out
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1
Minimized SOP has a potential glitch (XY’Z -> XY’Z’)
Glitch-free design based on prime implicants

## Slide 10: Primary Benefits
Low Power
  Perfect Clock Gating
  Glitch-Free Design
  No Clock Power
  Minimized Idle Power
  Automatic Voltage Scaling
High Throughput
  Average Case Timing
  Micropipelining
V | MIPS | mW | pJ/in | MIPS/W
1.8 1.1 0.9 0.8 0.5 | 200 100 66 48 4 | 10 20.7 9.2 4.4 0.170 | 500 207 139 92 43 | 1800 4830 7200 10900 23000
Caltech Lutonium with voltage Scaling

## Slide 11: Design Difficulties
Fully delay insensitive design often impossible
Estimate delay of all gates
Requires glitch free design
Little optimization possible
Feedback loops are a core part of the design
No system level logic simulations
Micropipelines may require additional stages
Wire delays cannot be ignored in nanoscale design

## Slide 12: Testing Difficulties
Feedback loops
  Can use some tests where failure causes system to stall
Functional tests insufficient
  Only up to 60% fault coverage without Design For Test (DFT) circuitry
  Up to 50% additional area for 100% stuck-at coverage

## Slide 13: Asynchronous Microprocessors
First CAM (Caltech Asynchronous Microprocessor), 1989
Others from Sun, Tokyo Institute of Technology, ARM, etc.
All showed similar trends
  Low power
  Resistant to environmental factors
  Moderate throughput
  Low testability

## Slide 14: Asynchronous Microprocessors (cont.)
# | Processor | Word | Tech [/um] | Freq [/MHz] | Power per bit | Energy [/10-10 J] | Et2 [10-26 Js2]
1 2 | MiniMIPS (sim) MiniMIPS (fab) | 32 32 | 0.6 0.6 | 280 180 | 0.219 0.125 | 7.8 7 | 1.0 2.1
3 4 5 | R3000 (CPU) R3000A (CPU) VR3600 (CPU+FPU) | 32 32 32 | 1.2 1.0 0.8 | 25 33 40 |  |  | 
6 7 8 9 10 | R4600 21064 R4400 SH7708 P6 | 64 64 64 16/32 32 | 0.64 0.6 0.6 0.5 0.6 | 150 20 150 60 150 | 0.0719 0.469 0.234 0.018 1.8 | 4.8 23.5 15.6 3 120 | 2.1 2.1 7.0 8.3 52
Caltech MiniMIPS compared to similar CPUs
uP at 5.0V | Frequency (MHz) | MIPS | Power (mW) | MIPS/mW
AMULET 1a ARM 6 | - 20 | 12 18 | 150 150 | 0.08 0.12
uP at 3.0V | Frequency (MHz) | MIPS | Power (mW) | MIPS/mW
AMULET 2e ARM 710 ARM 710 ARM 810 | - 25 40 72 | 40 23 36 86 Drystone | 150 120 500 500 | 0.265 0.190 0.072 0.170
Amulet vs other ARM CPUs

## Slide 15: Elastic Circuits
Chart: Elasticity
| 0 | 0.3 | 0.5 | 0.9 | 1 | 0.6
Y-Axis | 0 | 0.2 | 0.2 | 0.6 | 1 | 0.4
Circuits with adaptive timing
Synchronous - inelastic
Delay insensitive - perfectly elastic

## Slide 16: GALS (Globally Asynchronous, Locally Synchronous)
Multiple clock domains
Asynchronous request/acknowledge protocol
Uses:
  System on Chip
  Multicore Processors
  Single core with multiple clock domains
Average throughput: 1 operation every 2 ns
Average throughput: 1 operation every 1 ns

## Slide 17: Elastic Clock
Vary the width of each clock cycle
Each cycle matched to instruction
Current Uses
  GALS
  Frequency Scaling
Possible Uses:
  Single Cycle CPU
  Better Than Worst Case
  Aperiodic Testing
  Pipeline Voting
  GALS with one input clock

## Slide 18: Multi-Ring Oscillator
Initial idea – did not work

## Slide 19: Multi-Ring Oscillator (cont.)

## Slide 20: Pausable Ring Oscillator
Used in GALS
2 phase communication with 2 clocks
Equivalent to asynchronous circuit with artificial worst case paths
Very close to average case throughput
Simple to implement
Not delay insensitive

## Slide 21: Counter
Counter increments on every input clock cycle
Each instruction has associated number
Can store each instruction number in reprogrammable memory
When the counter matches the number for the current instruction, the counter resets and the output is toggled
50% duty cycle, but very fast input clock
CLK_in
CLK_out
Inst.
RST

## Slide 22: Multi-Phase Clock
Length of instruction used to select next phase line
Select flip-flops updated on falling edge of the output clock
Minimum clock = input clock
2 parts: Multiphase generator and selector

## Slide 23: Stop Clock
Similar to clock throttling used in ACPI
  Throttling turns off the clock for X cycles and on for N-X cycles
Stop output clock for X cycles and reset
Output is similar to multiphase clock – Uses less area
Slower input clock that Counter
Clock Throttling

## Slide 24: CPU Test
Single Cycle Architecture
Calculate Fibonacci Sequence (0, 1, 1, 2, 3, 5, 8, 13, 21…) for 100 iterations
CPU optimized for area
  Delay optimization improved worst case path by increasing other paths – overall performance loss with elastic clock
CPU uses low power transistors
Clock circuits use high speed transistors
Initialize | A = 0, B = 1, D = 0
Add | C = A + B
Store | A -> Mem
Add immediate | A <= B + 0
Load | B <- Mem
Add immediate | D + 1
Branch to end | if D = 100
Jump to Add | 
Jump to end | End

## Slide 25: Initial Test

## Slide 26: Counter Test

## Slide 27: Multi-Phase Test

## Slide 28: Power Results
Test | # Gates | Power (avg, mW) | Power (RMS, mW) | Test Time (µs) | Total Energy (nJ)
Synchronous | 2709 | 0.58885 | 0.5832 | 3.1648 | 1.8636
CPU + Elastic Clock | - | 0.79538 | 0.79745 | - | -
Compare | 51 | 0.16337 | 0.29986 | 2.0608 | 1.9758
Multiphase | 82 | 0.1290 | 0.26299 | 2.0608 | 1.905
Test times do not include setup
Multiphase uses ½ frequency of the comparator’s input clock
Energy is calculated as total avg power * time

## Slide 29: Future Work
Create fully asynchronous cache model
Compare to pipeline implementation
Expand model to 32 bit architecture
Mix low power and high speed transistors in CPU
Improve clock control circuitry
Test various levels of optimization
Add Stop Clock method

## Slide 30: Sources for Figures and Tables
Microprocessor Reference Guide, http://www.intel.com/pressroom/kits/quickreffam.htm (3)
Chris J. Myers, "Asynchronous Circuit Design", John Wiley & Sons, Inc., 2001 (5, 9)
Alain J. Martin, Mika Nystrm and Catherine G. Wong. "Three Generations of Asynchronous Microprocessors" in IEEE Design & Test of Computers, special issue on Clockless VLSI Design, November/December 2003 (10, 14)
Marc Belleville and Cyril Condemine "Energy Autonomous Micro and Nano Systems", John Wiley & Sons, Inc., 2012 (14)
J. Carmona, J. Cotadella, M. Kishinevsky and A. Taubin, "Elastic Circuits", in IEEE Transactions on Computer Aided Design of Integrated Circuits and Systems, Vol. 28, No. 10, October 2009 (15)
"Advanced Configuration and Power Interface Specification", Copyright 2014-2015 Unified EFI, inc. (23)

## Slide 31
Questions?