## Slide 1: Security Design for IEEE P1687
Hejia Liu
Major Professor: Vishwani D. Agrawal

## Slide 2: Introduction
Part 1: Introduction of IEEE P1687 (IJTAG)
security risks in P1687
Part 2: Security design and expected unlocking time
Part 3: Discussion of a proposal and improvement in security

## Slide 3: IEEE 1149.1 (JTAG) Interface

## Slide 4: What is P1687/ IJTAG?
IEEE P1687 is a valuable tool for accessing on-chip instruments during test, diagnosis, debug and board configurations.
P1687 is a proposed IEEE Standard that has 3 components
  A flexible set of serial scan chain techniques for the instrument access architecture (called the network)
  A network description language (called instrument connectivity language, ICL)
  An instrument vector language (called procedure description language, PDL)
Notes: IEEE P1687 is a valuable tool for accessing on-chip instruments during test, diagnosis, debug and board configurations.

## Slide 5: Communication between Chips
An example of communication P1687 network between 3 chips

## Slide 6: Instruments, IPs
An IP (Intellectual property core) with a P1687 compliant interface is named instrument.
IPs: Analog, digital or mixed signal circuitry performing particular functions, such as a clock a generator, an interface to an external measurement probe, a radio tuner, an analog signal converter, a digital signal processor, etc.

## Slide 7: P1687 Network
Rst
Optional
Notes: TAP controller : All transitions between states are determined by TMS
Decoder: EXTEST, SAMPLE/PRELOAD, IDCODE, BYPASS
SIB can provide 2 accessing path. When a SIB is open, it will include the segments in the next level to the scan path. SIB is closed, exclude the next level path to scan path.

## Slide 8: FSM of TAP Controller
Notes: FSM: only the shaded states affect the ASIC core logic, the other states are intermediate steps
The pause states let the controller jog in place while the tester reloads its memory with a new set of test vectors

## Slide 9: Security Risks
Depending on the application, data may be stored on-chip, including chip ID, codes, and encryption keys.
An attacker can access a targeted instrument and obtain the secret data easily.
Notes: Open every SIBs in the network will let the attacker access targeted instrument.

## Slide 10: A Possible Break-in Procedure
Step 1: Load Instruction code in TAP
Step 2: Shift in an attempt vector
Step 3: Clock the TAP controller
Step 4: If attempt successful, access instrument
Step 5: Else, repeat from step 2

## Slide 11: Security Levels
Insecurity: Break-in time at the level of days
Weak security: Break-in time at the level of years
Strong security: Break-in time at the level of ten years
Full Security: Break-in time in the level of thousand years
Notes: The security design doesn’t need to be a silver bullet solution for protecting something absolutely critical. We aim to make the attacker pay more efforts when we increase the security level of structure.

## Slide 12: Structure of SIB (Segment Insertion Bit)
From_TDO2
To_TDI2
Select
TDI
ShiftEn
Select
To_TDO1
TCK
UpdateEn
0
1
0
1
0
1
Shift cell
Update cell
1
Select=1 ShiftEn=1
Notes: There are 2 flip flops in 1 SIB.
The label with No.1 is belonging to the current level
The label with No. 2 is for the next level
TDI is always as an input
In this image, SIB includes the input from next level

## Slide 13: Structure of SIB (Segment Insertion Bit)
From_TDO2
To_TDI2
Select
TDI
ShiftEn
Select
To_TDO1
TCK
updateEn
0
1
0
1
0
1
Shift cell
Update cell
0
Select=0 ShiftEn=1
Notes: There are 2 flip flops in 1 SIB.
The label with No.1 is belonging to the current level
The label with No. 2 is for the next level
TDI is always as an input
In this image, SIB excludes the input from next level
SIB IS CLOSE.

## Slide 14: The Structure of SIB (Segment Insertion Bit)
From_TDO2
To_TDI2
Select
TDI
ShiftEn
Select
To_TDO1
TCK
UpdateEn
0
1
0
1
0
1
Shift cell
1
Update cell
1
ShiftEn=0 UpdateEn=1
Notes: How to Change the value in UPDATE cell
Clock TAP FSM in UPDAREdr UPDATE en=1
Then the value will be delivered from the shiftCELL
1 shift in value in shift cell
2 clock TAP to updatecDR state and deliver the value from shift cell to update cell

## Slide 15: Locking-SIB With Trap
From_TDO1
To_TDI2
Select
TDI
ShiftEn
Select
To_TDO1
TCK
UpdateEn
0
1
0
1
0
1
Shift cell
Update cell
Key[0]
Key[n]
Trap feedback select signal
RST
Whether the key and trap feedback value is 1 or 0 is decided by structure
Dworak, et al.. ,”Don’t forget to lock your SIB:Hiding instrument using P1687,” ITC 2013
Notes: Select signal of mux in frond of UPDATE cell is repaced by the output of and gate
Locking part: The keys are from other cell in the scan chain.
Trap part: The current value of Update cell will also feed back to AND gate
Only KEYS and current value in update cell ARE CORRECT , the updateEN will be delivered to the multiplexer and active the path from Shift cell to update cell.

## Slide 16
Unsecure and Secure P1687 Networks

## Slide 17: Break-in Procedure
Cost(LSIB unlock attempt w/Trap)
Prob(opening SIB with key of k bits)
=
Expected Cost(LSIB unlock w/Trap)
)
Dworak, et al., “Don’t forget to lock your SIB: Hiding instrument using P1687,” ITC 2013

## Slide 18: Complex Structure Security Strategies
Break-in procedures:
Step 1: Break-in the first level
Step 2: Figure out the CARE BITs
a: Shift in attempt vectors
b: Clock TAP in UpdateDR
c: Test positive feedback
Step 3: Break-in the next level
Step 4: Repeat step 2 and step 3 until
the instrument is accessed

## Slide 19: Expected Results (f = 100MHz)
Key length K | Chain Length N | Expected time to unlock LSIB with Trap | 
 |  | Days | Years
8 | 640 | 7.79E-07 | 2.13E-09
16 | 1280 | 3.94E-04 | 1.08E-06
32 | 2560 | 5.13E+01 | 1.41E-01
48 | 5120 | 6.69E+06 | 1.83E+04
64 | 10240 | 8.76E+11 | 2.40E+09
80 | 20480 | 1.15E+17 | 3.15E+14
96 | 40960 | 1.50E+22 | 4.11E+19

## Slide 20: Features of Secure Structure
The order of magnitudes for break-in time:
An attacker uses the scan chain length as a feedback
What if we hide the length of the scan path?

## Slide 21: An Original Proposal: Use SLFSR (Secure LFSR) to Hide Scan Path Length

## Slide 22: SLFSR Example
3-stage SLFSR, R=

## Slide 23: Break-in Procedure
1 attempt=
n*

## Slide 24: Attacker’s Strategies
Condition 1: Attempt length is n*< N
Condition 2: Attempt length is n*= N
Condition 3: Attempt length n*> N

## Slide 25: Expected Results (f = 100MHz)
Condition 3:
Key length K | Chain length N | Expected time to unlock LSIB with SLFSR(days) |  | cycles | %Increase Compared to Trap without SLFSR
 |  | Days | Years |  | 
8 | 32 | 2.32E-07 | 6.36E-10 | 2.01e+05 | 395.9596
16 | 64 | 9.34E-05 | 2.56E-07 | 8.07e+07 | 377.9141
32 | 128 | 1.06E+01 | 2.90E-02 | 9.14E+12 | 365.6357
40 | 160 | 3.28e+03 | 8.98 | 2.83E+15 | 362.8169
48 | 192 | 9.85E+05 | 2.70E+03 | 8.51E+17 | 360.8592
56 | 224 | 2.90E+08 | 7.93e+05 | 2.50E+20 | 359.4203
64 | 256 | 8.37E+10 | 2.29e+08 | 7.23E+22 | 358.3181
80 | 320 | 6.74E+15 | 1.85E+13 | 5.82E+27 | 356.7407
96 | 384 | 5.24E+20 | 1.44E+18 | 4.53E+32 | 355.6663

## Slide 26: Disadvantage Compared to Structure without SLFSR
In fact, we are increasing the feedback keys alternately.
For the secure chain without LFSR,
without LFSR
=
For the secure chain in the worst case condition (condition 3) :
=
Comparing 2 equations, for large n, the efficiency ratio:

## Slide 27: Conclusion
It is useful we replace the non-functional segments with SLFSR
Security SLFSR increases attacker’s effort as breaking not only depends on the structure we build up, but also the strategies that attacker chooses.
We should be concerned about the “lucky” attacker