## Slide 1: SoC TAM Design to Minimize Test Application Time
Advisor
Dr. Vishwani D. Agrawal
Committee Members
Dr. Victor P. Nelson, Dr. Adit D. Singh
Apr 9, 2015
Master’s Project Defense
Huiting Zhang

## Slide 2
Outline
Background
IEEE 1500 Overview
Hardware Constraint of SoC testing
MILP Formulation (session-less and session-based)
Benchmark Introduction
Results
Limitation, future work, and conclusion
References
Apr 9, 2015

## Slide 3
Background
Whst is System On Chip
-More of a System not a Chip
-Large and Complex
~5-10 Million Gates
~1-64 MB memory
-Many complex subsystems
• Processor
• Graphics/communications/
• Memory
• Interface logic
• Analog
Apr 9, 2015

## Slide 4
Background
.
  -Reduced Space, higher device integration
  -High performance
  -Low power
  -Hard to Design
  -Lack of flexibility
  -component testing needs access mechanism.
  -lower yields
Apr 9, 2015
SoC Advantages:
SoC Disadvantages:

## Slide 5
Testing of SoC
  Source – to apply test stimuli
  Sink – to capture test results
  TAM – test access mechanism to transport test & its results
  Wrapper – Interface between TAM and the embedded core
IEEE 1500 Overview
Apr 9, 2015

## Slide 6
TAM Architecture
In this figure, Total TAM width of 7 is partitioned among three test buses.
TAM are modeled as TAM buses in this work.
The number of TAM correspond to the number of scan chains of each core, double
the TAM wires reduce the test time of the core to half.
Apr 9, 2015

## Slide 7
Rectangle Bin Packing Problem
Apr 9, 2015

## Slide 8
Hardware Constraint of SoC Testing
Hardware compatibility between cores of each SoC is given by benchmark[10], eg. {1,2,4} means module1, module2 and module 4 are compatible.
Cores on different Voltage Island are
independent with each others, which
Means they could operate at different
Voltages at the same time.
Cores that share the same voltage
island need to operate in the same
voltage and frequency pair if they
are to be scheduled concurrently.
Apr 9, 2015
7

## Slide 9
Session-based and Sessionless
Apr 9, 2015
How does the effect of these two differs in the benchmark?

## Slide 10
MILP (Sessionless Test Scheduling)
Each pin choice corresponds to different TAM pins numbers
Apr 9, 2015
This is the objective function of MILP

## Slide 11
MILP (Sessionless Test Scheduling)
    λL is the TAT of the longest possible test schedule
Apr 9, 2015

## Slide 12
t1
t2
When two tests overlaps
MILP (Sessionless Test Scheduling)
Apr 9, 2015

## Slide 13
MILP (Sessionless Test Scheduling)
Apr 9, 2015
t1
t2
Eg. P(t2,t1)+ P(t2,t3)+ p(t2)<=Pbound
t3
    Constant power model is used for simplicity, peak power is used to
    guarantee the accuracy, but somewhat make this design pessimistic

## Slide 14
    λp is the TAT of the longest possible test schedule
MILP (Sessionless Test Scheduling)
Apr 9, 2015

## Slide 15
MILP (Sessionless Test Scheduling)
Apr 9, 2015
14
t1
t2
Eg. W(t2,t1)+ W(t2,t3)+ W(t2)<=Wbound
t3

## Slide 16
MILP (Sessionless Test Scheduling)
Apr 9, 2015
15

## Slide 17
MILP (Session-based Test Scheduling)
16
Apr 9, 2015
    The decision variable ‘final’ contains 4 variables, which
    makes the session-based Test scheduling a very slow process

## Slide 18
MILP (Session-based Test Scheduling)
17
Apr 9, 2015

## Slide 19
MILP (Session-based Test Scheduling)
18
Apr 9, 2015
    Overlap of tests in session-based algorithm means the start time of
    tests is the same

## Slide 20
Experiment Setup
Apr 9, 2015

## Slide 21
Results_case1
    DVFS_N/DVFS_Y refer to scheduling Without/With DVFS
    Same naming scheme applies to TAM_N/TAM_Y
Apr 9, 2015

## Slide 22
Results_case2
Apr 9, 2015

## Slide 23
Results__case3
Apr 9, 2015

## Slide 24
Results__case4
    Reference work doesn’t consider hardware compatibility, Voltage Island and TAM bounds!
23
Apr 9, 2015
Compatibility file of d695
1 1 4 5
2 2 3 6 9
3 2 3 6 9
4 1 4 5
5 1 5 4
6 2 3 9
7 7 8
8 7 8
9 2 3 6 9

## Slide 25
Results__case5
WHY?
Apr 9, 2015

## Slide 26
In this work, SoC hierarchy is not considered. In real SoC, TAM allocation between parent cell and children cell are more difficult.
ITC’02, the most universally adopted SoC so far, is incomplete. For more accurate test scheduling result, more details are needed.
Some faults are only detectable at certain voltage.
Limitation
Apr 9, 2015

## Slide 27
Future Work
Some schedules may require individual tests to be executed at one or more specific voltage/frequency values. The reason for this is that some faults are voltage/frequency dependent and can only be detected at such voltage/frequency values. Constraint below can be forced to solve this problem:
∀pin ∈C Assign(t, n, pin) = 1 for the required t and n.
Apr 9, 2015

## Slide 28
Conclusion
TAM rescheduling could achieve maximally up to 61% reduction in TAT
DVFS and TAM rescheduling combined could result to TAT reduction range from 50.9% to 69.1%.
Session-based scheduling requires a lot more time to schedule than session-less scheduling, and we could also end up with the conclusion that session-less is no worse than session-based in terms of TAT result.
Apr 9, 2015

## Slide 29
References
[1]S. K. Millican and K. K. Saluja, “Formulating Optimal Test Scheduling Problem with Dynamic Voltage and Frequency Scaling,” in 22nd AsianTest Symposium (ATS), pp. 165–170, IEEE, Nov. 2013.
[2]S. Millican and K. K. Saluja "Optimal Test Scheduling of Stacked Circuits Under Various Hardware and Power Constraints," International Conference on VLSI Design , January 2015.
[3]V. Iyengar, K. Chakrabarty, and E. J. Marinissen, “Test access mechanism optimization, test scheduling, and tester data volume reduction for system-on-chip,”,2011
[4]V. Sheshardi, V. D. Agrawal, and P. Agrawal, “Optimal PowerConstrained SoC Test Schedules With Customizable Clock Rates,” in IEEE International SOC Conference (SOCC), (San Jose, CA), pp. 271–276, Oct. 2012.
[5]S. K. Millican and K. K. Saluja, “Formulating Optimal Test Scheduling Problem with Dynamic Voltage and Frequency Scaling,” in 22nd AsianTest Symposium (ATS), pp. 165–170, IEEE, Nov. 2013.
[6] Sheshardi, V. D. Agrawal, and P. Agrawal, “Optimum Test Schedule for SoC with Specified Clock Frequencies and Supply Voltages,” in 26th International Conference on VLSI Design and International Conference on Embedded Systems, (Pune, India), pp. 267 – 272, Jan. 2013.
Apr 9, 2015

## Slide 30
[7] V. Iyengar, K. Chakrabarty, and E. J. Marinissen, “Test access mechanism optimization, test scheduling, and tester data volume reduction for system-on-chip,” IEEE Transactions on Computers, vol. 52, pp. 1619– 1631, Dec. 2003.
[8] Sheshardi, V. D. Agrawal, and P. Agrawal, “power aware SoC test optimization through dynamic voltage and frequency scaling,” in 21st International conference on VLSI-SoC, 102-107, oct, 2013
[9]ITC’02 SoC Testing Benchmark, url:http://itc02socbenchm.pratt.duke.edu/
[10] 3DIC SoC Test Benchmark url:http://3dsocbench.ece.wisc.edu/ (based on ITC’02)
References
Apr 9, 2015

## Slide 31
Questions?
THANK YOU
Apr 9, 2015