## Slide 1: Reducing ATE Test Time by Voltage and Frequency Scaling
BY
Praveen Venkataramani
Committee Members:
Prof. Vishwani D. Agrawal (Chair)
Prof. Fa Foster Dai
Prof. Adit Singh
External Reader:
Prof. Sanjeev Baskiyar

## Slide 2: Acknowledgment
Prof. Vishwani Agrawal for his invaluable guidance throughout my work,
Prof. Adit Singh and Prof. Foster Dai for being my committee members and for their courses,
Prof. Sanjeev Baskiyar for being my external reader,
Prof. Victor Nelson for his course on CAD tools which helped me understand the tools I used, for assisting me with the ATE issues and calibrations,
All staff members of EE department,
My friends and family for their support throughout my research.

## Slide 3: Overview
Background
Theorem
Scaling Voltage
Scaling Frequency
Conclusion

## Slide 4: Background
Types of device under test
  Combinational – simpler to model and generate patterns
  Sequential – more complex and hard to generate patterns

## Slide 5: Scan chains
DFF
DFF
PI
PO
SI
SO
SE
Combo Logic
Circuits with many flip flop groups connected as a chain, each group is shown in one color

## Slide 6: Testing Methods
AUTOMATIC TEST EQUIPMENT

## Slide 7: What is an ATE?
Automatic test equipment
Used to generate patterns and clock, to test circuits in real time
Contains
  Main frame- contains the main power supply
  User Interface – Interface between the user and the ATE
  Test head – measurement modules and test head
Has limited channels and memory
Is expensive.
The time spent on the tester is added to the cost of a chip.
Reducing cost of chip -> spend less time on the ATE

## Slide 8: Test cost economics- example [LTXC’10]
Item | Cost
ATE purchase price | 985,000
Depreciation | 20%
Maintenance | 4%
Operating Cost | 10%
Production weeks/year | 52
Production days / week | 7
Production shift/week | 3
Production hours/shift | 8
Devices per slot | 7000
Good devices test time | 5 seconds
Bad devices test time | 0.3 seconds
Yield | 98%

## Slide 9: Test cost economics- example
The cost analysis according to [Bushnell and Agrawal ’00] is given as
Running Cost = Depreciation + Maintenance + Operating Cost
Using the data in the table ,
Running Cost | 
 | = $334,900
Tester Usage | = Weeks/year * Days/week * number shifts * Hours/shift * 3600 sec
Running Cost | 
 | = $334,900
Tester Usage | = Weeks/year * Days/week * number shifts * Hours/shift * 3600 sec

## Slide 10: Test cost economics- example
Testing Cost | 
Total Test Time | 
Total Cost | 
Cost per good die | 
Reducing test time by 30% | 
Testing Cost | 
Total Test Time | 
Total Cost | 
Cost per good die | 
Reducing test time by 30% | 

## Slide 11: Test time and power
Test pattern have almost no functional relation, and are only to activate and observe a fault.
Unwanted signal transitions may be caused in the circuit, thus causing excessive power dissipation.
Excessive power dissipation might cause “overtest” where a good device might fail due to IR drop delays or failure in the chip due to overheating.
Increase the time period => Lower power => increased test time, or
Reduce energy by choosing patterns that lower signal transitions => more patterns to achieve high fault coverage => increased test time.

## Slide 12: Power Metrics [Girard ‘10]
Energy per cycle: Energy dissipated due to switching activity in one clock cycle.
Power per cycle: It is the energy dissipated during one clock cycle divided by the period.
Average power: It is total energy dissipated over the entire test divided by the test time.
Maximum power: It is the maximum power consumed by any one cycle during the entire test.
Maximum energy: It is the energy dissipated by the cycle having the maximum signal transitions.
Total energy: It is the energy dissipated during the entire test.

## Slide 13: Problem Statement
Power consumption during test must not exceed the specified budget often implying increased test time.
Long test time increases cost; test time can be very long for scan based testing.
Need to reduce test time without exceeding power budget.

## Slide 14: Test time reduction techniques
SO
SI
Multiple scan chains
1 1 0 0 0
1 0 1 0 0
1 0 1 0 1
1 0 1 1 1
Original tests:
V1 V2 V3 V4 V5
Test vector Reordering [Chloupek’12]
Reordered tests:
V1 V3 V5 V4 V2
1 0 0 0 1
1 1 0 0 0
1 1 1 0 0
1 1 1 1 0
SO
SI
Deserializer
Serializer
SerDes scan structure [Sanghani ‘11]
Combo Logic
P
R
P
G
M
I
S
R
Built In Self Test + ATE [Hashempour’02]

## Slide 15: Test time theorem
For power constrained testing where the peak power during any clock must not exceed the rated power of the device, the test time has a lower bound,
where ETOTAL(test) is the total energy consumed during the entire test, PMAX(rated) is the maximum rated power for the device, PAVG is the average power of the entire test and TT is the total test time.

## Slide 16: Test power per cycle
Test Time can be reduced by
  Scaling the power supply used for test
  Varying the frequency based on the power dissipated during each cycle

## Slide 17: Reduced supply voltage test
Test at lower than nominal supply voltage has existed from early 90’s. [Hao and McClusky ‘93]
Effects of low supply voltage tests are –
  Resistive shorts and hot carrier defects are more pronounced.
  Force malfunction of weak chips, while retaining truly good ones.
  Gate delay increases but wire delay is not affected much.
  Changes in critical paths.
  Alternative to expensive burn-in tests.
  Can detect pattern dependent faults

## Slide 18: Effects of scaling supply voltage
Certain effects are to be considered-
  Change in the critical path – can be observed by implementing a critical path monitor
  Effects of threshold voltage variations due to variations in the manufacturing process.
In this work we assume
  There are no critical path variation
  There are no threshold voltage variations
Gate delay can be approximated by using a alpha power law delay model. [Sakurai and Newton ‘90]
Effect of voltage variation on the critical path delay can be observed by simulating a chain of inverters.

## Slide 19: Alpha power law delay model
The gate delay can be approximated using
Where,
is the velocity saturation index, 1 if velocity saturated and 2 if no velocity saturation,
K is a proportionality constant,
is the supply voltage,
is the threshold,
is the delay.

## Slide 20: Chain of Inverters
Chain was simulated for every voltage
Delay at each voltage is measured
Initial delay was calculated with arbitrary values for the unknowns
Curve fitting was used to find the actual values for the unknowns
The velocity saturation index was found to be 2.
The value for K is circuit dependent
IN
OUT

## Slide 21: Scaled test supply voltage
Quadratic reduction in power.
Critical path delay increases.
Power dissipation depends on the time period used
To maintain the same power dissipation, clock period can be reduced.
Power constrain: A test is power constrained, if the minimum test clock period is limited by the maximum rated power for the circuit under test.
Structure constrain: A test is structure constrained if the minimum test clock period is limited by the structural (critical path) delay of the circuit under test.

## Slide 22: Scaling test supply voltage

## Slide 23: s298 Example

## Slide 24: Optimum voltage
For minimum test time, the period should satisfy both structure and power constraints.
i.e.
The test period based on our observation, the test clock period is equal to the structural clock period at the voltage .
Equating the test period and the structural delay at we will get
If and , then
Since the highest power is 3 and is solvable using any Numerical solver such as MATLAB.

## Slide 25: Optimum voltage

## Slide 26: Simulation results
Circuit Name | Total Scan test cycles | Max Per cycle Power | Nominal Voltage (@ 1.8 V) |  | Optimum Voltage |  |  | Test time reduction
 |  |  | Test Freq (MHz) | Test Time (µs) | Supply Voltage | Test Freq (MHz) | Test Time (µs) | 
s298 | 450 | 0.0012 | 216.30 | 2.08 | 1.10 | 562.00 | 0.8 | 61.5
s298 | 498 | 0.0012 | 187.00 | 2.66 | 1.07 | 512.00 | 0.971 | 63.0
s298 | 540 | 0.0012 | 184.00 | 2.92 | 1.07 | 529.00 | 1.02 | 65.0
s382 | 704 | 0.0029 | 292.00 | 2.41 | 1.44 | 457.00 | 1.54 | 36.0
s713 | 810 | 0.0015 | 137.28 | 5.9 | 1.33 | 249.23 | 3.25 | 45.0
s1423 | 6975 | 0.0045 | 135.90 | 51.3 | 1.60 | 148.40 | 47 | 13.0
s1423 | 6975 | 0.0030 | 90.58 | 77 | 1.49 | 132.10 | 52.7 | 31.5
s13207 | 62237 | 0.0213 | 168.00 | 369 | 1.62 | 208.80 | 298 | 19.2
s15850 | 101708 | 0.2400 | 67.35 | 1510 | 1.30 | 128.90 | 789 | 47.7
s38584 | 224113 | 0.3500 | 88.54 | 2531 | 1.30 | 172.30 | 1300 | 48.6

## Slide 27: Matlab results
Circuit name | Proporti-onality constant K () | Maximum switched capacitance CL (pF) | Total Scan test cycles | Peak per cycle power (mW) | Nominal voltage (@ 1.8 V) |  | Optimum voltage |  |  | Reduction (%)
 |  |  |  |  | Test freq. (MHz) | Test time (µs) | Supply voltage | Test freq. (MHz) | Test time (µs) | 
s298 | 0.85 | 1.76 | 450 | 0.0012 | 216.3 | 2.08 | 1.1 | 562 | 0.8 | 61.5
s298 | 0.85 | 2.04 | 498 | 0.0012 | 187 | 2.66 | 1.073 | 512 | 0.971 | 63
s298 | 0.85 | 2.06 | 540 | 0.0012 | 184 | 2.92 | 1.07 | 529 | 1.02 | 65
s382 | 1.75 | 3.07 | 704 | 0.0029 | 292 | 2.41 | 1.44 | 434 | 1.54 | 36
s713 | 2.79 | 3.36 | 810 | 0.0015 | 132.3 | 5.9 | 1.34 | 249.23 | 3.25 | 45
s1423 | 6.38 | 10.22 | 6975 | 0.0045 | 135.9 | 51.3 | 1.66 | 158.5 | 44 | 14.2
s1423 | 6.38 | 10.22 | 6975 | 0.0030 | 90.6 | 77 | 1.49 | 131.7 | 52.9 | 31.2
s13207 | 4.65 | 38.9 | 62237 | 0.0213 | 168 | 369 | 1.62 | 208.8 | 298 | 19.2
s15850 | 5.12 | 109 | 101708 | 0.0240 | 67.3 | 1510 | 1.31 | 128.9 | 789 | 47.7
s38584 | 4.03 | 156.8 | 224113 | 0.0350 | 88.5 | 2531 | 1.31 | 172.4 | 1300 | 48.6
Circuit name |  | Maximum switched capacitance CL (pF) | Total Scan test cycles | Peak per cycle power (mW) | Nominal voltage (@ 1.8 V) |  | Optimum voltage |  |  | Reduction (%)
 |  |  |  |  | Test freq. (MHz) | Test time (µs) | Supply voltage | Test freq. (MHz) | Test time (µs) | 
s298 | 0.85 | 1.76 | 450 | 0.0012 | 216.3 | 2.08 | 1.1 | 562 | 0.8 | 61.5
s298 | 0.85 | 2.04 | 498 | 0.0012 | 187 | 2.66 | 1.073 | 512 | 0.971 | 63
s298 | 0.85 | 2.06 | 540 | 0.0012 | 184 | 2.92 | 1.07 | 529 | 1.02 | 65
s382 | 1.75 | 3.07 | 704 | 0.0029 | 292 | 2.41 | 1.44 | 434 | 1.54 | 36
s713 | 2.79 | 3.36 | 810 | 0.0015 | 132.3 | 5.9 | 1.34 | 249.23 | 3.25 | 45
s1423 | 6.38 | 10.22 | 6975 | 0.0045 | 135.9 | 51.3 | 1.66 | 158.5 | 44 | 14.2
s1423 | 6.38 | 10.22 | 6975 | 0.0030 | 90.6 | 77 | 1.49 | 131.7 | 52.9 | 31.2
s13207 | 4.65 | 38.9 | 62237 | 0.0213 | 168 | 369 | 1.62 | 208.8 | 298 | 19.2
s15850 | 5.12 | 109 | 101708 | 0.0240 | 67.3 | 1510 | 1.31 | 128.9 | 789 | 47.7
s38584 | 4.03 | 156.8 | 224113 | 0.0350 | 88.5 | 2531 | 1.31 | 172.4 | 1300 | 48.6

## Slide 28: Revisiting periodic clock test

## Slide 29: Scaling test clock frequency
From the theorem, the total test time using a conventional periodic clock test can be written as
To obtain the lower bound for test time => Denominator must be large.
The arithmetic mean is maximum when all the values in the function is equal to the maximum value of that function.
Implies, for , every cycle must dissipate the power equal to

## Slide 30: Aperiodic test

## Slide 31: Aperiodic clock test
Each period can be either structure constrained or power constrained, i.e.,
where,
Ti is the period of each test cycle
Ei is the energy dissipated by each cycle
This is termed as aperiodic clock test where each cycle may not use exactly the same period as its neighboring cycle.
For any given voltage an aperiodic clock test can run faster than the periodic clock test at that voltage

## Slide 32: s298 circuit example
Aperiodic Clock
Periodic Clock

## Slide 33: Aperiodic clock simulation results
Circuit name | Peak per cycle power (mW) | Max per cycle energy (pJ) | Total energy (nJ) | Periodic clock |  | Aperiodic clock test time (µs) | Reduction (%)
 |  |  |  | Test freq. (MHz) | Test time (µs) |  | 
s298 | 0.0012 | 5.71 | 1.83 | 216.3 | 2.08 | 1.48 | 28.5
s298 | 0.0012 | 6.61 | 1.83 | 187.0 | 2.66 | 1.49 | 44.0
s298 | 0.0012 | 6.68 | 1.89 | 184.0 | 2.92 | 1.54 | 47.2
s382 | 0.0029 | 9.96 | 4.69 | 292.0 | 2.41 | 1.62 | 32.7
s713 | 0.0015 | 10.90 | 4.22 | 132.3 | 5.9 | 2.83 | 52.0
s1423 | 0.0045 | 33.14 | 166.68 | 135.9 | 51.3 | 39.8 | 22.4
s1423 | 0.0030 | 33.14 | 166.68 | 90.6 | 77 | 55.6 | 28.0
s13207 | 0.0213 | 126.3 | 660 | 168.0 | 369 | 312.2 | 15.0
s15850 | 0.0240 | 213.8 | 2610 | 67.3 | 1510 | 1088 | 27.8
s38584 | 0.0350 | 609.8 | 9470 | 88.5 | 2531 | 2101.5 | 17.0

## Slide 34: Experiments on ATE
Experimental Setup
  The test was implemented on the Advantest T2000GS ATE at Auburn University.
  Maximum clock speed of 250 MHz
  CUT is an FPGA configured for ISCAS‘89 benchmark circuit.
  FPGA is configured on the run using the ATE.
  All clock periods for aperiodic clock test are determined prior to external test based on the amount of energy dissipated during each cycle.
Limitations in tester framework sets few margins to the clock periods and the granularity in their variations
  Only 4 unique clock periods can be provided for each test flow

## Slide 35: Changes to test programming
The clock periods were grouped into 4 sets.
Each set contains patterns of one clock period.
For periodic test the maximum period is used as the fixed clock period.
The figure shows the cycle periods determined for each test cycle.
Test cycle will use the clock (dotted line) just above the period

## Slide 36: Periodic clock test period

## Slide 37: Aperiodic test on ATE

## Slide 38: Scaling supply voltage- Aperiodic Test

## Slide 39: Experimental results - s298

## Slide 40: Simulation results
Circuit name | Total Scan test cycles | Peak per cycle power (mW) | Nominal voltage (@ 1.8 V) |  | Optimum voltage |  | Reduction (%)
 |  |  | Test freq. (MHz) | Test time (µs) | Supply voltage (V) | Test time (µs) | 
s298 | 450 | 0.0012 | 216.3 | 2.08 | 1.20 | 0.72 | 65.4
s298 | 498 | 0.0012 | 187 | 2.66 | 1.25 | 0.77 | 71
s298 | 540 | 0.0012 | 184 | 2.92 | 1.25 | 0.81 | 72.2
s382 | 704 | 0.0029 | 292 | 2.41 | 1.59 | 1.37 | 43.5
s713 | 810 | 0.0015 | 132.28 | 5.9 | 1.62 | 2.49 | 57.7
s1423 | 6975 | 0.0045 | 135.9 | 51.3 | 1.82 | 39.7 | 26.7
s1423 | 6975 | 0.0030 | 90.58 | 77 | 1.55 | 49.5 | 35.7
s13207 | 62237 | 0.0213 | 168 | 369 | 1.70 | 281 | 23.8
s15850 | 101708 | 0.0240 | 67.35 | 1510 | 1.43 | 702 | 53.5
s38584 | 224113 | 0.0350 | 88.54 | 2531 | 1.41 | 1290 | 49

## Slide 41: Conclusion
Periodic test time is reduced by,
  Scaling supply voltage down
  Scaling cycle frequency upward
Aperiodic clock test produces lower test time at any voltage as long as there are some test cycles that are power constrained.
According to the test time theorem, aperiodic test time is always less than or equal to the periodic test time.
Future works
  Finding optimum number of periods for aperiodic clock test to achieve better test time reduction.
  Include process variations and make the method more adaptive.

## Slide 42: Posters and Papers Presented
Praveen Venkataramani, Vishwani D. Agrawal, “ATE Test Time Reduction Using Aperiodic Clock Test,” Proc. International Test Conference, Anaheim CA, 2013, Paper 15.3.
Praveen Venkataramani, Suraj Sindia, Vishwani D. Agrawal, “A Test Time Theorem and Its Applications,” Proc. 14th Latin American Test Workshop (LATW), April 2013, pp.1-5.
Praveen Venkataramani, Suraj Sindia, Vishwani D. Agrawal “Finding Best Voltage and Frequency to Shorten Power Constrained Test Time,” Proc. 31st IEEE VLSI Test Symposium, April 2013, pp. 19-24.
Praveen Venkataramani, Vishwani D. Agrawal “Reducing Test Time of Power Constrained Test by Optimal Selection of Supply Voltage,” Proc. 26th International Conference on VLSI Design, Jan. 2013, pp. 273-278.
Praveen Venkataramani, Vishwani D. Agrawal “Test-Time Reduction in ATE Using Aperiodic Clocking,” 6th IEEE International Workshop on Design for Manufacturing and Yield, San Francisco, CA, 4 July 2012 (Poster).
Praveen Venkataramani, Vishwani D. Agrawal “Reducing Test Time for Power Constrained Scan Circuits Using Aperiodic Clocking,” International Test Conference, Anaheim, CA, 5-9 November 2012 (Poster).

## Slide 43: References
[AGILENT_EDITORIAL] http://www.home.agilent.com/agilent/editorial.jspx?&id=875011&cc=US&lc=eng
[Girard’10] P. Girard, N. Nicolici, and X. Wen, Power Aware Testing and Test Strategies for Low Power Devices, Springer Publications 2010, New York, ISBN-978-1-4419-0927
[Hashempour’02] H. Hashempour, F. J. Meyer, and F. Lombardi, “Test Time Reduction in a Manufacturing Environment by Combining BIST and ATE,” in Proc. 17th IEEE International Symposium on Defect and Fault Tolerance in VLSI Systems, 2002, pp. 186–194.
[Shanmugasundaram’12] P. Shanmugasundaram and V. D. Agrawal, “Externally Tested Scan Circuit with Built-In Activity Monitor and Adaptive Test Clock,” in Proc. 25th International Conf. VLSI Design, Jan. 2012, pp. 448–453.
[Chloupek’12] M. Chloupek, O. Novak, and J. Jenicek, “On Test Time Reduction Using Pattern Overlapping, Broadcasting and On-Chip Decompression,” in Proc. IEEE 15th International Symp. on Design and Diagnostics of Electronic Circuits Systems (DDECS), Apr. 2012, pp. 300–305.
[Sanghani ‘11] Sanghani, A.; Bo Yang; Natarajan, K.; Chunsheng Liu, "Design and implementation of a time-division multiplexing scan architecture using serializer and deserializer in GPU chips," Proc. 29th IEEE VLSI Test Symposium (VTS), May 2011, pp. 219,224.