## Slide 1: Power-Aware System-On-Chip Test Optimization through Frequncy and Voltage Scaling
Dept. of Electrical and Computer Engineering
Auburn University, AL 36849, USA
Committee Chair: Dr. Prathima Agrawal
Committee Members: Dr. Vishwani D. Agrawal
(co-chair)
Dr. Adit Singh
Final Exam
Vijay Sheshadri

## Slide 2: Acknowledgements
Dr. Prathima Agrawal and Dr. Vishwani D. Agrawal
Dr. Adit Singh
Dr. Sanjeev Baskiyar
Dr. Alice Smith and Dr. Chase Murray
Dr. Victor Nelson
Family and friends

## Slide 3: Outline
Introduction
Problem Statement
Background on SoC Testing
Frequency and Voltage Scaling
MILP-based Optimization
Heuristic-based Optimization
Conclusion

## Slide 4: Introduction
What is System-on-Chip?

## Slide 5: Introduction
What is System-on-Chip?
  A complete system integrated onto a single chip.
*http://www.xbitlabs.com/news/mobile/display/20080603141353_Nvidia_Unleashes_Tegra_System_on_Chip_for_Handheld_Devices.html

## Slide 6: Introduction
SoC & Smartphone:
  SoCs are backbone of Smartphone growth .
2004
2008
2009
2010
2011
2012
2013
Single-core, 400-800 MHz
Single-core, 1GHz
Dual-core, 1–1.5 GHz
Quad-core, 1.5 GHz
Octa-core, 1.6 GHz
*Compiled from: http://en.wikipedia.org/wiki/Comparison_of_smartphones#2004
Notes: Advent of SoC has ushered in an era of Smartphone

## Slide 7: Introduction
SoC advantages:
  Small area.
  Low power.
  Modularity.
Notes: Modularity – SoCs made up of kinds of blocks/cores, each possibly from a diff. vendor. Helpful during testing SoCs

## Slide 8: Introduction
Testing a SoC:
  Modular testing – individual (often independent) core tests.
Test Source
Test Sink
Core ‘A’
Core ‘B’
SoC
Notes: Due to modularity each core has its own test set and can be tested independently
Here is a simple set up

## Slide 9: Introduction
Testing a SoC:
  Modular testing – individual (often independent) core tests.
Test Source
Test Sink
Core ‘A’
Core ‘B’
SoC
Test
Data
Notes: Test source provides test data *

## Slide 10: Introduction
Testing a SoC:
  Modular testing – individual (often independent) core tests.
Test Source
Test Sink
Core ‘A’
Core ‘B’
SoC
Test
Data
Test Bus
Notes: Which is carried on the test bus 

## Slide 11: Introduction
Testing a SoC:
  Modular testing – individual (often independent) core tests.
Test Source
Test Sink
Core ‘A’
Core ‘B’
SoC
Test
Data
Test Bus
T_In
T_In
T_Out
T_Out
Test
Data
Notes: To the test sink

## Slide 12: Introduction
Testing a SoC:
  More cores → larger test data → longer test time.
Test Source
Test Sink
Core ‘A’
Core ‘B’
SoC
Test
Data
Test Bus
Test
Data
Core ‘C’
Core ‘E’
Core ‘D’
Notes: Technology scaling has led to an increase in the no. of cores in the SoC

## Slide 13: Introduction
Testing a SoC:
  More cores → larger test data → longer test time.
Test multiple cores simultaneously
  Increased power consumption.

## Slide 14: Outline
Introduction
Problem Statement
Background on SoC Testing
Frequency and Voltage Scaling
MILP-based Optimization
Heuristic-based Optimization
Conclusion

## Slide 15: Problem Statement
How to test all cores of SoC as quickly as possible, for a given power budget?
Notes: *read*

## Slide 16: Problem Statement
Given an SoC with N core tests and a peak power budget, find a test schedule to:
  Test all cores.
  Reduce overall test time.
  Conform to SoC test power budget.
Notes: Or more formally *read*

## Slide 17: Case Study
Example benchmark: ASIC Z*
RAM 2
(61,241)
RAM 3
(38,213)
ROM 1
(102,279)
ROM 2
(102,279)
RAM 1
(69,282)
RAM 4
(23,96)
Reg. file
(10,95)
Random logic 1 (134, 295)
Random logic 2 (160, 352)
Pmax= 900
Block
(test time, power)
Blocks of ASIC Z, and their test time (in a.u.) and test power (in mW)
* Y. Zorian, “A distributed control scheme for complex VLSI devices,” Proc. VTS, Apr. 1993, pp. 4–9.
Notes: As a case study for this work, lets consider ASIC Z

## Slide 18: Outline
Introduction
Problem Statement
Background on SoC Testing
Frequency and Voltage Scaling
MILP-based Optimization
Heuristic-based Optimization
Conclusion
Notes: ----- Meeting Notes (2/20/14 18:27) -----
Lets review some basics of SoC testing

## Slide 19: SoC Testing
3-D Optimization Problem:
  Minimize test time for given test resources and test power limit.
Test Time
Test Power
Test Resources
Pmax
Rmax
Larsson, E., & Ravikumar, C. P. (2010). Power-Aware System-Level Test Planning. In Power-Aware Testing and Test Strategies for Low Power Devices (pp. 175-211). Springer US.

## Slide 20: Test Scheduling
Test Schedule:
  Arrangement of SoC core tests satisfying power and resource constraints.
  Can be optimized to minimize overall test time.

## Slide 21: Test Scheduling
Sequential:
Concurrent:
Power
Time
T1
Power limit
T2
T3
Power
Time
T1
Power limit
T2
T3
Session 1
Session 2
Power
Time
T1
Power limit
T2
T3
Session-Based
Sessionless

## Slide 22: Prior Work
Resource-constrained optimization:
  Test Access Mechanism (TAM) and Wrapper Optimization.
    TAM and wrapper form interface between SoC pins and core scan chains.
    Optimal design of TAM and wrapper can minimize test time.
Core
TAM
TAM
Wrapper
Internal Scan Chains
Notes: Previous work on SoC testing has been in both resource and power constrained optimization. In resource constrained optimization, the focus has mostly been on TAM and wrapper optimization

## Slide 23: Prior Work
Power-constrained optimization:
  Max. peak power limit defined for SoC and cores.
  Published optimal test times for ASIC Z:
    Session-based testing: 300 units*.
    Sessionless testing: 262 units*.
* E. Larsson, Z. Peng, and K. Chakrabarty. "An integrated framework for the design and optimization of SOC test solutions." SOC (System-on-a-Chip) Testing for Plug and Play Test Automation. Springer US, 2002. 21-36.
Notes: In power-constrained optimization, test time is optimized for a max. power limit

## Slide 24: Outline
Introduction
Problem Statement
Background on SoC Testing
Frequency and Voltage Scaling
MILP-based Optimization
Heuristic-based Optimization
Conclusion
Notes: This work tackles the problem of power constrained optimization by scaling voltage and frequency

## Slide 25: Variable Test Clock Frequency
Test time and power linearly dependent on test clock rate
Increasing test clock frequency by a factor f =>
Test time, and Test power,
Proper choice f for each test session can optimize overall test time

## Slide 26: Core Frequency Constraints
Each core’s max. clock rate decided by:
  Max. power limit of core (power constraint)
  Critical path delay (structure constraint)
Both constraints also influenced by VDD.
  Power Constraint:
  Structure constraint:
(Alpha power law*)
* T. Sakurai and A. R. Newton, “Alpha-Power Law MOSFET Model and its Applications to CMOS Inverter Delay and Other Formulas,” IEEE Journal of Solid-State Circuits, vol. 25, no. 2, pp. 584–594, Apr. 1990.
Notes: The critical path delay’s dependence on VDD is given by the alpha power law

## Slide 27: Optimum VDD point
P. Venkataramani , S. Sindia and V. D. Agrawal, “A Test Time Theorem and Its Applications,” Proc. 14th IEEE LATW, Apr. 2013.
Notes: Since test power is much higher than functional power, test clock is mostly power constrained (right-half of the plot)
Hence, both VDD and frequency are needed to reduce test time

## Slide 28: Lower Bound on Test Time
Lower bound on the total test time is given by the ratio of the total energy spent during the test and the power budget*.
P. Venkataramani , S. Sindia and V. D. Agrawal, “A Test Time Theorem and Its Applications,” Proc. 14th IEEE LATW, Apr. 2013.
Pt i , Tt i = Test power and time of Test, ti
Vnom = nominal VDD
Vmin = minimum VDD

## Slide 29: Lower Bound on Test Time
Theorem: SoC test time is lowest when each core test scheduled at clock rate:
where fnom = nominal clock rate of SoC.
Lower bound on ASIC Z test time:
  220.19 units for Vnom = Vmin = 1.0V.
  79.27 units for Vnom = 1.0V and Vmin = 0.6 V.

## Slide 30: Outline
Introduction
Problem Statement
Background on SoC Testing
Frequency and Voltage Scaling
MILP-based Optimization
Heuristic-based Optimization
Conclusion

## Slide 31: Mixed-Integer Linear Program (MILP)
Objective:
      Minimize
      , where
Subject to:
  Power Budget Constraint:
Notes: Test time is now divided by the frequency factor

## Slide 32: MILP Formulation
Subject to:
  Clock Constraint:
    Power constraint:
    Structure constraint:
  Other constraints:
    Each session scheduled at only one VDD value.
    Test completeness constraint.

## Slide 33: MILP Results
Results compared:
  Case 1: VDD and test clock fixed at nominal value (nominal case).
  Case 2: Nominal VDD ; test clock optimized per session.
  Case 3: VDD and test clock optimized per session.
Assumptions:
  VDD range = [1.0V, 0.6V]
  VTH = 0.5V, α = 1.0
Notes: For comparison, three optimization cases are considered
A common VDD range of 1V to 0.6V is assumed for all cores

## Slide 34: MILP Results
ASIC Z:
  Case 1: Nominal case = 300 units
Case 2 |  | 
Session | Freq. factor | Test time
RAM1, ROM1 | 1.5 | 68
RAM2, RAM3 | 1.98 | 30.771
RAM4, Reg. File | 4.712 | 4.881
ROM2, RL1, RL2 | 0.972 | 164.622
Total Test time = |  | 268.274
Case 3 |  |  | 
Session | Freq. factor | VDD | Test time
Reg. File | 12.5 | 0.8V | 0.8
RAM 1,2,3,4 | 2.56 | 0.65V | 26.95
ROM 1,2, RL 1,2 | 1.3278 | 0.75V | 120.5
Total Test time = |  |  | 148.25
Notes: According to the cases we considered earlier, the nominal case yields 300 units. Optimizing only test clock reduces to 268.274. Optimizing VDD and clock reduces test time to 148.25 units

## Slide 35: MILP Results
Benchmark | No. of cores | Pmax (mW) | Case 1 | Case 2 | Case 3 |  | 
 |  |  | Test time | Test time | Test time | % Reduction over | 
 |  |  |  |  |  | Case 1 | Case 2
a586710* | 7 | 800 | 1.4E+07 | 1.3E+07 | 6799115 | 52.36 | 47.74
h953* | 8 | 800 | 122636 | 121715 | 79318.8 | 35.32 | 34.84
ASIC Z | 9 | 900 | 300 | 268.274 | 148.25 | 50.58 | 44.74
d695* | 10 | 400 | 15188 | 12733.2 | 7173 | 52.77 | 43.67
Test time reduction:
 50% over Case 1  40-45% over Case 2
* ITC 2002 SOC Benchmarking Initiative: http://www.extra.research.philips.com/itc02socbenchm
Power profile for benchmarks from: S. K. Millican and K. K. Saluja (http://homepages.cae.wisc.edu/~millican/bench/)
Notes: One shortcoming of ILP method is that as no. of cores increases the time required for optimization increases exponentially

## Slide 36: Outline
Introduction
Problem Statement
Background on SoC Testing
Frequency and Voltage Scaling
MILP-based Optimization
Heuristic-based Optimization
Conclusion

## Slide 37: Heuristic Algorithms
ILP methods NP-hard*
  Problem size grows quickly with no. of cores.
  Rapid increase in CPU time.
Heuristic methods offer better alternative:
  Often based on greedy approach.
  Capable of near-optimal solutions.
  Less CPU time than ILP method for larger SoC.
* K. Chakrabarty, “Test Scheduling for Core-Based Systems,” Proc. IEEE/ACM ICCAD, Nov. 1999, pp.391–394.

## Slide 38: Simulated Annealing
Directed search algorithm, based on metal annealing process.
Moves to better solutions neighboring current solution.
Sometimes accepts worse solution to avoid local optimum.

## Slide 39: Simulated Annealing
  Randomly group tests into sessions such that session test power does not exceed Pmax.
Swap randomly chosen tests from two different sessions.

## Slide 40: Voltage and Frequency Scaling
After swap, perform voltage and clock scaling to optimize test time.
tsch = test time of the test schedule
Voltage and Frequency scaling

## Slide 41: Heuristics Results
Algorithm repeated for 100 starting points.
  Best solution among them is chosen.
  CPU time averaged over the 100 iterations.
Benchmark | SA based heuristic method |  | MILP method |  | % Difference in Test time
 | Test time | CPU time | Test time | CPU time | 
a586710 | 6799118 | 0.12 sec | 6799115 | 12.03 sec | 4.73E-05
h953 | 79319.1 | 0.09 sec | 79318.76 | 48.17 sec | 0.000454
ASIC Z | 150.26 | 0.11 sec | 148.25 | 501.18 sec | 1.356
d695 | 7173.04 | 0.17 sec | 7173 | 3649.52 sec | 0.00056
Notes: Since the heuristic may be dependent on initial solution

## Slide 42: Heuristic Results
For larger SoCs:
Benchmark | No. of cores | Pmax (mW) | Case 1 | Case 2 | Case 3 |  | 
 |  |  | Test time | Test time | Test time | % Reduction over | 
 |  |  |  |  |  | Case 1 | Case 2
g1023 | 14 | 400 | 21245 | 19888.7 | 12193.1 | 42.6 | 38.7
p34392 | 19 | 400 | 952199 | 758200 | 369692 | 61.17 | 51.24
t512505 | 31 | 400 | 5589002 | 5414047 | 3038173 | 45.64 | 43.88
p93791 | 32 | 400 | 178568 | 160619 | 90391.8 | 49.38 | 43.72
R100* | 100 | 900 | 1347 | 1213.56 | 730.4 | 45.77 | 39.81
R200* | 200 | 900 | 2837 | 2502.29 | 1536.35 | 45.84 | 38.6
R500* | 500 | 900 | 7706 | 6653.01 | 4212.27 | 45.34 | 36.68
* SoCs created by random assignment of test time and test power. Not a part of ITC’02 benchmarks.

## Slide 43: Run Time of Optimization Methods
Chart: No. of cores
| 7.0 | 8.0 | 9.0 | 10.0 | 14.0 | 19.0 | 31.0 | 32.0 | 100.0 | 200.0 | 500.0
Heuristic method | 0.12 | 0.09 | 0.11 | 0.17 | 0.16 | 0.19 | 0.19 | 0.18 | 1.36 | 2.6 | 6.28
MILP method | 12.03 | 48.27 | 501.18 | 3649.52
Experiments performed on Dell workstation with 3.4GHz Intel Pentium processor and 2GB memory.

## Slide 44: Optimizing Sessionless Testing
Sessionless testing lacks session boundaries.
  Can be preemptive*:
    Test can be interrupted or restarted anytime.
  Or Non-preemptive:
    Tests are run to completion without interruption.
Test ‘X’
Test time = t
Test ‘X1’
Test ‘X2’
Test time = t1
t2
(t1 + t2 = t)
* V. Iyengar and K. Chakrabarty, ”Precedence-Based, Preemptive and Power Constrained Test Scheduling for System-on-Chip,” Proc. VTS’02, pp 253-258

## Slide 45: Optimizing Sessionless Testing
Heuristic employed is same as session-based testing.
New addition to algorithm: Merge function.
  After new solution generated, sessions ‘merged’ to form sessionless test schedule.

## Slide 46: Optimizing Sessionless Testing
Reference case, for comparison, obtained from Best-Fit Decreasing algorithm.
  This is also a sessionless test scheduling algorithm.
  Voltage and clock frequency fixed at nominal values.
  Algorithm description on the next slide.

## Slide 47: Reference Case
V. Sheshadri, V. D. Agrawal and P. Agrawal, “Power-aware SoC test optimization through dynamic voltage and frequency scaling”, Proc. VLSI-SoC, 2013.

## Slide 48: Results: Test Time Reduction
*Test time reduction with respect to reference case.
Chart: % Reduction in test time*
| a586710 | h953 | ASIC Z | d695 | g1023 | p34392 | t512505 | p93791 | R100 | R200 | R500
Non-Preemptive | 58.85 | 50.42 | 47.38 | 60.83 | 50.79 | 60.15 | 44.97 | 50.62 | 48.2 | 43.47 | 39.8
Preemptive | 58.81 | 50.45 | 50.4 | 60.86 | 50.79 | 59.9 | 44.97 | 49.27 | 45.99 | 38.45 | 35.53

## Slide 49: Run Time of Heuristic
*CPU time averaged over 100 iterations of the heuristic.
Chart: No. of cores
| 7.0 | 8.0 | 9.0 | 10.0 | 14.0 | 19.0 | 31.0 | 32.0 | 100.0 | 200.0 | 500.0
Non-Preemptive | 0.27 | 0.265 | 0.34 | 0.46 | 0.63 | 1 | 2 | 2.02 | 4.68 | 9.39 | 23.22
Preemptive | 0.33 | 0.38 | 0.43 | 0.56 | 0.87 | 1.28 | 3.53 | 3.41 | 6.89 | 21.12 | 35.22

## Slide 50: Sessionless or Session-Based?
TAM
Core
Core
Core
Control
Session-Based testing
TAM
Core
Core
Core
Control
Control
Sessionless testing
Notes: The objective of this work is to only provide the optimization methods and not side with either of the testing schemes. Concurrent testing requires cores to be distributed on different TAM partitions. For sessionless testing these partitions have to operate independently

## Slide 51: Sessionless or Session-Based?
Notes: Control overhead justified if the saving on test time is significant

## Slide 52: Sessionless or Session-Based?
Chart: Normalized Test time*
| a586710 | h953 | ASIC Z | d695 | g1023 | p34392 | t512505 | p93791 | R100 | R200 | R500
Session-based testing | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Sessionless testing | 0.8527 | 0.76659 | 0.91741 | 0.72588 | 0.72983 | 0.75623 | 0.96801 | 0.75934 | 0.85683 | 0.87049 | 0.83034
* Test time normalized with respect to that of session-based test schedule.

## Slide 53: Outline
Introduction
Problem Statement
Background on SoC Testing
Frequency and Voltage Scaling
MILP-based Optimization
Heuristic-based Optimization
Conclusion

## Slide 54: Conclusion
Main contribution: Optimal selection of VDD and clock rate for power-aware SoC test optimization.
  Applicable for both session-based and sessionless test scheduling.
  MILP and heuristic optimization methods presented.
  Results show up to 60% reduction in test time compared to SoC test schedule at nominal VDD and clock.

## Slide 55: THANK YOU

## Slide 56: Results
Benchmarks | Test time (Reference Case) | Non-preemptive testing |  | Preemptive testing | 
 |  | Test time | % Reduction | Test time | % Reduction
a586710 | 14090716 | 5797579 | 58.85 | 5803598 | 58.81
h953 | 122636 | 60805.6 | 50.42 | 60771.5 | 50.45
ASIC Z | 262 | 137.85 | 47.38 | 129.98 | 50.4
d695 | 13301 | 5210.05 | 60.83 | 5205.9 | 60.86
g1023 | 18084 | 8898.82 | 50.79 | 8898.82 | 50.79
p34392 | 701684 | 279571 | 60.15 | 281358 | 59.9
t512505 | 5344747 | 2940986 | 44.97 | 2940986 | 44.97
p93791 | 139008 | 68638.3 | 50.62 | 70517.1 | 49.27
R100 | 1208 | 625.83 | 48.2 | 652.42 | 45.99
R200 | 2366 | 1252.4 | 47.06 | 1334.97 | 43.47
R500 | 5807 | 3435.65 | 40.84 | 3743.39 | 35.53