## Slide 1: Managing Performance and Efficiency of a Processor
Advisor: Dr. Vishwani Agrawal
Committee: Dr. Adit Singh and Dr. Victor Nelson
Department of Electrical and Computer Engineering
Auburn University
Master’s Project Defense
Aditi Shinde

## Slide 2: Outline
Motivation
  Chip Power Density
  System Optimization Triangle
Performance
  Characteristic of a Performance Metric
  Existing Metrics
Energy Efficiency
  Energy Efficiency Metrics
  Problem Statement
  Proposed Work
Characterization of Intel Pentium M
  Cycle Efficiency
  Cycle Efficiency and Performance
Conclusion
Limitations
Future Work
References

## Slide 3
4004
8008
8080
8085
8086
286
386
486
Pentium®
P6
1
10
100
1000
10000
1970
1980
1990
2000
2010
Year
Power Density (W/cm2)
Hot Plate
Nuclear
Reactor
Rocket
Nozzle
Sun’s
Surface
Source: Patrick P. Gelsinger , Keynote, ISSCC, Feb. 2001
Motivation
VLSI Chip Power Density
3

## Slide 4: Motivation (continued)
Area
Performance
Power
System Optimization Triangle

## Slide 5: Performance
How fast is your computer ?
Performance =
Source: D. A. Patterson and J. L. Hennessy, Computer Organization & Design, the hardware/Software Interface, Fourth Edition, San Francisco, California: Morgan Kaufman Publishers, Inc., 2008.

## Slide 6: Characteristic of a Performance Metric
Linearity
Reliability
Repeatability
Easiness of measurement
Consistency
Independence
Source: D. J. Lilja, ”Measuring Computer Performance: A Practitioner’s Guide”, Cambridge University Press, New York, NY, 2000

## Slide 7: Existing Performance Metrics
Clock Rate
MIPS
MFLOPS
SPEC
QUIPS
Synthetic Benchmarks
Execution Time

## Slide 8: Energy Efficiency
Performance achieved per unit power.
Useful in determining battery life of a computer system.

## Slide 9: Energy efficiency Metrics
Et2 Energy and Time (square) Product
Power × Time (Energy per Operation)
Source: M. Hicks,” Energy Efficient Branch Prediction” in Doctor of Philosophy thesis, University of Hertfordshire, Dec. 2007

## Slide 10: Problem statement
Given a limited source of energy, can we determine the number of cycles (and hence the number of instructions) that can be executed for a given processor?

## Slide 11: Proposed work
We characterize the Intel Pentium M processor and define a new metric called ‘Cycle Efficiency’ and analyze it.
11

## Slide 12: Energy per Cycle of 8 bit adder
Source: K. Kim, “Ultra Low Power CMOS Design” in Doctor of Philosophy’s dissertation, Auburn University, Dept. of ECE, Auburn, Alabama, May 2011.

## Slide 13: Energy per Cycle for Intel Pentium M
Chart: Vdd in Volts
| 0.1 | 0.2 | 0.30000000000000032 | 0.4 | 0.5 | 0.60000000000000064 | 0.70000000000000062 | 0.8 | 0.9 | 1 | 1.1000000000000001 | 1.2 | 1.3
 | 2.5749 | 1.5564 | 3.0631 | 6.0572 | 9.8654 | 14.1787 | 19.052 | 24.905 | 32.5214 | 43.049 | 58 | 79.25 | 109.044

## Slide 14: Cycle efficiency
We define new metric, cycle efficiency as

## Slide 15: and Frequency vs. voltage
Chart: Vdd (Volts)
| 8.0000000000000043E-2 | 9.0000000000000024E-2 | 0.1 | 0.15000000000000024 | 0.18000000000000024 | 0.19 | 0.2 | 0.22 | 0.24000000000000021 | 0.25 | 0.30000000000000032 | 0.4 | 0.5 | 0.60000000000000064 | 0.70000000000000062 | 0.8 | 0.9 | 1 | 1.1000000000000001 | 1.2
Cycle Efficiency | 0.31284 | 0.34912 | 0.388 | 0.59921 | 0.65852 | 0.65599 | 0.645 | 0.59023 | 0.52018 | 0.48416 | 0.3264 | 0.165 | 0.1013 | 0.0705 | 0.0524 | 0.0401 | 0.0307 | 0.0232 | 0.01724 | 0.0126
Frequency | 0.05851 | 0.075 | 0.089 | 0.095 | 0.11413 | 0.13 | 0.14 | 0.15 | 0.16923 | 0.22602 | 0.28675 | 0.35411 | 0.43158 | 0.52416 | 0.6394 | 0.79024 | 0.99977 | 1.3159

## Slide 16: Example
For a program that executes in 1.3 billion clock cycles.
Voltage | Frequency | Cycle Efficiency | Time | Total Energy Consumed
1.2 V | 1.3 GHz | 15 megacycles/joule | 1 seconds | 86.7 Joules
0.6 V | 350 MHz | 70 megacycles/joule | 4 seconds | 18.6 Joules
200 mV | 100 MHz | 660 megacycles/joule | 13 seconds | 1.97 Joules
Aditi Shinde: MEE Project Defense
16
Fastest !
Lowest Power Consumption !

## Slide 17: Cycle efficiency v/s frequency PLOt
Chart: 
| 169 | 226 | 286 | 350 | 431 | 524 | 639 | 790 | 999 | 1300
Cycle Efficiency v/s Frequency | 326 | 165 | 101 | 70 | 52 | 40 | 30 | 23 | 17 | 15
November 1, 2012
Aditi Shinde: MEE Project Defense
17

## Slide 18: vs. Performance
Performance =
Say, Time factor =
Energy Efficiency =
=

## Slide 19: Conclusion
Performance proportional to Time Factor.
Energy Efficiency proportional to Cycle Efficiency.
Role played is analogous.

## Slide 20: Conclusion
Number of cycles that can be completed per given energy resource can be determined.
Number of instructions and hence what part of the program that can be executed knowing the cycles taken per instruction can be determined.

## Slide 21: Limitations
Power values are benchmark program dependent.
‘Almost Perfect Approximation’ by curve fitting and trend line insertion techniques.

## Slide 22: Future Work
Running benchmark programs on actual processor and finding the energy per cycle.
Averaging values over number of benchmark programs to reduce program dependency.

## Slide 23: Future Work
Other approaches, like using the Alpha Power Law Model for MOSFETS can also be used for characterization.
Designing a method where operating points between ‘best energy efficient’ and ‘best performance’ can be derived depending on our requirements.

## Slide 24: References
Synopsys, Inc., “HSPICE User Guide: Simulation and Analysis”, www.synopsys.com.
H. Hanson, K. Rajamani, S. Keckler, F. Rawson, S. Ghiasi, J. Rubio, “Thermal Response to DVFS: Analysis with an Intel Pentium M,” In Proceedings of International Symposium on Low Power Electronics and Design, August 27–29, 2007, Portland, Oregon, pp. 219-224
M. Hicks,” Energy Efficient Branch Prediction” in Doctor of Philosophy thesis, University of Hertfordshire, Dec. 2007.
D. J. Lilja, ”Measuring Computer Performance: A Practitioner’s Guide,” Cambridge University Press, New York, NY, 2000.
K. Kim, “Ultra Low Power CMOS Design,” Doctor of Philosophy’s dissertation, Auburn University, Dept. of ECE, Auburn, Alabama, May 2011.
Patrick P. Gelsinger , Keynote, ISSCC, Feb. 2001.
24

## Slide 25: References
7. D. A. Patterson and J. L. Hennessy, Computer Organization & Design, the Hardware/Software Interface, Fourth Edition, San Francisco, California: Morgan Kaufman Publishers, Inc., 2008.
8. W. Zhao and Y. Cao, “New Generation of Predictive Technology Model for Sub-45nm Early Design Exploration,“ IEEE Transactions on Electron Devices, vol. 53, no. 11, pp. 2816–2823, 2006.
25

## Slide 26: Questions ?
26