## Slide 1: Dual-Threshold Voltage Design of Sub-threshold Circuits
Jia Yao
Dept. of ECE, Auburn University
Doctoral Final Examination
Dissertation Committee:
Dr. Vishwani D. Agrawal ( Chair )
Dr. Victor P. Nelson, Dr. Bogdan M. Wilamowski
University Reader: Dr. Xiao Qin
May 19, 2014

## Slide 2: Outline
Motivation
Background
Contributions of This Work
Future Work
Summary

## Slide 3: Motivation
Demand for energy constrained design has
increased tremendously, like portable
electronics, medical electronics and sensors
Minimum energy operation typically
occurs in sub-threshold region [1]
Increasing problems of leakage currents as
technology scales down
Dual-Vth technique is an effective approach to
suppress leakage but has not been explored in
sub-threshold region
[1] A. Wang, B. H. Calhoun and A. P. Chandrakasan, Sub-threshold design for ultra low-power systems, Springer, 2006

## Slide 4: Objective
Demonstrate the effectiveness of dual-Vth
method on energy per cycle (EPC) reduction
Minimum EPC design of sub-threshold
circuits by dual-Vth method

## Slide 5: Outline
Motivation
Background
Contributions of This Work
Future Work
Conclusion

## Slide 6: Sub-threshold Circuit Applications
Wrist watch in 1970s
Analog circuits like amplifier, oscillator
in 1970 and 80 s
[3-7]
Micro sensors, pacemakers
since 1990s [8-9]
Digital CMOS circuits:
DLMS filter, sensor processor, FFT processor, μ controller
since 2000s [10-13]
Energy constrained circuits, portable devices, Gyroscope

## Slide 7: Sub-threshold Circuits: Vdd < Vth
Low power and energy consumption compared to above-threshold circuits
Minimum EPC typically occurs in sub-threshold range
Minimum energy is
achieved when dynamic
energy is equal to leakage energy
HSPICE simulation of an 8-bit Ripple Carry Adder

## Slide 8: Kim: 16-bit Ripple Carry Adder (RCA)
K. Kim, Ultra Low Power CMOS Design, PhD Dissertation, Auburn University, May 2100.
Need dual voltage supply, level converters, . . .
Can we get more saving with dual threshold voltages?
Energy Saving
23.6%

## Slide 9: MOSFET Sub-threshold Operation Vgs < Vth
Sub-threshold operation or Weak inversion operation
Transistor is NOT completely OFF
Small amount of electrons flow from Drain to Source

## Slide 10: MOSFET Sub-threshold Operation Vgs < Vth
Sub-threshold current Isub is dominant [1]
when Vds > 3Vt , Isub can be further simplified to
where
Note: μ is effective mobility, Cox is oxide capacitance, W is transistor width, L is transistor length, Vgs is gate-source voltage, Vds is drain-source voltage, Vt is thermal voltage
( 25mV at 300K ), Vth is threshold voltage, n is sub-threshold slope, η is DIBL effect coefficient

## Slide 11: MOSFET Sub-threshold Operation Vgs < Vth
HSPICE simulation results of drain current ID vs. gate-source voltage VGS for PTM 32nm bulk CMOS technology NMOS transistor with Wn=5L , Vth = 0.329V at Vdd = 0.9 V

## Slide 12
Sub-threshold Inverter
HSPICE simulation results of Voltage Transfer Curve of an inverter in PTM 32nm bulk CMOS technology at Vdd=0.2V with varying transistor sizing ratio β = Wp / Wn
Circuits function correctly in sub-threshold region
but come with large delay ( 500x larger )
Supply Voltage Vdd (V) | Inverter Delay (ns)
Vdd = 0.2 | 7.01
Vdd = 0.3 | 0.51
Vdd = 0.4 | 0.101
Vdd = 0.5 | 0.019
Vdd = 0.7 | 0.015
Vdd = 0.9 | 0.014
HSPICE simulation results of Inverter delay under varying supply voltages in PTM 32nm bulk CMOS technology with Wn = 5L and Wp = 12L, fan-out is one inverter

## Slide 13: Outline
Motivation
Background
Contributions of This Work
  Single-Vth design
  Dual-Vth minimum EPC design
Future Work
Conclusion

## Slide 14: Single-Vth Design of Sub-threshold Circuits
EPC is independent of Vth
Increasing Vth can not reduce EPC
HSPICE simulations for EPC for 32-bit RCA single-Vth designs in PTM 32nm bulk CMOS technology with Wn=5L Wp=12L.Each design runs at its maximum operating frequency
EPC for single low Vth and single high Vth designs remain same
High Vth design reduces leakage power but increases delay
Two effects cancel out
 | NMOS | PMOS
HS model | 0.328 V | -0.291 V
LP model | 0.549 V | -0.486 V
Threshold voltage of PTM 32nm models calculated in HSPICE at Vdd = 0.9 V

## Slide 15: Single-Vth Design of Sub-threshold Circuits
On current Ion
with Vgs = Vdd
Off current Ioff
with Vgs = 0
Gate delay D
C is gate capacitance of a characteristic inverter

## Slide 16: Single-Vth Design of Sub-threshold Circuits
Circuit delay Tc
C is gate capacitance of a characteristic inverter, Ceff is average switched capacitance per clock cycle in the circuit, l is the length of critical path in terms of a characteristic inverter
Vth factor is
canceled out

## Slide 17: General Dual-Vth Design Procedure
Low Vth gate is fast but more leaky;
used on critical paths to maintain high speed
High Vth gate is slow but less leaky;
used on non-critical paths to reduce leakage
Normally, start with assigning low Vth to all gates
and switch as many gates as possible to high Vth to reduce leakage [2]
[2] D. Flynn, R. Aitken, A. Gibbons and K. Shi, Low Power Methodology Manual: For System-on-Chip Design. New York: Springer, 2007

## Slide 18: Dual-Vth Minimum EPC Design
Dual Vth design reduces EPC by
inserting high Vth gates to reduce leakage power while keeping the operating frequency unchanged
  This is the maximum operating frequency obtained for the single low Vth design
For given circuit netlist, the proposed framework uses the gate slack based algorithm to generate optimum dual-Vth design with minimum EPC, optimum Vdd, optimum high Vth level and estimate the EPC

## Slide 19: Example
Assuming each gate has one unit time (t0) of gate delay, gate 9 is regarded as non-critical path gate. However, if gate 9 is a high Vth gate with 4 t0 delay, a new critical path would be created. The critical path delay would be changed from 6 t0 to 8 t0

## Slide 20: Gate Slack Based Dual-Vth Algorithm *
Name | Definition
Tpi (i) | the longest time for an event to arrive from PI to gate i
Tpo (i) | the longest time for an event to reach a PO from gate i
D (i) | Gate delay of gate i
Dp (i) | The path delay of the longest path through gate i Dp (i) = Tpi (i) + Tpo (i) + D (i)
Tc | Critical path delay of the whole circuit Tc = Max { Dp (i) }
S (i) | Gate slack S (i) = Tc – Dp (i)
Dh (i) , Dl (i) | Gate delay of gate i with low Vth or high Vth
Delta (i) | Gate delay difference for gate i Delta (i) = Dh (i) – Dl (i)
Su | Upper boundary for slack Su = (k-1) / k * Tc and k = Tc’ / Tc
Sl | Lower boundary for slack Sl = Min { Delta (i) }
* Note: Algorithm is modified for dual-Vth design based on previous work in [14-17]

## Slide 21: Gate Slack Based Dual-Vth Algorithm
Step 1: Library Characterization
  Construct high Vth gate by applying different
  reverse body bias voltages on PTM HS model
Low Vth Gate
zero bias
High Vth Gate
reverse bias = 0.1 V
Body bias | Threshold voltage | 
 | NMOS | PMOS
zero bias | 0.328 V | -0.291 V
bias = 0.1V | 0.348 V | -0.309 V
bias = 0.2 V | 0.367 V | -0.327 V
bias = 0.3 V | 0.385 V | -0.344 V
bias = 0.4 V | 0.402 V | -0.360 V
bias = 0.5 V | 0.419 V | -0.375 V
bias = 0.6 V | 0.435 V | -0.389 V
bias = 0.7 V | 0.450 V | -0.403 V
bias = 0.8 V | 0.465 V | -0.417 V
Threshold voltage of PTM 32nm bulk CMOS technology HS models with varying reverse bias voltages calculated by HSPICE at Vdd = 0.9 V

## Slide 22: Gate Slack Based Dual-Vth Algorithm
Step 1: Library Characterization
  Calculate gate delay, power consumption, nodal capacitance of basic logic gates under varying Vdd, Vth, fan-out conditions
Step 2: Initialization
Assign each gate to low Vth initially
Step 3: First Round of Selection
Run Static Timing Analysis (STA),
If S (i) > Su, gate i can directly switch to high Vth
If S (i) < Sl, gate i can never switch to high Vth
If S (i) > Delta (i), gate i can possibly switch

## Slide 23
Gate slack analysis for 8-bit Ripple Carry Adder
Su
35
Sl
37

## Slide 24: Gate Slack Based Dual-Vth Algorithm
Step 4: Verification
For any gate j selected in step 3, switch it to high Vth, and re-run STA to calculate circuit delay Tc,
If newly calculated Tc_new ! > original Tc, gate j can switch to high Vth
Step 5: Results
Generate dual Vth design, estimate EPC and
find out optimum Vdd and high Vth level with lowest
EPC
EPC estimation
Ceff (i) = α (i) * C (i) = the product of gate output activity and nodal capacitance
C (i) and Pleak (i) are obtained from HSPICE simulations of basic logic gates under varying conditions, α (i) is obtained from Modelsim simulations with real gate delays

## Slide 25: Implementation Results 32-bit RCA
HSPICE simulations of EPC for 32-bit RCA single and dual-Vth designs
in PTM 32nm bulk CMOS technology with Wp=12L and Wn=5L
Single-Vth design
Min EPC = 2.268E-014 J
Optimum Vdd = 0.31V
Frequency = 3.99 MHz
Dual-Vth design
Min EPC = 1.610E-014J
Optimum Vdd = 0.24V
Optimum Bias = 0.3V
Frequency = 0.82 MHz
Min EPC reduction: 29%

## Slide 26: Implementation Results 32-bit RCA
High Vth Vs. Normalized minimum EPC points
from single-Vth and dual-Vth designs
High Vth Vs. Optimal Vdd points
from single-Vth and dual-Vth designs
Single low
Vth design
Single high
Vth design
Single low
Vth design
Single high
Vth design
Bias = 0.3V
Bias = 0.3V

## Slide 27: Implementation Results Summary
Circuit Name | Single-Vth Emin | Single-Vth Vddopt | Dual-Vth Emin | Dual-Vth Vddopt | Emin Drop
4-by-4 Multiplier | 7.59 E-15 J | 0.26 V | 6.77 E-15 J | 0.21 V | 10.8%
C432 | 7.21 E-15 J | 0.28 V | 6.32 E-15 J | 0.26 V | 12.4%
C499 | 2.13 E-14 J | 0.27 V | 1.85 E-14 J | 0.26 V | 13.2%
C880 | 1.43 E-14 J | 0.25 V | 1.06 E-14 J | 0.22 V | 25.9%
C1355 | 1.98 E-14 J | 0.26 V | 1.73 E-14 J | 0.24 V | 12.28%
C1980 | 3.14 E-14 J | 0.27 V | 2.68 E-14 J | 0.25 V | 14.52%
C2670 | 5.09 E-14 J | 0.22V | 3.71 E-14 J | 0.19V | 27.1%
32 RCA | 2.26 E-014 J | 0.31V | 1.610 E-014 J | 0.24 V | 29%
Minimum EPC reduction is between 10.8% and 29% from
4-by-4 multiplier and 32-bit RCA respectively

## Slide 28: Implementation Results Estimation Accuracy
HSPICE Simulation
Min EPC = 1.61E-014J
Optimum Vdd = 0.24V
Estimation
Min EPC = 1.77E-014J
Optimum Vdd = 0.25V
The average error
between estimation and
simulation is 6.99%
HSPICE simulations Vs. estimation for EPC for 32-bit RCA dual-Vth design at bias = 0.3V in PTM 32nm bulk CMOS technology

## Slide 29: Result Analysis
Minimum EPC occurs
when dynamic energy is equal to leakage energy
Minimum EPC reduction comes from Vdd reduction
Reduction of leakage
energy comes from
leakage power reduction
and unchanged circuit
period
Dynamic energy and leakage energy analysis for 32-bit RCA single-Vth and dual-Vth design

## Slide 30: Results Analysis
Theoretical analysis to verify the observed 29%
minimum EPC reduction on 32-bit RCA
  Step 1: Leakage energy characterized as 3rd degree polynomials
  based on HSPICE simulation results on leakage power of 32-bit RCA with single low Vth or high Vth (with bias=0.3V) as well as circuit delay with single low Vth
where p1 = -2.9 E-12, p2 = 3.46 E-12,
p3 = -1.4 E-12 and p4 = 1.95 E-13
where h1 = -3.4 E-13, h2 = 4.19 E-13,
h3 = -1.75 E-13 and h4 = 2.54 E-14
RMSE and regression coefficient R-squared analysis of polynomial fit for leakage energy

## Slide 31: Results Analysis
  Step 2: Dynamic energy characterized as 2nd degree polynomial
  based on HSPICE simulation results on total energy and leakage energy of 32-bit RCA with single low Vth
Where a = 1.65 E-13 and b = -2.1 E-16
  Step 3: Single-Vth design
Optimal Vdd = 0.305 V
where p1 = -2.9 E-12, p2 = 3.46 E-12, p3 = -1.4 E-12, p4 = 1.95 E-13
a = 1.65 E-13 and b = -2.1 E-16

## Slide 32: Results Analysis
  Step 4: Dual-Vth design
  X = fraction of high Vth gates in the circuit and
  1- X = fraction of low Vth gates
Optimal Vdd = 0.254 V
Where K1 = x * h1 + (1-x) * p1
K2 = x * h2 + (1-x) * p2 + a
K3 = x * h3 + (1-x) * p3
K4 = x * h4 + (1-x) * p4 +b
X = 198/288 in optimal dual-Vth design
where p1 = -2.9 E-12, p2 = 3.46 E-12, p3 = -1.4 E-12, p4 = 1.95 E-13, a = 1.65 E-13, b = -2.1 E-16, h1 = -3.4 E-13, h2 = 4.19 E-13, h3 = -1.75 E-13 and h4 = 2.54 E-14

## Slide 33: Results Analysis
  Step 5: Calculate minimum EPC saving between single-low Vth and dual-Vth design
HSPICE simulation results vs. theoretical analysis of energy ratio of 32-bit RCA dual-Vth design with bias = 0.3V and single-Vth design
Single
Low Vth
Single
High Vth
Dual Vth
Theoretical results show
minimum EPC saving is
33.4 %
Blue curve only express
a lower bound of energy
saving
In practical, circuit delay
increases as Vth in
single-Vth design increseas

## Slide 34: Outline
Motivation
Backgroud
Contributions of This Work
Future Work
Conclusion

## Slide 35: Future Work
Robust Dual-Vth Design
Why do we need robust design?
Process variation causes variance in circuit performance
and lower yield
Process variation issue gets worse in sub-threshold
circuits due to exponential relation between Isub and Vth

## Slide 36: Future Work
Combine Dual-Vth with Different
Low Power Design Methods
Dual-Vth only reduces leakage energy
Dual-Vth and Dual-Vdd : Reduce both dynamic and leakage energy
Dual-Vth and Transistor Sizing: Reduce both dynamic and leakage

## Slide 37: Outline
Motivation
Backgroud
Contributions of This Work
Future Work
Conclusion

## Slide 38: Conclusion
EPC of single-Vth design is independent of Vth
Dual-Vth approach is effective to suppress leakage and
reduce minimum EPC
For given circuit, the proposed framework uses the gate slack based algorithm to generate optimum dual-Vth design with minimum EPC, optimum Vdd, optimum high Vth level and estimate the EPC
For 32-bit RCA, minimum EPC is reduced by 29% by dual-Vth approach; for 4-by-4 multiplier, minimum EPC is reduced by 10.8%; for ISCAS85 benchmark circuits, energy saving is between this range

## Slide 39
[1] A. Wang, B. H. Calhoun and A. P. Chandrakasan, Sub-threshold design for ultra low-power systems, Springer, 2006
[2] D. Flynn, R. Aitken, A. Gibbons and K. Shi, Low Power Methodology Manual: For System-on-Chip Design, New York: Springer, 2007
[3] M. Degrauwe, J. Rijmenants, E. Vittoz, and H. D. Man, “Adaptive biasing CMOS ampliers,” IEEE Journal of Solid State Circuits, vol. 17, no. 13, pp. 522-528, June 1982.
[4] E. Vittoz, “Micropower switched-capacitor oscillator," IEEE Journal of Solid State Circuits, vol. 14, no. 3, pp. 622-624, June 1979.
[5] E. Vittoz, \Quartz oscillators for watches," Proceeding 10th International Congress of Chronometry, pp. 131-140, 1979.
[6] Y. P. Tsividis and R. W. Ulmer, “A CMOS voltage reference," IEEE Journal of Solid State Circuits, vol. 13, no. 6, pp. 774-778, December 1978.
[7] E. Vittoz and F. Krummenacher, “Micropower SC filters in Si-gate CMOS technology," Proceeding ECCTD'80, pp. 61-72, 1980.
[8] A. P. Pentland, M. Petrazzouli, A. Gerega, A. P. Pentland, and T. Starner, “Digital doctor: An experiment in wearable telemedicine," Proceeding of Intl. Symp. on Wearable Computers, pp. 173-174, October 1997.
References

## Slide 40
[9] L. A. Geddes, “Historical highlights in cardiac pacing," IEEE Engineering in Medicine and Biology Magazine, pp. 12-18, June 1990.
[10] C. H. Kim, H. Soeleman, and K. Roy, “Ultra-low-power DLMS adaptive filter for hearing aid applications," IEEE Tran. Very Large Scale Integration (VLSI) Systems, vol. 11, no. 6, pp.1058-1067, December 2003
[11] A. Wang and A. Chandrakasan, “A 180mV FFT Processor Using Sub-threshold Circuit Techniques,” in IEEE International Solid-State Circuits Conference Digest of Technical Papers, 2004, pp. 292–529.
[12] B. Zhai et al., “A 2.60pJ/Inst Sub-threshold Sensor Processor for Optimal Energy Efficiency,” Proc. of Symposium on VLSI circuits, 2006, pp.154-155
[13] J. Kwong et al, “A 65nm Sub-Vt Microcontroller with Integrated SRAM and Switched-Capacitor DC-DC Converter,” Proc. ISSCC, 2008.
[14] K. Kim, Ultra Low Power CMOS Design, PhD thesis, Auburn University, ECE Dept., Auburn, AL, May 2011.
[15] K. Kim and V. D. Agrawal, “Dual voltage design for minimum energy using gate slack,” Proc. of IEEE Intl. Conf. on Industrial Technology, March 2011, pp. 419-424.
[16] M. Allani, Polynomial-time algorithms for designing dual-voltage energy efficient circuits, Master's thesis, Auburn University, ECE Dep., Auburn, AL, December 2011.
References

## Slide 41: References
[17] M. Allani and V. D. Agrawal, “Energy-Efficient Dual-Voltage Design using Topological Constraints,” Journal of Low Power Electronics, vol. 9, no. 3, pp. 275-287, October 2011
[18] J. Yao and V. D. Agrawal, “Dual-Threshold Design of Sub-Threshold Circuits,” in Proc. IEEE SOI-3D-Subthreshold Microelectronics Technology Conference, Oct. 2013, pp. 77–78.
[19] J. Yao and V. D. Agrawal, “Dual-Threshold Voltage Design of Ultra-Low Voltage Circuits,” submitted to IEEE Custom Integrated Circuits Conference 2014

## Slide 42
Thank You