ELEC 2200-002 Digital Logic Circuits 
Fall 2008

Homework 1 Problems

Assigned 8/25/08, due 9/3/08

Problem 1: Perform binary addition of five-bit string, 01111 and 11011. Ignore the final carry, if any. Interpret these and the sum string as decimal integers assuming that they are: (a) 2’s complement integers, (b) 1’s complement integers, and (c) signed integers. Verify correctness of the addition for the three cases.

Problem 2: For following five-bit 2’s complement binary integers, perform addition, check overflow and verify correctness of results by interpreting numbers as decimal integers:

- 01100 + 01001

- 01100 + 10111

Problem 3: For five-bit 2’s complement integers perform the subtraction 10111 – 00011.

Problem 4: Devise a simple circuit to convert five-bit 2’s complement integers into eight-bit 2’s complement integers.