ELEC 2200-002 Digital Logic Circuits 
Fall 2008

Homework 6 Problems

Assigned 10/22/08, due 10/29/08

# Problem 1: Using Karnaugh map, find the minimum sum of products (MSOP) form for the four-variable Boolean function:

# F(A,B,C,D) = ( m(1, 4, 5, 7, 13) + d(0, 6, 14, 15)

# Problem 2: Using the consensus theorem and absorption theorem, find all prime implicants (PI) of the function,

# (Corrected)

# Show that there are no essential prime implicants (EPI). Find the MSOP form. Illustrate all PI’s on Karnaugh map.

# Problem 3: Use the Quine-McCluskey method to minimize the Boolean function,

# F(A,B,C,D) = ( m(0, 1, 3, 4, 5, 6, 7, 11, 14)

# Show the final result on Karnaugh map.