ELEC 2200-001 Digital Logic Circuits 
Fall 2010

Homework 3 Problems

Assigned 9/21/10, due 9/28/10

Answer the following questions, selecting just one answer per question.

--------------------------------------------------------------------------------------------

1. What types of electronic circuits does a transceiver contain?

- Digital

- Analog

- Memory

(  Combination of RF, mixed-signal and digital

- None of the above

--------------------------------------------------------------------------------------------

2. What are the five building blocks of a digital computer?

- Memory, logic, passive and active componnets

(   Datapath, control, memory, input and output

- Display screen, keyboard, mouse, power supply and cooling fan

- Transistors, chips, resistors, capacitors and inductors

- Hardware, software, firmware, programmer and operator

--------------------------------------------------------------------------------------------

3.  What is the radix for binary numbers?

- 16

- 10

- 8

- 4

(   2

--------------------------------------------------------------------------------------------

4.  What format does a modern digital computers use to represent integers?

- Signed magnitude

- Decimal

- 1’s complement

(    2’s complement

- IEEE 754

--------------------------------------------------------------------------------------------

5.  How can you tell whether a 2’s complement integer is positive or negative?

- By complementing all bits

- By complementing all bits and then adding 1

- Negative if adding the number to its magnitude produces 0, otherwise positive

(   Positive if MSB = 0, negative if MSB = 1

- Negative if MSB = 0, positive if MSB = 1

---------------------------------------------------------------------------------------------

6. One-bit right shift divides a 2’s complement integer by 2. How should the MSB be filled during the shift?

- Leave blank

- Fill 0

- Fill 1

(   Copy pre-shift MSB

- Copy pre-shift LSB

--------------------------------------------------------------------------------------------

7. One-bit left shift multiplies a 2’s complement integer by 2. How should the LSB be filled during the shift?

- Leave blank

(   Fill 0

- Fill 1

(   Copy pre-shift MSB

(   Copy pre-shift LSB

--------------------------------------------------------------------------------------------

8. What is the negation rule for 2’s complement numbers?

- Invert the MSB

- Invert all bits

(  Invert all bits and add 1

- Change MSB to 1

- Invert all bits and subtract 1

--------------------------------------------------------------------------------------------

9. What indicates overflow when two n-bit 2’s complement integers are added?

- A carry of 1 is generated when MSB’s are added

- Two numbers being added have opposite signs

- Two numbers being added have the same sign

(   The two numbers have the same MSB, which differs from the MSB of sum

- None of the above

--------------------------------------------------------------------------------------------

10. Which is the fastest n-bit adder circuit?

- Ripple-carry adder, time complexity O(n)

- Carry-skip adder; time complexity O(√n)

(   Carry look-ahead adder; time complexity O(log2n)

- Carry-select adder; time complexity O(√n)

- None of the above

--------------------------------------------------------------------------------------------

11. What is the critical path of a digital circuit?

- Input to output path with largest number of gates

(   Input to output combinational path with longest delay

- Path that is always active

- Path that is never active

- Fastest signal path between input and output

--------------------------------------------------------------------------------------------

12. What is the number of bits needed to hold the product of two n-bit 2’s complement integers?

- n

- More than n

(   2n

- n +1

- n2

--------------------------------------------------------------------------------------------

13. What is the time complexity of an array multiplier?

(   O(n)

- O(n2)

- O(n1.5)

- O(n log n)

- Exponential in n

--------------------------------------------------------------------------------------------

14. How many iterations does binary division of n-bit integers require?

- 1

- Many until the result converges

- n/2

(   Exactly n

- n2

--------------------------------------------------------------------------------------------

15. What is the Hamming distance between two n-bit binary vectors?

- Cartesian distance between the tips of the two vectors

- Manhattan distance

- 0 ≤ Hamming distance ≤ n

- Number of bits in which the two binary vectors match

(   Number of bits in which the two binary vectors differ

--------------------------------------------------------------------------------------------

16. How many error bits can a single parity bit detect?

(   Any odd number

- Any even number

- 1

- 2

- None

--------------------------------------------------------------------------------------------

17. What is the bias used for the exponent of an IEEE 754 floating point number?

- None

- 255

- – 255

- Biased exponent = true exponent – 127

(   Biased exponent = true exponent + 127

--------------------------------------------------------------------------------------------

18. How will you determine the sign of an IEEE 754 floating point number?

- All numbers above certain threshold are negative

- MSB = 0 for negative, MSB = 1 for positive

(   MSB = 0 for positive, MSB = 1 for negative

- Always positive

- Cannot tell

--------------------------------------------------------------------------------------------

19. What is the decimal value of the 32-bit floating point number, 1 10000001 1100 0000 0000 0000 0000 000, represented in the IEEE 754 format?

- 7.0

(   – 7.0

- Negative 0

- Negative infinity

- 0, due to underflow

--------------------------------------------------------------------------------------------

20. How are two floating point numbers in IEEE 754 format multiplied by a digital circuit?

- Both numbers converted to integers and multiplied

- Convert multiplier to integer and add multiplicand to itself that many times

- Numbers converted to logarithms and added

(   Multiply significands, add exponents, normalize, roundoff, add sign (corrected)

- Cannot be done