ELEC 2200-003 Digital Logic Circuits 
Fall 2011

Homework 1 Problems

Assigned 8/22/11, due 8/29/11

# Problem 1: Find the decimal values of 6-bit binary strings, 000101, 100110, 111001 and 111000, assuming that their format is (a) signed integer, (b) 1’s complement, (c) 2’s complement.

Problem 2: Perform binary addition of five-bit binary numbers, 01110 and 11111. Ignore the final carry, if any, to obtain a five-bit result. Interpret these and the sum strings as decimal integers assuming that they are: (a) 2’s complement integers, (b) 1’s complement integers, and (c) signed integers. Verify correctness of the addition for the three cases.

Problem 3: For following four-bit 2’s complement binary integers, perform addition, check overflow and verify correctness of results by converting numbers as decimal integers:

- 0100 + 0100

- 0111 + 1001

# Problem 4: Add the following pairs of 4-bit 2’s complement integers. If an overflow occurs, then expand the numbers to 8-bit representation and add:

# 0101 + 1101

# 1011 + 1101

# 1011 + 1011

Problem 5: Devise a simple circuit to convert four-bit 2’s complement integers into eight-bit 2’s complement integers.