ELEC 2200-003 Digital Logic Circuits 
Fall 2011

Homework 2 Problems

Assigned 9/2/11, due 9/12/11

# Problem 1: Using the method of positive binary integer multiplication, multiply 4-bit 2’s complement integers, 1110 × 1101, to obtain an 8-bit result. Show the steps of computation.

# Problem 2: Multiply 4-bit 2’s complement integers, 1110 × 1101, using the direct multiplication of 2’s complement integers. Show the steps of computation.

# Problem 3: Carry out the calculation steps for 4-bit binary division of positive numbers 1001/0100 (i.e., 9/4) using the restoring division algorithm.

# Problem 4: Carry out the calculation steps for 4-bit binary division of positive numbers 1001/0100 (i.e., 9/4) using the non-restoring division algorithm.