ELEC 2200-002 Digital Logic Circuits 
Fall 2015

Homework 1 Solution

Assigned 9/8/14, due 9/16/14

# Problem 1: Find the decimal values of 5-bit binary strings, 01100, 00110, 11001 and 11000, assuming that their format is (a) signed integer, (b) 1’s complement, or (c) 2’s complement.

Answer:

| Binary number | Decimal value |
| --- | --- |
|  | Signed integer (a) | 1’s complement (b) | 2’s complement (c) |
| 001100 | 12 | 12 | 12 |
| 100110 | 6 | 6 | 6 |
| 111001 | – 9 | – 6 | – 7 |
| 111000 | – 8 | – 7 | – 8 |

Problem 2: Perform binary addition of four-bit binary numbers, 01110 and 11111. Ignore the final carry, if any, to obtain a five-bit result. Determine the decimal values for the two given and the sum binary strings assuming that they are: (a) 2’s complement integers, (b) 1’s complement integers, and (c) signed integers. Verify correctness of the addition for the three cases.

Answer:

0110

+	1111

0101

- 2’s complement, 6 + (– 1) = 5, result is correct.

- 1’s complement, 6 + (– 0) ≠ 5, result is incorrect.

- Signed integers, 6 + (– 7) ≠ 5, result is incorrect.

Problem 3: For following four-bit 2’s complement binary integers, perform addition, check overflow and verify correctness of results by converting numbers as decimal integers:

- 0100 + 0100

- 0111 + 1001

Answer:

- 0100 + 0100 = 1000 (overflow), or in decimal 4 + 4 ≠ – 8, result is incorrect due to overflow.

- 0111 + 1001 = 0000 (no overflow), or in decimal 7 + (– 7) = 0, result is correct.

# Problem 4: Add the following pairs of 4-bit 2’s complement integers. If an overflow occurs, then expand the numbers to 8-bit representation and add:

# 0101 + 1101

# 1011 + 1101

# 1011 + 1011

# Answer:

# 0 1 0 1

# + 1 1 0 1

# 0 0 1 0	no overflow, result is correct (5 – 3 = 2)

# 1 0 1 1

# + 1 1 0 1

# 1 0 0 0	no overflow, result is correct (– 5 – 3 = – 8)

# 1 0 1 1

# + 1 0 1 1

# 0 1 1 0	overflow, because MSB = 1 indicates that the two numbers have same (negative) sign and the sum has opposite (positive) sign (MSB = 0).

# We extend the representations to 8 bits and add:

# 1 1 1 1 1 0 1 1

# + 1 1 1 1 1 0 1 1

# 1 1 1 1 0 1 1 0	no overflow, result is correct (– 5 – 5 = – 10)

# Problem 5: Multiply 4-bit 2’s complement integers, 0110 × 1100, using the direct multiplication (i.e., without separating the signs) of 2’s complement integers. Show the steps of computation.

# Answer: The table below shows the multiplication:

# Multiplicand = 0110,	Multiplier = 1100

# –	Multiplicand = 1010

| Iteration | Action | 5-bit Multiplicand | 9-bit Product |
| --- | --- | --- | --- |
| 0 | Initialize Product = 00000, multiplier | 00110 | 00000 1100 |
| 1 | Product LSB = 0, do nothing |  | 00000 1100 |
|  | Right shift Product |  | 00000 0110 |
| 2 | Product LSB = 0, do nothing |  | 00000 0110 |
|  | Right shift Product |  | 00000 0011 |
| 3 | Product LSB = 1, add Multiplicand |  | 00110 0011 |
|  | Right shift Product |  | 00011 0001 |
| 4 | Product LSB = 1, subtract* Multiplicand |  | 11101 0001 |
|  | Right shift Product |  | 11110 1000 |

# * Subtract because this is the last iteration.

# Final 8-bit Product = 11101000

# Product is negative, magnitude = 00011000 = 24, Product =  – 24

# Verification: (6) × (– 4) = – 24

# Problem 6: Carry out the calculation steps for 4-bit binary division of positive numbers 1000/0101 (i.e., 8/5) using the restoring division algorithm.

# Answer: Restoring division (R: 5-bit remainder, Q: 4-bit quotient, M: 5-bit divisor):

| Iteration | Step | Action | $R | $Q | $M |
| --- | --- | --- | --- | --- | --- |
| 0 |  | Initialization | 00000 | 1000 | 00101 |
| 1 | 1 | 1-bit left shift on ($R, $Q) | 00001 | 0000 | 00101 |
|  | 2 | Add – $M = 11011 to $R | 11100 | 0000 | 00101 |
|  | 3 | MSB($R) = 1, restore, add $M = 00101 to $R | 00001 | 0000 | 00101 |
| 2 | 1 | 1-bit left shift on ($R, $Q) | 00010 | 0000 | 00101 |
|  | 2 | Add – $M = 11011 to $R | 11101 | 0000 | 00101 |
|  | 3 | MSB($R) = 1, restore, add $M = 00101 to $R | 00010 | 0000 | 00101 |
| 3 | 1 | 1-bit left shift on ($R, $Q) | 00100 | 0000 | 00101 |
|  | 2 | Add – $M = 11011 to $R | 11111 | 0000 | 00101 |
|  | 3 | MSB($R) = 1, restore, add $M = 00101 to $R | 00100 | 0000 | 00101 |
| 4 | 1 | 1-bit left shift on ($R, $Q) | 01000 | 0000 | 00101 |
|  | 2 | Add – $M = 11011 to $R | 00011 | 0000 | 00101 |
|  | 3 | MSB($R) = 0, LSB($Q) = 1 | 00011 | 0001 | 00101 |

# Result: Quotient $Q = 0001 = 1, Remainder $R = 00011 = 3

# Problem 7: Carry out the calculation steps for 4-bit binary division of positive numbers 1001/0100 (i.e., 9/4) using the non-restoring division algorithm.

# Answer: Non-restoring division (R: 5-bit remainder, Q: 4-bit quotient, M: 5-bit divisor):

| Iteration | Step | Action | R | Q | M |
| --- | --- | --- | --- | --- | --- |
| 0 | 0 | Initialization: R = 0, Q = dividend = 1001, M = divisor = 00100, – M = 11100 | 00000 | 1001 | 00100 |
| 1 | 1 | 1-bit left shift (R, Q) | 00001 | 0010 | 00100 |
|  | 2 | Add (– M) = 11100 to R | 11101 | 0010 | 00100 |
|  | 3 | Since MSB(R) = 1, set LSB(Q) = 0 | 11101 | 0010 | 00100 |
| 2 | 1 | 1-bit left shift (R, Q) | 11010 | 0100 | 00100 |
|  | 2 | Iter# 1 MSB(R) = 1, Add M = 00100 to R | 11110 | 0100 | 00100 |
|  | 3 | Since MSB(R) = 1, set LSB(Q) = 0 | 11110 | 0100 | 00100 |
| 3 | 1 | 1-bit left shift (R, Q) | 11100 | 1000 | 00100 |
|  | 2 | Iter# 2 MSB(R) = 1, Add M = 00100 to R | 00000 | 1000 | 00100 |
|  | 3 | Since MSB(R) = 0, set LSB(Q) = 1 | 00000 | 1001 | 00100 |
| 4 | 1 | 1-bit left shift (R, Q) | 00001 | 0010 | 00100 |
|  | 2 | Iter# 3 MSB(R) = 0, Add (– M) = 11100 to R | 11101 | 0010 | 00100 |
|  | 3 | Since MSB(R) = 1, set LSB(Q) = 0 and add M to R | 00001 | 0010 | 00100 |

# Result: Quotient Q = 0010 = 2, Remainder R = 00001 = 1

# Problem 8:  For 3-bit 2’s complement binary integers, construct 4-bit even and odd parity codes by adding a parity bit in the most significant bit position.

# Answer: The following table gives the codes with the first bit as parity:

| Decimal number | 2’s complement | Even parity code | Odd parity code |
| --- | --- | --- | --- |
| 0 | 000 | 0 000 | 1 000 |
| 1 | 001 | 1 001 | 0 001 |
| 2 | 010 | 1 010 | 0 010 |
| 3 | 011 | 0 011 | 1 011 |
| – 4 | 100 | 1 100 | 0 100 |
| – 3 | 101 | 0 101 | 1 101 |
| – 2 | 110 | 0 110 | 1 110 |
| – 1 | 111 | 1 111 | 0 111 |

# Problem 9: Consider a set of n-bit binary vectors {Xi} such that for any pair of distinctly different vectors the Hamming distance (HD) ≥ p, where p ≤ n. Suppose, we also have another set of m-bit binary vectors {Yj} such that any pair of them has HD ≥ q, where q ≤ m. We form a new set of (n + m) bit binary vectors {Zij} by concatenating the bits of Xi and Yj. Show that for any pair of vectors Zij and Zkl from the new set, such that i ≠ k and j ≠ l, the HD ≥ p + q.

# Answer: The required result follows from the fact that HD is always a positive integer. Let us consider a vector Zij obtained by concatenating the bits of Xi and Yj. Similarly, consider another vector Zkl obtained by concatenating the bits of Xk and Yl. Then, we have,

# HD(Zij, Zkl)	=	Distance contribution of X bits + distance contribution of Y bits

# =	HD(Xi, Xk) + HD(Yj, Yl)

# Because i ≠ k, HD(Xi, Xk) ≥ p, and because j ≠ l, HD(Yj, Yl) ≥ q. Therefore,

# HD(Zij, Zkl)	≥	p + q								■

Problem 10: A digital system uses four symbols, A, B, C and D. For these symbols:

- Define a minimum length binary code. What is the minimum Hamming distance between any pair of codes?

- Define a minimum length binary code such that any single-bit error can be detected. What is the Hamming distance between any pair of codes?

Answer:

- For four symbols, we need a two-bit code, which allows four patterns. A possible assignment is: 00 – A, 01 – B, 10 – C, and 11 – D. For any pair of these codes, HD ≥ 1, i.e., minimum Hamming distance is 1.

- A single-bit error can be detected by adding a parity bit. Suppose we add even parity to the codes in (a) as MSB: 000 – A, 101 – B, 110 – C and 011 – D. For this code, HD = 2 for any pair of codes, which satisfies the requirement HD ≥ 2 for single-bit error detection.

Problem 11: Find the decimal values for the following 32-bit floating point numbers expressed in the IEEE 754 format

- 1 10000000 10000000000000000000000

- 1 01111111 00000000000000000000000

- 0 10000111 00010001000000000000000

Answer:

- Sign: Number is negative because sign bit = 1.

Exponent: Interpreting 10000000 as unsigned integer, its value is 128. Unbiased exponent = 128 – 127 = 1

Significand: 1 + 2 – 1 = 1.5

Number 	= 	– 1.5 × 21 	=	– 3.0

- Sign: Number is negative because sign bit = 1.

Exponent: Interpreting biased exponents 01111111 as unsigned integer, its value is 127.

Unbiased exponent = 127 – 127 = 0

Significand = 1.0

Number 	= 	– 1.0 × 20 	=	– 1.0

- Sign: Number is positive because sign bit = 0.

Exponent: Interpreting 10000111 as unsigned integer, its value is 135.

Unbiased exponent = 135 – 127 = 8.

Significand = 1.00010001 = 1 + 2 – 4 + 2 – 8

Number 	= 	(1 + 2 – 4 + 2 – 8) × 28

=	(28 + 24 + 1)

=	(256 + 16 + 1)	=	 273

Problem 12: Consider the following 32-bit real numbers in the IEEE 754 format,

X = 0 10001001 00000000000000000000000

Y = 0 10000010 01000000000000000000000

- What are decimal values of X and Y?

- Determine X + Y using the binary addition method for real numbers. Express the result in the IEEE 754 format.

- Perform binary multiplication X × Y, expressing the result in IEEE 754 format.

Answer:

- X: MSB is 0, number is positive.

Real exponent = biased exponent – 127 = 10001001 + 10000001 = 00001010

Significand = 1.0

X = + 1.0 × 21010 or 1.0 × 210ten = 1,024

Y: MSB is 0, number is positive.

Real exponent = biased exponent – 127 = 10000010 + 10000001 = 00000011

Significand = + 1.01 × 211 or (1 + 0.25) × 23ten = 1.25 × 8 = 10

- Addition X+Y:

Equalize exponents:

X has larger exponent, difference = 00001010 – 00000011 = 111 = 7

Binary point of Y is moved 7 positions to the left and significands are added:

Significand of X:	1.00000000000000000000000

Significand of Y:	0.00000010100000000000000

Significand of X+Y:	1.00000010100000000000000

X+Y in IEEE 754 format:

0 10001001 00000010100000000000000

Decimal value of X+Y = (1 + 2–7 + 2–9) × 210ten = 1,034

- Multiplication X×Y:

Add real (unbiased) exponents	   00001010

+ 00000011

00001101 or 1310

For biased exponent, add 127		+ 01111111

Biased exponent is			   10001100

Multiply significands: Because Significand (X) = 1.0

Significand (X×Y) = Significand (Y)

X×Y in IEEE 754 format:

0 10001100 01000000000000000000000

Decimal value of X×Y = (1 + 2–2) × 213ten = 10,240