ELEC 2200-002 Digital Logic Circuits 
Fall 2015

Homework 2 Problems

Assigned 9/28/15, due 10/5/15

Problem 1: Prove that the number of elements in a Boolean algebra must be even.

# Problem 2: For two elements, a and b, of a Boolean algebra, use axioms to prove that:

# Problem 3: For three variables a, b and c of a Boolean algebra, use Venn diagram to prove that:

# Problem 4: Show that a two-valued switching algebra of variables that can take only two values {0, 1} and contains OR (+) and AND (·) operations is a Boolean algebra. The two operations are defined as follows:

| OR (+) | 0 | 1 |
| --- | --- | --- |
| 0 | 0 | 1 |
| 1 | 1 | 1 |

| AND (·) | 0 | 1 |
| --- | --- | --- |
| 0 | 0 | 0 |
| 1 | 0 | 1 |

# Hint: Verify postulates 1 through 6 of Boolean algebra. One way to verify the correctness of an equation is to use a method called the perfect induction, where the equation is satisfied by all possible combinations of values assigned to the variables occurring in the equation.

# Problem 5: A house alarm system is designed to sense several conditions represented by binary (0,1) Boolean variables, A, F, M, and W, defined as:

# A	=	1	means alarm is activated (usually when house is unoccupied)

# F	=	1	means smoke is detected

# M	=	1	means motion is detected

# W	=	1	Window or door sensor activated due to a possible break-in

# Write an expression for a Boolean function B(A,F,M,W), such that B = 1 will sound a buzzer when smoke is detected, or when alarm is active and either motion is detected or a break-in occurs. Sketch a relay network to connect a battery to the buzzer.