ELEC 2200-002 Digital Logic Circuits 
Fall 2015

Homework 3 Problems

Assigned 10/14/15, due 10/23/15

# Problem 1:

# What is the total number of minterns possible with n Boolean variables?

# How many distinctly different switching functions of four Boolean variables are possible?

# Using the postulates and theorems of Boolean algebra, show that for three binary variables A, B and C,

# Problem 2: Consider Boolean function of three variables, F(a, b, c) = Σ m (3, 4, 5, 6, 7):

# Construct a truth table for this function.

# Show the function on Karnaugh map.

# Minimize the function using Karnaugh map.

# Sketch a logic gate circuit that will implement the minimized function. How many transistors will this circuit require if implemented in CMOS technology?

# Can this function be implemented with fewer transistors? If yes, sketch the most economical gate-level circuit, specifying how many transistors it will need.

Problem 3: Express the following three-variable functions as sums of minterms:

Are these functions equivalent?

Problem 4: A microwave oven has a user operated on-off switch that controls a Boolean variable S such that S = 0 (off) and S = 1 (on). However, the power in the oven is not turned on as long as the door is open or the oven contains any metallic object in the cooking area. The door has a sensor that generates a Boolean variable D to indicate the state of the door such that D = 0 (open) and D = 1 (closed). The oven has a metal detector that sets a Boolean variable M as follows:

M = 1, when a metal object is present

M = 0, when there is no metal object found

Sketch a transistor-level CMOS circuit to generate a Boolean variable P from S, D and M, such that P = 1 will turn the power on.

# Problem 5: A 2’s complement binary adder circuit adds two integers whose most significant bits (MSB) are A and B. The MSB of the sum produced by the adder is C. Give a truth table for a Boolean variable Z that the adder should provide such that Z equals 1 only when an overflow has occurred. Express Z as a sum of products expression.